## Slide 1: IEEE 802.11 Auto TIG Consideration on existing systems and standards for ITS using IEEE802.11 technologies
Date: 11 November 2024
Authors:
Name | Company | Address Phone | Email
Friedbert Berens | FBConsulting Sarl |  | Friedbert.berens@me.com
John Kenney | Toyota Motor North America |  | jkenney@us.Toyota-itc.com

## Slide 2: Consideration on existing systems and standards for ITS using IEEE802.11 technologies
11. November 2024
John Kenney, Toyota Motor North America
Friedbert Berens, FBConsulting Sarl

## Slide 3: Overview
Groups working on Intelligent Transport Systems (ITS) based on IEEE802.11 technologies
  ETSI TC ITS
  Car2Car Communication consortium
  SAE
  IEEE 802.11 WG previously produced IEEE 802.11p and IEEE 802.11bd
Some deployed Use Cases in ITS based on IEEE802.11 technologies
  Awareness services (e.g. CAM, BSM) promoting road safety
  Cooperative Awareness messages (CPS) promoting road safety and automated driving
  Infrastructure based service like greenlight assistance, priority switches, etc. promoting road safety and traffic efficiency
Further discussions
Legend:
CAM = Cooperative Awareness Message
BSM = Basic Safety Message
CPS = Collective Perception Service

## Slide 4: ETSI TC ITS
TC ITS shall have responsibility:
  Development and maintenance of Standards, Specifications and other deliverables to support the development and implementation of ITS Service provision across the network, for transport networks, vehicles and transport users, including interface aspects and multiple modes of transport and interoperability between systems, but not including ITS application standards, radio matters, and EMC.
  Scope includes communication media, and associated physical layer, transport layer, network layer, security, lawful intercept and the provision of generic web services
  From: https://portal.etsi.org/TB-SiteMap/ITS/its-tor

## Slide 5: Awareness Services CAM and BSM
Cooperative Awareness Services:
  ETSI TS 103 900 V2.1.1 (2023-11): „Intelligent Transport Systems (ITS); Vehicular Communications; Basic Set of Applications; Cooperative Awareness Service; Release 2“
Basic Safety Message (BSM)
  SAE J2735 (2024): V2X Communications Message Set Dictionary
  SAE J3161/1: Onboard System Reqs for LTE-V2X V2X Safety Communications
Legend:
CAM = Cooperative Awareness Message
BSM = Basic Safety Message

## Slide 6: Advanced Services examples
ETSI draft TS 103 561 „Intelligent Transport Systems (ITS); Vehicular Communications; Basic Set of Applications; Manoeuvre Coordination Service (MCS) Specification; Release 2”
ETSI TS 103 324 V2.1.1 (2023/06) “Intelligent Transport System (ITS); Vehicular Communications; Basic Set of Applications; Collective Perception Service; Release 2”
SAE J3224 (2022): Sensor-Sharing for Cooperative and Automated Driving

## Slide 7: Example use cases for Manoeuvre Coordination Service (MCS)

## Slide 8: Example use case for Collective Perception Service (CPS)
Vehicle 2 is not equipped with C-ITS
Vehicle Ego cannot see Vehicle 2, but it is aware of Vehicle 3 via CAM
Vehicle 1 can see Vehicle 2 and can put this information into the CPM message
Vehicle Ego is thus aware of Vehicle 2 via the received CPM from Vehicle 1
CAM = Cooperative Awareness Message
CPM = Collective Perception Message

## Slide 9: Combined use case MCS and CPS
MCS = Maneuover Coordination Service
CPS = Collective Perception Service
John Kenney (TMNA), Friedbert Berens (FBConsulting Sarl)

## Slide 10: Car-2-Car Communication Consortium
The Car-2-Car Communication Consortium:
  Enhancing road safety and traffic efficiency by means of Cooperative Intelligent Transport Systems and Services (C-ITS) is the dedicated goal of the CAR 2 CAR Communication Consortium. The industrial driven, non-commercial association was founded in 2002 by vehicle manufacturers affiliated with the idea of cooperative road traffic based on Vehicle-to-Vehicle Communications (V2V) and supported by Vehicle-to-Infrastructure Communications (V2I). The Consortium members represent worldwide major vehicle manufactures, equipment suppliers and research organisations.
  The principal output of C2C-CC is the Basic System Profile (BSP), currently at version 2.0.1
  https://www.car-2-car.org

## Slide 11: 802.11p PHY features (2010)
based on 802.11a and 802.11j allowing 5MHz, 10MHz and 20 MHZ channels
  Only 10 MHz option is currently in use
Traditional CC channel coder allowing for iterative channel estimation based on decoded data parts
  Enhanced receivers for 802.11p support very high relative speeds above 500 km/h, see measurements in high-speed trains
Introduced optional enhanced channel rejection specification

## Slide 12: 802.11bd PHY features (2022)
Backwards compatible with 802.11p systems
Pilots for enhanced channel estimation process in high mobility channels
Enhanced channel coding (LDPC)
Fully backward compatible 20 MHz channel operation
  Possibility of 20 MHz and 10 MHz operation in overlapping channels
Enhanced positioning capabilities based on 802.11az
60 GHz option added

## Slide 13: 802.11p/bd MAC features
Introduced communication “outside the context of a BSS” (i.e. OCB)
STAs communicate directly with each other
STAs do not join a BSS
Note: CSMA/CA channel access is unchanged from “normal” IEEE 802.11

## Slide 14: Further discussions
The existing cooperative ITS services involve vehicles, infrastructure and other road traffic participants
Operation is in the 5.9 GHz frequency band, which is harmonized in most of the world
In mobile environment it is essential to have systems capable of handling multipath fading channels at high vehicle speeds
Even in quasistatic environments where the receiver and transmitter are static the reflections in a dense mobile environment can significantly influence the performance.
Higher layer protocols like ITS-G5 and IEEE1609 should be taken into account where possible

## Slide 15: Next steps in Automotive TIG
The Automotive TIG should take the presented solutions and standards into account in the further development
  Solutions could be re-used
Finding during the development of 802.11p and 802.11db should be taken into account
  OCB operation
  Channel estimation for mobile channels
  Channel bandwidth considerations
Harmonization between the 802.11p/11bd systems with any new set of vehicle communication features should be taken into account