## Slide 1: Some Details on NPCA Operation
Date: 2025-01-10
Authors:

## Slide 2
Introduction
According to the NPCA operation, two main steps are as follows.
  Switching to the NPCA PCH: NPCA AP and NPCA STAs switch from the PCH to the NPCA PCH on detecting an inter-BSS PPDU on the PCH.
  Switching back to the PCH: NPCA AP and NPCA STAs switch back from the NPCA PCH to the PCH before the end of the inter-BSS activity and contend for the PCH.
In this contribution, we point out to some issues when switching to the NPCA PCH and switching back to the PCH, and provide some solutions.

## Slide 3: Switching to the NPCA PCH
According to the NPCA baseline operation, if AP-1 and STA-1 in BSS-1 detect an inter-BSS PPDU (e.g., communication in the BSS-2), AP-1 and STA-1 switch from the PCH to the NPCA PCH.
AP-1 and STA-1 may then communicate on the NPCA PCH.
AP-1
BSS-2
PCH
NPCA PCH
PCH
Switch to NPCA PCH
Frame exchanges in BSS-2
STA-1
PCH
NPCA PCH
ICF
ICR
PPDU
BA
Switch to NPCA PCH
NPCA PCH

## Slide 4: Problem While Switching to the NPCA PCH
If AP-1 detects an inter-BSS PPDU, it switches from the PCH to the NPCA PCH. On the other hand, if STA-1 is outside the communication range of BSS-2, it may not hear the inter-BSS PPDU and stays on the PCH.
AP-1 and STA-1 may not communicate on the NPCA PCH. This results in inefficient use of available resources.
AP-1
BSS-2
PCH
NPCA PCH
PCH
Switch to NPCA PCH
Frame exchanges in BSS-2
STA-1
PCH
NPCA PCH
ICF
Cannot switch to NPCA PCH
NPCA PCH

## Slide 5: Some of the Earlier Proposals
According to one approach [1], if there is a control link, the transmitter (e.g., AP1) can indicate on it that it has detected OBSS/or other busy activity and is moving on to the next set of channels.
   There may not be a control link available between the AP and the STAs
According to another approach [2], each STA/AP keeps a list of OBSS APs that they can hear. If STA1 hears OBSS PPDU of another AP (e.g., AP3, not AP2 that the AP1 can hear), it does not move to NPCA PCH.
 This approach does not help STA-1 switch to the NPCA PCH when the AP switches
According to another approach [3], OBSS AP (e.g., AP2) queries AP1 of an upcoming OBSS transmission. AP1 responds to this query, and notifies STAs to switch to the NPCA PCH. After that, AP2 starts OBSS transmission.
 OBSS PPDU transmission may be delayed

## Slide 6: Proposed Approach for Switching to the NPCA PCH
After detecting an inter-BSS PPDU, AP-1 transmits an indication to STA-1 (or to all STAs) on the PCH using spatial reuse (or with lower transmit power) to inform STA-1 of an inter-BSS PPDU on the PCH. AP-1 may adjust its transmit power based on prior information of whether each STA hearing AP-2 or not.
After transmitting the indication, AP-1 switches to the NPCA PCH.
After receiving the indication, STA-1 switches to the NPCA PCH.
AP-1
BSS-2
PCH
NPCA PCH
PCH
Switch to NPCA PCH
Frame exchanges in BSS-2
STA-1
PCH
NPCA PCH
ICF
ICR
PPDU
BA
Switch to NPCA PCH
Ind.
NPCA PCH

## Slide 7: Evaluation of the Proposed Approach
Pros:
  STAs that may not hear BSS-2 activity may switch to the NPCA PCH together with AP-1.
  Scenarios such as AP-1 switching to the NPCA PCH and not being able to transmit buffered data can be prevented.
Cons:
  STAs that hear BSS-2 and switch immediately to the NPCA PCH may win channel access before AP-1 (can be addressed with disabling untriggered uplink transmissions).

## Slide 8: Switching Back to the PCH
In a different scenario, there may be a STA not switching to NPCA PCH (STA may not support/enable NPCA operation). This STA stays on the PCH while NCPA AP/STAs may switch to the NPCA PCH.
On detecting an inter-BSS PPDU (e.g., transmitted by OBSS AP/STA) and obtaining the NAV duration from the PPDU, UHR AP and STA may set their basic NAVs. While the STA stays on the PCH, UHR AP switches to the NPCA PCH and exchanges frames with its associated STAs that switched to the NPCA PCH.
Before the end of NAV duration, UHR AP may switch back to PCH and may contend for the channel after the basic NAV expires. STA may also contend for the channel after the basic NAV expires.
UHR AP
OBSS AP
PCH
NPCA PCH
PCH
Frame exchanges between OBSS AP and its associated STAs
STA
PCH
NPCA PCH
Frame exchanges between UHR AP and its associated STAs
Switch to NPCA PCH
NPCA PCH
NAV
Switch to PCH
STA stays on PCH
NAV
Frame

## Slide 9: Problems due to TXOP Truncation on the PCH
If OBSS AP terminates the communication before the end of the NAV duration, UHR STA being on the NPCA PCH may not switch to the PCH before the end of the NAV duration (since it does not know about the TXOP truncation) and may not contend for the PCH.
STA (e.g., associated with UHR AP) may reset the basic NAV and may win the channel access. STA transmits a frame to UHR AP. STA may not receive a response from the UHR AP.
When UHR AP switches back to the PCH by the end of the NAV duration and contends for the channel, it may not obtain the PCH access (e.g., another STA may already have the channel access).
UHR AP
OBSS AP
PCH
NPCA PCH
PCH
Frame exchanges between OBSS AP and its associated STAs
STA
PCH
NPCA PCH
Frame exch. between UHR AP and its assoc. STAs
Switch to NPCA PCH
NPCA PCH
NAV
Switch to PCH
STA stays on PCH
TXOP truncation
Frame
Cannot obtain the PCH access
NAV
Basic NAV reset

## Slide 10: Proposed Solutions for TXOP Truncation on the PCH
OBSS AP does not perform TXOP truncation on the PCH while there is a UHR AP on the NPCA PCH.
  UHR AP may inform OBSS AP in advance that it has enabled NPCA operation.
  UHR AP does not become disadvantageous when it contends for the PCH after switching back.
OBSS AP may inform UHR AP of TXOP truncation on the PCH.
  Informing may be before or after truncation of the TXOP.
  Informing may be via the NPCA PCH (if the NPCA PCH is idle) or via a reserved channel.
  Informing whether before or after truncation of TXOP has its own challenges including transmission by the OBSS AP over the NPCA PCH or unavailability of a reserved channel.
Notes: Assuming in the same NPCA PCH
PIFS/SIFS operation

## Slide 11: Conclusion
In this contribution, we pointed out to some issues when switching to the NPCA PCH and switching back to the PCH, and provided some solutions.
During an OBSS communication, some STAs may not hear the inter-BSS PPDU on the PCH and cannot switch to the NPCA PCH.
  As a solution, NPCA AP may instruct its associated NPCA STA(s) to switch from the PCH to the NPCA PCH after determining that a PPDU received via the PCH is an inter-BSS PPDU.
If an OBSS AP truncates TXOP on the PCH before the end of the TXOP duration, UHR AP/STAs may not gain channel access after they switch back to the PCH by the end of NAV duration.
  As one solution, OBSS AP may not truncate the TXOP on the PCH if there is an active NPCA operation.
  Alternatively, OBSS AP may inform the UHR AP of TXOP truncation on the PCH.

## Slide 12: References
[1] 23/0034r1, Non-primary Channel Utilization
[2] 23/2005r1, Non-primary Channel Access
[3] 24/0318r0, Robust Secondary Channel Access