## Slide 1: Discussion on Spatial Reuse in ELR Transmissions
Date: 2025-01-13
Authors:

## Slide 2: Abstract
Enhanced Long Range PPDU is one of the new features in 802.11bn [1-5].
An ELR PPDU will be helpful in reducing the downlink/uplink range asymmetry problem in current Wi-Fi.
Several contributions have shown +6 dB link improvements due to combinations of time and frequency domain duplications and power boosting. However, this may not be realistic in the presence of interference (e.g. STAs initiating spatial reuse transmissions).
In this presentation we present some discussions for ELR transmissions related to disabling spatial reuse.

## Slide 3: Interference During ELR Transmissions
For ELR transmissions, interference due to intra or inter-BSS STA transmission should be minimized to achieve range enhancement.
Interference may be due to
  A STA that does not support ELR PPDU and cannot detect the ELR PPDU legacy preamble.
  A STA purposely ignoring an on-going ELR PPDU transmission using spatial reuse (e.g. OBSS_PD Based SR) <- We focus on this problem
ELR STA 1
Non-HT PPDU range
ELR PPDU range
ELR AP
ELR STA 2
ELR PPDU
OBSS PD Based SR TX

## Slide 4: Spatial Reuse in 802.11be
26.10.2.2 General operation with non-SRG OBSS PD level
the PHY of a STA issues a PHY-CCA.indication(BUSY) followed by a PHYRXEARLYSIG.indication or PHY-RXSTART.indication due to a PPDU reception, then the STA’s MAC sublayer may:
a) issue a PHY-CCARESET.request primitive before the end of the PPDU and not update its basic NAV timer based on the PPDU, or
b) treat the PPDU as not having been received for purposes of its basic NAV timer (i.e., not update its basic NAV timer),
if (for either (a) or (b)) all the following conditions are met:
…
3) The received PPDU is an inter-BSS PPDU (see 26.2.2 (Intra-BSS and inter-BSS PPDU classification))…
…
5) The RXVECTOR parameter SPATIAL_REUSE subfield in the HE-SIG-A field (if present) of the received PPDU is not set to PSR_AND_NON_SRG_OBSS_PD_PROHIBITED
26.2.2 Intra-BSS and inter-BSS PPDU classification
A STA shall classify a received PPDU as an inter-BSS PPDU if at least one of the following conditions is true:
— The BSS color is not disabled (see 26.17.3.3 (Disabling BSS color)) and the RXVECTOR parameter BSS_COLOR is not 0 and is not the BSS color of the BSS of which the STA is a member.
…
An EHT/non-ELR UHR STA can classify an ELR PPDU as an inter-BSS PPDU (due to the U-SIG BSS Color field) and since RXVECTOR parameter SPATIAL_REUSE is not present, OBSS_PD based SR is allowed.

## Slide 5: Interference During ELR Transmissions
Simulations Parameters:
1Tx, 1Rx, 1SS for AP and STA
D-NLOS, LDPC, MCS0
ELR LTF – Dual 2xLTF mode LTF symbols with 3 dB power boost
Realistic Channel Estimation with smoothing
Bandwidth = 20 MHz
ELR PPDU with RRU52 4xDUP
Non-ELR PPDU with RRU242

## Slide 6: Disabling Spatial Reuse for UHR STAs
We propose to have a mechanism to disable spatial reuse in ELR Transmissions
  Option 1: Add a rule prohibiting OBSS_PD Based SR for ELR PPDUs by default.
  Option 2: Add an indication in the U-SIG of ELR PPDUs to enable/disable OBSS_PD Based SR.
  Option 3: Option 1 + add an indication in the ELR-SIG to enable OBSS_PD Based SR.

## Slide 7: Disabling Spatial Reuse for EHT STAs
For EHT STAs, we can disable spatial reuse by setting the U-SIG BSS Color field of the ELR PPDU to 0.
  [26.2.2 Intra-BSS and inter-BSS PPDU classification] A STA shall classify a received PPDU as an inter-BSS PPDU if at least one of the following conditions is true: - The BSS color is not disabled (see 26.17.3.3 (Disabling BSS color)) and the RXVECTOR parameter BSS_COLOR is not 0 and is not the BSS color of the BSS of which the STA is a member.
  Note: EHT STAs are not able to use spatial reuse unless they can categorize the PPDU as inter-BSS PPDU.
The actual BSS Color is also carried in the ELR MARK field.

## Slide 8: Conclusion
We discussed the problem of spatial reuse during ELR transmissions and discussed ways to disable it in both EHT and UHR STAs.

## Slide 9: Strawpoll
Do you support adding in the SFD,
11bn defines a mechanism for disabling spatial reuse for ELR transmissions.
Y
N
A

## Slide 10: References
https://mentor.ieee.org/802.11/dcn/24/11-24-0921-00-00bn-an-enhanced-long-range-ppdu.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-0873-00-00bn-design-targets-and-considerations-for-enhanced-long-range.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-0875-01-00bn-uhr-enhanced-long-range-support.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1478-02-00bn-elr-ppdu-design.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1573-00-00bn-an-elr-ppdu-follow-up.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1488-00-00bn-elr-ppdu-transmission-design.pptx