## Slide 1: Control frames and MAPC for Colocated BSSID Set
Feb 2025
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Javier Contreras | Cisco Systems |  | 

## Slide 2: Situation (1/4) In 802.11, Colocated BSSID Set = Multiple BSSID Set xor Co-hosted BSSID Set
Transmitted BSSID (bold)
Nontransmitted BSSID (normal)
The same AP radio hardware supports virtual APs and virtual BSSs, typically one per SSID
  Common in the enterprise and now the home too (e.g., core devices + guest devices)
These virtual BSSs make up a Colocated BSSID Set, as one of:
  Multiple BSSID Set
    Beacon + Probe Response frame sharing/compression
    Used predominantly at 6 GHz; harder to use at 2.4/5 GHz due to legacy
  xor Co-hosted BSSID Set
    Separate Beacon + Probe Response frames for each BSSID
    Predominant VBSS mechanism at 2.4+5 GHz due to legacy
Colocated BSSID Set
Multiple BSSID Set
APa
APb
APc
APd
Co-hosted BSSID Set
APa
APb
APc
APd
xor
APa
Key:
APb
[1]

## Slide 3: Situation (2/4) Both kinds of sets are identified via similar signalling
Both kinds of sets are identified via the number of variable LSBs of the BSSID
  E.g., If the virtual BSSs’ BSSIDs can take the form of 0x012345x (x = 0x0...0xf), with a max of 16 BSSIDs in the set, then this is signaled as n = 4
Multiple BSSID Set [1]
Co-Hosted BSSID Set [1]

## Slide 4: Situation (3/4) Enhanced Control frame features are confined to Multiple BSSID Sets
11ax and 11be features are consistently defined for Multiple BSSID Sets but erratically defined for Co-hosted BSSID Sets:
Both Multiple BSSID Sets and Co-hosted BSSID Sets
  BSS Color (§3.2 [1])
  Intra-BSS and inter-BSS PPDU classification (§26.2.2 [1])
  Dual NAV (§26.2.4 [1])
  Non-SRG & SRG OBSS PD level (§26.2.3, §26.10.2 [1])
  PSR-based SR (§26.10.3 [1])
Multiple BSSID Sets only
  Rx Control Frame To MultiBSS (§9.4.2.247.2 [1]), which allows set-wide operation of:
    MU-RTS + CTS (§26.2.6.3 [1])
    NDPA + NDP (§26.7.3 [1])
    MU PPDU
    Trigger + TB PPDU (§26.5.2.2.1, §26.5.2.2.4, §26.5.2.3.1 [1])
    Multi-STA BA (§26.4.1 [1])
    HE dynamic SM power save (§26.14.4 [1])

## Slide 5: Situation (4/4) In reality, Colocated BSSID Set = Multiple BSSID Set xor Co-hosted BSSID Set is not true
Since certain clients are challenged by Beacon frames with a higher number of octets, then a Colocated BSSID Set with a high number of SSIDs~BSSIDs~virtual APs is enabled via multiple MBSSID Beacons
  Basically, a co-hosted set of Multiple BSSID Sets
  But 802.11 has no language to account for this
    In 802.11, VBSSIDs are always one or the other
Colocated BSSID Set
MBSSID Set1
AP1a
AP1b
MBSSID Set2
AP2c
AP2d
Transmitted BSSID (bold)
Nontransmitted BSSID (normal)
Colocated BSSID Set
Multiple BSSID Set
APa
APb
APc
APd
Co-hosted BSSID Set
APa
APb
APc
APd
xor
APa
Key:
APb
What IEEE says today:
What exists in reality (especially at 6 GHz):

## Slide 6: Three Problems
We’re solving Co-TDMA across non-colocated APs
  So, we should also address the equivalent – and easier! – problem of Co-TDMA among colocated APs
We have a sharing AP granting a portion of a TXOP via Co-TDMA to a coordinated AP
  But the TXOP grant – and residue return – should operate at the Colocated BSSID Set level, not the individual AP level (see also [2])
Overheads from 802.11’s xIFS and preamble means that MU+TB PPDUs are the key path to efficiency
  So aggregation across STAs, regardless of which BSS in a Colocated BSSID Set they are associated to, is an important efficiency we can leverage
  That is, we should extend the Rx Control Frame To MultiBSS feature-set

## Slide 7: Solution for Problem A (1/2) Use Co-TDMA to Serve All Clients of a Colocated BSSID Set in one TXOP
Ditto
Ditto
No need for AP1b to tell AP1b OTA that it is done
MU-RTS TXS + CRF transmitted by the same radio that receives neither frame!?
ICF+CRFis redundant for colocated APs; only needed for non-colocated APs
Now, applying the Co-TDMA protocol directly to colocated BSSs leads to inefficiencies (and weirdness!)
AP1a (TXOP holder)
Colocated BSSID Set
MBSSID1
AP1a
AP1b
Cohosted1
AP1c
AP1d
C1a
C1b
C1c
C1d
C1b
AP1c (chained NAV)
C1c
AP1d
C1d
ICF
MU-RTS TXS
NAV
TXOP return
CRF
C1a
AP1b (chained NAV)
CRF
Intra-BSS1a PPDUs
CRF
Intra-BSS1b PPDUs
MU-RTS TXS
TXOP return
CRF
Intra-BSS1c PPDUs
CRF
Note: no regulatory impediment to AP1b directly granting a portion of the TXOP to AP1c instead of a return to AP1a then grant to AP1c. Ditto AP1c to AP1d

## Slide 8: Solution for Problem A (2/2) Let Co-TDMA Serve All Clients of a Colocated BSSID Set in one TXOP
AP1a (initial TXOP holder)
Colocated BSSID Set
MBSSID1
AP1a
AP1b
Cohosted1
AP1c
AP1d
C1a
C1b
C1c
C1d
C1b
AP1c (chained NAV)
C1c
AP1d
C1d
NAV
C1a
AP1b (chained NAV)
Intra-BSS1a PPDUs
Intra-BSS1b PPDUs
Intra-BSS1c PPDUs
… but these can be optimized away, for a great efficiency improvement
(Keep the chained NAV to avoid clients in BSS1b/c from sleeping during their BSS’ portion)

## Slide 9: Solution for Problem B (1/2) MAPC Grants Should be Between Colocated BSSID Sets not between APs
Colocated BSSID Set 1
MBSSID1
AP1a
AP1b
Cohosted2
AP1c
AP1d
C1a
C1b
C1c
C1d
Colocated BSSID Set 2
MBSSID2
AP2a
AP2b
Cohosted2
AP2c
AP2d
C2a
C2b
C2c
C2d
Current proposals suggest that sharing AP1a should a grant portion of a TXOP to AP2a then AP2b via sequential grants:
  MU-RTS TXS(AP2a) + CRF + <grantedPortionAtAP2a> + TXOPreturn(AP1a)
  MU-RTS TXS(AP2b) + CRF + <grantedPortionAtAP2b> + TXOPreturn(AP1a)
This has very high overheads
MU-RTS TXS + CRF transmitted by the same radio that receives neither frame
No need for AP2a to tell AP1a that it is done
AP1a (TXOP holder)
C2a
AP2b (chained NAV)
C2b
ICF
MU-RTS TXS
NAV
TXOP return
C1a
AP2a (chained NAV)
CRF
Intra-BSS1a PPDUs
CRF
Intra-BSS2a PPDUs
MU-RTS TXS
TXOP return
CRF
Intra-BSS2b PPDUs
CRF

## Slide 10: Solution for Problem B (2/2) MAPC Grants Should be Between Colocated BSSID Sets not between APs
Colocated BSSID Set 1
MBSSID1
AP1a
AP1b
Cohosted2
AP1c
AP1d
C1a
C1b
C1c
C1d
Colocated BSSID Set 2
MBSSID2
AP2a
AP2b
Cohosted2
AP2c
AP2d
C2a
C2b
C2c
C2d
AP1a (TXOP holder)
C2a
AP2b (chained NAV)
C2b
ICF
MU-RTS TXS
NAV
C1a
AP2a (chained NAV)
CRF
Intra-BSS1a PPDUs
CRF
Intra-BSS2a PPDUs
TXOP return
Intra-BSS2b PPDUs
CRF can summarize AP2a/b/c/d
The much more efficient solution is for grants – and TXOP returns – should operate at the Colocated BSSID Set level
  Still based on traffic priority, MAPC agreements, etc
As before, AP1a/b/c/d could directly use the next portion of the TXOP
As before, no regulatory impediment to AP2a directly granting a portion of the TXOP to AP2b instead of a return to AP1a then grant to AP2b.

## Slide 11: Solution for Problem C (1/3) High Level
Explicitly signal the Colocated BSSID Set
  Via the number of variable LSBs in the BSSID, sent in the UHR Operation element
  (Similar to Multiple BSSID Set / Co-hosted BSSID Set signaling)
Introduce the Rx Control Frame To Colocated BSSID Set field
  Use this to extend the Rx Control Frame To MultiBSS feature-set to all VAPs/VBSSs/VBSSIDs in the Colocated BSSID Set
  Wherever a feature is conditioned on “Rx Control Frame To MultiBSS” today, extend that condition, in the UHR draft, to be “Rx Control Frame To MultiBSS = 1 or Rx Control Frame To Colocated BSSID Set = 1”
    Or similar, since the details are always a little more involved
  Assume all information (PM, DL buffer sizes, BSR, SCS(QC), etc) is shared among APs of a Colocated BSSID Set
Colocated BSSID Set - can mix’n’match anything
Multiple BSSID Set1
AP1a
AP1b
AP2c
AP2d
Co-hosted BSSID Set3
AP3e
AP3f
AP4g
AP5h
Multiple BSSID Set2
AP6i
AP6j
Co-hosted BSSID Set7
AP7k
AP7l
AP8m
Multiple BSSID Set6
or leave anything out (with a sufficiently different BSSID)

## Slide 12: Solution for Problem C (2/3) Need Colocated BSSID Set BSSID(s), analogous to Transmitted BSSID
Rx Control Frame To MultiBSS feature-set uses the Transmitted BSSID when sending control frames for the entire Multiple BSSID Set. Something similar is needed for a Colocated BSSID Set
Rx Control Frame To Colocated BSSID Set can go two ways:
  Option A: A Colocated BSSID Set has a single Colocated BSSID Set BSSID
    Complete aggregation & efficiency for UHR STAs, but certain legacy STAs can never participate
  Option B: A Colocated BSSID Set uses any (transmitted) BSSID in the set as a Colocated BSSID Set BSSID
    Complete aggregation & efficiency for UHR STAs + all legacy STAs have a way to participate
Key:
Participating Legacy Non-AP STA
Participating UHR Non-AP STA
Colocated BSSID Set
MBSSID1
AP1a
AP1b
MBSSID2
AP2c
X
AP2d
X
Colocated BSSID Set
MBSSID1
AP1a
AP1b
MBSSID2
AP2c
~
AP2d
~
Colocated BSSID Set
MBSSID1
AP1a
~
AP1b
~
MBSSID2
AP2c
AP2d
Option A
All TXOPs
Option B
Transmitted BSSID (bold)
AP2a
Colocated BSSID Set BSSID
Later TXOP
X
Legacy Non-AP STA that can never participate
~
Legacy Non-AP STA not participating in this TXOP
AP1a
Earlier TXOP

## Slide 13: Solution for Problem C (3/3) Simplest if AIDs are unique across STAs of a Colocated BSSID Set
Simplest if AIDs are unique across STAs of a Colocated BSSID Set
  Since then the STAID is unique too
In a Multiple BSSID Set, the first 2n AIDs are reserved to indicate groupcast traffic in the TIM element in Beacon frames
  This is still only needed per Multiple BSSID Set – no change
  Since the co-hosted BSSIDs and “nothing” BSSIDs still have their own Beacon frames

## Slide 14: Summary
APs in a Colocated BSSID Set currently contend independently, and would benefit from Co-TDMA
  Yet naively applying the current Co-TDMA protocol to colocated APs leads to inefficiency (and weirdness)
  The natural solution is an optimized variant of Co-TDMA for APs in a Colocated BSSID Set that omits OTA communication between colocated APs
When “APs” grant or return a portion of a TXOP to each other via Co-TDMA (or any resource via any MAPC technique), to minimize overheads, the grant or return should be at the Colocated BSSID Set level (if present)
As well, we have a great opportunity for efficiency improvements via combining users across
  The multiple Multiple BSSID Sets at 6 GHz, and
  The Co-hosted BSSID Set at 2.4+5 GHz
… by enlarging the “Rx Control Frame To MultiBSS” feature to “Rx Control Frame To Colocated BSSID Set”
  MU-RTS + CTS, NDPA + NDP, MU PPDU, Trigger + TB PPDU, Multi-STA BA and HE Dynamic SM Power Save across all virtual BSSs

## Slide 15: Strawpoll 1
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn draft shall define optimized Co-TDMA for colocated APs in a Colocated BSSID Set
Y / N / A

## Slide 16: Strawpoll 2
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn draft shall define how MAPC-related resource sharing can operate at the Colocated BSSID Set level
Y / N / A

## Slide 17: Strawpoll 3
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn draft shall define how a Colocated BSSID Set can be signaled
  The 802.11bn draft shall define how exchanges that involve control frames (namely MU-RTS + CTS, NDPA + NDP, MU PPDU, Trigger + TB PPDU, Multi-STA BA and HE dynamic SM power save) can include multiple STAs associated to multiple APs of the same Colocated BSSID Set
Y / N / A

## Slide 18: References
[1] 802.11REVme Draft 7.0
[2] 24/719 “MAP set operation”, Jay Yang

## Slide 19: Backup