## Slide 1: ERD: Enhanced Reverse Direction Protocol to Support TXOP Sharing and Low-Latency Traffic Exchange
Date: 2024-11-08
Authors:

## Slide 2: Problem Statement
If AP is the TXOP holder
  It can send DL traffic to one or more STAs during its acquired TXOP
  A non-AP STA can use BSR to request resources from the AP
    802.11ax uses Trigger-based resource allocations to enable non-AP STAs to send UL traffic
    802.11be TXS Mode 1 enables non-AP STA to send SU UL
    802.11be TXS Mode 2 enables non-AP STA to perform Peer-to-Peer (P2P) transmissions with other non-AP STAs
  Shortcoming: If a non-AP STA needs to send peer-to-peer traffic to another non-AP STA, it cannot request for resources from the AP (e.g., when relaying operation is required)
If a non-AP STA is the TXOP holder
  Enhancements have been proposed to share TXOP with AP using control frames
  Shortcoming: The current proposals do not provide a low-overhead method for allowing the AP to request TXOP sharing from non-AP STAs
In this contribution, we propose enhancements to the Reverse Direction (RD) protocol to address the above shortcomings

## Slide 3: Related Contributions
Some contributions show the effectiveness of using RD for interactive and Low-Latency (LL) traffic exchanges
[11-23/1387r0] [11-23/1874r0] [11-24/0668r1]

## Slide 4: Overview of the existing Reverse Direction (RD) Protocol
The Reverse Direction (RD) protocol allows for bidirectional frame exchange during TXOPs
The TXOP Holder exchanges bidirectional traffic with the TXOP Responder
AP: TXOP
Responder
PPDU
RDG/More PPDU = 0
Non-AP STA: TXOP Holder
BA
PPDU
RDG/More PPDU = 1
BA
RDG/More PPDU = 1
PPDU
RDG/More PPDU = 1
PPDU
RDG/More PPDU = 0
BA
RDG/More PPDU = 0
PPDU
RDG/More PPDU = 0
BA
TXOP Duration
One burst of PPDUs from TXOP Responder
(no ACK between these PPDUs)

## Slide 5: Enhancements to the Reverse Direction (RD) Protocol
The RD protocol utilizes two bits: (1) Reverse Direction Grant (RDG), and (2) AC Constraint
  Both fields are located in the Command and Status (CAS) subfield, which is in the A-control subfield
We propose using an extended encoding of these two bits to support new operational modes
  A STA (AP or non-AP) can request another STA to share its TXOP with the requester
  A STA can request for TXOP sharing to perform P2P traffic exchange
Using the proposed extended encoding, we can avoid exchanging control frames to enable these new operational modes
  In addition to the proposed encoding, the reserved bits in the CAS subfield and the remaining bits in the A-Control subfield can be leveraged to enhance RD and convey additional information, such as:
    e.g., permissible traffic types during the shared TXOP
    e.g., indication of the type and amount of peer-to-peer traffic in buffer
    e.g., duration of the TXOP sharing

## Slide 6
Frames sent by TXOP Holder | RDG/More PPDU | AC Constraint | Unused bits in CAS and A-Control subfields
None | 0 | 0 | Additional information TBD (see appendix)
*TXOP Sharing Offer (TSO): Sharing for communication with 3rd party STAs | *0 | *1 | 
TXOP Sharing Offer (TSO): Sharing without AC constraint | 1 | 0 | 
TXOP Sharing Offer (TSO): Sharing with AC constraint | 1 | 1 | 
Items marked with * are the newly proposed features
Frames sent by TXOP Responder | RDG/More PPDU | AC Constraint | Unused bits in CAS and A-Control subfields
None/Offer Rejection | 0 | 0 | Additional information TBD (see appendix)
*Requesting sharing for communication with 3rd party (communication with the TXOP Holder is allowed) | *0 | *1 | 
Accepting TXOP sharing offer | 1 | 0 | 
*Requesting sharing for communication with TXOP Holder | *1 | *1 | 

## Slide 7
TXOP Responder (AP)
PPDU
TXOP Holder (non-AP STA)
BA
RDG/More PPDU = 0
AC Constraint = 1
PPDU
RDG/More PPDU = 0
AC Constraint = 1
PPDU
RDG/More PPDU = 0
AC Constraint = 0
3rd Party STA
BA
RDG/More PPDU = 1
AC Constraint = 0
The AP may communicate with
3rd party STAs and
the TXOP Holder
Accepting offer
PPDU
RDG/More PPDU = 0
AC Constraint = 0
TXOP Duration
Make a TXOP sharing request
TXOP sharing offer for communication with 3rd party STAs (STAs other than the TXOP Holder) and/or the TXOP Holder

## Slide 8
TXOP Responder (non-AP STA)
PPDU
TXOP Holder (AP)
BA
RDG/More PPDU = 0
AC Constraint = 1
PPDU
RDG/More PPDU = 0
AC Constraint = 1
PPDU
RDG/More PPDU = 0
AC Constraint = 0
3rd Party STA
BA
RDG/More PPDU = 1
AC Constraint = 0
The non-AP STA performs peer-to-peer communication
Accepting offer
PPDU
RDG/More PPDU = 0
AC Constraint = 0
P2P
communication
TXOP Duration
Make a TXOP sharing request
Indicate its peer-to-peer traffic type/size
Indicate the requested duration
TXOP sharing offer for peer-to-peer communication
TXOP Sharing Duration

## Slide 9: Summary
The RD protocol is an efficient way to allow a TXOP holder to share its TXOP with the TXOP responder
Using RD, no control frames are required to perform sharing
We proposed enhancements to the RD protocol allowing:
  A TXOP responder (AP or non-AP STA) to request TXOP sharing from the holder
  A TXOP responder can request to perform peer-to-peer traffic exchange

## Slide 10: Straw Polls
Do you agree that 11bn should enhance the RD protocol to allow non-AP STAs to share their TXOPs with the associated AP?
YES/NO/ABSTAIN
Do you agree that 11bn should enhance the RD protocol to allow a non-AP STA to request part of its associated AP's TXOP for P2P communication
YES/NO/ABSTAIN

## Slide 11
Appendix:
Conveying Permissible Traffic Types and TXOP Sharing Duration

## Slide 12
A-Control (30 bits total) |  |  |  |  |  | 
 | CAS (8 bits total) |  |  |  |  | 
4 bits | 1 bit | 1 bit | 1 bit | 5 bits (reserved) | 4 bits | 14 bits
CAS Control ID value: 6 | AC Constraint (*extended encoding) | RDG/More PPDU (*extended encoding) | PSRT PPDU | *TXS-TCI TXOP Holder: Permissible traffic types TXOP Responder: Buffer report | *A new Control ID value (between 10 to 14) | *TXS-DU TXOP Holder: TXOP sharing duration TXOP Responder: Requested TXOP sharing duration
TXS-TCI: TXOP Sharing-Traffic Characteristics Indication
TXS-DU: TXOP Sharing-Duration
For the AC Constraint and RDG/More PPDU fields, we propose extended bit encodings, in addition to those available in the existing RD protocol (in 802.11ax/be)
A sample method for presenting permissible traffic types and TXOP sharing duration
Items marked with * are the newly introduced subfields

## Slide 13
Appendix
Related Contributions and Straw Polls

## Slide 14: Related Contributions
The benefits of enabling non-AP STAs to share their TXOP with the AP have been demonstrated in various works and several solutions have been proposed
  [11-24/1224r2 (Samsung)] [11-24/068r0 (TCL)] [11-23/1886r3 (Qualcomm)] [11-24/0168r0 (NXP)] [11-24/0389r0 (Apple)] [11-23/581r0 (WILUS)]
Some of these works, however, only allow a non-AP STA to share the unused portion of its TXOP with the AP
  [11-23/1874r0 (Broadcom)] [US9655136B2 (Huawei)]
Some of these works present their contribution within the context of facilitating LL traffic exchange
  [11-23/1886r3 (Qualcomm)] [11-24/0168r0 (NXP)] [11-24/1207r0 (Huawei)] [11-24/0389r0 (Apple)]
  There exist contributions related to the priority of channel access during TXOPs
    [11-24/1257r0 (Huawei)] [11-24/416r1 (Samsung)]
Another category of works show how TXOP sharing can be leveraged to enhance relaying performance
  This is particularly useful for XR applications [11-24/0105r0 (LG)] [11-24/0668r1 (Samsung)]
  There exist contributions related to the negotiation process of such communication
    [11-23/1958r0 (Meta)] [11-24/0073r0 (Huawei)] [11-24/1885r1 (Qualcomm)]

## Slide 15: Related Straw Polls
Allow non-AP STAs to share their TXOPs with the associated AP
[11-24/068r0 (TCL)] [11-23/581r0 and 11-23/1847r0 (both WILUS)] [11-23/1387r0 (Intel)] [11-23/1874r0 (Broadcom)] [11-24/1224r2 (Samsung)] [11-24/0668r1 (Samsung)] [11-23/1886r3 (Qualcomm)] [11-24/0168r0 (NXP)] [11-24/1207r0 (Huawei)] [11-24/0389r0 (Apple)]
Do you support allowing a non-AP STA initiate downlink transmissions with its associated AP in TGbn?
[11-24/1224r2 (Samsung)] [11-24/0168r0 (NXP)] [11-23/1886r3 (Qualcomm)] [11-24/0389r0 (Apple)]
Do you support allowing a non-AP STA initiate downlink/uplink transmissions with its associated AP and P2P transmissions with its peer STA(s) in the same TXOP in TGbn?
[11-24/1224r2 (Samsung)] [11-24/0668r1 (Samsung)]
Do you support enhancing relaying operation for AP-STA1-STA2 communication?
[11-24/0105r0 (LG)] [11-24/0668r1 (Samsung)] [11-23/1958r0 (Meta)] [11-24/1885r1 (Qualcomm)]