## Slide 1: Solutions for Beacon Bloating
Authors:

## Slide 2
Beacon frames grow by each 802.11 generation
  Pre-11be, or even pre-11ax, Beacon sizes of 300-400 bytes per BSSID are common
  11be adds about additional 100-200 bytes
  If no Beacon design change in 11bn, more IEs would be added to Beacon frame
  Support of Multi-BSSID is mandatory in 6GHz
    With 2-7 BSSIDs, Beacon frame could get as large as 880 to 1700 bytes
    Due to large Multi-BSSID Beacons, enterprise AP vendors have resorted to temporary solutions, e.g. splitting multi-BSSIDs Beacon into multiple Beacons
Channel inefficiency: Beacon frames consume more medium time
  Particularly when transmitted lowest MCS and when there are multiple BSSIDs per AP
Large Beacons increase (associated/scanning) STAs power consumption
Problem Statement (1)

## Slide 3
Legacy approach: Include all the legacy IEs and UHR IEs in the Beacon frame
  No limit for Beacon bloating
Proposal: Do not add new UHR-related IEs in Beacon
  Short UHR capability bit(s) are added to the beacon
  A STA obtains the complete UHR parameters during Probing/Association
Beacon Content
Candidate UHR Parameters:
UHR Capabilities IE
UHR Operation IE
IEs maybe defined in relation to newly-proposed UHR features:
  DSO
  NPCA
  DPS
  ELR
  Multi-AP
  …

## Slide 4
Short discovery mechanism for unassociated STAs
  Repurpose a reserved bit in the Capability Info to indicated UHR BSS:
    UHR BSS (1 bit): indicates that the AP supports UHR
  Reduced Neighbor Report (RNR) signal also whether the reported AP supports UHR
To obtain complete set of UHR parameters
  An unassociated STA may send a (ML) Probe Request and obtain the complete set of UHR parameters from (ML) Probe Response
  Or a STA may obtain the complete set of UHR parameters during authentication or association
  Or as part of pre-roaming procedure, the STA may obtain a min set of capabilities of the UHR AP from its serving AP
Proposal – UHR IE Classification

## Slide 5
Beacon frame signals critical BSS parameter change by:
  Setting BSS Critical Update flag to 1
  Increasing BSS Parameter Change Count (BPCC) by 1. (BPCC value is modulo(256))
Associated STAs shall obtain the BSS parameters before the STA send data frames to the AP
After a critical update, the Beacon carry the updated IEs for multiple DTIM intervals
  The updated UHR IEs are carried for multiple DTIM intervals, to make sure associated STAs that may be in power save also obtain the updated IEs from Beacon frame. For efficiency, only the updated UHR IEs are carried
  Proposal: To efficiently help associated STAs that modified UHR IEs are carried, we propose to define a separate critical update flag, by repurposing a reserved bit in the Capability Info, to indicate that the Beacon frame carries the UHR IEs
  Note: Per baseline spec, a STA may exchange ML Probe Req/Response to acquire modified UHR parameters. However, this is less desirable due to additional STA power consumption.
Proposal: UHR Parameters Update for Associated STAs

## Slide 6: Problem Statement (2)
Beacon signals BSS parameter changes which helps STA to detect when parameters are updated
Critical Update Flag (1 bit) in Capabilities Information field
  Stays on until the next DTIM only
  Early in the Beacon, received by STAs using early termination
BSS Parameter Change Count (BPCC) (1 octet)
  BPCC of transmitting AP is in Multilink element and BPCCs of affiliated APs are in RNR
  A complete Beacon frame must be received to obtain BPCC values
BSS Parameter change

## Slide 7: Proposal
Example: Links 1 and 2 have Multiple-BSSID Beaconing
  BSS22 gets critical parameter update
SBPC signals the updated Sum of all BSS Parameter Change Counts Modulo(255) on all Beacons
  STA cannot miss critical parameter update. The SBPC is visible on all beacons
AP MLD1
AP MLD2
Link 1
Link 2
BPCC 108
SBPC 94
BSS 12
BPCC 26
SBPC 94
BSS 11
BPCC 155
SBPC 94
BSS 22
BPCC 60
SBPC 94
BSS 21
AP MLD1
AP MLD2
Link 1
Link 2
BPCC 108
SBPC 95
BSS 12
BPCC 26
SBPC 95
BSS 11
BPCC 156
SBPC 95
BSS 22
BPCC 60
SBPC 95
BSS 21
Before Critical Parameter Update
After Critical Parameter Update
Proposal: include an indication of BPCC of all links in an element that appears early in the Beacon frame:
  Sum of BSS Parameter Change Counts (SBPC): The sum of BPCC fields of all links and all BSSs

## Slide 8
Increasing Beacon size over many 802.11 generations is a problem, and it will become even worse in upcoming generations
  802.11bn shall provide means for beacon size reduction for UHR and all following 802.11 generations
The proposals are:
  1) to add to Beacon frame a short indication of presence of a UHR BSS, and
  2) avoid adding static UHR BSS parameters to Beacon. A STA may obtain the UHR parameters during probing or association
Summary

## Slide 9
Do you agree that no UHR defined elements carrying static BSS parameters are included in Beacon frames, except for a field indicating that the AP is a UHR AP
  The UHR BSS parameters are obtained by STAs pre-association through Probe Response and (Re)Association Response frames
  Whether certain dynamic BSS parameters can also be excluded is TBD
Straw Poll 1

## Slide 10
If there is a change to one or more UHR parameters, then a UHR AP provides an indication of the update.
  The indication that an update exists follows a similar TGbe mechanism, but using a different (TBD) set of fields
  It is TBD how UHR non-AP STAs obtains the updates.
Straw Poll 2

## Slide 11
[1] 23-1938r1: Beacon design with and without multiple BSSID support, Liwen Chu
References