## Slide 1: Seamless Roaming
Date: 2024-11-11
Authors:

## Slide 2: Introduction
TGbn has agreed to specify a new mechanism [Jan 2024] for seamless roaming of a non-AP MLD from a current AP MLD to a target AP MLD with the following characteristics:
  [Jul 2024] Context related to the non-AP MLD can be (at least partially) transferred from the current to the target AP MLD
  [Jul 2024] After a request/response exchange initiating the DS mapping change, buffered DL data can be:
    Delivered by the current AP MLD – retrieved by the non-AP MLD on the old link
    Forwarded from the current AP MLD to the target AP MLD so that the non-AP MLD may retrieve it on the new link
  [Sept 2024] A request/response exchange is defined from a non-AP MLD in state 4 to
    Transfer the context
    Perform necessary DS mapping change

## Slide 3: Seamless Roaming requirements
Should be seamless
  No disruption to on-going QoS flows
  Avoid unnecessary overhead (reduce frame exchange/processing)
  Reliable roaming (can be prepared in advance and correct expectations are set for clients)
Should be scalable
  To support mobility within a network consisting of large number of APs
Should be simple
  E.g., Rely on existing frameworks as much as possible
Should be flexible
  To cover different use cases such as home, enterprise, warehouse, etc.

## Slide 4: Seamless Roaming Mobility Domain (SRMD)
To fulfill the requirements of Seamless Roaming (SR), one of the key aspects is to identify the group of AP MLDs over which the SR protocol can be used.
A Seamless Roaming Mobility Domain (SRMD) shall be defined and identified with a unique identifier (SRMD ID) to facilitate the operations involved in the transition between a current AP MLD and a target AP MLD belonging to the same SRMD can be carried while referring to such an SRMD ID, for example:
  Discovery of the AP MLDs within the SRMD across which the non-AP MLD can seamlessly roam
  Security
  Consistency of BA operation
  Set up links
While SR can provide the most seamless experience within the SRMD, it is expected mobility in larger ecosystems (e.g., between SRMDs) can be aided by fast BSS transition (FT).
FT MD
SRMD 1
SRMD 2
SR
SRMD 3
FT
AP MLD 1
AP MLD 2
AP MLD 4
AP MLD 3

## Slide 5: Seamless Roaming In Steps
Preparation
To deliver a smooth experience, Seamless Roaming extends over different steps:
  Discovery: the client discovers the neighboring AP MLDs in the SRMD
  Preparation: the client can receive recommendations on suitable candidate AP MLDs in the SRMD that can meet the client’s requirements
    E.g., considering client’s context, loading conditions, check on the backhaul, etc.
    BTM signaling can be considered, e.g.:
      BTM query/request  solicited
      BTM request  unsolicited
  Setup: the client requests the current AP MLD to set up a target AP MLD in the SMRD over the backhaul
    Set up of the links
    First instance of context transfer
    Signaling for the client/current AP MLD request/response exchange is TBD (e.g., ML reconfiguration)
    Combination with the Preparation step can be considered
  Transition: the client request to roam to the target AP MLD in the SMRD
    Second instance of context transfer
    Necessary DS mapping switch
    Both exchange client-current and client-target AP MLD can be considered (current in the figure)
    Accepted if request is received within a timeout after Setup completion
AP MLD0
AP MLD1
AP MLD2
Client
Discovery/Scanning
Set up links
context transfer (1)
Setup Request
AP MLD 1
Setup Response
context transfer (2)
Necessary DS map switch
Transition request
AP MLD 1
Transition Response
Setup timeout
(Transition request is accepted if performed within timeout after Setup completion)

## Slide 6: Discussion on the Roaming Setup
Some of the key operations for SR that are expected are
  Context transfer
  Link set up
Such operations are expected to require some latency (e.g., some tens of ms), therefore it is preferable to avoid service disruption (e.g., interruption of DL/UL communications) while such operations are carried out.
Propose to decouple the request/response exchange for the roaming transition (which can involve DS mapping switch and therefore service interruption) by introducing a link setup step in the SR sequence. The context transfer can initiate at this time.
  It can be further considered that after the Setup is performed, the current AP MLD shall accept the Transition request at least if received within a timeout after Setup completion, in this way the expectation is set for successful roaming transition.

## Slide 7: Conclusion
A Seamless Roaming Mobility Domain (SMRD) is introduced and identified by a unique identifier
  A client can use the SR protocol between the AP MLDs within the SMRD
The SR protocol develops in steps including:
  Discovery: AP MLDs within the SMRD
  Preparation: network recommendation for candidate AP MLDs
  Setup: set up the links and transfer the context to the target AP MLD
  Transition: context transfer and necessary DS mapping switch

## Slide 8: SP1
Do you agree to define a seamless roaming mobility domain, characterized by an identifier, encompassing multiple AP MLDs, where a non-AP MLD can use the seamless roaming procedure to roam between such AP MLDs.

## Slide 9: SP2
Do you agree to define in 11bn a mechanism so that in seamless roaming, before the request/response message for requesting the transition of the non-AP MLD from the current AP MLD to the target AP MLD:
Context can be transferred to the target AP MLD
Links are set up with the target AP MLD

## Slide 10: Thank You