## Slide 1: NPCA with eMLSR, DPS, coex modes
Date: 2024-11-09
Authors:
SP

## Slide 2: eMLSR/DPS/Coex with NPCA
We are defining or enhancing several modes in 11bn for a non-AP STA that lead their associated AP to initiate frame exchanges with the non-AP STA with initial control frames:
  eMLSR enabled at the non-AP MLD the STA is affiliated with
  Dynamic power save (DPS)
  Dynamic unavailability operation (DUO) (coex mode)
For each of these modes, there are different constraints on the type of initial control frame that is sent, and on the inclusion in the initial control frame of intermediate FCS field and amount of padding
  Different padding requirement for different modes, different frames, …

## Slide 3: Coexistence of these modes with NPCA
NPCA also requires that initial control frame precedes every frame exchange on the NPCA primary channel, in order to ensure that the 2 NPCA peers have effectively transitioned to the NPCA primary channel
We need NPCA to coexist with these modes as they are important for power save or operation efficiency on the STA side

## Slide 4: Coexistence of these modes with NPCA
When a STA affiliated with an eMLSR non-AP MLD is in listen mode and transitions from the BSS primary channel to the NPCA primary channel, it still is in listen mode on the NPCA PC
  The associated AP shall therefore initiate frame exchanges with the STA following the eMLSR procedure, and therefore with eMLSR initial control frames, on the NPCA PC the same way it would do on the BSS PC
When a DPS STA is in low capability mode and transitions from the BSS primary channel to the NPCA primary channel, it still is in low capability mode
  The associated AP shall therefore initiate frame exchanges with the STA following the DPS procedure, and therefore with DPS initial control frames
When a STA in dynamic coex mode (DUO) transitions from the BSS primary channel to the NPCA primary channel, it still is in dynamic coex mode
  The associated AP shall therefore initiate frame exchanges with the STA with an initial control frame that allows the STA to respond with an ICR that can contain the dynamic unavailability information

## Slide 5: Proposal
The proposal is very simple and straightforward:
For eMLSR, DPS and Dynamic unavailability operation (DUO – name TBD) or the combinations of those enabled on an NPCA STA, its associated NPCA AP shall use the same ICF-ICR rules that it uses on the BSS primary channel on the NPCA primary channel, except that RTS frame can not be used on the NPCA primary channel.

## Slide 6: eMLSR/DPS with NPCA
NPCA STA operating under eMLSR or DPS mode may have a longer NPCA transition delay than when operating outside of eMLSR/DPS because the operating BW in listen mode likely won’t include the NPCA PC.
Need to be able to have different transition delay depending on whether the STA enabled/disabled eMLSR and/or DPS.
Advertising different transition delay for all these cases in advance does not seem a good solution
Simple solution is to advertise the transition delays when enabling NPCA
  This allows the STA to re-enable NPCA with the updated transition delay if there is a mode change for eMLSR/DPS

## Slide 7: Straw poll 1
Do you agree to add to the 11bn SFD the following:
  For eMLSR, DPS and DUO or the combinations of those enabled on an NPCA STA, its associated NPCA AP shall use the same ICF-ICR rules that it uses on the BSS primary channel on the NPCA primary channel, except that RTS frame can not be used on the NPCA primary channel.