## Slide 1: Seamless Roaming Follow Up 2
Date: 2024-11-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Seamless Roaming
Seamless roaming procedure:
  (optional) step1: Candidate target serving AP MLD acquiring
    A non-AP MLD acquires the candidate target serving AP MLDs through its current serving AP MLD.
  Step 2: establishing the links with the target serving AP MLD.
  Step 3: roaming from the current serving AP MLD to the target AP MLD
    DS mapping update with access server, router, or ethernet switch.
    Frame exchange context transfer to the target AP MLD
    The UL frame changes for UL Data frames are suspended during step 3.
  Step 4: stopping the frame exchanges of Data frames with the current serving AP MLD, and executing the frame exchanges of Data frames with the target serving AP MLD.
    It is possible that both AP MLDs transmit the DL Data frames for some times after step 4.
    The UL Data frames can only be transmitted to the target AP MLD.
MLD level features are either in AP MLD level or in roaming domain level.
Frame exchange context:
  DL: Parameters of Block Ack agreement, SN space, maximal SN being allocated to the frame.
  UL: Parameters of Block Ack agreement, Maximal SN whose frame being sent to the up layer, duplicate detection information.
    The reorder buffer may be forwarded to the target AP MLD.

## Slide 3: Roaming Domain Level and MLD Level Features
Roaming domain level features:
  Authentication,
  Discovery of neighbor target AP MLD in roaming domain,
  BSS transition management for neighbor target AP MLDs in roaming domain,
  ML set up,
  Multi-Link power management
    maximal idle period
  PTK key negotiation,
  SCS,
  BA,
  EPCS.

## Slide 4: Roaming Domain Level and MLD Level Features
MLD level features:
  Discovery of Reported AP in one AP MLD,
  BSS transition management for reported link or neighbor AP MLDs outside the roaming domain,
  BSS parameter critical update,
  ML procedure for channel switch and channel quieting,
  ML power management without maximal idle period,
  Unicast frame delivery,
  MLO group-addressed frames,
  STR,
  NSTR,
  MLSR/EMLSR/EMLMR,
  AID allocation,
  TID-to-Link mapping,
  MLD TWT.

## Slide 5: MLD Level Frame Delivery vs Roaming Domain Level BA Agreement
The MLD level frame delivery means that
  the reorder buffer is identified by the peer MLD MAC address and TID of the BA agreement.
  The TA, RA, BSSID of unicast QoS Data frame are replaced by the respective MLD addresses instead of roaming domain MAC address.
if a non-AP MLD decides to receive unicast DL QoS Data frames from two AP MLDs during the roaming stage, it is up to the non-AP MLD to decide which AP MLD’s address to identify the peer MLD address during the roaming stage.
  E.g. the local mapping from the serving AP MLD address to target AP MLD address is done at the MLD level.

## Slide 6: UL TID with BA Agreement (1)
A reorder buffer of the current serving AP MLD may or may not be moved to the target AP MLD.
  If the current serving AP MLD flushes the reorder buffer where largest SN of received frames is SNmax, the WinStartB in the new serving AP MLD will be the SNmax + 1.
    The retransmission of the frames whose sequence numbers are less than WinStartB to the new serving AP MLD will be discarded.
  If the current serving AP MLD forwards its reorder buffer to the target AP MLD, the WinStartB in the new serving AP MLD will be the same as the WinStartB of the current serving AP MLD.
    The discarding of the frames in Transmit Buffer may create unnecessary frame discarding
Non-AP
MLD1
AP
MLD1
A-MPDU with
SN 0 to 63
BA
MPDU with SN = 0,
SN= 10 are not received.
AP MLD1’s reorder buffer with WinStartB=0, WinEndB=63
has the MPDUs except MPDU with SN = 0, SN = 10.
WinStartO is 0,
WinEndO is 63
Roam to AP MLD 2
WinStartO is 0,
WinEndO is 63
AP
MLD2
AP MLD1 flushes the reorder buffer (the largest
SN = 63) and Notifies 63 +1 as WinStartB to AP MLD 2.
AP MLD1 notifies the WinStartO with AP MLD2 needs to be 64..
AP MLD2’s reorder buffer with WinStartB=64, WinEndB=127
has no frames in its reorder buffer.

## Slide 7: UL TID with BA Agreement (2)
Sending BAR to the target AP MLD doesn’t work:
  The current serving AP MLD notifies the target AP MLD its scoreboard context.
    This is not reliable because of partial state operation.
    The new behavior to scoreboard context needs to be defined if the reorder buffer is flushed.
Solution:
  The target/current serving AP MLD notifies the non-AP MLD the WinStartB of each UL TID with the BA agreement (largest SN whose frame is sent to the up layer) at the new serving AP MLD (or whether the frames in reorder buffer are forward to the new serving AP MLD).
    The non-AP MLD uses the WinStartB as its WinStartO.

## Slide 8: DL Frame Tx from Two AP MLDs
When both current serving AP MLD and the target AP MLD send the DL frames of a BA agreement at the same time period, the frame exchange context for the BA agreement needs to include the WinStartO besides the maximal SN being allocated to the frames of the BA agreement. Otherwise, the transmitted frames from the current serving AP MLD may be discarded as the “old” frames.
  The following is an example:
    The current AP MLD (AP MLD1) has WinStartO=0. the maximal SN being allocated to the frames of a BA agreement with buffer size 64 is 31. the frames with SN 0, 15 to 29 are not received correctly.
    The current AP MLD notifies the target AP MLD (AP MLD2) the maximal SN 31 through frame exchange context transfer.
    After DS mapping, frame exchange context transfer is done (the roaming response frame is transmitted), both AP MLD1 and AP MLD2 transmits the frames of the BA agreement.
      AP MLD2 transmits frame with SN equal to 32 to 200 are correctly while AP MLD1 are still transmit frame with SN 0, 15 to 29.
        AP1’s transmission doesn’t make sense.

## Slide 9: Link Pair to Two AP MLD
The links connecting to two AP MLDs may have some restriction that can’t execute simultaneous frame exchanges with the serving AP MLD and target AP MLD.
The non-AP MLD announces such restriction to the AP MLDs unless the non-AP MLD doesn’t have the links with the two AP MLDs in awake state simultaneously.

## Slide 10: Summary
The following are discussed in the presentation:
  Frame exchange context when two AP MLD send DL frames of a BA agreement
  Frame context notification to the non-AP MLD under seamless roaming.

## Slide 11: SP 1
Do you support to define a way to make available to the non-AP MLD the following during the roaming?
  the latest SN that has been passed up (and will be) to the next MAC process for existing UL BA agreement by the current AP MLD.