## Slide 1: Low Capability Mode Follow Up
Date: 2024-11-09
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Low-capacity Listening Mode Capability Announcement
In order to save power through low capability mode, a STA needs to be in low capability mode while its peer device needs to initiate its TXOP by transmitting a soliciting control frame.
  The STA switches to high capability mode after receiving the soliciting control frame.
  Two roles exist for supporting power save through low capability mode.
Both AP and non-AP STA can be in low capability mode.
A STA needs to announce whether it is capable to solicit peer STA’s switch from low capability mode to high capability mode.
  The capability can be announced in a subfield (DPS Initiating Support) in UHR Capabilities element.
A non-AP STA that has the capability of switch from low capability mode to high capability mode doesn’t announce its capability.
  However, the non-AP STA can enable its low capability mode.

## Slide 3: Low Capability Mode Enabling/Disabling (1)
A non-AP STA enables/disables its low capability mode if its associated AP announces the support of low capability mode initiating (DPS Initiating Support subfield in UHR Capabilities element equal to 1).
  One variant is that each regular AP has its DPS Initiating Support equal to 1.
  The protected UHR Action frame Low Capability Mode Request/Response frame can be defined.
  The Action frame transmitted by the non-AP STA trying to enables its low capability mode carries the following requirements
    the STA’s padding delay from low capability mode to high capability mode (DPS Padding Delay).
    The STA’s transition delay from high capability mode to low capability mode (DPS Transition Delay).
    The DPS Padding Delay and DPS Transition Delay have smallest value 0 and maximal value 256us with granularity of 4us.

## Slide 4: Switching Back to Low Capability Mode
When a STA as the TXOP responder is in high capability mode and does the frame exchanges with its peer device in a TXOP, the STA switch back to low capability mode as follows:
  The STA as the TXOP responder switches back to low capability mode if the condition related to EMLSR STA’s switching back to listening mode happens.

## Slide 5: SP 1
Do you agree to have the same rules as eMLSR for a DPS STA to switch back from high capability mode to low capability mode?
  Specific details are TBD.

## Slide 6: Back Up Slide

## Slide 7: Low Capability Mode Enabling/Disabling (2)
An AP with non-zero DPS Padding Delay that belongs to neither multiple BSSID AP set nor co-hosted AP set can enable its low capability mode if the following conditions are true.
  All associated STAs have their DPS Initiating Support equal to 1.
An AP with zero DPS Padding Delay that belongs to neither multiple BSSID AP set nor co-hosted AP set can enable its low capability mode if the following conditions are true.
  All associated STAs are HE STAs.
An AP announces its future TBTT when the AP will enable its low capability mode or disable its low capability mode as indicated in the related field of the Beacon (in a new defined element).
  The future TBTT is defined by the number of BIs indicated in the related field of the transmitted Beacon (in a new defined element).
  After each TBTT, the number of BIs indicated in the related field of the transmitted Beacon is decreased by 1.
  When the number of BIs indicated in the related field of the transmitted Beacon becomes 0, the AP enable/disable its low capability mode as announced.
  The new defined element also includes the padding delay for the switch from low capability state to high capability state, and the transition delay from the high capability state to low capability state.

## Slide 8: Low Capability Mode Enabling/Disabling under MLO
The switch between low capability mode and high capability mode in a link of an AP MLD is a critical event.
When the AP MLD announces the link1’s mode switch through the new defined element, the BPCC of the related link is increased by 1. One of the Critical Update Flag and the Nontransmitted BSSID Critical Update Flag related to the AP MLD is set to 1 until the TBTT of link1 when the mode switch happens arrives. The link1’s new defined element for the capability mode switch is not announced in another link’s Beacon.
  Another variant is that the link1’s new defined element for the capability mode switch is also announced in another link’s Beacon.
When the new defined element about the capability mode switch of link1 is transmitted in another link, the number of BIs related to the target TBTT is defined based on link1’s TBTT, beacon interval.
When a STA affiliated with a non-AP MLD in link1 enables/disables its low capability mode by exchanging Low Capability Mode Negotiation Request/Response frame, the Negotiation Request/Response frame can be transmitted in another link.

## Slide 9: Initiating Frame for Mode Switch
Observation:
  A STA in low listening mode can receive any type of frame in 20MHz BW, restricted PPDU format and data rate.
    It seems any frame satisfies such requirement can be used as the initiating frame.
To simplify the implementation and inter-op test, some restriction should be applied to the initiating frame
  MU-RTS
  BSRP Trigger
  RTS if no padding requirement for low capability mode is required.

## Slide 10: Frame Solicited by Initiating Frame for Mode Switch
CTS solicited by RTS
  RTS + CTS may be used if the following are true: no padding, single TXOP responder, no control frame protection, no IDC feedback
CTS solicited by MU-RTS
  MU-RTS + CTS may be used if the following are true: single TXOP responder, no control frame protection, no IDC feedback
QoS solicited by BSRP Trigger
  BSRP Trigger + QoS Null may be used if the following are true: no control frame protection, no IDC feedback
Multi-STA BA solicited by BSRP Trigger
  BSRP Trigger + Multi-STA BA needs to be used if at least one of the following is true: control frame protection, IDC feedback