## Slide 1: SMD Architecture
Date: 2024-11-04
Authors:

## Slide 2: Introduction
TGbn SFD Motion 279 defines a logical SMD-ME (SMD management entity) that provides SMD level association, authentication and RSNA key management (PMKSA and PTKSA) functions
SMD defines a set of AP MLDs across which a non-AP MLD can perform seamless roaming
SFD Motion 280 defines support for following two SMD roaming architectures:
  SMD arch with separate MAC-SAP per AP MLD – this enables seamless roaming between AP MLDs of an SMD where each AP MLD exposes its own MAC-SAP to the DS for the data path (distributed SMD arch).
  SMD arch with a single MAC-SAP for the SMD – this enables seamless roaming between AP MLDs of an SMD where a single MAC-SAP is exposed to the DS across all AP MLDs of the SMD for the data path (centralized SMD arch).
In this presentation we describe a common SMD framework/architecture that would support both variants of SMD roaming architecture

## Slide 3: SMD Architecture (1)
In the SMD architecture, logical SMD-ME provides single anchor point for SMD level authentication (including 802.1X Authenticator), association and RSNA Key Management, across all AP MLDs of the SMD.
  SMD-ME has a unique SMD Identifier (48-bit MAC Address), which is also the 802.1X Authenticator address (AA) of that SMD-ME
  PMK and shared PTK keys are established between SMD-ME (identified by SMD Identifier, also AA) and the non-AP MLD (identified by non-AP MAC address, also SPA)
Upper MAC functions are split between AP MLDs and the SMD-ME, generically shown as ‘SMD Upper MAC Part 1’ and ‘SMD Upper MAC Part 2’.
  Upper MAC functions at the SMD-ME include management functions of authentication, association and security association mgmt. Split of other upper MAC functions between SMD-ME and AP MLDs is based on distributed vs centralized SMD arch.
  AP2AP interface used for context transfer during seamless roaming (in distributed SMD arch.)
(11be D7.0: 5.1.5.1a MLD MAC sublayer functions)

## Slide 4: SMD Architecture (2)
The logical SMD-ME can be hosted on a centralized controller/WLC or on individual AP MLDs of the SMD in physical network deployments
SMD-ME hosted on a WLC:
WLC provides SMD level authentication (including 802.1X Authenticator), association, and RSNA key mgmt for non-AP MLDs
This deployment is possible both for distributed and centralized SMD architecture
Context related to a non-AP MLD is transferred between AP MLDs during SR in distributed SMD arch
SMD-ME hosted on AP MLDs:
In a distributed SMD arch, the logical SMD-ME can be hosted on each AP MLDs of the SMD
SMD level authentication (including 802.1X Authenticator), association and RSNA key management functions for non-AP MLDs are hosted in a distributed manner on AP MLDs
Context related to a non-AP MLD is transferred between AP MLDs during SR

## Slide 5: SMD Architecture – Management of 802.1X Ports (1)
SMD-ME has the 802.1X Authenticator that provides 802.1X authentication functions for non-AP MLDs. Data path to the DS is managed via 802.1X Controlled and Uncontrolled Ports filtering as defined in the baseline.
In a distributed SMD arch, 802.1X Controlled and Uncontrolled Port filtering is performed at each AP MLD. In a centralized SMD arch, 802.1X Controlled and Uncontrolled Port filtering is performed at the SMD-ME.
In a distributed SMD arch, a component of the 802.1X Authenticator on each AP MLD manages the blocking and unblocking of 802.1X Controlled ports at the AP MLD level, based on the point of latest attachment for the non-AP MLD.
  At initial SMD association with AP MLD1, the 802.1X Controlled Port at AP MLD1 is unblocked
Case 1: Distributed SMD arch with logical SMD-ME
  Access to DS via C-port is enabled only through MAC-SAP of one of the AP MLDs at a time
  During seamless roaming execution, 802.1X Controlled port at current AP MLD1 is blocked (for the UL) and the 802.1X Controlled port at target AP MLD2 becomes unblocked (for DL and UL)
  After DS mapping change, Tx/Rx with DS is opened through Controlled-port of target AP MLD2.

## Slide 6: SMD Architecture – Management of 802.1X Ports (2)
Case 1b: Distributed SMD arch with SMD-ME hosted at each AP MLD
  Each AP MLD is hosting 802.1X Authenticator component as part of SMD-ME
  During SR, after receiving roaming execution request, 802.1X Controller port at current AP MLD1 is blocked (for UL)
    Note: DL data from the DS can keep flowing to AP MLD1 during SR execution until DS mapping change happens
  As part of the roaming execution, the 802.1X Controlled port at the target AP MLD2 is unblocked, after DS mapping change is initiated
  802.1X Authenticator of the SMD-ME at the current and target AP MLDs is identified by same AA address (the SMD Identifier)
  The MAC-SAP of each AP MLD is identified by the AP MLD MAC address (as in EHT)
Distirbuted SMD arch (fully distributed physical deployment)
Case 1: Distributed SMD arch
  On the non-AP MLD/Supplicant side, the 802.1X Controlled port is unblocked for passing MSDUs to the upper layer at initial association to SMD-ME, and remains unblocked during SR execution

## Slide 7: DS Mapping change for Distributed SMD Arch
For distributed SMD architecture, the logical SMD-ME component on the target AP MLD should initiate DS mapping change, since non-AP MLD associates with the SMD-ME. The DS SAP primitive is enhanced to support this.
  Add a new APMLDMACAddress parameter that specifies the MLD MAC address of the AP MLD trough which the non-AP MLD specified by the STAAddress is now connected within the SMD.
  The DS would deliver MAC service tuples that are destined for the non-AP MLD to the AP MLD specified by the APMLDMACAddress
  DS-STA-NOTIFY.request(
STAAddress,
APMLDMACAddress,
UpdateType
)

## Slide 8: SMD Architecture – Management of 802.1X Ports (3)
Case 2: Centralized SMD arch
  SMD-ME is hosted at a centralized entity that exposes the single MAC-SAP
  The single MAC-SAP is identified by the SMD Identifier (48-bit MAC Address)
  The 802.1X Authenticator (identified by SMD Identifier) manages 802.1X Controlled ports blocking and unblocking for the non-AP MLDs
  During SR to AP MLD2, no DS mapping change is initiated. However, attachment point for the non-AP MLD is changed from AP MLD1 to AP MLD2.
  Split of Upper MAC data path functionality between AP MLD and SMD-ME can be implementation dependent
Case 2: Centralized SMD arch
  On the non-AP MLD/Supplicant side, the 802.1X Controlled port is unblocked for passing MSDUs to the upper layer at initial association to SMD-ME, and remains unblocked during SR execution

## Slide 9: Access to DS for non 802.1X Auth Schemes
In case of non 802.1X authentication (e.g. SAE, PSK), access to the DS for non-AP MLD during SR is not controlled via the 802.1X Controlled ports, but follows similar logic
For distributed SMD arch, following behavior would apply (similar to 802.1X auth):
  For initial association to SMD-ME, access to the DS at the AP MLD MAC-SAP is opened after RSNA keys are established & installed post 4-way HS (per baseline)
  During SR, after receiving roaming exec request, UL Tx to DS on current AP MLD is blocked (after flushing buffered UL data). DL from DS remains open until DS mapping change happens at the target AP MLD
  At the target AP MLD, as part of roaming execution, DS mapping change is initiated and that opens Tx/Rx access to the DS for the non-AP MLD
    Note: PTKSA (with shared PTK or per-AP MLD TK) is already setup at the target AP as part of roaming prep phase
For centralized SMD arch, access to the DS via single SMD MAC-SAP is opened after RSNA keys are established & installed post 4-way HS during initial assoc to SMD-ME
  Tx/Rx access to DS remains open through SR execution

## Slide 10
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
1. Non-AP MLD is connected to DS through the links of AP MLD1.
Case 1: Seamless Roaming with Distributed SMD Arch (1)

## Slide 11
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
2. Non-AP MLD performs roaming execution to AP MLD2 using Link Reconfig Req/Resp. UL data to DS is blocked from AP MLD1 during roaming execution. After DS mapping change is initiated by AP MLD 2, UL and DL data with DS is enabled with AP MLD2.
Case 1: Seamless Roaming with Distributed SMD Arch (2)
Context transfer

## Slide 12
SMD-ME
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
MLD Upper MAC
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
SMD-ME
SMD Upper MAC Part 1
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
3. Non-AP MLD has completed roaming execution (& any download of buffered DL) and is now connected to DS through the links of AP MLD2.
Case 1: Seamless Roaming with Distributed SMD Arch (3)

## Slide 13: Case 2: Seamless Roaming with Centralized SMD Arch (1)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
1. Non-AP MLD is connected to DS through the links of AP MLD1.

## Slide 14: Case 2: Seamless Roaming with Centralized SMD Arch (2)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
2. Non-AP MLD performs roaming execution to AP MLD2 using Link Reconfig Req/Resp. Tx/Rx can remain open between AP MLD1, AP MLD2 and SMD-ME during roaming execution, however client UL behavior may be same as distributed case for consistent behavior. Tx/Rx remains open with the DS via SMD MAC-SAP.

## Slide 15: Case 2: Seamless Roaming with Centralized SMD Arch (3)
AP MLD1
MLD Lower MAC
AP11
PHY
MLD Lower MAC
AP12
PHY
AP MLD2
MLD Lower MAC
AP21
PHY
MLD Lower MAC
AP22
PHY
MLD Upper MAC
MLD Upper MAC
SMD
SMD Upper MAC Part 1
AP MLD3
MLD Lower MAC
AP31
PHY
MLD Lower MAC
AP32
PHY
MLD Upper MAC
SMD Upper MAC Part 1
SMD Upper MAC Part 1
SMD Upper MAC Part 2
SMD-ME
MAC SAP
MAC SAP
MAC SAP
MAC SAP
DS (Distribution System)
STA 1
Non-AP MLD
STA 2
3. Non-AP MLD has completed roaming execution and is connected to DS through the links of AP MLD2.

## Slide 16: Conclusion
We covered a common SMD framework to support both variants of SMD roaming arch.
  Distributed SMD arch with separate MAC-SAP per AP MLD of the SMD
  Centralized SMD arch with a single MAC-SAP for the SMD
A logical SMD-ME provides single anchor point for SMD level authentication (including 802.1X Authenticator), association and RSNA Key Management, across all AP MLDs of the SMD
In the case of distributed SMD arch, the 802.1X Authenticator component manages blocking and unblocking of 802.1X Controlled ports at per AP MLD level, as the non-AP MLD roams within the SMD
In the case of centralized SMD arch, the 802.1X Authenticator in the SMD-ME manages blocking and unblocking of 802.1X Controlled ports for the non-AP MLD at the SMD-ME
  SMD-ME supports upper MAC data path functionality
For non 802.1X Auth schemes (e.g. SAE, PSK), in distributed SMD arch managing access to the DS follows similar logic as blocking/unblocking of 802.1X controlled ports
On the non-AP MLD/Supplicant side, 802.1X Controlled port is unblocked for passing MSDUs to the upper layer at initial association to SMD-ME, and remains unblocked during SR execution

## Slide 17: SP1
Do you support that for a Seamless Mobility Domain (SMD), the SMD and the 802.1X Authenticator component in the corresponding SMD-ME are uniquely identified by an SMD Identifier?
The SMD identifier is in the format of a 48-bit MAC address
The SMD Identifier is used in establishing single PMKSA and PTKSA for a non-AP MLD that associates with the SMD-ME

## Slide 18: SP2
Do you support that for an SMD, in the case of a separate MAC-SAP per AP MLD architecture, the 802.1X Authenticator component manages blocking and unblocking of 802.1X Controlled ports for a non-AP MLD at the AP MLDs of the SMD, as the non-AP MLD roams within the SMD?
At initial association to SMD-ME through an AP MLD1, the 802.1X Authenticator unblocks 802.1X Controlled Port at the AP MLD1 for the non-AP MLD
During seamless roaming execution, 802.1X Authenticator blocks 802.1X Controlled port at the current AP MLD1 for UL direction and unblocks 802.1X Controlled port at the target AP MLD2, after the DS mapping change is initiated at the target AP MLD