## Slide 1: Control Frame Protection Keys
Date: 2024-11-10
Nehru Bhandaru (Broadcom)
Name(s) | Affiliation | Address | Contact Phone | Contact Email
Nehru Bhandaru | Broadcom | 250 Innovation Drive, San Jose CA 95134 | +1 408 391 2159 | nehru.bhandaru@broadcom.com
Thomas Derham | Broadcom |  |  | thomas.derham@broadcom.com

## Slide 2: Introduction
Control Frame Protection (CFP) has been proposed for 11bn in multiple contributions, e.g. [1], [2]
Various aspects of CFP design need to be determined, e.g.
  Which keys are needed and where do the keys come from
  What is the algorithm for integrity protection of these frames
  What is the PN Space and Replay Protection
  Changes to Signaling/Negotiation
  What frames to protect
    unicast - Trigger, BA, BAR Frames
    Multi-STA BAR needs group keys
  What is the frame format
  MLD Support, per-link keys
  How many keys - Unicast and for BSS Group
This contribution proposes several of these details, particularly on the key usage, protection algorithm and PN management

## Slide 3: CFP keys, algorithm and PN management
Where do the keys for CFP come from – use same key as for data/management frames, or define separate keys for CFP?
If a new key is derived for CFP it would require:
  Additional hardware storage space in implementations to store the new keys (particularly for AP MLDs, which need to store an additional key per non-AP MLD)
  Work to define the KDF (e.g. AES-CMAC vs HMAC-Hash KDF) and other aspects of the key management
Using the same key for CFP and data/management frames is preferable
  Nonce collisions can be avoided in a simple way by partitioning the PN space so that a dedicated part is used for for CFP only.
  Since the number of protected control frames will be much less than the number of management frames, minimize reduction of PN space for data/mgmt frames by setting TBD MSBs of PN to all-ones for CFP, and using all other values of the MSBs for data/mgmt frames
  In order that the TK is always used with the same cipher family (see [3]), require unicast data/management frames to use GCMP-256 and unicast control frames to use GMAC-256
Protected control frames will have their own replay counter
Nonce construction does not change except for PN space usage
  TA identifies the link
  MLD address used in the Nonce as before
No changes to existing key derivation

## Slide 4: Strawpoll
SP: Do you support the following?
The key to protect individually addressed Trigger/BA/BAR is the same as TK. Further, GCMP-256 shall be used as the pairwise cipher for individually addressed data and management frame, TBD most significant bits of PN for protecting individually addressed Trigger/BA/BAR shall be set to all 1, and same TBD most significant bits of PN for protecting individually addressed data and management shall not be set to all 1

## Slide 5: References
11-23/2001r2: Secure Control Frames Follow Up, Alfred Asterjadhi
11-24/0497r0: Security Enhancement Control Frame Protection Follow-up, Liwen Chu
NIST SP 800 38D