## Slide 1: Trigger Frame Protection Signaling
Date: 2024-11-10
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Ido Ouzieli |  |  |  | 
Danny Alexander |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Trigger frame protection has been discussed in various presentations
  Key ID field, PN field, and MIC field are required to enable authentication of the Trigger frame
  Padding field may be required to provide enough time for MIC computation
In this presentation, we provide further details for the design consideration above.

## Slide 3: Location of Key ID field
Key ID field, likely one bit, is required for the receiver to retrieve the key
Retrieve the key early can enable early computation of MIC while doing reception and potentially reduce the required padding
Proposal: have the Key ID bit in the common info field of the UHR-variant Trigger frame
  The earliest location to have the bit
  To enable Trigger frame protection while UHR is aggregated with legacy HE/EHT STA in HE/EHT-variant Trigger frame, the same proposal can apply to HE/EHT-variant Trigger frame

## Slide 4: Location of MIC and PN field
We need to insert MIC and PN in the Trigger frame in the legacy compatible fashion
  This is the same design consideration for IFCS
  Expect that MIC and PN fields are in front of the IFCS if both are present in a Trigger frame
Proposal: using similar ways to include MIC/PN fields and IFCS fields.

## Slide 5: Indication whether Trigger frame is protected
When none of the receiving UHR non-AP STA support Trigger frame protection, there is no need to include PN and MIC fields
If PN and MIC fields are not included, then Key ID field does not have any meaning.
Proposal: Have a bit in Trigger frame to indicate whether Trigger frame is protected or not
  Bit is reserved if the Trigger frame is not protected
  Needs to be in the same place of Key ID field. Common Info field is then the natural place
  UHR non-AP STA that supports Trigger frame protection can skip MIC computation and further parsing if Trigger frame is not protected

## Slide 6: Indication whether BA/BAR is protected
From AP’s point of view, an indication whether the BA/BAR frame is protected can eliminate the need for key searching if the bit is set to 0
  Using only TA field to check if there is a key requires additional time
In M-BA, the M-BA maybe sent by AP using group addressed frame, so the same consideration from Trigger frame to have the protection indication applies.
Similar consideration with Trigger frame, the bit should be in the same place as Key ID field, and as early as possible. BAR control and BA control are the natural places.
Proposal:
  In a BA/BAR frame that is defined to be protected, one bit is used to indicate that the BA/BAR frame is protected, i.e., with PN and MIC
    For protected Multi-STA BA, the bit is indicated in BA control field
    For protected compressed BAR variant and protected Multi-TID BAR variant, the bit is indicated in BAR control field

## Slide 7: Location of Padding bits
Fortunately, we already have padding mechanism in Trigger frame.
Padding in the Trigger frame can use existing mechanism to provide backward compatibility
Padding needs to be after PN and MIC field
  Similar consideration that padding needs to be after IFCS
A summary of different cases is the following
  With PN/MIC and IFCS
    PN, MIC, IFCS, padding, FCS
  With PN/MIC and without IFCS
    PN, MIC, padding, FCS
  Without PN/MIC and with IFCS
    IFCS, padding, FCS

## Slide 8: Conclusion
We discuss the Trigger Frame protection format with the following considerations
  Location of Key ID field
  Location of PN and MIC fields
  Indication whether Trigger frame is protected or not
  Location of Padding bits
On the similar not of indicating Trigger frame is protected or not, have similar indication for BA/BAR that are defined to be protected in BA control and BAR control

## Slide 9: Straw Poll:
Do you agree with the following:
  for UHR-variant trigger frame TF protected or not: 1 bit field in UHR-variant common info field
    TBD for HE/EHT-variant
  in a BA/BAR frame that is defined to be protected, one bit is used to indicate that the BA/BAR frame is protected, i.e., with PN and MIC?
    For protected Multi-STA BA, the bit is indicated in BA control field
    For protected compressed BAR variant and protected Multi-TID BAR variant, the bit is indicated in BAR control field

## Slide 10: Reference
[1] 11-23-286 Trigger frame protection
[2] 11-23-0312 Thoughts on Secure Control frames
[3] 11-23-1914 Enhanced Security Considerations in UHR
[4] 11-23-1915 Enhanced Security for Control frame in 11bn
[5] 11-23-1933 security enhancement follow up
[6] 11-23-2001 Secure Control frames - Follow up
[7] 11-24-0151 Establishment of Security Key for Control Frame
[8] 11-24-497 security enhancement (control frame protection) follow up
[9] 11-24-547 Secure Control frames - Follow Up
[10] 11-24-1226 ICF-ICR design