## Slide 1: Protection Improvement for C-RTWT
Date: 2024-05-05
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | OPPO |  |  | v-xinliangxiao@oppo.com
Liuming Lu |  |  |  | 
Chaoming Luo |  |  |  | 
Wei Dong |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 

## Slide 2: Introduction
TGbe introduced a low latency mechanism R-TWT which provides intra-BSS protection for low latency traffic during R-TWT SP.
TGbn has passed the motion of adding C-RTWT to SFD, which provides inter-BSS protection for R-TWT SP.
However, the current R-TWT SP protection (i.e., TXOP-end rule) may discourage STAs to respect the R-TWT SP.
In this contribution, we discuss how to improve the R-TWT SP protection to encourage more STAs to follow the TXOP-end rule.

## Slide 3: Current R-TWT Protection
A R-TWT enabled STA shall end its TXOP before the start time of an R-TWT SP.
The performance of R-TWT depends on the ratio of R-TWT enabled STAs in the BSS and the number of OBSS STAs.
  The R-TWT works only when the ratio of R-TWT enabled STAs in the BSS is high.
  The R-TWT SP is not respected by OBSS.
Therefore, the key to success is to encourage more intra-BSS and inter-BSS STAs to follow the R-TWT rule.
R-TWT SP
RTS
CTS
BO
End TXOP

## Slide 4: Reasons to not enable R-TWT
STAs are selfish.
If a STA enables R-TWT feature, it has to shorten its TXOP before the start time of R-TWT SP, which is not good for its throughput and latency!!!
STA may occupy more than 20MHz bandwidth for transmission.
  In current standard, if STA ends its TXOP on the primary channel, it has to end the TXOP on the secondary channel as well.
  STA loses more TXOP resource.
R-TWT SP
P80
S80
RTS
CTS
BO
End TXOP

## Slide 5: Proposed Solution
NPCA/DSO operation
  STA contends on primary channel to obtain TXOP
  If STA obtains the TXOP of multiple 20MHz channel, it
    Ends the TXOP on the primary 20 MHz channel,
    Continues to transmit on other non-primary channels.
  The primary channel is idle for the R-TWT SP.
OBSS R-TWT SP
P80
S80
ICF
ICR
DATA
BA
BO
DATA
BA
ICF
ICR
DATA
BA

## Slide 6: Benefits of Proposed Solution
The proposed NPCA/DSO operation does not require special channel access mechanism.
The proposed solution allows to continue the on-going TXOP on the non-primary channel when the primary channel is scheduled for R-TWT SP.
  Good for TXOP holder: TXOP holder can continue transmission.
  Good for R-TWT SP: R-TWT STAs can contend on the primary channel.

## Slide 7: Summary
In this contribution, we show that NPCA/DSO can help STA to continue its on-going TXOP on the secondary channel when the primary channel is unavailable.

## Slide 8: SP1
Do you support to include the following in SFD?
  When STA is a TXOP holder, it may stop the TXOP on the primary channel but continue the TXOP on the other non-primary channel.