## Slide 1: High-Capability Protection in DPS Follow Up
Date: 2024-11-25
Authors:

## Slide 2: Introduction
Low power listen mode was proposed by [1]. References[2-6] continue to develop the low power listen mode to dynamic power save (DPS) and provide more details.
References[4, 5, 7] propose to add a new Intermediate FCS field before the padding so that the STA can use the padding time to change bandwidth.
STA in DPS mode will start switch from the high-capability mode to the low-capability mode under TBD conditions.
When capability switching involves bandwidth changing, the round-trip switch delay is relatively large [9].

## Slide 3: Motivation
The round-trip switch delay (e.g. 512 µs ) accounts for a high proportion of the time-limited TXOP.
If the data transmission has not been completed and capability switches are performed each TXOP, there will be a large unnecessary padding cost and time waste.
For some data transmission tasks, the transmission duration can be roughly estimated in advance based on the amount of data and PHY capabilities.
If it is determined in advance that the data transmission task cannot be completed within one TXOP, it is not appropriate to force the DPS STA to return to the low-capability mode at the end of the TXOP and reawaken it in the next TXOP (e.g. a total of 512 μs will be wasted).
Slide 3
High-capability mode
ICF
Low-capability mode
Switch delay
Switch back delay
Duration
Low-capability mode
padding

## Slide 4: Proposal 1: High-capability protection time
Taking STA DPS as an example.
ICF from AP can indicate time or duration information based on data volume and capabilities in high-capability mode.
STA replies ICR, which also contains time information based on ICF.
STA starts switching back on or after the indicated end time.
If the time span exceeds the TXOP, AP does not need to switch the STA to high-capability mode on next TXOP, it can directly communicate with the STA in high-capability.
If AP need to increase or decrease the time, it can send ICF w/o padding but w/ time information to update the end time. STA replies ICR containing the updated time information.
High-capability mode
ICF
Low-capability mode
Switch delay
Switch back delay
Duration
Low-capability mode
padding
TXOP
TXOP
TXOP

## Slide 5: Proposal 1: High-capability protection time
High-capability mode
ICF
Switch delay
Duration
padding
Switch back delay
Low-capability mode
Low-capability mode
Time information in ICF and ICR can be used to protect high capability. First, the time can be initially estimated; Second, the time can be updated based on the actual transmission progress.
High-capability protection mode can be enabled in scenarios where data transmission is expected to be completed as soon as possible.
High-capability protection time can be used for both TXOP level DPS and cross-TXOP DPS.

## Slide 6: Proposal 2: Flexible timeout interval
If the time without successful frame exchange between AP and DPS STA exceeds a timeout interval, the DPS STA starts switching back. (The timeout interval can be indicated during DPS operation parameters update phase. It can be larger than EMLSR’s timeout interval because DPS does not need to switch as sensitively as EMLSR. The larger timeout interval offers robustness for DPS. Robustness is another way to protect high-capability.)
DPS STA
Switch back delay
STA starts switching back
Timeout interval
AP
Data
ACK
In EMLSR, the timeout interval is predefined to be aSIFSTime + aSlotTime + aRxPHYStartDelay.
DPS and EMLSR have different purposes and characteristics. The purpose of EMLSR is to find a frequency band with better channel quality, so once it finds a problem with the current band, it will switch to another. However, the problem may not be a problem for DPS. For example, AP can wake up multiple DPS STAs at the same time, with a larger timeout interval, some STAs are allowed to wait for a period of time instead of switching back immediately once it finds that the current frame is not for themselves.
Low-capability mode
High-capability mode

## Slide 7: Proposal 2: Flexible timeout interval
In addition, it takes more time to change the bandwidth in DPS. When data transmission has not been completed, oversensitive switchback mechanism may reduce goodput and counteract power saving. Being more robust can avoid the time, padding and power overhead of unnecessary frequent switching.
In another case, when AP does not complete data transmission within the current TXOP and the AP regains a new TXOP within the timeout interval, it can directly send packets to the DPS STA in high-capability mode without spending time to wait the DPS STA go back to low-capability mode and wake it up again.
DPS STA
AP
High-capability mode
TXOP
STA starts switching back
Switch back delay
Timeout interval
TXOP
Timeout interval
Low-capability mode
If the time without successful frame exchange between AP and DPS STA exceeds a timeout interval, the DPS STA starts switching back. (The timeout interval can be indicated during DPS operation parameters update phase. It can be larger than EMLSR’s timeout interval because DPS does not need to switch as sensitively as EMLSR. The larger timeout interval offers robustness for DPS. Robustness is another way to protect high-capability.)
DPS STA
Switch back delay
STA starts switching back
Timeout interval
AP
Data
ACK
Low-capability mode
High-capability mode

## Slide 8: Proposal 2: Flexible timeout interval
Use case 1: When an error occurs in data reception, the AP is allowed to retransmit the frame before the DPS STA switches back to low-capability mode with a larger timeout interval.
Use case 3: If the original TXOP initiator does not regain a new TXOP within the timeout interval, the DPS STA will start switch back at the end of the countdown.
Use case 2: When the data is not completely transmitted, and the original TXOP initiator regains a new TXOP within the timeout interval, the DPS STA can maintain high-capability mode across TXOPs.
Use case 4: AP wakes up multiple DPS STAs at the same time, AP can prioritize some STAs or temporarily schedule other STAs.
Use case 5: To be compatible with new features, such as CoBF and CSR.

## Slide 9: Summary
In this contribution, we propose high-capability protection methods in DPS to avoid frequent capability states switching and unnecessary time, padding, and power overhead before data transmission is completed.
Due to the introduction of high-capability protection, it is possible to achieve DPS across TXOPs in the case where the data transmission is not completed within one TXOP.
The switchback conditions can be used for both TXOP level DPS and cross-TXOP DPS.
Switch-back conditions with high-capability protection can cope with various practical scenarios in DPS.

## Slide 10: References
[1] 11-22-1414-00-0uhr-low-power-listening-mode
[2] 11-23-0010-00-0uhr-considerations-for-enabling-ap-power-save
[3] 11-23-1875-01-00bn-power-save-proposal-for-non-ap-mobile-ap
[4] 11-23-2003-00-00bn-client-power-save
[5] 11-23-1965-00-00bn-dynamic-power-save-follow-up
[6] 11-24-0485-00-00bn-low-power-listening-mode-for-clients
[7] 11-23-1873-00-00bn-post-fcs-mac-padding
[8] 11-23-1942-00-00bn-inter-ppdu-low-power-listening-scheme
[9] 11-24-0844-00-00bn-padding-time-in-dynamic-power-save

## Slide 11: SP 1
Do you support to include the following in the 11bn SFD?
  For DPS non-AP STA(s) and UHR EMLSR non-AP STA, the switch-back behavior is the same as EMLSR, with the following exceptions:
  – The timeout interval may be explicitly indicated, which replaces the default timeout value.

## Slide 12: SP 2
Do you support to include the following in the 11bn SFD?
  The high-capability duration in DPS can be exchanged and updated through ICF and ICR.

## Slide 13: SP 3
Do you support to include the following in the 11bn SFD?
  When data transmission for DPS STA is not completed, the DPS STA are allowed to maintain the high-capability mode across TXOPs under TBD conditions.