## Slide 1: NPCA Primary Channel Access
Date: 2024-12-12
Authors:

## Slide 2: Introduction
According to SFD [1], TGbn has agreed to define a non-primary channel access (NPCA) mode that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  A BSS shall only have a single NPCA primary channel
In this proposal, we discuss how to access NPCA primary channel (PCH)

## Slide 3: Background
Many contributions have discussed the “switching then access” procedure; ideally, AP and non-AP STAs switch to NPCA PCH synchronously/simultaneously
  See references in [Sec 3.4 Non-primary channel access, 1] and [2]
A potential approach is to enable only AP triggered transmission in accessing NPCA PCH (trigger-only mode)

## Slide 4: Contention-enable Mode
However, with trigger-only mode
  Non-AP STAs passively lose the opportunity for channel contention after switching
  especially for those that have the capability to maintain medium synchronization in NPCA PCH
As such, it would be more beneficial to consider both trigger-only mode and contention-enable mode for accessing NPCA PCH
Besides, we may define another restricted contention-enable mode, see next page

## Slide 5: Proposed Solution 1 Enable Restricted Contention-enable Mode
What is a restricted contention-enable?
  Let non-AP use EDCA to access NPCA PCH, then share wireless resources to AP on NPCA PCH
  AP may choose whether to reply/accept depending on its capability and channel state
    e.g., whether can reply on NPCA PCH
  AP may perform BW extension to find more available channels after being shared
    A special case: PCH is idle on AP side, then PCH can potential also be utilized

## Slide 6: Proposed Solution 2 Improvement for Accessing Efficiency
Improvement 1: AP signals a maximum acceptable switch time
  AP can have control over the maximum acceptable switch time to improve access efficiency for performing NPCA
    Considering switch time for some non-AP STAs may be too long to access a certain NPCA PCH, especially when beyond its operating bw
Improvement 2: Non-AP signals a preferred ending time
  Non-AP can choose to keep staying on NPCA PCH after this NPCA occurrence ends, to avoid frequently switching back and forth
    It can change its choice for each NPCA occurrence by updating this time value

## Slide 7: Summary
In this contribution, we discussed how to access NPCA PCH and corresponding solutions
  Solution 1: Enable trigger-only access mode & contention-enable access mode
  Solution 2: Improvement for accessing efficiency
Notes: In this proposal, we focus on the TXOP level preemption, introducing a credibility criterion to assist the fair classification among streams and honest behavior between STAs to further promote the preemption feature

## Slide 8: Straw Poll 1
Do you agree to define a mode in NPCA where the non-AP can access NPCA primary channel after switching under TBD conditions?
NOTE – Whether to mandate the non-AP to share wireless resources to AP on NPCA PCH is TBD

## Slide 9: Straw Poll 2
Do you agree that the AP may signal a maximum acceptable switch time in NPCA?

## Slide 10: Straw Poll 3
Do you agree that the non-AP may signal a preferred ending time when responding on the NPCA primary channel?

## Slide 11: References
11-24/209r6, Specification Framework for TGbn
11-23-2005-01-00bn-non-primary-channel-access-npca