## Slide 1: NPCA Triggered by Intra-BSS TXOP
Date: 2024-11-12
Authors:

## Slide 2: Introduction
NPCA has been proposed in TGbn to improve medium efficiency
  When OBSS transmissions occupy the primary channel, NPCA operation can be triggered
Discussions are ongoing about using a separate NPCA EDCA state variable in addition to the existing EDCA state variable
This contribution proposes NPCA operation triggered by intra-BSS TXOP exploiting NPCA EDCA behavior
  Considering the asymmetric operational bandwidth between AP and STAs
  Leveraging preemption mechanism

## Slide 3: NPCA Triggered by Intra-BSS TXOP
A non-AP STA acquires TXOP occupying only a part of the BSS operational bandwidth
  The NPCA primary channel remains unoccupied
  It is assumed that the non-AP STA allows preemption within its TXOP
The AP initiates NPCA EDCA operation within the non-AP STA's TXOP
  The timing of EDCA initiation may vary depending on the AP's hardware capability and in-band interference

## Slide 4: NPCA Triggered by Intra-BSS TXOP
A Preemption Request is sent by one or more STAs
When the AP responds with a control frame (e.g., BSRP), it includes idle NPCA channels
  Only when the NPCA backoff counter reaches zero
The NPCA TXOP should be terminated before the end of the primary channel TXOP

## Slide 5: Summary
This contribution proposes NPCA operation triggered by intra-BSS TXOP to enhance medium efficiency
  The approach leverages NPCA EDCA behavior and preemption within non-AP STA TXOP