## Slide 1: Intention Announcement and Feedback in Multi-AP Coordination
Date: 2024-11-28
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Lyutianyang Zhang |  |  |  | 

## Slide 2: Introduction
TGbn has agreed to define a procedure for a TXOP owner AP to announce its intention of sharing a portion of the time resource of its TXOP for Co-TDMA operation, in an Initial Control frame (exact ICF and name TBD) sent at the beginning of the TXOP. The frame polls AP(s) with whom it may share the TXOP to determine their interest. [1] [Motion #156]
A candidate AP that is polled by the sharing AP shall provide, via a response,
  Its intention not to participate in TXOP sharing during the current TXOP.
    Note: If the sharing AP doesn’t receive a response from a polled AP, it assumes that the polled AP is not interested in TXOP sharing during the current TXOP.
  Its intention to participate in TXOP sharing during the current TXOP.
  Signaling details (including traffic indication) are TBD. [1] [Motion #157]
In this contribution, we discuss the details of the above procedure.

## Slide 3: Polling & Announcement
The purpose of polling frame (from the sharing AP) is to determine whether the polled AP has resource request. This is needed because otherwise the sharing AP does not know which AP to share the resource with.
  Note-other Multi-AP schemes (e.g., Co-BF, Co-SR) may also need this polling procedure.
The purpose of the announcement frame is to advertise the sharing AP’s decision so that the shared APs can start preparing the data.
The announcement frame and the polling frame should be separate because the decision can only be made after the polling phase.

## Slide 4: Polling & Response
The polling & response procedure is also named ICF/ICR exchange between APs
BSRP is a good candidate for the ICF since the purpose of the ICF is to check the polled AP’s resource need (it’s the basic function of BSRP)
  Note-BSRP is just an example, other frames are also possible
Regarding ICR, the current BSR may not be a perfect choice since it only provides the number of bytes in the buffer. However, the CTDMA procedure is a time allocation procedure. Hence, it’s better to define a way for the polled AP to report the requested time duration.
Multi-STA BA frame is a good option to be the ICR since it is extensible to carry the above information.
  Note-It is also used in other scenarios, e.g., DUO mode.

## Slide 5: Contents in the ICR
The following information should be carried in the ICR
  Requested medium time: the duration that the polled AP requested to be allocated from the sharing AP
  Scaling factor: the unit of the requested medium time
  Requested BW: the BW that the polled AP intends to be allocated
    Note1-the polled AP may have preference on the BW to be used during CTDMA, based on its own/associated STA’s capabilities
    Note2-this will affect the requested medium time. If the allocated BW is smaller than requested BW, then the requested medium time is longer
  TID/AC: the TID/AC of the buffer
  Deadline: the expiration time of the buffered data.

## Slide 6: Announcement
After the ICF/ICR exchange between the sharing AP and the polled APs, the sharing AP can decide which APs to share the medium time with.
The sharing AP can send an announcement frame to all the shared APs, and indicates the following information:
  The expected transmission starting time of each shared AP
  The expected allocation duration of each shared AP
After the announcement frame, the sharing AP can allocate time resource to each of the shared AP following the MU-RTS TXS procedure.

## Slide 7: Conclusion
We discuss the details of the poll and announcement procedure for Multi-AP, especially for the CTDMA
The poll/response (ICR/ICR) procedure enables the polled AP to report its resource needs to the sharing AP, and should be time based
The announcement procedure indicates the sharing AP’s final decision for sharing, and gives shared AP time to prepare for the data transmission.
Poll (ICF) and announcement frames should be two different frames.
Since resource request is needed for other Multi-AP schemes (e.g., Co-BF, Co-SR), the proposed ICF/ICR details can also be used for them.

## Slide 8: Reference
[1] 11-24-0171r20: 11-24-0171-20-00bn-tgbn-motions-list-part-1

## Slide 9: SP
SP1: Do you support to include in the 11bn SFD:
• A TXOP owner AP shall announce the decision of sharing a portion of the time resource of its TXOP for Co-TDMA operation, in an announcement frame (exact frame TBD) immediately after the ICF/response frame exchange at the beginning of the TXOP
  The announcement frame indicates the expected transmission starting time and the expected allocation duration of the shared AP.