## Slide 1: IDC Scenarios and unavailable period indication
Date: 2024-12-31
Authors:

## Slide 2: Recap.
Unavailability information could be used for Co-ex and even for power save.
TGbn has passed several motions on TXOP level unavailability information indication and we have following items in SFD [1] [2] :
  [Motion #30]
  11bn defines a mechanism for a non-AP STA to report unavailability at TXOP level and define or reuse/update existing mechanism for a non-AP STA to report long term (periodic) unavailability.
  [Motion #146]
  A non-AP STA that is a TXOP responder can indicate in a response frame 1) for how long it will be available, if known and/or 2) whether it will be unavailable after a specific point in time and, if known, for how long
    The response frame is a multi-STA BlockAck frame sent by the non-AP STA in response to the initial control frame or to MPDUs that solicit an immediate response.
    [3] and [4] proposed that BSRP frame can be used as ICF to trigger the M-STA BA as ICR indicating the unavailability information.
    [5] proposes to use BSRP as ICF to indicate availability/unavailability information directly.

## Slide 3: response to a BSRP TF
We have following rules for the response to a BSRP TF in current SPEC (26.5.5 Buffer status report operation in REVme D7.0) :
  The non-AP STA shall include in the HE TB PPDU one or more QoS Null frames containing one or more of the following:
  — The QoS Control field(s) with Queue Size subfields for each of the TIDs for which the non- AP STA has queue size to report to the AP.
  — The BSR Control subfield with the Queue Size All subfield indicating the queue size for the ACs, indicated by the ACI Bitmap subfield, for which the non-AP STA has queue size to report to the AP if the AP has indicated its support in the BSR Support subfield of its HE Capabilities element. The non-AP STA shall set Delta TID, Scaling Factor, ACI High, and Queue Size High subfields of the BSR Control subfield as defined in 9.2.4.7.4 (BSR Control).
For allowing the solicited unavailability information indication by carrying in a multi-STA BA solicited by a BSRP TF as a ICF, the aggregation rules (A-MPDU context :control response A-MPDU contexts) and the response rules for BSRP might be changed.
  — A QoS-Null data frame with BSR and a multi-STA Block ACK frame with unavailability information will be aggregated in an A-MPDU as a response in a TB PPDU for the BSRP TF.

## Slide 4: unsolicited unavailability information indication
For unsolicited unavailability information indication, there might be two options at present.
  BSRP TF
  Multi-STA BA;
• Both of them need to change aggregation rules in some cases
• Both of them can’t be acked to make sure the peer get the information

## Slide 5: unavailable period indication by (A-)control field
[6] has mentioned that a new (A-)control field for IDC Info can be included in QoS Data/Null frames, Management frames (similar to BSR).
Indicating unavailable period by A-control field might be an alternative option for both solicited or unsolicited case.
  -Can be piggyback in QoS Data/Null frames
    Easier indicate a sudden IDC event during a TXOP.
    The aggregation rules may not change.
  -May reduce the signaling overhead.
  -May be suitable for the burst cases of co-ex event.

## Slide 6: unavailable period indication by (A-)control field
There are two options for unavailable period indication by A-control field:
  Opt1. use 9 or more bits to indicate unavailability duration.
    Imply that the unavailability duration will start after this PPDU or the response PPDU of this PPDU
  Opt2. use 9*2 bits to indicate unavailability start time and duration [5] [7] .
Control ID | Unavailability duration
4 bits | 9 or more bits
Control ID | Unavailability start time | Unavailability duration
4 bits | 9 bits | 9 bits

## Slide 7: Summary
This presentation proposes to use A-Control field for the unavailable period indication.

## Slide 8: SP 1
Do you agree to add the following text to the 11bn SFD?
  A UHR STA can indicate in an A-control field 1) for how long it will be available, if known and/or 2) whether it will be unavailable after a specific point in time and, if known, for how long.

## Slide 9: References
[1] 11-24-0171-21-00bn-tgbn-motions-list-part-1
[2] 11-24-0209-07-00bn-specification-framework-for-tgbn
[3] 11-24-1550-01-00bn-in-device-coexistence-follow-up
[4] 11-24-1558-02-00bn-in-device-coexistence-follow-up
[5] 11-24-1893-00-00bn-icf-follow-up
[6] 11-24-0834-01-00bn-some-details-on-in-device-coexistence
[7] 11-24-1974-03-00bn-detailed-text-proposal-on-coexistence