## Slide 1: TXOP protection after preemption
Date: 2024-12-27
Authors:
Name | Affiliations | Address | Phone | email
Hang Yang | Ruijie Networks Co., Ltd. |  |  | yanghang1@ruijie.com.cn
Ke Zhong | Ruijie Networks Co., Ltd. |  |  | zhongke@ruijie.com.cn
Hui Che | Ruijie Networks Co., Ltd. |  |  | chehui@ruijie.com.cn
Fachang Guo |  |  |  | 

## Slide 2: Introduction
In UHR PAR[1], the latency reduction is a key objective of 802.11bn.
Preemption, i.e., when a latency sensitive packet arrives, the AP/non-AP STA could request transmission without waiting for the ongoing TXOP to end, is a solution to reduce the waiting time of latency sensitive traffic. Various preemption methods have been proposed in many contributions[2,3,4].
Preemption duration protection issue is raised in [5]. Once the preemption happens, it will take up a period of transmission time, causing the protection set by the initial TXOP to fail. And the continued transmission could be interfered with.
In this contribution, we give consideration on:
  Initial TXOP duration protection after preemption
  Preemption end indication

## Slide 3: Protection Issue caused by Preemption
RTS
CTS
PPDU 1
PRI
TF
LL PPDU
ACK
ACK
PPDU 2
ACK
Preemption =
Transmission before preemption = t1
SIFS
Current transmission before preemption
Preemption transmission
Protected TXOP duration set by initial RTS/CTS = T
Remain transmission after preemption
Current transmission after preemption
Transmission w/o protect = tp
TXOP holder and responder set the initial protected TXOP duration T via RTS/CTS exchange
Preemption happened in TXOP and occupied time tp
To prevent current transmission after preemption from being transmitted without protect:
  Option 1: Continues to transmit data and ends the transmission before time T
    No further frame required
    The remaining data may not be fully transmitted
  Option 2: Extend the protection duration and continues to transmit remaining data
    Frames are needed to indicate new duration
    All the data in initial TXOP could be fully transmitted
  To minimize the impact to the initial TXOP, Option 2 is preferred

## Slide 4: Preemption end process using RTS/CTS
AP 1
STA1
RTS
CTS
PPDU 1
ACK
RTS
CTS
PPDU 2
ACK
New TXOP duration
STA 2
(hidden from AP 1)
NAV
NAV
PPDU
Cancel the transmission
SIFS
SIFS
SIFS
xIFS
Current transmission before preemption
Preemption transmission
time =
Protected TXOP duration set by initial RTS/CTS = T
In DL TXOP, when preemption ends, AP1 (TXOP holder) and STA1 (TXOP responder) send RTS/CTS before continuing the transmission
  RTS/CTS indicates new protected TXOP duration of remain traffic
  Related STAs may update the NAV timer according to RTS/CTS frame

## Slide 5: Preemption end process using RTS/CTS
AP 1
STA1
RTS
CTS
PPDU 1
ACK
CTS
PPDU
ACK
Indicate new TXOP duration
STA 2
(hidden from STA 1)
NAV
NAV
PPDU
Cancel the transmission
SIFS
SIFS
xIFS
Current transmission before preemption
Preemption transmission
time =
Protected TXOP duration set by initial RTS/CTS = T
STA 3
(hidden from AP 1)
NAV
NAV
Medium Busy
In UL TXOP, when preemption ends, AP1 (TXOP responder) send a CTS to STA1 (TXOP holder)
  As the preemption end indication, the CTS frame solicits STA1 to continue transmission
  CTS indicates new protected TXOP duration of remain traffic
  Related STAs may update the NAV timer according to CTS frame
  STAs hidden from AP1 could listen PPDU from STA1, and set NAV according to PPDU’s duration field

## Slide 6: Summary
To solve the initial TXOP duration protection invalid caused by preemption, RTS/CTS frames could be used as the indication of preemption ends
  RTS/CTS indicates new protected TXOP duration of remain traffic
  Related STAs may update the NAV timer according to RTS/CTS frame
  In UL TXOP, the CTS frame solicits STA1 to continue transmission as the preemption end indication

## Slide 7: References
[1] IEEE 802.11-23/480r3, UHR Proposed PAR
[2] IEEE 802.11-23/1174r0, TXOP Preemption Follow Up
[3] IEEE 802.11-23/1886r3, Preemption techniques to meet low-latency (LL) targets
[4] IEEE 802.11-24/0390r0, A Uniform Procedure for Preemption
[5] IEEE 802.11-24/1074r0, Preemption TXOP