## Slide 1: TGbn Motions List - Part 2
Date: 2025-01-01
Authors:

## Slide 2: IEEE 802.11 TGbn: Enhancements for Ultra High Reliability (UHR) WLAN Task Group
Motions List from January 2025
Chair: Alfred Asterjadhi (Qualcomm Inc.)
Vice Chairs: Laurent Cariou (Intel), Jianhan Liu (Mediatek), Kiseon Ryu (NXP)
Secretary: Yusuke Asai (NTT)
Technical Editor: Ross Jian Yu (Huawei)
PHY Ad-hoc chairs: Dongguk Lim (LGE), Sigurd Schelstraete (MaxLinear), Tianyu Wu (Apple)
MAC Ad-hoc chairs: Srinivas Kandala (Samsung), Jeongki Kim (Ofinno), Xiaofei Wang (Interdigital)

## Slide 3: Motions on January 14th

## Slide 4: Motion 190 (PHY)
Move to add to the TGbn SFD the following:
The MCS field in the User field of UHR-SIG field consists of 5 bits.
  The B11 ~ B15 of the UHR-SIG field is assigned for the MCS field
  The configuration of MCS field is TBD.
Move: Dongguk Lim Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1427r2]. SP result: No objection.

## Slide 5: Motion 191 (PHY)
Move to add to the TGbn SFD the following:
Define the assigned bits for the NSS field and Spatial Configuration field by considering the maximum NSS is 8 in 11bn
  For non-MU-MIMO allocation of the UHR SIG field
    NSS field consists of 3 bits in the User field
For MU-MIMO allocation of the UHR SIG field
  Spatial Configuration field consists of 4 bits in the User field.
Move: Dongguk Lim Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1427r2]. SP result: No objection.

## Slide 6: Motion 192
INTENTIONALLY LEFT BLANK

## Slide 7: Motion 193 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/1985r3 to the latest TGbn draft (TGbn D0.1)
Move: Rui Cao Second: Rethna Pulikkoonattu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1985r3]. SP result: No objection.

## Slide 8: Motion 194 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1966r2 to the latest TGbn draft (TGbn D0.1)
Move: Giovanni Chisci Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1966r2]. SP result: No objection.

## Slide 9: Motion 195 (PHY)
Move to add to the TGbn SFD the following:
In the 5bit MCS table
  MCS17 signals QPSK rate 2/3; MCS19 signals 16QAM rate 2/3;
  MCS20 signals 16QAM rate 5/6; MCS23 signals 256QAM rate 2/3
Move: Ron Porat Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1826r1]. SP result: No objection.

## Slide 10: Motion 196 (PHY)
Move to add to the TGbn SFD the following:
MU-MIMO+OFDMA in both DL and UL is limited to UHR PPDU of 160 and 320MHz only
  160MHz PPDU – 996 and, when the PPDU is punctured, 484+242
  320 MHz PPDU: 2x996, 3x996 and, when the PPDU is punctured, 996+484, 2x996+484
MU-MIMO+OFDMA is further limited to a maximum of 2RUs supporting MU-MIMO and each 80MHz segment is either MU-MIMO or OFDMA
RU Allocation table in UHR-SIG is the same as that in EHT-SIG except that the rows for RU 242, 484 and 3x996+484 with two or more users are changed to Validate
Move: Ron Porat Second: Eugene Baik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1827r1]. SP result: No objection.

## Slide 11: Motion 197 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2046r4 to the latest TGbn draft (TGbn D0.1)
Move: Jianhan Liu Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2046r4]. SP result: No objection.

## Slide 12: Motion 198 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2025r1 to the latest TGbn draft (TGbn D0.1)
Move: Eunsung Park Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2025r1]. SP result: No objection.

## Slide 13: Motion 199 (PHY)
Move to add to the TGbn SFD the following:
Exclude BPSK from UHR UEQM.
Move: Rethna Pulikkoonattu Second: Ying Wang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6, 24/1807r0]. SP result: No objection.

## Slide 14: Motion 200 (PHY)
Move to add to the TGbn SFD the following:
Include 4K QAM in UHR UEQM.
Move: Juan Fang Second: Rui Cao
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 15: Motion 201 (PHY)
Move to add to the TGbn SFD the following:
Reuse HT stream parser for UHR UEQM with the following restrictions and extension
Move: Juan Fang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6, 24/1451r2]. SP result: No objection.

## Slide 16: Motion 202 (PHY)
Move to add to the TGbn SFD the following:
For equal modulation, UHR stream parser remains the same as EHT.
Move: Juan Fang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 17: Motion 203 (PHY)
Move to add to the TGbn SFD the following:
For bandwidths greater than 80 MHz, the coded bit parsing of UHR is stream parsing first followed by segment parsing.
Move: Juan Fang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 18: Motion 204 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2028r3 to the latest TGbn draft (TGbn D0.1)
Move: You-Wei Chen Second: Ross Jian Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/2028r3]. SP result: No objection.

## Slide 19: Motion 205 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1961r4 to the latest TGbn draft (TGbn D0.1)
Note to Editor: Insert (TBD) at the end of the caption for Figure 37.X.
Move: Sanket Kalamkar Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1961r4]. SP result: No objection.

## Slide 20: Motion 206 (PHY)
Move to add to the TGbn SFD the following:
CoBF is only applied in DL non-OFDMA MU MIMO transmission
C-SR is only applied in DL SU transmission in each BSS
The entire U-SIG format in a UHR MU PPDU is as in the following figure
BSS color 1 and 2 are the BSS color of the two Coordinated BSSs with the order TBD
Move: Alice Chen Second: You-Wei Chen
Discussion: Some discussion.
Preliminary Result: 159Y, 22N, 52A (pass)
Reference docs:[24/1834r4, 24/1831r3, 24/1864r1]. SP result: 55Y/8N/22A.

## Slide 21: Motion 207 (PHY-PDT)
Move to insert the proposed text changes below to Section 38.3.19.2 (Pre-correction accuracy requirements) of 11-24/1981r3, and to the latest TGbn draft (TGbn D0.1)
For the ELR PPDU carrying immediate response frame in response to a preceding soliciting frame, after compensation, the absolute value of residual CFO error with respect to the preceding PPDU carrying soliciting frame shall not exceed 15 kHz at the 10% point of the complementary cumulative distribution function (CCDF) of CFO error in AWGN at a received power of -82 dBm in the primary 20 MHz channel.
Move: Rui Cao Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1841r1]. SP result: No objection.
Chair’s note: Ensured instructions are clear to the group and TGbn editor.

## Slide 22: Motion 208 (PHY-PDT)
Move to replace the “TBD” to “8 us” for the PE block in the Figure 38-xx (UHR ELR PPDU format) in Section 38.3.6 (UHR PPDU formats) of 11-24/1981r3, and in the latest TGbn draft (TGbn D0.1)
Note: the PE value applies for UHR ELR PPDU.
Move: Rui Cao Second: Wook Bong Lee
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1841r1]. SP result: No objection.
Chair’s note: Ensured instructions are clear to the group and TGbn editor.

## Slide 23: Motion 209 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2022r2 to the latest TGbn draft (TGbn D0.1)
Move: Frank Hsu Second: George Kuo
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2022r2]. SP result: No objection.

## Slide 24: Motion 210
INTENTIONALLY LEFT BLANK

## Slide 25: Motion 211 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2007r3 to the latest TGbn draft (TGbn D0.1)
Move: Dmitry Akhmetov Second: Kiseon Ryu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2007r3]. SP result: No objection.

## Slide 26: Motion 212 (MAC)
Move to add to the TGbn SFD the following:
An AP transmitting a BSRP Trigger frame as an ICF which is addressed to at least a UHR non-AP STA that has enabled a dynamic unavailability operation mode, shall ensure that the UL Length field is set to a sufficient length so that the PPDU that contains a Multi-STA BA as an ICR, includes unavailability information in the Multi-STA BA in addition to other baseline requirements
Move: Hongwon Lee Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1464r2]. SP result: No objection.

## Slide 27: Motion 213 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/1992r3 to the latest TGbn draft (TGbn D0.1)
Move: Rethna Pulikkoonattu Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1992r3]. SP result: No objection.

## Slide 28: Motion 214 (PHY)
Move to add to the TGbn SFD the following:
1-bit indication in the per-user SIG field to resolve the BSS color for COBF transmissions.
  The coding bit is re-purposed for this indication
Move: Shengquan Hu Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1829r2, 11-24/1822r4]. SP result: No objection.

## Slide 29: Motion 215 (PHY)
Move to add to the TGbn SFD the following:
The cyclic shift for pre-UHR modulated fields in UHR MU PPDU used for Co-BF transmission is based on local transmit chain index at each AP.
Move: Juan Fang Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[None]. SP result: No objection.

## Slide 30: Motion 216 (PHY)
Move to add to the TGbn SFD the following:
Mandatory support MCSs of QPSK with code rate 2/3; 16QAM with code rate 2/3; 16QAM with code rate 5/6; 256QAM with code rate 2/3.
  Support for 256QAM with code rate 2/3 for 20MHz only devices is TBD.
Move: Jianhan Liu Second: Eugene Baik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0469r0, 24/0753r1]. SP result: No objection.

## Slide 31: Motion 217 (PHY)
Move to add to the TGbn SFD the following:
The maximum number of spatial streams transmitted by each AP in CSR is 4.
Move: Jianhan Liu Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[None]. SP result: No objection.

## Slide 32: Motion 218 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2017r0 to the latest TGbn draft (TGbn D0.1)
Move: Yusuke Asai Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2017r0]. SP result: No objection.

## Slide 33: Motion 219 (PHY)
Move to add to the TGbn SFD the following:
For the COBF case, the information in the NDPA for the responding AP has a unified design for joint-NDP based sounding as well as cross-BSS section of sequential sounding.
Move: Sameer Vermani Second: Eugene Baik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1822r4]. SP result: No objection.

## Slide 34: Motion 220 (PHY)
Move to add to the TGbn SFD the following:
2 BSS colors are indicated in the preamble of a COBF PPDU.
  One BSS color for the sharing AP and another BSS color for the shared AP.
Move: Sameer Vermani Second: Rethna Pulikkoonattu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1822r4]. SP result: No objection.

## Slide 35: Motion 221 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2032r1 to the latest TGbn draft (TGbn D0.1)
Move: Dongguk Lim Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2032r1]. SP result: No objection.

## Slide 36: Motion 222 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2033r3 to the latest TGbn draft (TGbn D0.1)
Move: Dongguk Lim Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2033r3]. SP result: No objection.

## Slide 37: Motion 223
INTENTIONALLY LEFT BLANK

## Slide 38: Motion 224 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2023r3 to the latest TGbn draft (TGbn D0.1)
Move: Junghoon Suh Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2023r3]. SP result: No objection.

## Slide 39: Motion 225 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2034r1 to the latest TGbn draft (TGbn D0.1)
Move: Chenchen LIU Second: Yan Xin
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2034r1]. SP result: No objection.

## Slide 40: Motion 226 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2135r0 to the latest TGbn draft (TGbn D0.1)
Move: Bo Gong Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2135r0]. SP result: No objection.

## Slide 41: Motion 227 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2009r6 to the latest TGbn draft (TGbn D0.1)
Move: Mengshi Hu Second: Junghoon Suh
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2009r6]. SP result: No objection.

## Slide 42: Motion 228 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2027r1 to the latest TGbn draft (TGbn D0.1)
Move: Eugene Baik Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2027r1]. SP result: No objection.

## Slide 43: Motion 229 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2049r6 to the latest TGbn draft (TGbn D0.1)
Move: Arik Klein Second: Shimi Shilo
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2049r6]. SP result: No objection.

## Slide 44: Motion 230 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1762r23 to the latest TGbn draft (TGbn D0.1)
Move: Matthew Fischer Second: Liuming Lu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1762r23]. SP result: Find result.

## Slide 45: Motion 231 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2005r1 to the latest TGbn draft (TGbn D0.1)
Move: Eugene Baik Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2005r1]. SP result: No objection.

## Slide 46: Motion 232 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2006r2 to the latest TGbn draft (TGbn D0.1)
Move: Eugene Baik Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2006r2]. SP result: No objection.

## Slide 47: Motion 233 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2016r3 to the latest TGbn draft (TGbn D0.1)
Move: Laurent Cariou Second: Matthew Fischer
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2016r3]. SP result: 124Y, 27N, 55A.

## Slide 48: Motion 234
INTENTIONALLY LEFT BLANK

## Slide 49: Motion 235 (MAC)
Move to add to the TGbn SFD the following:
An AP MLD may optionally include a QoS Map element within the SCS Response frame transmitted by the AP MLD to update the DSCP-to-UP mapping for UL if the following conditions are true
  the TID and the User Priority subfields of the Control Info field in the associated QoS Characteristics element are set to different values within 0~7
  the AP MLD and the non-AP MLD supports the QoS map operation
Move: Guogang Huang Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/2123r1]. SP result: Super Majority.

## Slide 50: Motion 236 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2024r0 to the latest TGbn draft (TGbn D0.1)
Move: Eunsung Park Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2024r0]. SP result: No objection.

## Slide 51: Motion 237 (PHY)
Move to add to the TGbn SFD the following:
For 160 MHz and 320 MHz PPDUs, in only the non-punctured primary 80 MHz subblock, the following distribution bandwidth mode is allowed for DRU
  20 MHz + 20 MHz + 40 MHz (or 40 MHz + 20 MHz + 20 MHz)
Move: Lin Yang Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/100r0]. SP result: No objection.

## Slide 52: Motion 238 (PHY)
Move to add to the TGbn SFD the following:
For distributed transmission, apply global CSD to UHR-STF only, and UHR-LTF and data still apply local per stream CSD, just like RRU
Move: Lin Yang Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/100r0]. SP result: No objection.

## Slide 53: Motion 239 (PHY-PDT)
Move to add the following note into the TGbn D0.1, under the section “38.3.2.x RU and MRU restrictions for 20 MHz operation”
“NOTE – When a 20 MHz operating STA participates in an 80 MHz or wider UHR TB PPDU using 20 MHz distribution bandwidth, the TX LO leakage of the STA might interfere with some of the data subcarriers within the 20 MHz distribution bandwidth such that for some DRUs in that 20MHz DBW performance of high MCS may be significantly degraded.”
Move: Lin Yang Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/100r0]. SP result: No objection.

## Slide 54: Motion 240 (PHY)
Move to add to the TGbn SFD the following:
11bn supports indicating a 60 MHz DBW using a value of 3 in the 2-bit DBW indication subfield within the UHR variant User Info field of a Trigger Frame in the case of DRU
Move: Mahmoud Hasabelnaby Second: Yan Xin
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0129r0]. SP result: ??.

## Slide 55: Motion 241 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2035r1 to the latest TGbn draft (TGbn D0.1)
Move: Ross J. Yu Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2035r1]. SP result: No objection.

## Slide 56: Motion 242 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2011r1 to the latest TGbn draft (TGbn D0.1)
Move: Mengshi Hu Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2011r1]. SP result: No objection.

## Slide 57: Motion 243 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2012r3 to the latest TGbn draft (TGbn D0.1)
Move: Mengshi Hu Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2012r3]. SP result: No objection.

## Slide 58: Motion 244 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2031r5 to the latest TGbn draft (TGbn D0.1)
Move: Jason Yuchen Guo Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2031r5]. SP result: No objection.

## Slide 59: Motion 245 (PHY)
Move to add to the TGbn SFD the following:
The Interference Mitigation feature is only defined with LDPC
Move: Shimi Shilo Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1785r2]. SP result: No objection.

## Slide 60: Motion 246 (PHY)
Move to add to the TGbn SFD the following:
For each bandwidth, there is a fixed number of IM pilots (value TBD)
Move: Shimi Shilo Second: Genadiy Tsodik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1785r2]. SP result: No objection.

## Slide 61: Motion 247 (PHY)
Move to add to the TGbn SFD the following:
Within any transmission that uses IM pilots, they are used in every data OFDM symbol and in the same corresponding subcarriers positions, for a given BW
Move: Shimi Shilo Second: Oded Redlich
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1785r2]. SP result: No objection.

## Slide 62: Motion 248 (MAC-PDT)
Move to incorporate the proposed text changes in 11-25/88r3 to the latest TGbn draft (TGbn D0.1)
Move: Rubayet Shafin Second: Vishnu Ratnam
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/88r3]. SP result: No objection.

## Slide 63: Motion 249 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2042r1 to the latest TGbn draft (TGbn D0.1)
Move: Juan Fang Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2042r1]. SP result: No objection.

## Slide 64: Motion 250 (PHY)
Move to add to the TGbn SFD the following:
11bn defines 5 bit Recommended CSI MCS subfield in the 2nd Special STA Info field of the NDPA targeted for OBSS AP in the UHR CoBF sounding
  It is set from B20 to B24 in the 2nd Special STA Info field
  The 5-bit MCS level includes “No Recommendation” MCS entry in addition to the UHR MCS entries
    Index 31 indicates “No Recommendation”
  The Recommended CSI MCS is for the OBSS AP to set the MCS in the BFRP trigger frame sent in the future Cross-BSS sounding / Joint Sounding sequence
  When there are multiple OBSS STAs to feedback the CSI report, the Recommended CSI MCS can be set to the lowest MCS among all those OBSS STAs
Move: Junghoon Suh Second: Mahmoud Hasabelnaby
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0078r0]. SP result: No objection.

## Slide 65: Motion 251 (PHY)
Move to add to the TGbn SFD the following:
In the UHR MU PPDU in 11bn, the PE requirements of UEQM with the constellation order x of the first spatial stream is equal to the PE requirements of EQM with the constellation order x
Move: Mengshi Hu Second: Shimi Shilo
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0128r0]. SP result: No objection.

## Slide 66: Motion 252 (PHY)
Move to add to the TGbn SFD the following:
11bn defines the following modes for co-SR transmission:
  Mode 1: trigger + same L-SIG contents, could be different U-SIG contents.
    For UHR+EHT, or EHT+UHR or EHT+EHT co-SR transmission.
    Provided no changes to non-UHR EHT non-AP STAs are needed.
  Mode 2: Tigger + same L-SIG contents + same U-SIG contents
    For UHR+UHR co-SR transmission.
  For all modes, the two PPDUs will start and end at the same time.
  UHR PPDU for co-SR transmission will be used for either mode 1 or mode 2 when UHR transmission exists.
    There exists an indication in U-SIG field to indicate the UHR PPDU is a UHR PPDU for co-SR transmission.
Move: Ross Jian Yu Second: Jason Y. Guo
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0104r0]. SP result: 41Y, 7N, 20A.

## Slide 67: Motion 253 (Joint)
Move to add to the TGbn SFD the following:
In Coordinated Spatial Reuse:
  A sharing AP that intends to initiate a Coordinated Spatial Reuse transmission shall transmit a Trigger frame to initiate concurrent CSR transmissions with one (whether to allow more is TBD) other AP within its obtained TXOP BW;
  When all addressed non-AP STAs are UHR STAs, the concurrent CSR transmission starts SIFS after the Trigger frame
  Which trigger frame is TBD
Move: Jason Y. Guo Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-23/1868, 11-24/1092]. SP result: No Objection

## Slide 68: Motion 254 (Joint)
Move to add to the TGbn SFD the following:
In Coordinated Spatial Reuse, the following information shall be carried in the Trigger frame that initiates concurrent CSR transmissions of the 2 APs
  The duration of the data PPDU transmitted by the sharing AP and of the data PPDU transmitted by the shared AP, which are the same, after the Trigger frame
  Other parameters TBD
Move: Jason Y. Guo Second: Yunbo Li
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-23/1868, 11-24/1092]. SP result: No objection.

## Slide 69: Motion 255 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1881r7 to the latest TGbn draft (TGbn D0.1)
Move: Duncan Ho Second: Mike Montemurro
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1881r7]. SP result: 135Y, 18N, 39A.

## Slide 70: Motion 256 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2040r9 to the latest TGbn draft (TGbn D0.1)
Move: Laurent Cariou Second: Qi Wang
Discussion: None
Result: Approved with unanimous consent.
Reference docs:[11-24/2040r9]. SP result: No objection

## Slide 71: Motion 257 (MAC)
Move to add to the TGbn SFD the following:
Define an Enhanced BSR Control subfield in A-ctrl to report a larger per TID queue size
  The Enhanced BSR Control subfield consists of at least a TID subfield and an unsigned value subfield to report the larger queue size (QS) of the TID
  The reported QS is equal to 2147328 Octets + the value reported in the Queue Size field of the defined Enhanced BSR Control subfield
  When the QoS Control with the same TID as the Enhanced BSR Control subfield is present in the same MPDU, the QS subfield of the QoS Control is set to value 254
  TBD if the Enhanced BSR Control subfield shares the control ID with other Control subfield proposals in UHR
  Note: The baseline rules which regulate HT control field to be the same in all MPDUs of the same frame type in an A-MPDU do not change
  Note: Encoding of the baseline QS subfield in QoS Control does not change.
  Note: Length of the Enhanced BSR Control subfield allows to aggregate the UPH in the same A-Control subfield
Move: Frank Hsu Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/0963, 11-23/2007]. SP result: No objection

## Slide 72: Motion 258 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2068r1 to the latest TGbn draft (TGbn D0.1)
Move: Ming Gan Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2068r1]. SP result: No objection.

## Slide 73: Motion 259 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2069r1 to the latest TGbn draft (TGbn D0.1)
Move: Ming Gan Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2069r1]. SP result: No objection.

## Slide 74: Motion 260 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2020r1 to the latest TGbn draft (TGbn D0.1)
Move: George Cherian Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2020r1]. SP result: No objection

## Slide 75: Motions on January 15th

## Slide 76: Motion 261 (MAC)
Move to add to the TGbn SFD the following:
Include the CoEx unavailability information in a new “Special User Info” field with AID12 set to 2008 of the BSRP Trigger frame when used as an ICF to report CoEx unavailability information
  A feedback type field (name TBD) (4 bits field – B12 to B15 of the “Special User Info” field) which is set to 0 to indicate that the “Special User Info” field is carrying CoEx unavailability information
  CoEx unavailability information includes two parameters: Unavailability Target Start Time and Unavailability Duration (these fields are already defined)
Move: Sherief Helwa Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1558, 11-24/1464r3, 11-24/494r2]. SP result: No objection.

## Slide 77: Motion 262 (PHY)
Move to add to the TGbn SFD the following:
When the initiating AP requests the responding AP to join the CoBF sounding, the red subfields in the first and second User Info fields of the NDPA shall be set as follows.
  NDPA Version Identifier is set to 0 for CoBF sounding in UHR
  Number of LTF symbols is set to 0 and 1 for 4 and 8 symbols, respectively
  Starting Spatial Stream is set to 0 and 1 for the 1st and 5th streams, respectively
  Number of spatial streams is set to 0 and 1 for the 4 and 8 streams, respectively
  LTF+GI is set to 0 and 1 for 2x LTF+0.8us GI and 2x LTF+1.6us GI, respectively
  B20-26, which are shown as Reserved in the second User Info field, can be used in the future
Move: Sameer Vermani Second:
Discussion:
Result:
Reference docs:[11-24/1822r4, 11-24/1835r3, 11-24/1865r3]. SP result: No objection.

## Slide 78: Motion 263 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/1977r6 to the latest TGbn draft (TGbn D0.1)
Move: Alice Chen Second:
Discussion:
Result:
Reference docs:[11-24/1977r6]. SP result: No objection.

## Slide 79: Motion 264 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2043r1 to the latest TGbn draft (TGbn D0.1)
Move: Juan Fang Second:
Discussion:
Result:
Reference docs:[11-24/2043r1]. SP result: No objection.

## Slide 80: Motion 265 (MAC)
Move to add to the TGbn SFD the following:
As a part of M-AP coordination agreement procedure, an AP may assign an AP ID to another AP with the following constraints:
  The AP ID is used for the AP to identify another AP as a coordinated AP, when necessary.
  The AP ID field has the same size and the field value has a range as defined in AID field (see 9.4.1.8)
  The AP shall ensure that the AP ID value is not assigned by the AP or by its affiliated MLD to any other STA (e.g., STA is an associated non-AP STA, an unassociated non-AP STA that has been allocated a RSID , or any other coordinated AP), or a non-AP MLD that is associated with the AP MLD
  It's TBD whether the AP ID value is greater than 2^n where n is the maximum of the value carried in the MBSSID Indicator (n) field of the Multiple BSSID element for any AP affiliated with the AP MLD that belongs to a multiple BSSID set
Move: Jay Yang Second:
Discussion:
Result:
Reference docs:[11-23/1837r2,11-24/1389r0, 11-24/1217r2, 11-24/0842r0,11-24/0843r0, 11-24/1016r2,11-24/1017r0, 11-23/1895r2, 11-24/0423r0,11-24/1225r0, 24/1220r0,25/0007r2]. SP result: No objection.

## Slide 81: Motion 266 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2015r6 to the latest TGbn draft (TGbn D0.1)
Move: Ron Porat Second:
Discussion:
Result:
Reference docs:[11-24/2015r6]. SP result: No objection.

## Slide 82: Motion 267 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2056r1 to the latest TGbn draft (TGbn D0.1)
Move: Kumail Haider Second:
Discussion:
Result:
Reference docs:[11-24/2056r1]. SP result: No objection.

## Slide 83: Motion 268 (MAC)
Move to amend the text below in the TGbn SFD:
Do you agree that a TXOP owner AP shall announce its intention of sharing a portion of the time resource of its TXOP for C-TDMA operation, in an Initial Control frame (exact ICF and name TBD) sent at the beginning of the TXOP and that the frame polls AP(s) with whom it may share the TXOP to determine their interest? o A TXOP owner AP that intends to share its TXOP is referred to as a sharing AP. o A candidate AP identified (polled) in the Initial Control frame is referred to as a polled AP. o The Duration field of the frame is set to the length of time required to transmit the solicited response frame plus one SIFS. o Whether or not the sharing AP is mandated to send the Initial Control frame that announces that intention is TBD.
Move: Sanket Kalamkar Second:
Discussion:
Result:
Reference docs:[11-23/1895, 11-23/1912r2, 11-24/0423, 11-24/1016, 11-24/1017, 11-24/1225]. SP result: No objection.

## Slide 84: Motion 269 (MAC)
Move to add to the TGbn SFD the following:
The ICF (polling frame) sent as part of Co-TDMA operation shall be a BSRP Trigger frame
Move: Sanket Kalamkar Second:
Discussion:
Result:
Reference docs:[11-24/1225, 11-24/0843r0]. SP result: No objection.

## Slide 85: Motion 270 (MAC)
Move to add to the TGbn SFD the following:
As part of Co-TDMA operation, a poll response from a polled AP solicited by the ICF shall be carried in an M-BA frame
Move: Sanket Kalamkar Second:
Discussion:
Result:
Reference docs:[11-24/1225, 11-24/0843r0]. SP result: No objection.

## Slide 86: Motion 271 (MAC)
Move to add to the TGbn SFD the following:
In response to BSRP Trigger frame as an ICF transmitted by a non-AP STA as the TXOP holder, an AP transmits a Multi-STA BlockAck frame
  Whether Block Ack Starting Sequence Control subfield and Block Ack Bitmap subfield are present or not is TBD
  Values of Ack Type and TID are TBD
Move: Hongwon Lee Second:
Discussion:
Result:
Reference docs:[24/1464]. SP result: No objection.

## Slide 87: Motion 272 (MAC)
Move to add to the TGbn SFD the following:
Define HIP EDCA in UHR where a STA with Low Latency traffic may be allowed, based on TBD conditions, to send a Defer Signal (it is TBD whether CTS or RTS is used) to start a protected short contention for pending LL data
  Conditions to be allowed to send a Defer Signal is TBD
  STA in HiP EDCA always use RTS/CTS as initial frame exchange and retry.
  Duration of protected short contention is TBD.
  Access parameters (AIFSN, CW and the expansion rules) used to transmit the Defer Signal are TBD. The retry count where the Defer Signal is allowed to be sent is TBD
  Contention parameters for the protected short contention are TBD. The STAs that transmitted a Defer Signal but did not win the protected short contention will initiate a new retry.
  Low Latency traffic is treated as AC_VO traffic. Other cases are TBD.
  The solution would provide control on the degree of collisions that may occur while using it and, allows for autonomous randomness or/and controlled by the AP
  No new mandatory synchronization requirement on STA side
  HIP EDCA is used by the STAs in a BSS only when this feature is enabled by the AP
Move: Dmitry Akhmetov Second:
Discussion:
Result:
Reference docs:[24/1144r1, 24/0864r1, 24/1193r1]. SP result: 150Y, 14N, 70A.

## Slide 88: Motion 273 (MAC)
Move to add to the TGbn SFD the following:
TGbn defines or improves an existing mechanism so that a non-AP STA that is a TXOP responder can indicate its buffered low latency traffic needs (for traffic from the TxOP responder to the TxOP Holder) in a control response frame. The TXOP holder should consider the indication in determining subsequent actions. Subsequent actions related to this indication are out of the scope of the standard.
  Note: whether an AP can Indicate its low latency needs is TBD
Move: Mohamed Abouelseoud Second
Discussion:
Result:
Reference docs:[24/0389r0, 24/168r0,24-0416/r1, 24-0442/r3, 24-1195/r1, 23/885, 24/264, 23/1886, 24/1156, 24/1871r1, 24/1074, 23/1909r1, 24/131r0, 24/1156r0]. SP result: 192Y, 10N, 29A.

## Slide 89: Motion 274 (MAC)
Move to add to the TGbn SFD the following:
Define a mechanism as part of the procedure of time sharing during a TXOP (e.g. C-TDMA, TXS, …) to support fairness to neighboring STAs (APs and non-APs)?
  Exact mechanism is TBD
Move: Dibakar Das Second
Discussion:
Result:
Reference docs:[1-24-93, 11-25-86r0]. SP result: 144Y/27N/42A.

## Slide 90: Motion 275 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1978r3 to the latest TGbn draft (TGbn D0.1)
Move: Second:
Discussion:
Result:
Reference docs:[11-24/1978r3]. SP result: No objection on R2.

## Slide 91: Motion 276 (MAC)
Move to add to the TGbn SFD the following:
UHR should allow more than two TIDs to be mapped to high priority ACs (i.e., VO or VI)?
Up to one TID for each AC currently assigned to BE and BK are remapped.
Those TIDs may be used dynamically (e.g., following an SCS flow setup).
Move: Dibakar Das Second:
Discussion:
Result:
Reference docs:[24/463r1, 24/1899, 23/0069, 24/2123]. SP result: No objection.

## Slide 92: Motion 277 (MAC)
Move to add to the TGbn SFD the following:
As part of Co-TDMA operation, TGbn defines a mechanism for a Co-TDMA sharing AP to transmit to a Co-TDMA coordinated AP an indication of whether the Co-TDMA coordinated AP is to return the remainder of the allocated time (if any) back to the Co-TDMA sharing AP.
  How to signal the indication is TBD
  Note: This mechanism is to be enabled only if the Co-TDMA sharing AP is capable of receiving the TXOP return.
Move: Second:
Discussion:
Result:
Reference docs:[24/1250, 24/1701, 24/0843, 24/1017]. SP result: No objection.

## Slide 93: Motion 278 (MAC)
Move to add to the TGbn SFD the following:
For UHR-variant Trigger frame:
  iFCS present: 1 bit field in UHR-variant Common Info field
    TBD for HE/EHT-variant
Move: Sherief Helwa Second:
Discussion:
Result:
Reference docs:[11-24/544, 11-24.1129]. SP result: No objection.

## Slide 94: Motion 279 (MAC)
Move to add to the TGbn SFD the following:
11bn defines a Seamless Mobility Domain (SMD, exact name TBD) that covers multiple AP MLDs, where a non-AP MLD can use the UHR seamless roaming procedure to roam between the AP MLDs of the SMD
  A logical SMD Management Entity (SMD-ME, exact name TBD) provides association, IEEE 802.1X Authenticator (except for the management of 802.1X control ports which is TBD) and RSNA Key management for non-AP MLDs across all AP MLDs of the SMD.
  A non-AP MLD transitions between AP MLDs within the SMD while maintaining its association and security association with the SMD-ME.
  The non-AP MLD can transition from one SMD to another SMD that are part of the same MD (Mobility Domain) using FT with improvements
Move: Mike Montemurro Second:
Discussion:
Result:
Reference docs:[24/2072, 24/1894, 24/0052, 23/1884, 23/1937, 23/1996, 24/830, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1425, 24/881, 24/1882, 24/1883, 23/1897, 24/0349, 24/0480, 23/1416, 24/0881, 23/1897, 24/0349, 24/1746]. SP result: No objection

## Slide 95: Motion 280 (MAC)
Move to add to the TGbn SFD the following:
11bn defines that within a Seamless Mobility Domain (SMD, exact name TBD) the data path includes either one MAC-SAP for the SMD or a separate MAC-SAP per AP MLD of the SMD.
  In the case of a separate MAC-SAP per AP MLD, the DS mapping is updated when the non-AP MLD roams to another AP MLD within the SMD.
  In the case of a separate MAC-SAP per AP MLD, the component of the 802.1X Authenticator in the SMD-ME interacts with an 802.1X Authenticator component in the AP MLD that manages the 802.1X controlled port for the non-AP MLD.
  In the case of a single MAC-SAP for the SMD, the 802.1X Authenticator in the SMD-ME manages the 802.1X controlled port for the non-AP MLD.
Move: Mike Montemurro Second:
Discussion:
Result:
Reference docs:[24/2072, 24/1894, 24/0052, 23/1884, 23/1937, 23/1996, 24/830, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1425, 24/881, 24/1882, 24/1883, 23/1897, 24/0349, 24/0480, 23/1416, 24/0881, 23/1897, 24/0349, 24/1746]. SP result: No objection

## Slide 96: Motion 281 (MAC)
Move to add to the TGbn SFD the following:
For negotiation over the wireless medium, an AP that requests protection for its R-TWT schedule(s) via negotiations with another AP includes information carried in TBD fields of the Broadcast TWT Parameter Set field corresponding to each R-TWT schedule being negotiated in a TBD individually addressed Management frame that it transmits to the other AP.
Move: SunHee Baek Second:
Discussion:
Result:
Reference docs:[24/160, 23/1916, 23/355, 24/1346, 24/1220, 24/407, 24/2045, 23/1887, 23/0226]. SP result: No objection.

## Slide 97: Motion 282 (MAC)
Move to add to the TGbn SFD the following:
When a non-AP MLD is in the process of roaming from a current AP MLD to a target AP MLD, the non-AP MLD can request to the current AP MLD what context needs to be transferred from the current AP MLD to the target AP MLD.
  What context can be requested is TBD
  It applies when the current AP MLD and the Target AP MLD support the context transfer
Move: Second:
Discussion:
Result:
Reference docs:[24/1516, 24/0396, 24/830, 24/1883, 24/1890, 24/1746, 24/1851, 23/1416, 24.1898, 24/0052]. SP result: 180Y, 14N, 57A

## Slide 98: Motion 282 (MAC)
Move to add to the TGbn SFD the following:
When a non-AP MLD is in the process of roaming from a current AP MLD to a target AP MLD, the non-AP MLD can request to the current AP MLD what context needs to be transferred from the current AP MLD to the target AP MLD.
  What context can be requested is TBD
  It applies when the current AP MLD and the Target AP MLD support the context transfer
Move: Second:
Discussion:
Result:
Reference docs:[24/1516, 24/0396, 24/830, 24/1883, 24/1890, 24/1746, 24/1851, 23/1416, 24.1898, 24/0052]. SP result: 180Y, 14N, 57A

## Slide 99: Motion 283 (MAC)
Move to add to the TGbn SFD the following:
As part of seamless roaming procedure, a non-AP MLD can initiate a roaming preparation procedure with a target AP MLD by sending a TBD request frame to its current AP MLD.
  The request frame indicates the set of links to be set up with the target AP MLD.
  The request frame indicates the context to be transferred or renegotiated with the target AP MLD.
  The current AP MLD sends a TBD response frame to the non-AP MLD to indicate the status (accept/reject) of the link setup.
    If the link setup is accepted, the transferable context is transferred to the target AP MLD.
  TBD on whether/how the renegotiation of context is performed in these request/response frames
  TBD – multiple candidate target AP MLDs selection
Move: Binita Gupta Second:
Discussion:
Result:
Reference docs:[24/0052, 23/1884, 23/1937, 23/1996, 24/830, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1425, 24/881, 24/1882, 24/1883, 23/1897, 24/0349, 24/0480, 23/1416, 24/1824]. SP result: 149Y, 4N, 52A.

## Slide 100: Motion 284 (MAC)
Move to add to the TGbn SFD the following:
As part of seamless roaming procedure, a non-AP MLD in state 4 with the SMD-ME can perform roaming transition through a target AP MLD that is a part of the SMD.
TBD on the conditions and details for performing roaming through target AP MLD
Move: Binita Gupta Second:
Discussion:
Result:
Reference docs:[24/0398, 24/1812]. SP result: No objection.

## Slide 101: Motion 285 (MAC)
Move to add to the TGbn SFD the following:
For security in seamless roaming, when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD within the SMD, the same PMKSA, established with the SMD-ME, shall be used to protect communications with the current AP MLD and the target AP MLD.
Move: Giovanni Chisci Second:
Discussion:
Result:
Reference docs:[23/1416, 24/2072, 24/1894, 24/0052, 23/1884, 23/1937, 23/1996, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1882, 24/1883]. SP result: No objection.

## Slide 102: Motion 286 (MAC)
Move to add to the TGbn SFD the following:
For security in seamless roaming, when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD within the SMD, the same PTKSA, established with the SMD-ME, shall be used to protect communications with the current AP MLD and the target AP MLD.
Move: Giovanni Chisci Second:
Discussion:
Result:
Reference docs:[23/1416, 24/2072, 24/1894, 24/0052, 23/1884, 23/1937, 23/1996, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1882, 24/1883]. SP result: No objection.

## Slide 103: Motion 287 (MAC)
Move to add to the TGbn SFD the following:
Legend: Green: allowed; Orange: disallowed
Move: Second:
Discussion:
Result:
Reference docs:[24/1558, 24/1221, 24/1225, 24/1563]. SP result: No objection.
Allowed UHR ICF to be transmitted by a non-AP STA (addressing the associated AP STA) |  |  |  |  |  |  | 
ICF | eMLSR | AP DPS | Solicited Coex | Unsolicited Coex | NPCA | C-TDMA (ICF) | Co-BF/Co-SR
RTS | N/A | Yes | N/A* | No | No | N/A | 
MU RTS |  | No |  | No | No |  | 
BSRP Trigger |  | No |  | No | No |  | 
BSRP GI3 |  | Yes |  | Yes | Yes |  | 
Notes: RTS solicits CTS frame; BSRP GI3 Trigger frame solicits an M-BA that is contained in a non-HT (dup) PPDU. C-TDMA, C-BF, CSR ICF transmission is to other APs. No expectations for non-AP STAs, unless due to other functionalities already enabled/supported by non-AP STA. Solicited and Unsolicited Coex are part of DUO. N/A means that either the non-AP STA is not allowed to send an ICF or the AP STA is not allowed to respond with ICR for this scheme/operation mode. *DUO is only approved for non-AP STAs. So, a non-AP STA cannot send an ICF to an AP soliciting unavailability information in ICR (i.e., solicited CoEx). Acronyms: DPS: Dynamic Power Save, DUO: Dynamic Unavailability Operation, Unsolicited CoEx: Reporting unavailability in ICF, Co-BF: Coordinated beamforming, Co-SR: Coordinated Spatial Reuse, BSRP GI3: BSRP Trigger soliciting an M-BA in non-HT (dup) PPDU |  |  |  |  |  |  | 

## Slide 104: Motion 288 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2066r1 to the latest TGbn draft (TGbn D0.1)
Move: Ming Gan Second:
Discussion:
Result:
Reference docs:[11-24/2066r1]. SP result: No objection.

## Slide 105: Motion 289 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2067r2 to the latest TGbn draft (TGbn D0.1)
Move: Ming Gan Second:
Discussion:
Result:
Reference docs:[11-24/2067r2]. SP result: No objection.

## Slide 106: Motion X
Move to instruct the TGbn Editor to create IEEE802.11bn D0.1 draft by incorporating the changes specified in all the approved proposed draft text (PDT) documents.
Move: Second:
Discussion:
Result:

## Slide 108: backup

## Slide 109: Motion X (SFD Template)
Move to add to the TGbn SFD the following:
Move: Second:
Discussion:
Result:
Reference docs:[]. SP result:

## Slide 110: Motion Y (Draft Template)
Move to incorporate the proposed text changes in 11-24/xxxxry to the latest TGbn draft (TGbn D0.1)
Move: Second:
Discussion:
Result:
Reference docs:[]. SP result: