## Slide 1: TGbn Motions List - Part 2
Date: 2025-04-11
Authors:

## Slide 2: IEEE 802.11 TGbn: Enhancements for Ultra High Reliability (UHR) WLAN Task Group
Motions List from January 2025
Chair: Alfred Asterjadhi (Qualcomm Inc.)
Vice Chairs: Laurent Cariou (Intel), Jianhan Liu (Mediatek), Kiseon Ryu (Wilus)
Secretary: Yusuke Asai (NTT)
Technical Editor: Ross Jian Yu (Huawei)
PHY Ad-hoc chairs: Dongguk Lim (LGE), Sigurd Schelstraete (MaxLinear), Tianyu Wu (Apple)
MAC Ad-hoc chairs: Srinivas Kandala (Samsung), Jeongki Kim (Ofinno), Xiaofei Wang (Interdigital)

## Slide 3: Motions on January 15th

## Slide 4: Motion 190 (PHY)
Move to add to the TGbn SFD the following:
The MCS field in the User field of UHR-SIG field consists of 5 bits.
  The B11 ~ B15 of the UHR-SIG field is assigned for the MCS field
  The configuration of MCS field is TBD.
Move: Dongguk Lim Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1427r2]. SP result: No objection.

## Slide 5: Motion 191 (PHY)
Move to add to the TGbn SFD the following:
Define the assigned bits for the NSS field and Spatial Configuration field by considering the maximum NSS is 8 in 11bn
  For non-MU-MIMO allocation of the UHR SIG field
    NSS field consists of 3 bits in the User field
For MU-MIMO allocation of the UHR SIG field
  Spatial Configuration field consists of 4 bits in the User field.
Move: Dongguk Lim Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1427r2]. SP result: No objection.

## Slide 6: Motion 192
INTENTIONALLY LEFT BLANK

## Slide 7: Motion 193 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/1985r3 to the latest TGbn draft (TGbn D0.1)
Move: Rui Cao Second: Rethna Pulikkoonattu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1985r3]. SP result: No objection.

## Slide 8: Motion 194 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1966r2 to the latest TGbn draft (TGbn D0.1)
Move: Giovanni Chisci Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1966r2]. SP result: No objection.

## Slide 9: Motion 195 (PHY)
Move to add to the TGbn SFD the following:
In the 5bit MCS table
  MCS17 signals QPSK rate 2/3; MCS19 signals 16QAM rate 2/3;
  MCS20 signals 16QAM rate 5/6; MCS23 signals 256QAM rate 2/3
Move: Ron Porat Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1826r1]. SP result: No objection.

## Slide 10: Motion 196 (PHY)
Move to add to the TGbn SFD the following:
MU-MIMO+OFDMA in both DL and UL is limited to UHR PPDU of 160 and 320MHz only
  160MHz PPDU – 996 and, when the PPDU is punctured, 484+242
  320 MHz PPDU: 2x996, 3x996 and, when the PPDU is punctured, 996+484, 2x996+484
MU-MIMO+OFDMA is further limited to a maximum of 2RUs supporting MU-MIMO and each 80MHz segment is either MU-MIMO or OFDMA
RU Allocation table in UHR-SIG is the same as that in EHT-SIG except that the rows for RU 242, 484 and 3x996+484 with two or more users are changed to Validate
Move: Ron Porat Second: Eugene Baik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1827r1]. SP result: No objection.

## Slide 11: Motion 197 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2046r4 to the latest TGbn draft (TGbn D0.1)
Move: Jianhan Liu Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2046r4]. SP result: No objection.

## Slide 12: Motion 198 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2025r1 to the latest TGbn draft (TGbn D0.1)
Move: Eunsung Park Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2025r1]. SP result: No objection.

## Slide 13: Motion 199 (PHY)
Move to add to the TGbn SFD the following:
Exclude BPSK from UHR UEQM.
Move: Rethna Pulikkoonattu Second: Ying Wang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6, 24/1807r0]. SP result: No objection.

## Slide 14: Motion 200 (PHY)
Move to add to the TGbn SFD the following:
Include 4K QAM in UHR UEQM.
Move: Juan Fang Second: Rui Cao
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 15: Motion 201 (PHY)
Move to add to the TGbn SFD the following:
Reuse HT stream parser for UHR UEQM with the following restrictions and extension
Move: Juan Fang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6, 24/1451r2]. SP result: No objection.

## Slide 16: Motion 202 (PHY)
Move to add to the TGbn SFD the following:
For equal modulation, UHR stream parser remains the same as EHT.
Move: Juan Fang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 17: Motion 203 (PHY)
Move to add to the TGbn SFD the following:
For bandwidths greater than 80 MHz, the coded bit parsing of UHR is stream parsing first followed by segment parsing.
Move: Juan Fang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 18: Motion 204 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2028r3 to the latest TGbn draft (TGbn D0.1)
Move: You-Wei Chen Second: Ross Jian Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/2028r3]. SP result: No objection.

## Slide 19: Motion 205 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1961r4 to the latest TGbn draft (TGbn D0.1)
Note to Editor: Insert (TBD) at the end of the caption for Figure 37.X.
Move: Sanket Kalamkar Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1961r4]. SP result: No objection.

## Slide 20: Motion 206 (PHY)
Move to add to the TGbn SFD the following:
CoBF is only applied in DL non-OFDMA MU MIMO transmission
C-SR is only applied in DL SU transmission in each BSS
The entire U-SIG format in a UHR MU PPDU is as in the following figure
BSS color 1 and 2 are the BSS color of the two Coordinated BSSs with the order TBD
Move: Alice Chen Second: You-Wei Chen
Discussion: Some discussion.
Preliminary Result: 159Y, 22N, 52A.
Result: 149Y, 22N, 49A (passes).
Reference docs:[24/1834r4, 24/1831r3, 24/1864r1]. SP result: 55Y/8N/22A.

## Slide 21: Motion 207 (PHY-PDT)
Move to insert the proposed text changes below to Section 38.3.19.2 (Pre-correction accuracy requirements) of 11-24/1981r3, and to the latest TGbn draft (TGbn D0.1)
For the ELR PPDU carrying immediate response frame in response to a preceding soliciting frame, after compensation, the absolute value of residual CFO error with respect to the preceding PPDU carrying soliciting frame shall not exceed 15 kHz at the 10% point of the complementary cumulative distribution function (CCDF) of CFO error in AWGN at a received power of -82 dBm in the primary 20 MHz channel.
Move: Rui Cao Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1841r1]. SP result: No objection.
Chair’s note: Ensured instructions are clear to the group and TGbn editor.

## Slide 22: Motion 208 (PHY-PDT)
Move to replace the “TBD” to “8 us” for the PE block in the Figure 38-xx (UHR ELR PPDU format) in Section 38.3.6 (UHR PPDU formats) of 11-24/1981r3, and in the latest TGbn draft (TGbn D0.1)
Note: the PE value applies for UHR ELR PPDU.
Move: Rui Cao Second: Wook Bong Lee
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1841r1]. SP result: No objection.
Chair’s note: Ensured instructions are clear to the group and TGbn editor.

## Slide 23: Motion 209 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2022r2 to the latest TGbn draft (TGbn D0.1)
Move: Frank Hsu Second: George Kuo
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2022r2]. SP result: No objection.

## Slide 24: Motion 210
INTENTIONALLY LEFT BLANK

## Slide 25: Motion 211 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2007r3 to the latest TGbn draft (TGbn D0.1)
Move: Dmitry Akhmetov Second: Kiseon Ryu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2007r3]. SP result: No objection.

## Slide 26: Motion 212 (MAC)
Move to add to the TGbn SFD the following:
An AP transmitting a BSRP Trigger frame as an ICF which is addressed to at least a UHR non-AP STA that has enabled a dynamic unavailability operation mode, shall ensure that the UL Length field is set to a sufficient length so that the PPDU that contains a Multi-STA BA as an ICR, includes unavailability information in the Multi-STA BA in addition to other baseline requirements
Move: Hongwon Lee Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1464r2]. SP result: No objection.

## Slide 27: Motion 213 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/1992r3 to the latest TGbn draft (TGbn D0.1)
Move: Rethna Pulikkoonattu Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1992r3]. SP result: No objection.

## Slide 28: Motion 214 (PHY)
Move to add to the TGbn SFD the following:
1-bit indication in the per-user SIG field to resolve the BSS color for COBF transmissions.
  The coding bit is re-purposed for this indication
Move: Shengquan Hu Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1829r2, 11-24/1822r4]. SP result: No objection.

## Slide 29: Motion 215 (PHY)
Move to add to the TGbn SFD the following:
The cyclic shift for pre-UHR modulated fields in UHR MU PPDU used for Co-BF transmission is based on local transmit chain index at each AP.
Move: Juan Fang Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[None]. SP result: No objection.

## Slide 30: Motion 216 (PHY)
Move to add to the TGbn SFD the following:
Mandatory support MCSs of QPSK with code rate 2/3; 16QAM with code rate 2/3; 16QAM with code rate 5/6; 256QAM with code rate 2/3.
  Support for 256QAM with code rate 2/3 for 20MHz only devices is TBD.
Move: Jianhan Liu Second: Eugene Baik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0469r0, 24/0753r1]. SP result: No objection.

## Slide 31: Motion 217 (PHY)
Move to add to the TGbn SFD the following:
The maximum number of spatial streams transmitted by each AP in CSR is 4.
Move: Jianhan Liu Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[None]. SP result: No objection.

## Slide 32: Motion 218 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2017r0 to the latest TGbn draft (TGbn D0.1)
Move: Yusuke Asai Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2017r0]. SP result: No objection.

## Slide 33: Motion 219 (PHY)
Move to add to the TGbn SFD the following:
For the COBF case, the information in the NDPA for the responding AP has a unified design for joint-NDP based sounding as well as cross-BSS section of sequential sounding.
Move: Sameer Vermani Second: Eugene Baik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1822r4]. SP result: No objection.

## Slide 34: Motion 220 (PHY)
Move to add to the TGbn SFD the following:
2 BSS colors are indicated in the preamble of a COBF PPDU.
  One BSS color for the sharing AP and another BSS color for the shared AP.
Move: Sameer Vermani Second: Rethna Pulikkoonattu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1822r4]. SP result: No objection.

## Slide 35: Motion 221 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2032r1 to the latest TGbn draft (TGbn D0.1)
Move: Dongguk Lim Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2032r1]. SP result: No objection.

## Slide 36: Motion 222 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2033r3 to the latest TGbn draft (TGbn D0.1)
Move: Dongguk Lim Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2033r3]. SP result: No objection.

## Slide 37: Motion 223
INTENTIONALLY LEFT BLANK

## Slide 38: Motion 224 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2023r3 to the latest TGbn draft (TGbn D0.1)
Move: Junghoon Suh Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2023r3]. SP result: No objection.

## Slide 39: Motion 225 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2034r1 to the latest TGbn draft (TGbn D0.1)
Move: Chenchen LIU Second: Yan Xin
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2034r1]. SP result: No objection.

## Slide 40: Motion 226 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2135r0 to the latest TGbn draft (TGbn D0.1)
Move: Bo Gong Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2135r0]. SP result: No objection.

## Slide 41: Motion 227 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2009r6 to the latest TGbn draft (TGbn D0.1)
Move: Mengshi Hu Second: Junghoon Suh
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2009r6]. SP result: No objection.

## Slide 42: Motion 228 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2027r1 to the latest TGbn draft (TGbn D0.1)
Move: Eugene Baik Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2027r1]. SP result: No objection.

## Slide 43: Motion 229 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2049r6 to the latest TGbn draft (TGbn D0.1)
Move: Arik Klein Second: Shimi Shilo
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2049r6]. SP result: No objection.

## Slide 44: Motion 230 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1762r23 to the latest TGbn draft (TGbn D0.1)
Move: Matthew Fischer Second: Liuming Lu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1762r23]. SP result: Find result.

## Slide 45: Motion 231 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2005r1 to the latest TGbn draft (TGbn D0.1)
Move: Eugene Baik Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2005r1]. SP result: No objection.

## Slide 46: Motion 232 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2006r2 to the latest TGbn draft (TGbn D0.1)
Move: Eugene Baik Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2006r2]. SP result: No objection.

## Slide 47: Motion 233 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2016r3 to the latest TGbn draft (TGbn D0.1)
Move: Laurent Cariou Second: Matthew Fischer
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2016r3]. SP result: 124Y, 27N, 55A.

## Slide 48: Motion 234
INTENTIONALLY LEFT BLANK

## Slide 49: Motion 235 (MAC)
Move to add to the TGbn SFD the following:
An AP MLD may optionally include a QoS Map element within the SCS Response frame transmitted by the AP MLD to update the DSCP-to-UP mapping for UL if the following conditions are true
  the TID and the User Priority subfields of the Control Info field in the associated QoS Characteristics element are set to different values within 0~7
  the AP MLD and the non-AP MLD supports the QoS map operation
Move: Guogang Huang Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/2123r1]. SP result: Super Majority.

## Slide 50: Motion 236 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2024r0 to the latest TGbn draft (TGbn D0.1)
Move: Eunsung Park Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2024r0]. SP result: No objection.

## Slide 51: Motion 237 (PHY)
Move to add to the TGbn SFD the following:
For 160 MHz and 320 MHz PPDUs, in only the non-punctured primary 80 MHz subblock, the following distribution bandwidth mode is allowed for DRU
  20 MHz + 20 MHz + 40 MHz (or 40 MHz + 20 MHz + 20 MHz)
Move: Lin Yang Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/100r0]. SP result: No objection.

## Slide 52: Motion 238 (PHY)
Move to add to the TGbn SFD the following:
For distributed transmission, apply global CSD to UHR-STF only, and UHR-LTF and data still apply local per stream CSD, just like RRU
Move: Lin Yang Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/100r0]. SP result: No objection.

## Slide 53: Motion 239 (PHY-PDT)
Move to add the following note into the TGbn D0.1, under the section “38.3.2.x RU and MRU restrictions for 20 MHz operation”
“NOTE – When a 20 MHz operating STA participates in an 80 MHz or wider UHR TB PPDU using 20 MHz distribution bandwidth, the TX LO leakage of the STA might interfere with some of the data subcarriers within the 20 MHz distribution bandwidth such that for some DRUs in that 20MHz DBW performance of high MCS may be significantly degraded.”
Move: Lin Yang Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/100r0]. SP result: No objection.

## Slide 54: Motion 240 (PHY)
Move to add to the TGbn SFD the following:
11bn supports indicating a 60 MHz DBW using a value of 3 in the 2-bit DBW indication subfield within the UHR variant User Info field of a Trigger Frame in the case of DRU
Move: Mahmoud Hasabelnaby Second: Yan Xin
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0129r0]. SP result: ??.

## Slide 55: Motion 241 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2035r1 to the latest TGbn draft (TGbn D0.1)
Move: Ross J. Yu Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2035r1]. SP result: No objection.

## Slide 56: Motion 242 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2011r1 to the latest TGbn draft (TGbn D0.1)
Move: Mengshi Hu Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2011r1]. SP result: No objection.

## Slide 57: Motion 243 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2012r3 to the latest TGbn draft (TGbn D0.1)
Move: Mengshi Hu Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2012r3]. SP result: No objection.

## Slide 58: Motion 244 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2031r5 to the latest TGbn draft (TGbn D0.1)
Move: Jason Yuchen Guo Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2031r5]. SP result: No objection.

## Slide 59: Motion 245 (PHY)
Move to add to the TGbn SFD the following:
The Interference Mitigation feature is only defined with LDPC
Move: Shimi Shilo Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1785r2]. SP result: No objection.

## Slide 60: Motion 246 (PHY)
Move to add to the TGbn SFD the following:
For each bandwidth, there is a fixed number of IM pilots (value TBD)
Move: Shimi Shilo Second: Genadiy Tsodik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1785r2]. SP result: No objection.

## Slide 61: Motion 247 (PHY)
Move to add to the TGbn SFD the following:
Within any transmission that uses IM pilots, they are used in every data OFDM symbol and in the same corresponding subcarriers positions, for a given BW
Move: Shimi Shilo Second: Oded Redlich
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1785r2]. SP result: No objection.

## Slide 62: Motion 248 (MAC-PDT)
Move to incorporate the proposed text changes in 11-25/88r3 to the latest TGbn draft (TGbn D0.1)
Move: Rubayet Shafin Second: Vishnu Ratnam
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/88r3]. SP result: No objection.

## Slide 63: Motion 249 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2042r1 to the latest TGbn draft (TGbn D0.1)
Move: Juan Fang Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2042r1]. SP result: No objection.

## Slide 64: Motion 250 (PHY)
Move to add to the TGbn SFD the following:
11bn defines 5 bit Recommended CSI MCS subfield in the 2nd Special STA Info field of the NDPA targeted for OBSS AP in the UHR CoBF sounding
  It is set from B20 to B24 in the 2nd Special STA Info field
  The 5-bit MCS level includes “No Recommendation” MCS entry in addition to the UHR MCS entries
    Index 31 indicates “No Recommendation”
  The Recommended CSI MCS is for the OBSS AP to set the MCS in the BFRP trigger frame sent in the future Cross-BSS sounding / Joint Sounding sequence
  When there are multiple OBSS STAs to feedback the CSI report, the Recommended CSI MCS can be set to the lowest MCS among all those OBSS STAs
Move: Junghoon Suh Second: Mahmoud Hasabelnaby
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0078r0]. SP result: No objection.

## Slide 65: Motion 251 (PHY)
Move to add to the TGbn SFD the following:
In the UHR MU PPDU in 11bn, the PE requirements of UEQM with the constellation order x of the first spatial stream is equal to the PE requirements of EQM with the constellation order x
Move: Mengshi Hu Second: Shimi Shilo
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0128r0]. SP result: No objection.

## Slide 66: Motion 252 (PHY)
Move to add to the TGbn SFD the following:
11bn defines the following modes for co-SR transmission:
  Mode 1: trigger + same L-SIG contents, could be different U-SIG contents.
    For UHR+EHT, or EHT+UHR or EHT+EHT co-SR transmission.
    Provided no changes to non-UHR EHT non-AP STAs are needed.
  Mode 2: Tigger + same L-SIG contents + same U-SIG contents
    For UHR+UHR co-SR transmission.
  For all modes, the two PPDUs will start and end at the same time.
  UHR PPDU for co-SR transmission will be used for either mode 1 or mode 2 when UHR transmission exists.
    There exists an indication in U-SIG field to indicate the UHR PPDU is a UHR PPDU for co-SR transmission.
Move: Ross Jian Yu Second: Jason Y. Guo
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0104r0]. SP result: 41Y, 7N, 20A.

## Slide 67: Motion 253 (Joint)
Move to add to the TGbn SFD the following:
In Coordinated Spatial Reuse:
  A sharing AP that intends to initiate a Coordinated Spatial Reuse transmission shall transmit a Trigger frame to initiate concurrent CSR transmissions with one (whether to allow more is TBD) other AP within its obtained TXOP BW;
  When all addressed non-AP STAs are UHR STAs, the concurrent CSR transmission starts SIFS after the Trigger frame
  Which trigger frame is TBD
Move: Jason Y. Guo Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-23/1868, 11-24/1092]. SP result: No Objection

## Slide 68: Motion 254 (Joint)
Move to add to the TGbn SFD the following:
In Coordinated Spatial Reuse, the following information shall be carried in the Trigger frame that initiates concurrent CSR transmissions of the 2 APs
  The duration of the data PPDU transmitted by the sharing AP and of the data PPDU transmitted by the shared AP, which are the same, after the Trigger frame
  Other parameters TBD
Move: Jason Y. Guo Second: Yunbo Li
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-23/1868, 11-24/1092]. SP result: No objection.

## Slide 69: Motion 255 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1881r7 to the latest TGbn draft (TGbn D0.1)
Move: Duncan Ho Second: Mike Montemurro
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1881r7]. SP result: 135Y, 18N, 39A.

## Slide 70: Motion 256 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2040r9 to the latest TGbn draft (TGbn D0.1)
Move: Laurent Cariou Second: Qi Wang
Discussion: None
Result: Approved with unanimous consent.
Reference docs:[11-24/2040r9]. SP result: No objection

## Slide 71: Motion 257 (MAC)
Move to add to the TGbn SFD the following:
Define an Enhanced BSR Control subfield in A-ctrl to report a larger per TID queue size
  The Enhanced BSR Control subfield consists of at least a TID subfield and an unsigned value subfield to report the larger queue size (QS) of the TID
  The reported QS is equal to 2147328 Octets + the value reported in the Queue Size field of the defined Enhanced BSR Control subfield
  When the QoS Control with the same TID as the Enhanced BSR Control subfield is present in the same MPDU, the QS subfield of the QoS Control is set to value 254
  TBD if the Enhanced BSR Control subfield shares the control ID with other Control subfield proposals in UHR
  Note: The baseline rules which regulate HT control field to be the same in all MPDUs of the same frame type in an A-MPDU do not change
  Note: Encoding of the baseline QS subfield in QoS Control does not change.
  Note: Length of the Enhanced BSR Control subfield allows to aggregate the UPH in the same A-Control subfield
Move: Frank Hsu Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/0963, 11-23/2007]. SP result: No objection

## Slide 72: Motion 258 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2068r1 to the latest TGbn draft (TGbn D0.1)
Move: Ming Gan Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2068r1]. SP result: No objection.

## Slide 73: Motion 259 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2069r1 to the latest TGbn draft (TGbn D0.1)
Move: Ming Gan Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2069r1]. SP result: No objection.

## Slide 74: Motion 260 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2020r1 to the latest TGbn draft (TGbn D0.1)
Move: George Cherian Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2020r1]. SP result: No objection

## Slide 75: Motions on January 16th

## Slide 76: Motion 261 (MAC)
Move to add to the TGbn SFD the following:
Include the CoEx unavailability information in a new “Special User Info” field with AID12 set to 2008 of the BSRP Trigger frame when used as an ICF to report CoEx unavailability information
  A feedback type field (name TBD) (4 bits field – B12 to B15 of the “Special User Info” field) which is set to 0 to indicate that the “Special User Info” field is carrying CoEx unavailability information
  CoEx unavailability information includes two parameters: Unavailability Target Start Time and Unavailability Duration (these fields are already defined)
Move: Sherief Helwa Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1558, 11-24/1464r3, 11-24/494r2]. SP result: No objection.

## Slide 77: Motion 262 (JOINT)
Move to add to the TGbn SFD the following:
When the initiating AP requests the responding AP to join the CoBF sounding, the red subfields in the first and second User Info fields of the NDPA shall be set as follows.
  NDPA Version Identifier is set to 0 for CoBF sounding in UHR
  Number of LTF symbols is set to 0 and 1 for 4 and 8 symbols, respectively
  Starting Spatial Stream is set to 0 and 1 for the 1st and 5th streams, respectively
  Number of spatial streams is set to 0 and 1 for the 4 and 8 streams, respectively
  LTF+GI is set to 0 and 1 for 2x LTF+0.8us GI and 2x LTF+1.6us GI, respectively
  B20-26, which are shown as Reserved in the second User Info field, can be used in the future
Move: Sameer Vermani Second: You-Wei Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1822r4, 11-24/1835r3, 11-24/1865r3]. SP result: No objection.

## Slide 78: Motion 263 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/1977r6 to the latest TGbn draft (TGbn D0.1)
Move: Alice Chen Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1977r6]. SP result: No objection.

## Slide 79: Motion 264 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2043r1 to the latest TGbn draft (TGbn D0.1)
Move: Juan Fang Second: Sameer Vermani
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2043r1]. SP result: No objection.

## Slide 80: Motion 265 (MAC)
Move to add to the TGbn SFD the following:
As a part of M-AP coordination agreement procedure, an AP may assign an AP ID to another AP with the following constraints:
  The AP ID is used for the AP to identify another AP as a coordinated AP, when necessary.
  The AP ID field has the same size and the field value has a range as defined in AID field (see 9.4.1.8)
  The AP shall ensure that the AP ID value is not assigned by the AP or by its affiliated MLD to any other STA (e.g., STA is an associated non-AP STA, an unassociated non-AP STA that has been allocated a RSID , or any other coordinated AP), or a non-AP MLD that is associated with the AP MLD
  It's TBD whether the AP ID value is greater than 2^n where n is the maximum of the value carried in the MBSSID Indicator (n) field of the Multiple BSSID element for any AP affiliated with the AP MLD that belongs to a multiple BSSID set
Move: Jay Yang Second: Xiangxin Gu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-23/1837r2,11-24/1389r0, 11-24/1217r2, 11-24/0842r0,11-24/0843r0, 11-24/1016r2,11-24/1017r0, 11-23/1895r2, 11-24/0423r0,11-24/1225r0, 24/1220r0,25/0007r2]. SP result: No objection.

## Slide 81: Motion 266 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2015r6 to the latest TGbn draft (TGbn D0.1)
Move: Ron Porat Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2015r6]. SP result: No objection.

## Slide 82: Motion 267 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2056r1 to the latest TGbn draft (TGbn D0.1)
Move: Kumail Haider Second: George Cherian
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2056r1]. SP result: No objection.

## Slide 83: Motion 268 (MAC)
Move to amend the text below in the TGbn SFD:
Do you agree that a TXOP owner AP shall announce its intention of sharing a portion of the time resource of its TXOP for C-TDMA operation, in an Initial Control frame (exact ICF and name TBD) sent at the beginning of the TXOP and that the frame polls AP(s) with whom it may share the TXOP to determine their interest? o A TXOP owner AP that intends to share its TXOP is referred to as a sharing AP. o A candidate AP identified (polled) in the Initial Control frame is referred to as a polled AP. o The Duration field of the frame is set to the length of time required to transmit the solicited response frame plus one SIFS. o Whether or not the sharing AP is mandated to send the Initial Control frame that announces that intention is TBD.
Move: Sanket Kalamkar Second: GeonHwan Kim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-23/1895, 11-23/1912r2, 11-24/0423, 11-24/1016, 11-24/1017, 11-24/1225]. SP result: No objection.

## Slide 84: Motion 269 (MAC)
Move to add to the TGbn SFD the following:
The ICF (polling frame) sent as part of Co-TDMA operation shall be a BSRP Trigger frame
Move: Sanket Kalamkar Second: Kumail Haider
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1225, 11-24/0843r0]. SP result: No objection.

## Slide 85: Motion 270 (MAC)
Move to add to the TGbn SFD the following:
As part of Co-TDMA operation, a poll response from a polled AP solicited by the ICF shall be carried in an M-BA frame
Move: Sanket Kalamkar Second: GeonHwan Kim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1225, 11-24/0843r0]. SP result: No objection.

## Slide 86: Motion 271 (MAC)
Move to add to the TGbn SFD the following:
In response to BSRP Trigger frame as an ICF transmitted by a non-AP STA as the TXOP holder, an AP transmits a Multi-STA BlockAck frame
  Whether Block Ack Starting Sequence Control subfield and Block Ack Bitmap subfield are present or not is TBD
  Values of Ack Type and TID are TBD
Move: Hongwon Lee Second: Insun Jang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1464]. SP result: No objection.

## Slide 87: Motion 272 (MAC)
Move to add to the TGbn SFD the following:
Define HIP EDCA in UHR where a STA with Low Latency traffic may be allowed, based on TBD conditions, to send a Defer Signal (it is TBD whether CTS or RTS is used) to start a protected short contention for pending LL data
  Conditions to be allowed to send a Defer Signal is TBD
  STA in HiP EDCA always use RTS/CTS as initial frame exchange and retry.
  Duration of protected short contention is TBD.
  Access parameters (AIFSN, CW and the expansion rules) used to transmit the Defer Signal are TBD. The retry count where the Defer Signal is allowed to be sent is TBD
  Contention parameters for the protected short contention are TBD. The STAs that transmitted a Defer Signal but did not win the protected short contention will initiate a new retry.
  Low Latency traffic is treated as AC_VO traffic. Other cases are TBD.
  The solution would provide control on the degree of collisions that may occur while using it and, allows for autonomous randomness or/and controlled by the AP
  No new mandatory synchronization requirement on STA side
  HIP EDCA is used by the STAs in a BSS only when this feature is enabled by the AP
Move: Dmitry Akhmetov Second: Kiseon Ryu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1144r1, 24/0864r1, 24/1193r1]. SP result: 150Y, 14N, 70A.

## Slide 88: Motion 273 (MAC)
Move to add to the TGbn SFD the following:
TGbn defines or improves an existing mechanism so that a non-AP STA that is a TXOP responder can indicate its buffered low latency traffic needs (for traffic from the TxOP responder to the TxOP Holder) in a control response frame. The TXOP holder should consider the indication in determining subsequent actions. Subsequent actions related to this indication are out of the scope of the standard.
  Note: whether an AP can Indicate its low latency needs is TBD
Move: Mohamed Abouelseoud Second: Dibakar Das
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0389r0, 24/168r0,24-0416/r1, 24-0442/r3, 24-1195/r1, 23/885, 24/264, 23/1886, 24/1156, 24/1871r1, 24/1074, 23/1909r1, 24/131r0, 24/1156r0]. SP result: 192Y, 10N, 29A.

## Slide 89: Motion 274 (MAC)
Move to add to the TGbn SFD the following:
Define a mechanism as part of the procedure of time sharing during a TXOP (e.g. C-TDMA, TXS, …) to support fairness to neighboring STAs (APs and non-APs)?
  Exact mechanism is TBD
Move: Dibakar Das Second: Si-Chan Noh
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/0093, 11-25/0086r0]. SP result: 144Y/27N/42A.

## Slide 90: Motion 275 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1978r3 to the latest TGbn draft (TGbn D0.1)
Move: Mohamed Abouelseoud Second: Anuj Batra
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1978r3]. SP result: No objection on R2.

## Slide 91: Motion 276 (MAC)
Move to add to the TGbn SFD the following:
UHR should allow more than two TIDs to be mapped to high priority ACs (i.e., VO or VI)?
Up to one TID for each AC currently assigned to BE and BK are remapped.
Those TIDs may be used dynamically (e.g., following an SCS flow setup).
Move: Dibakar Das Second: Abdel Ajami
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/463r1, 24/1899, 23/0069, 24/2123]. SP result: No objection.

## Slide 92: Motion 277 (MAC)
Move to add to the TGbn SFD the following:
As part of Co-TDMA operation, TGbn defines a mechanism for a Co-TDMA sharing AP to transmit to a Co-TDMA coordinated AP an indication of whether the Co-TDMA coordinated AP is to return the remainder of the allocated time (if any) back to the Co-TDMA sharing AP.
  How to signal the indication is TBD
  Note: This mechanism is to be enabled only if the Co-TDMA sharing AP is capable of receiving the TXOP return.
Move: Serhat Erkucuk Second: Insun Jang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1250, 24/1701, 24/0843, 24/1017]. SP result: No objection.

## Slide 93: Motion 278 (MAC)
Move to add to the TGbn SFD the following:
For UHR-variant Trigger frame:
  iFCS present: 1 bit field in UHR-variant Common Info field
    TBD for HE/EHT-variant
Move: Sherief Helwa Second: SunHee Baek
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/544, 11-24.1129]. SP result: No objection.

## Slide 94: Motion 279 (MAC)
Move to add to the TGbn SFD the following:
11bn defines a Seamless Mobility Domain (SMD, exact name TBD) that covers multiple AP MLDs, where a non-AP MLD can use the UHR seamless roaming procedure to roam between the AP MLDs of the SMD
  A logical SMD Management Entity (SMD-ME, exact name TBD) provides association, IEEE 802.1X Authenticator (except for the management of 802.1X control ports which is TBD) and RSNA Key management for non-AP MLDs across all AP MLDs of the SMD.
  A non-AP MLD transitions between AP MLDs within the SMD while maintaining its association and security association with the SMD-ME.
  The non-AP MLD can transition from one SMD to another SMD that are part of the same MD (Mobility Domain) using FT with improvements
Move: Mike Montemurro Second: Giovanni Chisci
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/2072, 24/1894, 24/0052, 23/1884, 23/1937, 23/1996, 24/830, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1425, 24/881, 24/1882, 24/1883, 23/1897, 24/0349, 24/0480, 23/1416, 24/0881, 23/1897, 24/0349, 24/1746]. SP result: No objection.

## Slide 95: Motion 280 (MAC)
Move to add to the TGbn SFD the following:
11bn defines that within a Seamless Mobility Domain (SMD, exact name TBD) the data path includes either one MAC-SAP for the SMD or a separate MAC-SAP per AP MLD of the SMD.
  In the case of a separate MAC-SAP per AP MLD, the DS mapping is updated when the non-AP MLD roams to another AP MLD within the SMD.
  In the case of a separate MAC-SAP per AP MLD, the component of the 802.1X Authenticator in the SMD-ME interacts with an 802.1X Authenticator component in the AP MLD that manages the 802.1X controlled port for the non-AP MLD.
  In the case of a single MAC-SAP for the SMD, the 802.1X Authenticator in the SMD-ME manages the 802.1X controlled port for the non-AP MLD.
Move: Mike Montemurro Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/2072, 24/1894, 24/0052, 23/1884, 23/1937, 23/1996, 24/830, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1425, 24/881, 24/1882, 24/1883, 23/1897, 24/0349, 24/0480, 23/1416, 24/0881, 23/1897, 24/0349, 24/1746]. SP result: No objection

## Slide 96: Motion 281 (MAC)
Move to add to the TGbn SFD the following:
For negotiation over the wireless medium, an AP that requests protection for its R-TWT schedule(s) via negotiations with another AP includes information carried in TBD fields of the Broadcast TWT Parameter Set field corresponding to each R-TWT schedule being negotiated in a TBD individually addressed Management frame that it transmits to the other AP.
Move: SunHee Baek Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/160, 23/1916, 23/355, 24/1346, 24/1220, 24/407, 24/2045, 23/1887, 23/0226, 22/1530, 23/860, 23/1932]. SP result: No objection.

## Slide 97: Motion 282 (MAC)
Move to add to the TGbn SFD the following:
When a non-AP MLD is in the process of roaming from a current AP MLD to a target AP MLD, the non-AP MLD can request to the current AP MLD what context needs to be transferred from the current AP MLD to the target AP MLD.
  What context can be requested is TBD
  It applies when the current AP MLD and the Target AP MLD support the context transfer
Move: Yelin Yoon Second: Pooya Monajemi
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1516, 24/0396, 24/830, 24/1883, 24/1890, 24/1746, 24/1851, 23/1416, 24.1898, 24/0052]. SP result: 180Y, 14N, 57A

## Slide 98: Motion 283 (MAC)
Move to add to the TGbn SFD the following:
As part of seamless roaming procedure, a non-AP MLD can initiate a roaming preparation procedure with a target AP MLD by sending a TBD request frame to its current AP MLD.
  The request frame indicates the set of links to be set up with the target AP MLD.
  The request frame indicates the context to be transferred or renegotiated with the target AP MLD.
  The current AP MLD sends a TBD response frame to the non-AP MLD to indicate the status (accept/reject) of the link setup.
    If the link setup is accepted, the transferable context is transferred to the target AP MLD.
  TBD on whether/how the renegotiation of context is performed in these request/response frames
  TBD – multiple candidate target AP MLDs selection
Move: Binita Gupta Second: Chittabrata Ghosh
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0052, 23/1884, 23/1937, 23/1996, 24/830, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1425, 24/881, 24/1882, 24/1883, 23/1897, 24/0349, 24/0480, 23/1416, 24/1824, 24/2129]. SP result: 149Y, 4N, 52A.

## Slide 99: Motion 284 (MAC)
Move to add to the TGbn SFD the following:
As part of seamless roaming procedure, a non-AP MLD in state 4 with the SMD-ME can perform roaming transition through a target AP MLD that is a part of the SMD.
TBD on the conditions and details for performing roaming through target AP MLD
Move: Binita Gupta Second: Giovanni Chisci
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0398, 24/1812, 24/1883, 23/1884, 24/0052]. SP result: No objection.

## Slide 100: Motion 285 (MAC)
Move to add to the TGbn SFD the following:
For security in seamless roaming, when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD within the SMD, the same PMKSA, established with the SMD-ME, shall be used to protect communications with the current AP MLD and the target AP MLD.
Move: Giovanni Chisci Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[23/1416, 24/2072, 24/1894, 24/0052, 23/1884, 23/1937, 23/1996, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1882, 24/1883]. SP result: No objection.

## Slide 101: Motion 286 (MAC)
Move to add to the TGbn SFD the following:
For security in seamless roaming, when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD within the SMD, the same PTKSA, established with the SMD-ME, shall be used to protect communications with the current AP MLD and the target AP MLD.
Move: Giovanni Chisci Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[23/1416, 24/2072, 24/1894, 24/0052, 23/1884, 23/1937, 23/1996, 24/0083, 24/0101, 24/0396, 24/1812, 24/0398, 24/0412, 24/0655, 23/2157, 24/679, 24/1882, 24/1883]. SP result: No objection.

## Slide 102: Motion 287 (MAC)
Move to add to the TGbn SFD the following:
Legend: Green: allowed; Orange: disallowed
Move: Sherief Helwa Second: Liwen Chu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1558, 24/1221, 24/1225, 24/1563]. SP result: No objection.
Allowed UHR ICF to be transmitted by a non-AP STA (addressing the associated AP STA) |  |  |  |  |  |  | 
ICF | eMLSR | AP DPS | Solicited Coex | Unsolicited Coex | NPCA | C-TDMA (ICF) | Co-BF/Co-SR
RTS | N/A | Yes | N/A* | No | No | N/A | 
MU RTS |  | No |  | No | No |  | 
BSRP Trigger |  | No |  | No | No |  | 
BSRP GI3 |  | Yes |  | Yes | Yes |  | 
Notes: RTS solicits CTS frame; BSRP GI3 Trigger frame solicits an M-BA that is contained in a non-HT (dup) PPDU. C-TDMA, C-BF, CSR ICF transmission is to other APs. No expectations for non-AP STAs, unless due to other functionalities already enabled/supported by non-AP STA. Solicited and Unsolicited Coex are part of DUO. N/A means that either the non-AP STA is not allowed to send an ICF or the AP STA is not allowed to respond with ICR for this scheme/operation mode. *DUO is only approved for non-AP STAs. So, a non-AP STA cannot send an ICF to an AP soliciting unavailability information in ICR (i.e., solicited CoEx). Acronyms: DPS: Dynamic Power Save, DUO: Dynamic Unavailability Operation, Unsolicited CoEx: Reporting unavailability in ICF, Co-BF: Coordinated beamforming, Co-SR: Coordinated Spatial Reuse, BSRP GI3: BSRP Trigger soliciting an M-BA in non-HT (dup) PPDU |  |  |  |  |  |  | 

## Slide 103: Motion 288 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2066r1 to the latest TGbn draft (TGbn D0.1)
Move: Ming Gan Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2066r1]. SP result: No objection.

## Slide 104: Motion 289 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/2067r2 to the latest TGbn draft (TGbn D0.1)
Move: Ming Gan Second: Matthew Fischer
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2067r2]. SP result: No objection.

## Slide 105: Motion 290 (Joint-PDT)
Move to incorporate the proposed text changes in 11-24/2030r8 to the latest TGbn draft (TGbn D0.1)
Move: Jason Y. Guo Second: Sherief Helwa
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2030r8]. SP result: No objection.

## Slide 106: Motion 291 (Joint-PDT)
Move to incorporate the proposed text changes in 11-24/2133r4 to the latest TGbn draft (TGbn D0.1)
Move: Alice Chen Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2133r4]. SP result: No objection.

## Slide 107: Motion 292 (Joint-PDT)
Move to incorporate the proposed text changes in 11-24/2029r1 to the latest TGbn draft (TGbn D0.1)
Move: Li Quan Second: Yan Li
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2029r1]. SP result: No objection.

## Slide 108: Motion 293 (Joint-PDT)
Move to incorporate the proposed text changes in 11-24/2026r4 to the latest TGbn draft (TGbn D0.1)
Move: Yan Li Second: Li Quan
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2026r4]. SP result: No objection.

## Slide 109: Motion 294 (MAC-PDT)
Move to incorporate the proposed text changes in 11-25/0102r2 to the latest TGbn draft (TGbn D0.1)
Move: Brian Hart Second: Jay Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0102r2]. SP result: No objection.

## Slide 110: Motion 295
Move to instruct the TGbn Editor to create IEEE802.11bn D0.1 draft by incorporating the changes specified in all the approved proposed draft text (PDT) documents.
Move: Abhishek Patil Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.

## Slide 111: Motions on march 13th , PM1

## Slide 112: Motion 296 (PHY)
Move to add to the TGbn SFD the following:
The Data and pilot subcarrier indices for DRUs in an 60 MHz DBW are defined in following table:
Move: Ross J. Yu
Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0154r0]. SP result: No objection

## Slide 113: Motion 297 (PHY)
Move to add to the TGbn SFD the following:
The Pilot subcarrier indices for DRUs in an 60 MHz DBW are defined in following table?
Move: Ross J. Yu Second: Yan Xin
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0154r0]. SP result: No objection

## Slide 114: Motion 298 (PHY)
Move to add to the TGbn SFD the following:
802.11bn defines the concept of a sync-reference AP and a sync-follower AP for CFO correction in COBF
  Sync-follower AP pre-corrections needed
  For sequential sounding:
    All the NDPs sent by it during sounding phase that are sent for the purpose of sounding the STAs in the other BSS (Mandatory)
    For the NDPs sent by it for sounding the STAs in its own BSS, it is recommended but not mandatory that the sync follower AP pre-correct those NDPs
  For joint sounding
    All the NDPs sent by it during the sounding phase (Mandatory)
    The COBF sync and COBF PPDU during transmission phase using the same frequency pre-correction value as the sounding phase, when it is the sharing AP
  Sync-reference AP does not pre-correct during transmission phase when it is the sharing AP
Move: Sameer Vermani Second: Yusuke Asai
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0083r1]. SP result: No objection.

## Slide 115: Motion 299 (PHY)
Move to add to the TGbn SFD the following:
The sync-follower AP shall use the NDPA frame sent by the sync-reference AP to pre-correct the NDP frequency to be within a TBD range (e.g., 350Hz) of the sync-reference AP’s frequency
  Applies to sequential and joint sounding
  The pre-correction of cross-BSS NDP and joint NDP is mandatory
  The pre-correction of in-BSS NDPs is recommended but not a mandatory requirement
Move: Sameer Vermani Second: Sherief Helwa
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0083r1]. SP result: No objection.

## Slide 116: Motion 300 (PHY)
Move to add to the TGbn SFD the following:
The sharing AP is the AP that transmits the final sync frame before the COBF PPDU
  Regardless of who is the sync-reference
  Note: This ensures a consistent protocol and a consistent behavior at sharing AP
Move: Sameer Vermani Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0083r1]. SP result: No objection.

## Slide 117: Motion 301 (PHY)
Move to add to the TGbn SFD the following:
The shared AP always pre-corrects COBF PPDU based on the final sync
  To bring the two APs within a TBD frequency range of each other (e.g., ~350Hz)
  Note: Regardless of which AP is the sync-reference, this ensures consistent behavior at shared AP
Move: Sameer Vermani Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0083r1]. SP result: No objection.

## Slide 118: Motion 302 (PDT-PHY)
Move to incorporate the proposed text changes in 11-25/0250r6 to the latest TGbn draft
Move: Genadiy Tsodik Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0250r6]. SP result: No objection.

## Slide 119: Motion 303 (PDT-PHY)
Move to incorporate the proposed text changes in 11-24/2008r2 to the latest TGbn draft
Move: Genadiy Tsodik Second: Yan Xin
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/2008r2]. SP result: No objection.

## Slide 120: Motion 304 (PHY)
Move to add to the TGbn SFD the following:
The COBF PPDU’s GI+LTF support and signaling is as follows:
  Support of following GI+LTF combinations to be mandatory at both AP and STA
    2x LTF +0.8us, 2xLTF+1.6us, 4xLTF+3.2us
  Additionally, 2x LTF+0.8us GI usage for a COBF pair is exchanged at the group formation stage
    Each AP conveys if it can use 2x+0.8us GI for this COBF group or not
    No further last-minute negotiation before COBF transmission
  Invite frame from sharing AP dictates the LTF+GI combination keeping the shared AP’s ability to use 2x LTF+0.8us in mind
Move: Sameer Vermani Second: Ron Porat
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0381r0]. SP result: 41Y/12N/32A

## Slide 121: Motion 305 (PHY)
Move to add to the TGbn SFD the following:
BSS ordering of per-user SIG fields in the preamble of a COBF transmission
  In the cases where the user fields of either BSS may go first while preserving the Nss in non-increasing order, the user fields of the sharing BSS go first
Move: Sameer Vermani Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0381r0]. SP result: No objection.

## Slide 122: Motion 306 (PHY)
Move to add to the TGbn SFD the following:
There shall be a frame-exchange before the COBF sounding between the two APs which will at-least serve the following goals:
  Unavailability/decline indication from the responding AP
    Used by responding AP to refuse participation in a COBF sounding process
  Exchange of sounding Nss capability of the STAs being sounded in the two BSSs
    The minimum sounding Nss capability of the participating STAs in each BSS will be exchanged
  Note: Design of the frames is TBD by MAC group
Move: Sameer Vermani Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0381r0]. SP result: No objection.

## Slide 123: Motion 307 (PHY)
Move to add to the TGbn SFD the following:
The first BSS color in U-SIG indicates the sharing AP and the second BSS color in U-SIG indicates the shared AP in UHR MU PPDU for Co-BF and Co-SR transmission
Move: You-Wei Chen Second: Juan Fang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/399r1]. SP result: No objection.

## Slide 124: Motion 308 (PHY)
Move to add to the TGbn SFD the following:
For Co-BF and Co-SR transmissions using UHR MU PPDU, TPE is fixed as 20us.
  nominal_packet_padding =20us and a factor =4.
Move: You-Wei Chen Second: Juan Fang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/399r1, 11-25/401r0]. SP result: No objection.

## Slide 125: Motion 309 (PHY)
Move to add to the TGbn SFD the following:
Joint/cross-BSS sounding feedback is limited to UL OFDMA if >1 STA is sounded
Move: Ron Porat Second: Sameer Vermani
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/411]. SP result: No objection.

## Slide 126: Motion 310 (PHY)
Move to add to the TGbn SFD the following:
Remove the requirement, for UHR STAs, to receive the forward-looking EHT ER SU preamble in the UHR RX procedure
Move: Lin Yang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/109r0]. SP result: No objection.

## Slide 127: Motion 311 (PHY)
Move to add to the TGbn SFD the following:
The CoBF Sync frame carries the following information
  How to indicate the information is TBD
Move: Alice Chen
Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/389r2, 25/399r0, 25/401r0, 25/0087r0].
SP result: No objection.
Category | 
Control | ‘CoBF Sync’
PHY Common Info | Length
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | BSS Color 1, BSS Color 2
 | TXOP
 | Number of UHR-SIG Symbols
 | GI+LTF Size
 | Number Of UHR-LTF Symbols
 | Number of CoBF Users
Per-User Info in Both BSS | STA ID
 | BSS Color Indication
 | MCS
 | Spatial Configuration
 | 2xLDPC

## Slide 128: Motion 312 (PHY)
Move to add to the TGbn SFD the following:
In each of the CoBF Invite, Response and Sync frames, if there is information for more than one users, the users are ordered according to Nss in non-increasing order
  The order of users in the sharing BSS in the Sync frame is aligned with that in the Invite frame.
  The order of users in the shared BSS in the Sync frame is aligned with that in the Response frame.
Move: Alice Chen Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/389r2, 11-25/381r0, 11-25/397r0]. SP result: No objection.

## Slide 129: Motion 313 (PHY)
Move to add to the TGbn SFD the following:
Transmit Constellation Error required values for the new MCSs 17, 19, 20 and 23 (QPSK 2/3, 16QAM 2/3, 16QAM 5/6 and 256QAM 2/3) for the UHR MU PPDU will be
Move: Genadiy Tsodik Second: Yan Xin
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/354r0, 11-25/392r0]. SP result: No objection.

## Slide 130: Motion 314 (PHY)
Move to add to the TGbn SFD the following:
The testing in the transmit and receive specification in IEEE 802.11bn spec should only use EQM (i.e., not use UEQM)
The testing in the transmit and receive specification in IEEE 802.11bn spec should not use 2xLDPC, if LDPC is used
Move: Alice Chen Second: Juan Fang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/392r0]. SP result: No objection.

## Slide 131: Motion 315 (PHY)
Move to add to the TGbn SFD the following:
In a COBF transmission, the per-user-UHR-SIG information of the BSS having the largest NSS for a Scheduled STA (largest being across the STAs of both BSSs) is sent first in the UHR-SIG User field followed by the per-user-UHR-SIG information of the other BSS?
  Within each BSS, the user information of the larger N_SS user is sent first
Move: Junghoon Suh Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/171r26, 11-25/381r0,389r0, 1-25/397r3]. SP result: No objection.

## Slide 132: Motion 316 (PHY)
Move to add to the TGbn SFD the following:
The order of user information in the Sync frame is aligned with the order of users in the UHR-SIG User field for CoBF transmission
Move: Junghoon Suh Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/389r0, 11-25/399r0, 1-25/397r3]. SP result: No objection.

## Slide 133: Motion 317 (PHY)
Move to add to the TGbn SFD the following:
The Rx minimum sensitivity and ACR/NACR specifications for the two ELR MCSs use the same value as EHT/UHR MCS0
Move: Juan Fang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/98r0, 11-25/392r0]. SP result: No objection.

## Slide 134: Motion 318 (PDT-PHY)
Move to incorporate the following changes to the latest TGbn draft
In Section 38.3.24.2 (Receiver minimum input sensitivity), change the two “TBDs” in Table 38-47 to “-82”
In Section 38.3.24.3 (Adjacent channel rejection), change the two “TBDs” in the column of "Adjacent channel rejection (dB)" in Table 38-49 to “16” and change the two “TBDs” in the column of " Nonadjacent channel rejection (dB)" in Table 38-49 to “32”
Move: Juan Fang Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/98r0, 11-25/392r0]. SP result: No objection.

## Slide 135: Motion 319 (PHY)
Move to amend the TGbn SFD as follows:
Mandatory support MCSs of QPSK with code rate 2/3; 16QAM with code rate 2/3; 16QAM with code rate 5/6; 256QAM with code rate 2/3.
  Support for 256QAM with code rate 2/3 for 20MHz only devices is TBD optional.
–[Motion #216, [264] and [274, 275]]
Move: Ross Jian Yu Second: Yan Xin
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0410r0]. SP result: No objection.

## Slide 136: Motion 320 (PHY)
Move to add to the TGbn SFD the following:
Encoding of the PS160 and RU allocation subfields in a UHR variant User Info field for DBW60 is defined as follows
Move: Eunsung Park
Second: Shengquan Hu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0359r0, 25/0358r0]. SP result: No objection

## Slide 137: Motion 321 (PHY)
Move to add to the TGbn SFD the following:
The constant shift value defined in the 80 MHz frequency subblock is used for DBW60
Move: Eunsung Park Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0359r0, 25/0358r0]. SP result: No objection

## Slide 138: Motion 322 (PHY)
Move to add to the TGbn SFD the following:
4xLTF sequence for DRU of 60MHz DBW is defined as follows
Move: Chenchen Liu Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0394r0]. SP result: No objection.

## Slide 139: Motion 323 (PHY)
Move to add to the TGbn SFD the following:
The occupied STFs tones of UHR-STF for DRU on DBW60 are the same as that of the largest MRU (i.e., 484+242) corresponding to the distribution BW 60MHz within the PPDU BW
Move: Shengquan Hu Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0358r0]. SP result: No objection.

## Slide 140: Motion 324 (PHY)
Move to add to the TGbn SFD the following:
DRU CSD start index assignment for DBW60 is defined as below
Move: Shengquan Hu Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0358r0, 25/0359r0]. SP result: No objection.

## Slide 141: Motion 325 (PHY)
Move to add to the TGbn SFD the following:
LDPC is the only FEC coding scheme for DL/UL MU-MIMO in 11bn
Move: Shengquan Hu Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0396r1]. SP result: No objection.

## Slide 142: Motion 326 (PHY)
Move to add to the TGbn SFD the following:
DL/UL MU-MIMO in UHR is optional for 20MHz only STA
Move: Shengquan Hu Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/0396r1]. SP result: No objection.

## Slide 143: Motion 327 (PHY)
Move to add to the TGbn SFD the following:
The CoBF Invite frame carries the following information
  How to indicate the information is TBD
Move: Alice Chen
Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/389r2, 11-25/399r0]. SP result: No objection.
Category | 
Control | ‘CoBF Invite’
PHY Common Info | Minimum Number of Data OFDM Symbols
 | Maximum Number of Data OFDM Symbols
 | PHY Version Identifier
 | Bandwidth
 | Punctured Channel Information
 | GI+LTF Size
 | Maximum Total Nss Allowed for shared AP
 | Number of CoBF Users in sharing BSS
Per-User Info in Sharing BSS | STA ID
 | Nss

## Slide 144: Motion 328 (PHY)
Move to add to the TGbn SFD the following:
The CoBF Response frame carries at least the following information
  How to indicate the information is TBD
Move: Alice Chen
Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/389r2, 11-25/399r0]. SP result: No objection.
Category | 
Control | ‘CoBF Acceptance’
PHY Common Info | Suggested Number of Data OFDM Symbols
 | PHY Version Identifier
 | Extra LTF Allowed
 | Number of CoBF Users in shared BSS
Per-User Info in Shared BSS | STA ID
 | MCS
 | Nss
 | 2xLDPC

## Slide 145: Motion 329 (MAC)
Move to add to the TGbn SFD the following:
The maximum time allocated by a sharing AP in a TXOP to all shared AP for CTDMA is not larger than the TXOP limit it advertised for the minimum between AC_VI TXOP limit and the TXOP Limit of the AC it obtains the TXOP with to its associated STAs.
  If TXOP limit for an AC is 0, there is no CTDMA in a TXOP obtained using that AC.
The sharing AP shall use at least a TBD portion of the obtained TXOP for data communication with its own associated STAs.
Note: similar consideration will apply for TXS mode 2
Move: Dibakar Das Second: Juan Fang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0093]. SP result: No objection.

## Slide 146: Motion 330 (PDT-MAC)
Move to incorporate the proposed text changes in 11-25/206r4 to the latest TGbn draft
Move: Dibakar Das Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/206r4 ]. SP result: No objection.

## Slide 147: Motion 331 (MAC)
Move to add to the TGbn SFD the following:
11bn defines a mechanism for non-AP STA to provide the delay report of LL buffered data to its AP.
  Note: this feature is optional.
  Note: the container carrying such information is TBD.
  Note: the delay report is the expiration time of the TBD MPDU/MSDU. The expression of the delay report is TBD.
Move: Liangxiao Xin Second:
Discussion:
Result:
Deferred.
Reference docs:[24/1692, 23/0885r0, 24/264r1, 24/0045r1]. SP result: 65%Y, 12%N, 23%A (101 votes)

## Slide 148: Motion 332 (MAC)
Move to add to the TGbn SFD the following:
TGbn defines a mechanism where a non-AP STA can be allocated frequency resources dynamically (i.e., on a per-TXOP basis) outside of the non-AP STA's current operating bandwidth and within the associated AP's BSS bandwidth
Move: Morteza Mehrnoush Second: Gaurang Naik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-22/2204, 11-23/2141 (Sindhu & Shubho), 11-23/843 (Liuming), 11-23/1496 (Kaiying), 11-23/1892 (Gaurang), 11-23/1913 (DongJu), 11-23/1935 (Liwen), 11-23/2027 (Vishnu), 11-24/591 (Morteza), 11-24/11571 (Hank Sung), 11-24/1863r1, 24/449r3]. SP result: No objection.

## Slide 149: Motion 333 (MAC)
Move to add to the TGbn SFD the following:
Define a mechanism to retrieve probe response content for neighboring AP MLD(s) of the current AP MLD, through the current AP MLD
Note. The neighboring AP MLD and the current AP MLD are in the same ESS
Move: Guogang Huang Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[23/1897, 24/1879, 24/658, 24/1884]. SP result: No objection.

## Slide 150: Motion 334 (MAC)
Move to add to the TGbn SFD the following:
11bn defines a mechanism for dynamic bandwidth expansion (DBE) that enables a UHR AP to modify (expand/reset) its Dynamic UHR operating BSS bandwidth for UHR STAs that support the DBE operation
  The dynamic bandwidth change is signaled using management frames and is announced for multiple beacon intervals in advance, and the AP shall stay on the expanded bandwidth until a subsequent dynamic bandwidth change occurs
  The primary channel does not change as part of the dynamic BW expansion.
  TBD on DBE signaling details
Move: Binita Gupta Second: Kumail Haider
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/88, 11-24/815]. SP result: No objection.

## Slide 151: Motion 335 (MAC)
Move to add to the TGbn SFD the following:
After the roaming preparation request/response exchange, there is an indicated timeout
  If there is no successful transmission of the roaming execution request frame from the non-AP MLD within the indicated timeout, then the target AP MLD may delete all preparation information related to the non-AP MLD
    NOTE - This includes security context, i.e., new derived TK if new TK is derived
  if the roaming preparation request for a target AP MLD is accepted in the roaming preparation response, and the non-AP MLD sends a following roaming execution request for the target AP MLD received within the indicated timeout, then the roaming execution request shall be accepted in the roaming execution response
  TBD on indication of the timeout
After the latest roaming preparation request/response exchange, the setup links with the target AP MLD is not modified until after the roaming execution request/response exchange is finished.
Move: Po-Kai Huang Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1874r1, 24/1883, 24/1884, 25/385r1, 25/388r0, 25/390r0, 25/391r0, 24/656]. SP result: No objection

## Slide 152: Motion 336 (MAC)
Move to add to the TGbn SFD the following:
There is only one target AP MLD indicated in the roaming preparation request frame from a non-AP MLD.
Move: Po-Kai Huang Second: Jarkko Kneckt
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1874r1, 24/1883, 24/1884, 24/656]. SP result: No objection

## Slide 153: Motion 337 (MAC)
Move to add to the TGbn SFD the following:
The roaming preparation request frame includes Listen Interval field of the non-AP MLD for the target AP MLD
The roaming execution request frame includes Listen Interval field of the non-AP MLD for the target AP MLD if there is no roaming preparation request/response exchange beforehand
After the roaming execution request/response exchange with the current AP MLD, the non-AP MLD is by default in power save mode for all the setup links with the target AP MLD
After the roaming execution request/response exchange with the current AP MLD, during the TBD period to receive DL data from the current AP MLD, the non-AP MLD is not required to listen to any Beacon frames of the APs affiliated with the target AP MLD.
Move: Po-Kai Huang Second: Giovanni Chisci
Discussion: None
Result: Approved with unanimous consent.
Reference docs:[24/1874r1, 24/1883, 24/1884]. SP result: No objection

## Slide 154: Motion 338 (MAC)
Move to add to the TGbn SFD the following:
After the roaming execution request/response exchange with the current AP MLD, the TBD period to receive DL data from the current AP MLD ends after the indicated timeout in the roaming execution response.
Move: Po-Kai Huang Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1874r1, 24/1883, 24/1884]. SP result: No objection

## Slide 155: Motion 339 (MAC)
Move to add to the TGbn SFD the following:
11bn defines CTS as Defer Signal to start protected short contention for the pending LL data
Move: Dmitry Akhmetov Second: Jay Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1918r1]. SP result: 99Y, 18N, 51A.

## Slide 156: Motion 340 (MAC)
Move to add to the TGbn SFD the following:
TGbn defines the reference value for the Protected Duration of the protected short contention
  The default value is equal to AIFSN[2] + 7 slots (97 us)
  The Defer Signal frame carry that Protected Duration in the Duration field
  UHR AP may advertise values other than default
Move: Dmitry Akhmetov Second: Kiseon Ryu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1918r1]. SP result: 101Y, 15N, 49A

## Slide 157: Motion 341 (MAC)
Move to add to the TGbn SFD the following:
Define default parameters for P-EDCA for AC_VO to be used during protected short contention period as follows:
  P-EDCA CWmin=7, P-EDCA CWmax=7
  P-EDCA AIFSN=2
  An UHR AP may advertise values other than default
Move: Dmitry Akhmetov Second: Mohamed Abouelseoud
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1918r1]. SP result: No objection.

## Slide 158: Motion 342 (MAC)
Move to add to the TGbn SFD the following:
Established coordination between two APs can be terminated by an explicit teardown performed by one of the two APs.
Move: Shawn Kim Second: Kiseon Ryu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1849r1, 24/1220]. SP result: No objection.

## Slide 159: Motion 343 (MAC)
Move to add to the TGbn SFD the following:
11bn allows a Multi-STA BA frame to include both Block Ack Bitmap and Feedback information if the preceding PPDU includes QoS Data frame(s) that solicit an immediate response (e.g., Ack or BlockAck context) and the non-AP STA is operating in a mode that allows inclusion of feedback information(e.g. DUO mode).
Move: Hongwon Lee Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1490r2]. SP result: No objection.

## Slide 160: Motion 344 (MAC)
Move to add to the TGbn SFD the following:
TGbn does not define a requirement for a UHR AP to report non-collocated APs in the Reduced Neighbor Report element that is carried in its Beacon and FILS Discovery frames
Move: Abhishek Patil Second: Pooya Monajemi
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1884r1, 24/1889]. SP result: No objection.

## Slide 161: Motion 345 (MAC)
Move to add to the TGbn SFD the following:
The Link Reconfiguration Request/Response frames (with necessary extensions) shall be used as the roaming preparation Request/Response frames
  The Per-STA Profile subelement of the Multi-Link shall be present and each corresponds to the requested/accepted links
  TBD signaling to indicate that the request is to initiate roaming preparation
  Other extension (if needed) TBD
Move: Abhishek Patil Second: Giovanni Chisci
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1884r1, 24/656, 25/385, 25/384, 25/386, 25/388, 25/390, 25/391, 25/393, 24/1883, 24/1889]. SP result: No objection.

## Slide 162: Motion 346 (MAC)
Move to add to the TGbn SFD the following:
The Link Reconfiguration Request/Response frames (with necessary extensions) shall be used as the roaming execution Request/Response frames?
  The Per-STA Profile subelement of Multi-Link element is not required to be present.
  TBD signaling to indicate that the request is to initiate roaming execution transition
  Other extension (if needed) TBD
Move: Abhishek Patil Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1884r1, 24/1889, 24/1883, 24/656, 25/385, 25/384, 25/386, 25/388, 25/390, 25/391, 25/393]. SP result: 69Y 17N 45A.

## Slide 163: Motion 347 (PDT-MAC)
Move to incorporate the proposed text changes in 11-25/0244r5 to the latest TGbn draft
Move: Jay Yang Second: Giovanni Chisci
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0244r5]. SP result: No objection.

## Slide 164: Motion 348 (MAC)
Move to add to the TGbn SFD the following:
TGbn allows a second mode for security in roaming (in addition to the first mode with single TK used across all AP MLDs of the SMD) where a non-AP MLD can derive a new TK under the same PTKSA with the target AP MLD
  The new TK is derived as part of the single PTKSA
  The PN is maintained per PTKSA: The new TK negotiated with the target AP MLD shares the same PN space with the TK of the current AP MLD (PN is monotonically increasing)
Move: Giovanni Chisci Second: Chittabrata Ghosh
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1882, 24/1883, 24/1884, 24/1874]. SP result: No objection.

## Slide 165: Motion 349 (MAC)
Move to add to the TGbn SFD the following:
During the TBD time for retrieving DL from the Current AP MLD, the non-AP MLD may provide an indication to the Target AP MLD that the TBD time for DL retrieval is early-terminated before the TBD time
TBD signaling of the indication
Move: Giovanni Chisci Second: Pooya Monajemi
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1882, 24/1883, 24/1884, 24/1898, 24/1874, 24/1857, 24/2147r1]. SP result: No objection.

## Slide 166: Motion 350 (MAC)
Move to add to the TGbn SFD the following:
During a roaming transition, the current AP MLD shall be capable of signaling termination of downlink data transmission to the non-AP MLD before the transient TBD time period to receive buffered downlink data from current AP MLD period ends
  Signaling TBD
NOTE: AP sends the indication when there is no more pending DL data (all TIDs). TBD other conditions.
Move: Pooya Monajemi Second: Tuncer Baykas
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1898r1, 11-24/1883r4, 11-24/1874r1, 24/2147r1, 24/1857r3]. SP result: No objection.

## Slide 167: Motion 351 (MAC)
Move to add to the TGbn SFD the following:
In the seamless roaming procedure, non-AP MLD can request not to transfer from the current AP MLD to the target AP MLD any of the following as part of the context transfer
  The next SN for existing DL BA agreements of all TIDs
  The latest SN that has been passed up for existing UL BA agreements of all TIDs
Move: Pooya Monajemi Second: Giovanni Chisci
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1898r1, 11-24/1874r1, 24/1883, 24/1884 ]. SP result: No objection.

## Slide 168: Motion 352 (MAC)
Move to add to the TGbn SFD the following:
11bn defines an SMD element that provides identification for the SMD and SMD level capabilities for a seamless mobility domain
  The SMD element is advertised in Probe Response frames
  The SMD element is included in Authentication frame when performing authentication with an SMD
  The SMD element is included in (Re)Association Request & Response frames when performing initial association with the SMD-ME
Move: Binita Gupta Second: Stephen Rodriguez
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/656, 24/1884, 24/1889]. SP result: No objection.

## Slide 169: Motion 353 (MAC)
Move to add to the TGbn SFD the following:
11bn enhances Neighbor Report element to provide SMD related information
  Add a ‘Same SMD’ indication in the BSSID Information in the NR element, to signal whether the reported neighboring AP is part of the same SMD as the reporting AP
  Allow including the SMD element as a subelement in the Optional Subelements of the Neighbor Report element, when reported neighboring AP is not part of the same SMD
Move: Binita Gupta Second: Tuncer Baykas
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/656, 24/1884, 24/1889]. SP result: No objection.

## Slide 170: Motion 354 (MAC)
Move to add to the TGbn SFD the following:
Enable the following contexts to be transferred to target AP MLD to preserve the data exchange context for the non-AP MLD
Block Ack Parameters and Block Ack Timeout Value indicated by the non-AP MLD for existing BA agreement of a TID
Next SN to be assigned for DL individually addressed data frame of each TID
Latest duplicate receiver cache for TID without BA agreement
latest SN that has been pass up for TID with UL BA agreement
Starting PN to be assigned for DL individually addressed frame by the target AP MLD
Initial value to be used by each replay counter of the target AP MLD for UL individually addressed frame
WinStartO of an existing DL BA agreement
  So that the target AP MLD does not exceed reordering buffer window of the non-AP MLD
TBD for other contexts
Move: Po-Kai Huang Second: Giovanni Chisci
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1874r1, 23/1884, 24/1883, 24/1884, 25/327, 24/656, 11-24/0083]. SP result: No objection.

## Slide 171: Motion 355 (MAC)
Move to add to the TGbn SFD the following:
Do you agree to the following conditions for transmitting unsolicited unavailability indications that can be sent by a non-AP as a TXOP holder in a BSRP GI3 trigger frame:
  No restriction when sent with QoS data transmitted in the TXOP
  When sent without QoS data transmitted in the TXOP, not more than MaxStandaloneDuoBSRP number of times every beacon interval where MaxStandaloneDuoBSRP is a non-zero value and part of the DUO parameter set indicated by the AP
  Note: BSRP GI3 Trigger frame is a BSRP Trigger frame that solicits an M-BA response that is carried in non-HT (dup) PPDU format
Move: Sindhu Verma Second: Laurent Cariou
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1559r1]. SP result: No objection.

## Slide 172: Motion 356 (MAC)
Move to add to the TGbn SFD the following:
TBD request frame initiating roaming preparation carries the Diffie-Hellman Parameter element of the non-AP MLD when new PTK is derived
TBD response frame during roaming preparation carries Diffie-Hellman Parameter element generated by the target AP MLD when new PTK is derived
Non-AP MLD and the target AP MLD derive the PTK based on the shared PMK and DHss in TBD request and TBD response frames
Note: Details of the algorithm used to derive the DHss are TBD
Move: Chittabrata Ghosh Second: Thomas Derham
Discussion: Some discussion. Recorded vote.
Preliminary Result: 123Y, 17N, 102A (pass)
Result: 122Y, 17N, 96A (pass)
Reference docs:[24/1882, 24/1883]. SP result: No objection.

## Slide 173: Motion 357 (PDT-MAC)
Move to incorporate the proposed text changes in 11-25/454r6 to the latest TGbn draft
Move: Morteza Mehrnoush Second: Vishnu Ratnam
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/454r6]. SP result: No objection.

## Slide 174: Motion 358 (MAC)
Move to add to the TGbn SFD the following:
TGbn defines new actions for Public Action frames for MAPC communications such as discovery and negotiations
  An action is defined for MAPC Discovery
  An action is defined for MAPC Negotiation Request
  An action is defined for MAPC Negotiation Response
  Others are TBD
Move: Giovanni Chisci Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1220, 24/0407r0]. SP result: No objection

## Slide 175: Motion 359 (MAC)
Move to add to the TGbn SFD the following:
When an AP use Management frames to discover the capabilities and/or parameters of individual M-AP coordination schemes, the AP shall use the defined MAPC Public Action frame with the following setting:
  The action field is set to MAPC Discovery
Move: Giovanni Chisci Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1220]. SP result: No objection

## Slide 176: Motion 360 (MAC)
Move to add to the TGbn SFD the following:
When an AP (AP1) uses an individually addressed Management frame to initiate a negotiation to establish agreements for M-AP coordination schemes (if enabled by another AP (AP2)), the AP (AP1) shall use the defined MAPC Public Action frame with the following setting:
  The action field is set to MAPC Negotiation Request
  If new negotiations are disabled by another AP (AP2) the AP (AP1) shall not send a negotiation request to the other AP (AP2)
  TBD details of ‘new negotiations disabled’
Move: Giovanni Chisci Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1220, 25/0378r0]. SP result: No objection

## Slide 177: Motion 361 (MAC)
Move to add to the TGbn SFD the following:
When an AP (AP2) receives an individually addressed Management frame that initiates a negotiation to establish agreements for M-AP coordination schemes, the AP (AP2) shall respond by using the defined MAPC Public Action frame with the following setting, if negotiations are enabled:
  The Action field is set to MAPC Negotiation Response
Move: Giovanni Chisci Second: Brian Hart
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1220]. SP result: No objection

## Slide 178: Motion 362 (MAC)
Move to add to the TGbn SFD the following:
A Co-RTWT Requesting AP shall include one or more Co-RTWT Parameter Set fields corresponding to each requested R-TWT schedule in the TBD individually addressed Management frame used for the request to the Co-RTWT Responding AP. The Co-RTWT Parameter Set field includes the following:
  Target Wake Time field
  Broadcast TWT ID field
  Broadcast TWT Persistence
  TWT Wake Interval Mantissa
  TWT Wake Interval Exponent
  Nominal Minimum TWT Wake Duration
  TBD other fields
Move: Giovanni Chisci Second: Kumail Haider
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1220, 23/1887r1, 24/160r1, 24/908r0, 24/0407r0]. SP result: 97 Y / 28 N / 66 A

## Slide 179: Motion 363 (MAC)
Move to add to the TGbn SFD the following:
The Co-TDMA sharing AP and the Co-TDMA coordinated AP shall have the same primary 20 MHz channel.
Move: Abhishek Patil Second: Gaurang Naik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-23/1895]. SP result: No objection.

## Slide 180: Motion 364 (MAC)
Move to add to the TGbn SFD the following:
A serving AP MLD can use the BTM procedure with update(s) (if required) to recommend one or more candidate target AP MLDs within the UHR seamless roaming mobility domain to a non-AP MLD for roaming.
  Note – An AP can transmit the BTM Request frame unsolicited or as a response to the BTM Query frame from a non-AP MLD.
TBD – detailed information to be carried
Move: Liwen Chu Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1889r1, 24/1883, 24/658, 24/1884]. SP result: No objection.

## Slide 181: Motion 365 (MAC)
Move to add to the TGbn SFD the following:
An AP shall not allow the use of NPCA within its BSS if the BSS operating bandwidth is less than or equal to 40 MHz.
Move: Liwen Chu Second: Gaurang Naik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1892r2]. SP result: No objection.

## Slide 182: Motion 366 (MAC)
Move to add to the TGbn SFD the following:
If a TXOP on the NPCA Primary channel overlaps with the TBTT, the AP shall not transmit the Beacon frame or group addressed frames until it switches back to the BSS Primary channel.
NOTE – The NPCA AP and non-AP STA participating in frame exchanges must not switch back to the BSS Primary channel at the TBTT and can continue operating on NPCA Primary until the OBSS transmission ends on BSS Primary channel. In such cases, the group addressed frame will be buffered and delivered immediately following the next DTIM Beacon, unless explicitly specified otherwise.
Move: Liwen Chu Second: Gaurang Naik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1891r2]. SP result: No objection.

## Slide 183: Motion 367 (MAC)
Move to amend the TGbn SFD as follows:
TGbn defines or improves an existing mechanism so that a non-AP STA that is a TXOP responder can indicate its buffered low latency LL traffic needs (for traffic from the TxOP TXOP responder to the TxOP TXOP Holder) in a control response frame Multi-STA Block Ack. The TXOP holder should consider the indication in determining subsequent actions. Subsequent actions related to this indication are out of the scope of the standard.
  Note: whether an AP can Indicate its low latency needs is TBD
  The Low Latency Indication is included in the Feedback field of the Feedback Per AID TID Info field (the one that carries control feedback).
  The Feedback Type field is set to 1
    Note: Feedback Type field set to 0 is used for DUO feedback
  TBD bit(s) in the Feedback field is(are) defined to provide the low latency need(s)
Move: Liwen Chu Second: Mohamed Abouelseoud
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0421r0, 25/439]. SP result: No objection.

## Slide 184: Motion 368 (MAC)
Move to add to the TGbn SFD the following:
For seamless roaming, a non-AP MLD is allowed to request preparing more than one candidate target AP MLDs in an SMD during the roaming preparation phase
  Preparation with multiple AP MLDs is performed using a separate roaming preparation request for each AP MLD
  If successful roaming preparation was performed with multiple candidate target AP MLDs, then the non-AP MLD shall attempt roaming execution with only one of those target AP MLDs at a time.
    Retries with other target AP MLDs are permitted for roaming execution
  TBD on policy indication from the AP on multiple target AP MLDs preparation
Move: Binita Gupta Second: Giovanni Chisci
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0656, 24/1883, 24/1884, 24/1857r3]. SP result: No objection.

## Slide 185: Motion 369 (MAC)
Move to add to the TGbn SFD the following:
For a Seamless Mobility Domain (SMD), the SMD and the 802.1X Authenticator component in the corresponding SMD-ME are uniquely identified by an SMD Identifier
  The SMD Identifier is in the format of a 48-bit MAC address
  The SMD Identifier is used in establishing single PMKSA and PTKSA for a non-AP MLD that associates with the SMD-ME
Move: Binita Gupta Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/0656, 24/1894, 23/1937, 24/1889, 24/1883, 24/1884, 24/1882]. SP result: No objection.

## Slide 186: Motion 370 (MAC)
Move to add to the TGbn SFD the following:
For the following features, if an AP supports the feature, then the AP shall accept a request from an associated STA to enable or disable the feature on its (STA) side
  Dynamic unavailability operation
  Dynamic power save
Move: Laurent Cariou Second: Liuming Lu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1226r0, 24/1261r3 ]. SP result: No objection.

## Slide 187: Motion 371 (PHY)
Move to add to the TGbn SFD the following:
The following information shall be exchanged before COBF PPDU:
  Min-Nsym and Max-Nsym indication about the COBF PPDU length sent in the COBF invite frame
  Suggested Nsym indication in the COBF response frame from shared AP
    Sharing AP is allowed to ignore the shared AP’s suggestion
    Suggested value shall not be smaller than the Min-Nsym value from sharing AP
Move: Sameer Vermani Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/381r1, ]. SP result: No objection.

## Slide 188: Motions on march 13th , PM2

## Slide 189: Motion 372 (Joint)
Move to add to the TGbn SFD the following:
UHR Co-BF sounding reuses EHT Compressed Beamforming/CQI report
Move: You-Wei Chen Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/81r0 ]. SP result: No objection.

## Slide 190: Motion 373 (Joint)
Move to add to the TGbn SFD the following:
EHT Compressed Beamforming/CQI report containing UHR Co-BF sounding feedback shall be carried in EHT TB PPDU
Move: You-Wei Chen Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/81r0 ]. SP result: No objection.

## Slide 191: Motion 374 (Joint)
Move to add to the TGbn SFD the following:
UHR Co-BF sounding reuses the EHT sounding segmentation and retransmission of 11be feedback segments rules.
Move: You-Wei Chen Second: Jay Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/81r0 ]. SP result: No objection.

## Slide 192: Motion 375 (Joint)
Move to add to the TGbn SFD the following:
UHR Co-BF sounding uses EHT MU full bandwidth feedback
Move: You-Wei Chen Second: Aiguo Yan
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[25/81r0 ]. SP result: No objection.

## Slide 193: Motion 376 (PDT-Joint)
Move to incorporate the proposed text changes in 11-24/0414r0 to the latest TGbn draft
Move: You-Wei Chen Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs: [11-24/0414r0]. SP result: No objection.

## Slide 194: Motion 377 (MAC)
Move to the TGbn SFD as follows:
Unavailability Target Start Time is indicated using 9 bits with a granularity of 64us
  This subfield contains a partial TSF time at which the unavailability event is expected to start
  Except that this subfield is reserved (i.e., invalid and to be ignored by the recipient) if the Unavailability Duration subfield is equal to 0
Unavailability Duration is indicated using 9 bits with a granularity of 64us
  This subfield is set to the estimated duration, in units of 64 microseconds, of the unavailability event except that
  The value 0 indicates that the STA is available
  The value 511 indicates that the STA is unavailable for an indefinite duration of time
  The STA shall not use the value 511 unless the unavailability duration is unknown
A non-AP STA that intends to transition to available state shall indicate to its associated AP that it transitions from being unavailable to being available by sending a BSRP GI3 Trigger frame with the Unavailability Duration field set to 0.
Move: Sherief Helwa Second: Qi Wang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1558, 25/430, 25/0063]. SP result: No objection.

## Slide 195: Motion 378 (MAC)
Move to add to the TGbn SFD the following:
If the SMD is part of an FT mobility domain the following applies
  The single PMKSA to be used in the SMD is the PMK-R1 SA and is bound to the SMD-ME, when the non-AP MLD initially associates with the SMD ME using FT initial MD association.
Move: Jarkko Kneckt Second: Yanjun Sun
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[???]. SP result: No objection.

## Slide 196: Motion 379
Move to instruct the TGbn Editor to create IEEE802.11bn D0.2 draft after incorporating the approved proposed draft changes as specified in all the applicable Motions from 296 to 378 (motions with numerical values).
Move: Abhishek Patil Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.

## Slide 197: TGbn MAC/PHY July Ad-Hoc
Approve a TGbn MAC/PHY (mixed mode) ad-hoc meeting on 23 to 25 July 2025, in TBD location, Europe for the purpose of TGbn comment resolution and consideration of document submissions
Move: Kumail Haider Second: Rubayet Shafin
Preliminary Result: 124Y, 7N, 44A (pass)
Result: 120Y, 7N, 43A (pass).

## Slide 198: Motions on April 24th

## Slide 199: Motion 380 (PHY)
Move to approve resolutions to the CIDs (41C):
1366, 1367, 2285 in 11-5/0505r0 [3 CIDs]
5, 6, 8, 321, 937, 938, 939, 940, 1163 in 11-25/0441r2 [9 CIDs]
2728, 3728, 2038, 2231, 288, 289, 456, 1070, 1071, 1102, 1368, 2039, 2040, 2232, 2550, 2729, 3291, 3529, 290, 2041, 2233, 2551, 2552, 3292, 615, 2042, 2703, 2730, 2731 in 11-25/0509r2 [29 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Alice Chen Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of March 24, 2025.

## Slide 200: Motion 381 (PHY)
Move to approve resolutions to the CIDs (70C):
72, 212, 609, 907, 957, 1193, 1519, 1933, 1938, 2337, 2785, 3553, 3554 in 11-25/0546r1 [13 CIDs]
110, 276, 397, 398, 461, 462, 472, 712, 716, 854, 860, 1032, 1034, 1328, 1672, 1673, 1674 in 11-25/0506r1 [17 CIDs]
1155 in 11-25/0518r1 & 595, 1172, 1590, 1748, 2304 in 11-25/0520r1 [6 CIDs]
48, 1621, 49, 50, 51, 2178, 3237, 211, 307, 2179, 575, 2269, 3533, 3555 in 11-25/0523r0 [14 CIDs]
310, 2286, 311 in 11-25/0548r0 [3 CIDs]
312, 2773, 935*, 2753, 584, 1090, 1346, 3472, 936, 2287, 2755, 3473, 3561 in 11-25/0549r0 [13 CIDs]
305, 1122, 1758, 2257 in 11-25/0522r0 [4 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Eunsung Park Second: Ross. J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of March 31, 2025.
*Typo identified by TGbn officers. Was 395 and was supposed to be 935. Fixed. Confirmed.

## Slide 201: Motion 382 (PHY)
Move to approve resolutions to the CIDs (50C):
31, 32, 33, 117, 180, 345, 346, 347, 766, 950, 1180, 1181, 1182, 1356, 1358, 1359, 1360, 1361, 1362, 1363, 1364, 1365, 1644, 1761, 2072, 2073, 2074, 2314, 2315, 2318, 2320, 2321, 2702, 2781, 2782, 2783, 3545, 3546, 3558 in 11-25/0564r3 [39 CIDs]
1099, 1192, 1655, 2335, 3312, 3313 in 11-25/0584r1 [6 CIDs]
339, 943, 944, 2184, 2303 in 11-25/0524r0 [5 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Juan Fang Second: Ross. J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of April 3, 2025.

## Slide 202: Motion 383 (PHY)
Move to approve resolutions to the CIDs (84C):
2732, 2234, 2043, 616, 1369, 2044, 2235, 118, 136, 275, 291, 561, 760, 1072, 1103, 1370, 1753, 1928, 1973, 2045, 2046, 2236, 2437, 2704, 2733, 3293, 3530, 3967, 3294, 2560, 562, 1104, 1105, 2734, 3531, 138, 2735 in 11-25/0577r2 [37 CIDs]
69, 1191, 1669, 1763 in 11-25/0580r2 & 1628 in 11-25/0581r1 & 1635 in 11-25/0582r2 [6 CIDs]
336, 340, 591, 596, 1171, 1173, 2299, 2305, 2307, 2777, 2778, 3524, 3525, 3559 in 11-25/0525r1 [14 CIDs]
337, 338, 592, 593, 594, 1641, 1898, 2183, 2300, 2301, 2302, 2306, 3523 in 11-25/0547r0 [13 CIDs]
1643, 599, 949, 1962, 2312, 1961, 600, 1178, 343, 1179, 2313, 2779*, 2780 in 25/0550r0 & 1631 in 25/0548r1 [14 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Dongguk Lim Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of April 7, 2025.
*2779 added last minute as it was accidentally missed.

## Slide 203: Motion 384 (PHY)
Move to approve resolutions to the CIDs [64C]:
2, 3, 83, 314, 316, 317, 585, 586, 1157, 1158, 1159, 1160, 1347, 1587, 2701, 2828, 3303, 3305 in 11-25/0603r0 [18 CIDs]
1675, 1676, 1677, 1678, 1679, 1979, 1980, 2547, 2826, 2829, 2835, 2853, 2910, 2911, 2917, 2918, 2957 in 11-25/0556r1 [17 CIDs]
1762, 2316, 2317, 2319, 2787, 29, 1357, 2788, 30, 1183, 2322 in 11-25/0608r2 [11 CIDs]
1345, 2443 in 25/0623r1 & 610, 958, 960, 1194, 3247, 3248 in 11-25/0585r1 [8 CIDs]
306, 1020, 1771, 1772, 2176, 2177, 2258, 2706, 2723, 2724 in 11-25/0570r1 [10 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Alice Chen Second: Ross. J. Yu
Discussion: Some clarificatory questions as to whether 570r1 or r3. It is r1.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of April 10, 2025.

## Slide 204: Motion 385 (MAC)
Move to approve resolutions to the CIDs (22C):
3848, 3852, 3853, 3859, 144 in 11-25/0551r3 [5 CIDs]
280 401 402 463 464 848 895 1459 1517 1966 1967 2572 2619 2660 2845 2846 2852 in 11-25/0527r2 [17 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Abhishek Patil Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of April 7, 2025.

## Slide 205: Motion 386 (MAC)
Move to approve resolutions to the CIDs (1C):
1378 in 11-25/0479r3 [1 CID]*
and incorporate the text changes into the latest TGbn draft.
Move: Dibakar Das Second: Dmitry Akhmetov
Discussion: Some discussion.
Result:
Defer. Target May F2F.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of April 7, 2025.
* SP result for CID 1378 was 43Y/13N/29A.

## Slide 206: Motion 387 (Withdrawal)
Move to approve “Rejected” resolutions to the CIDs (42C):
625, 626, 627, 628, 629, 630, 631, 632, 633, 634, 635, 636, 637, 638, 639, 640, 641, 642, 643, 644, 645, 646, 647, 648, 649, 650, 651, 652, 653, 654, 655, 656, 657, 658, 659, 660, 661, 662, 663, 664, 665, 666 [42 CIDs]
With the following rejection reason: “The commenter has withdrawn the comment”.
Move: Stephen McCann Second: Bin Tian
Discussion: None.
Result: Approved with unanimous consent.

## Slide 207: Motion 388 (MAC)
Move to add to the TGbn SFD the following for DSO:
For a non-AP STA, the channel with bandwidth equaling its operating bandwidth and including the BSS primary channel is referred to as primary sub-band
For a non-AP STA, a channel with the bandwidth equaling its operating bandwidth outside of its primary sub-band where it can be allocated resources by the AP is referred to as DSO sub-band for that non-AP STA
A non-AP STA that supports this mechanism is referred to as a DSO STA
Move: Morteza Mehrnoush Second: Yanjun Sun
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-24/1589, 11-22/2204, 11-23/2141, 11-23/2027, 11-23/843, 11-23/1496, 11-24/591, 11-23/1892, 11-23/1913, 11-23/1935, 11-24/1553, 11-24/1564, 11-24/1588, 11-24/2141, 11-24/1587]. SP result: No objection.

## Slide 208: Motions on May 15th, 2025 AM2

## Slide 209: Motion 389 (PHY)
Move to approve resolutions to the CIDs (15C):
1123, 1124, 2260, 2264 in 11-25/0612r1 [4 CIDs]
356, 357, 2180, 3300, 3562, 3566, 3671 in 11-25/0643r2 [7 CIDs]
1653, 3371, 1661, 1662 in 11-25/0644r2 [4 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Dongguk Lim Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of April 14, 2025.
*Changed to r1 per Eunsung’s request.

## Slide 210: Motion 390 (MAC)
Move to approve resolutions to the CIDs (54C):
111, 187, 200, 218, 219, 621, 622, 623, 670, 671, 672, 676, 679, 680, 681, 682, 683, 713, 748, 1027, 1468, 1469, 1527, 1698, 1706, 1707, 1708, 1709, 1738, 1863, 1904, 2445, 2464, 3323, 3324, 3325, 3326, 3328, 3329, 3330, 3331, 3332, 3334, 3382, 3383, 3384, 3440, 3599, 3788, 3875, 3878, 3879, 3880, 3882 in 11-25/0521r2 [54 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Rethna Pulikkoonattu Second: Yusuke Asai
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of April 14, 2025.

## Slide 211: Motion 391 (MAC)
Move to approve resolutions to the CIDs (27C):
175, 195, 1537, 1538, 1684, 1685, 2080, 2111, 2581, 2582, 2583, 2584, 2585, 2635, 2636, 2637, 2638, 2827, 2975, 2976, 2977, 3165, 3279, 3437, 3577, 3648, 3870 in 11-25/0513r4* [27 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Frank Hsu Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of April 17, 2025.
* SP Result: 47Y, 8N, 33A.

## Slide 212: Motion 392 (PHY)
Move to approve resolutions to the CIDs[69C]:
1630 in 11-25/0644r3 & 1624 in 11-25/0658r0 [2 CIDs]
4, 7, 179, 313, 318, 319, 587, 588, 1156, 1161, 1162, 2707, 3506 in 11-25/0588r2 [13 CIDs]
574, 889, 2259, 2261, 2262, 2263, 2265 in 11-25/0570r3 [7 CIDs]
297, 442, 444, 445, 566, 567, 568, 569, 1118, 1582, 1755, 1756, 1757, 2173, 2245, 2246, 2247, 2248, 2249, 2250, 2251, 2561, 2562, 3509, 3510, 3511, 3512, 3514, 3516 in 11-25/0656r1 [29 CIDs]
71, 369, 908, 1836, 2444, 1837, 1939, 1940, 1941, 1942, 2336, 3552, 3748, 3903, 3904, 3906, 3907, 3968 in 11-25/0663r2 [18 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Alice Chen Second: Rethna Pulikkoonattu
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of April 21st, 2025.

## Slide 213: Motion 393 (MAC)
Move to approve resolutions to the CIDs (2C):
174, 3667 in 11-25/0661r2* [2 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Kumail Haider Second: Rethna Pulikkoonattu
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of April 28, 2025.
* Ran SP on r1 but header of doc had a typo, which is fixed in r2.

## Slide 214: Motion 394 (PHY)
Move to approve resolutions to the CIDs (14C):
2689 in 11-25/0570r4 [1 CID]
194, 323, 324, 589, 590, 951, 963, 1164, 1165, 1520, 1531, 2069, 2774 in 11-25/0601r2 [13 CID]
and incorporate the text changes into the latest TGbn draft.
Move: Dongguk Lim Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of April 28, 2025.

## Slide 215: Motion 395 (PHY)
Move to accept the text proposed in 11-25/0695r1 as draft text for the UHR transmit procedure to be included in the next revision of the 802.11bn Draft:
Move: Dongguk Lim Second: Yusuke Asai
Discussion: None.
Result: Approved with unanimous consent.
Note: These are PDT documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of April 28, 2025.

## Slide 216: Motion 396 (PHY)
Move to approve resolutions to the CIDs [105 CIDs]:
62, 63, 64, 182, 210, 272, 549, 951, 963, 1080, 1126, 1334, 2065, 2066, 2266, 2267, 2268, 2350, 2439, 2756, 2757, 2758, 2759, 2760, 2761, 3298, 3299, 3540, 3547 in 11-25/0602r2 [29 CIDs]
1146, 1147, 2768, 1148, 931, 2275, 28, 761 in 11-25/0659r0 [8 CIDs]
27, 581, 582, 947, 948, 1086, 1087, 1138, 1139, 1140, 1141, 1142, 1143, 1144, 1145, 1341 1899, 1975, 2274, 2765, 2766, 2767, 3241, 3242 in 11-25/0672r3 [24 CIDs]
3751 in 11-25/0682r0 & 3905 in 11-25/0702r0 & 1617 in 25/0711r0 & 953, 954, 1656 in 11-25/0677r1 [6 CIDs]
324, 325, 326, 364, 942, 1636, 2288, 3306, 3307, 3497, 3498, 3499, 3500, 3745 in 11-25/0679r2 [14 CIDs]
41, 42, 43, 44, 45, 46, 332, 377, 441, 1094, 1170, 1639, 1640, 1956, 2296, 2297, 2298, 3244, 3311, 3502, 3503, 3504 in 11-25/0678r3* [22 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Dongguk Lim Second: Genadiy Tsodik
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc slot of Monday PM1, May 12, 2025.
*Updated to r3 on the fly.

## Slide 217: Motion 397 (PHY-PDT)
Move to incorporate into the latest TGbn draft the proposed text changes from the following documents:
11-25/0696r2,
11-25/0701r2,
11-24/2021r1
Move: Genadiy Tsodik Second: Ron Porat
Discussion: None.
Result: Approved with unanimous consent.
Note: These are proposed draft text documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc slot of Monday PM1, May 12, 2025.

## Slide 218: Motion 398 (Joint)
Move to approve resolutions to the CIDs (2C):
3159, 3160 in 11-25/0652r0 [2 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Yusuke Asai Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the Joint meeting slot of Monday AM2, May 12, 2025.

## Slide 219: Motion 399 (MAC)
Move to approve resolutions to the CIDs (97C):
108, 736, 759, 1614, 1740, 1796, 1848, 2012, 2205, 2534, 2999, 3365, 3909, 3005, 188, 507, 2000, 2352, 2001, 2356, 2533, 3589, 3920, 3912, 2002, 2003, 2004, 2353, 2006, 2014, 493, 2007, 2009, 2715, 3457, 3892, 3921, 499, 514, 515, 2790, 516, 517, 3922, 511, 2017, 2018, 3260, 3458, 3929, 518, 519, 520, 163, 3910, 3006, 3367, 522, 3590, 524, 525, 526, 527, 528, 530, 533, 2016, 3931, 154, 166, 490, 3470, 2005, 3459, 2186, 1811, 2402, 3002, 3003, 3386, 3913, 521, 2010, 3585, 2019, 3369, 1066, 3001, 3366, 3454, 3619, 489, 3461, 3891, 1022, 3927, 3004 in 11-25/0566r10 [97 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Duncan Ho Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc slot of Tuesday AM1, May 13, 2025.

## Slide 220: Motion 400 (MAC)
Move to approve resolutions to the CIDs (104C):
148, 152, 153, 160, 161, 181, 669, 775, 1318, 1319, 1320, 1324, 1395, 1398, 1399, 1428, 1491, 1494, 1739, 1788, 1789, 2466, 3254, 3438, 3606, 3779, 3780, 3781 in 11-25/0599r13 [28 CIDs]
202, 277, 439, 714, 742, 780, 781, 830, 832, 880, 901, 994, 1050, 1321, 1322, 1381, 1408, 1409, 1410, 1411, 1412, 1413, 1414, 1415, 1416, 1417, 1418, 1419, 1420, 1435, 1436, 1439, 1562, 1599, 1715, 1716, 1717, 1718, 1719, 1720, 1721, 1806, 1832, 1867, 1910, 2117, 2118, 2119, 2519, 2674, 3175, 3176, 3177, 3178, 3179, 3180, 3181, 3257, 3258, 3259, 3420, 3445, 3446, 3447, 3448, 3449, 3450, 3582, 3710, 3795, 3854, 3884 ,3885, 3886, 3887, 3888 in 11-25/0600r13 [76 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Giovanni Chisci Second: Jay Yang
Discussion: Some discussion.
Preliminary Result: 158Y, 59N, 54A (fails)
Result: 152Y, 56Nm 52A (fails)
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC meeting slot of Tuesday AM2, May 12, 2025.

## Slide 221: Motion 400A (MAC)
Move to approve resolutions to the CIDs (76C):
202, 277, 439, 714, 742, 780, 781, 830, 832, 880, 901, 994, 1050, 1321, 1322, 1381, 1408, 1409, 1410, 1411, 1412, 1413, 1414, 1415, 1416, 1417, 1418, 1419, 1420, 1435, 1436, 1439, 1562, 1599, 1715, 1716, 1717, 1718, 1719, 1720, 1721, 1806, 1832, 1867, 1910, 2117, 2118, 2119, 2519, 2674, 3175, 3176, 3177, 3178, 3179, 3180, 3181, 3257, 3258, 3259, 3420, 3445, 3446, 3447, 3448, 3449, 3450, 3582, 3710, 3795, 3854, 3884 ,3885, 3886, 3887, 3888 in 11-25/0600r13 [76 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Abhishek Patil Second: Rubayet Shafin
Discussion:.
Preliminary Result:
Tabled
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC meeting slot of Tuesday AM2, May 12, 2025.

## Slide 222: Motion 401 (PHY)
Move to approve resolutions to the CIDs (35C):
320, 1348, 1634, 3133 in 11-25/0670r0 & 355, 1948, 1949, 1950 in 11-25/0703r2 [8 CIDs]
284, 1612, 2955, 2956, 3526, 3708 in 11-25/0712r2 [6 CIDs]
301, 302, 303, 304, 448, 449, 450, 451, 1331, 1332, 1333, 1900, 2253, 2650, 2754, 3418, 3518, 3519, 3669, 3670, 3731 in 11-25/0750r1 [21 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Alice Chen Second: Eugene Baik
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY meeting slot of Tuesday AM2, May 12, 2025.

## Slide 223: Motion 402 (MAC)
Move to approve resolutions to the CIDs (9C):
1405, 1467, 1902, 1943, 2102, 2103, 2104 in 11-25/640r3 [7 CIDs]
1406 in 11-25/641r3 [1 CID]
1407 in 11-25/660r2 [1 CID]
and incorporate the text changes into the latest TGbn draft.
Move: SunHee Baek Second: Hong Won Lee
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC meeting slot of Tuesday PM2, May 12, 2025.

## Slide 224: Motion 403 (PHY)
Move to approve resolutions to the CIDs(81C):
3230, 674, 2063, 3231, 1895, 2796, 1896, 2554, 2795, 3232, 1974, 2064, 2810, 3233, 2555, 2556, 1897, 206, 1618, 2811, 124, 2797, 2750, 2705, 3234, 2798, 1958, 1959, 1119, 1120, 945, 3128, 1473, 1474, 2752, 2721, 2805, 2806, 2807, 2566, 1, 1584, 2642, 3235, 3236, 1583, 2563, 2751, 3744 in 11-25/0732r2 [49 CIDs]
583, 933, 1152, 1153, 1343, 1344, 1838, 2068, 2279, 2280, 2281, 2282, 2727, 2770, 2771, 3301, 3548, 3557 in 11-25/0615r0 [18 CIDs]
331, 333, 371, 3310, 1206, 1093, 1169, 1355, 2071, 2295, 3538, 551, 2182, 3539 in 11-25/0731r3* [14 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Oded Redlich Second: Julia Feng
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY meeting slot of Tuesday PM2, May 12, 2025.
*SP was run on 731r3 but no r3 in the server.

## Slide 225: Motion 404 (PHY-PDT)
Move to incorporate into the latest TGbn draft the proposed text changes from the following documents:
11-25/0754r3*,
11-25/0844r0
Move: Youhan Kim Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Note: These are proposed draft text documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc slot of Tuesday ??, May 12, 2025, and Wednesday AM1, May 14, 2025.
*Changed to r3 per Youhan’s request.

## Slide 226: Motion 405 (PHY)
Move to approve resolutions to the CIDs (47C):
65, 1088, 1149, 66, 1150, 1585, 2276, 67, 309, 1089, 1151, 1342, 1586, 2067, 2278, 2277, 68, 3505, 3551, 932, 2769, 3243 in 11-25/0846r1 [22 CIDs]
359, 80, 378, 379, 1100, 1195, 1664, 2338, 81, 379, 358, 361, 3707 in 11-25/0855r0 [13 CIDs]
178, 1121, 1670, 1960, 2722 in 11-25/0902r1 & 296, 926, 1021, 2172, 2800 in 11-25/0914r1 [10 CIDs]
2036 in 11-25/0886r0 & 2034 in 11-25/0804r0* [2 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Rui Cao Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc slot Wednesday AM1, May 14, 2025.
*Changed on the fly.

## Slide 227: Motion 406 (MAC)
Move to approve resolutions to the CIDs (18C):
1240, 1243, 1244, 1246, 1247, 1248, 1249, 1251 in 11-25/0713r7 [8 CIDs]
203, 505, 883, 3935, 3933, 2021, 3466, 720, 882, 3464 in 11-25/0736r8 [10 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Morteza Mehrnoush Second: Pooya Monajemi
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc slot Wednesday AM1, May 14, 2025.

## Slide 228: Motion 407 (PHY)
Move to approve resolutions to the CIDs (64C):
327, 52, 1976, 1977, 1978, 2775, 3536, 36, 116, 130, 1166, 1062, 1352, 2070, 2776, 3308, 3537, 328, 329, 376, 1091, 1167, 1589, 2290, 2291, 3309, 3501 in 11-25/0725r4 [27 CIDs]
114, 1350, 1351, 1588, 1637, 2181, 2289, 35, 440, 1638, 1955 in 11-25/0686r0 [11 CIDs]
353, 354,905,1654, 3753 in 11-25/0778r0 [5 CIDs]
271, 956, 959, 1657, 1658, 3246, 3249 in 11-25/0777r3 & 1625, 1626 in 11-25/0919r0 [9 CIDs]
1471, 3226, 2047, 2048, 2237, 2549, 2559, 2567, 2568, 2569, 2717, 3295 in 11-25/0881r1 [12 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Juan Fang Second: Eugene Baik
Discussion: Some discussion.
Preliminary Result: 124Y, 30N, 100A (passes)
Result: 123Y, 27N, 97A (passes)
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc slot Wednesday AM2, May 14, 2025.

## Slide 229: Motion 408 (PHY)
Move to approve resolutions to the CIDs (182C):
2270, 125, 1335, 1128, 1336, 576, 1129, 1337, 2762, 126, 2271, 1130, 1930, 1081, 2440, 127, 1082, 1131, 1338, 1759, 2763, 1339, 1132, 929, 1340, 577, 578, 1083, 2272, 2764, 308, 2725, 1622, 1133, 3238, 930, 1134, 1135, 579, 2273, 580, 1084, 2726, 1623, 946, 3239, 3240, 1136, 1931, 2441, 1085, 26, 1137, 1932, 2442 in 11-25/0884r3 [55 CIDs]
298, 3513, 3515, 3517, 446, 571, 2175, 299, 2174, 3274, 452, 447, 572 in 11-25/0927r3 [13 CIDs]
1616, 2438, 3227, 137, 904, 2736, 3126, 1371, 1372, 2050, 315, 1760, 3304, 139, 1106, 1107, 1108, 2049, 2238, 2737, 2738, 3296, 3342, 3343, 3483, 3750, 140, 141, 292, 563, 564, 678, 924, 925, 1109, 1110, 1111, 1112, 2051, 2052, 2239, 2241, 2718, 2719, 2720, 2739, 2740, 3228, 3357, 3358, 3359, 3360, 3484, 177, 1073, 1074, 1075, 1581, 1901, 2053, 2054, 2055, 2056, 2057, 2240, 2741, 2742, 3229, 3485, 3486, 3487, 3488, 119, 120, 121, 293, 294, 1076, 1077, 1113, 1114, 1115, 1116, 1373, 1929, 2058, 2059, 2242, 2743, 3370, 3489, 3490, 3491, 3492, 3493, 3496, 565, 2060, 2744, 3297, 2745, 1078, 2061, 2243, 2746, 2747, 3494, 295, 1079, 2062, 2244, 2748, 2749, 3495 in 11-5/0718r2 [114 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Yusuke Asai Second: Bo Sun
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc of Wednesday PM2, May 14, 2025.

## Slide 230: Motion 409 (MAC)
Move to approve resolutions to the CIDs (103C):
741, 2864, 2867, 2869, 2522, 2450, 630, 2428, 811, 403, 851, 3672, 898, 3201, 3202, 3624, 3826, 53, 1981, 3269, 1035, 2862, 896, 107, 465, 645, 850, 965, 3132, 2661, 1982, 1262, 1604, 2449, 717, 768, 1263, 1984, 3626, 3720, 85, 88, 3131, 2662, 1264, 897, 1532, 3134, 709, 3827, 2865, 1522, 2082, 2574, 2083, 86, 87, 1265, 1036, 2866, 1983, 2575, 109, 852, 2576, 3372, 3628, 2870, 3829, 3830, 812, 3373, 3721, 3723, 3831, 3832, 3833, 2871, 1735, 1842, 1266, 813, 814, 466, 467, 646, 647, 1857, 1905, 3374, 3834, 711, 740, 2872, 3203, 2577, 853, 2873, 1267, 57, 58 in 11-25/0438r7 except for the changes tagged as [#1261] [101 CIDs]
162, 3866 in 11-25/0676r5 [2 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Bo Cao Second: Laurent Cariou
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc of Wednesday PM2, May 14, 2025.

## Slide 231: Motions on May 15th, 2025 PM2 PART 1

## Slide 232: Motion 400A (MAC)
Move to approve resolutions to the CIDs (76C):
202, 277, 439, 714, 742, 780, 781, 830, 832, 880, 901, 994, 1050, 1321, 1322, 1381, 1408, 1409, 1410, 1411, 1412, 1413, 1414, 1415, 1416, 1417, 1418, 1419, 1420, 1435, 1436, 1439, 1562, 1599, 1715, 1716, 1717, 1718, 1719, 1720, 1721, 1806, 1832, 1867, 1910, 2117, 2118, 2119, 2519, 2674, 3175, 3176, 3177, 3178, 3179, 3180, 3181, 3257, 3258, 3259, 3420, 3445, 3446, 3447, 3448, 3449, 3450, 3582, 3710, 3795, 3854, 3884, 3885, 3886, 3887, 3888 in 11-25/0600r13 [76 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Abhishek Patil Second: Rubayet Shafin
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC meeting slot of Tuesday AM2, May 12, 2025.

## Slide 233: Motion 410 (MAC)
Move to approve resolutions to the CIDs (64C):
185 186 214 477 478 479 856 857 858 879 1044 1387 1426 1427 1483 1484 1488 1489 1490 1778 1805 1816 1846 1847 1858 2378 2379 2380 2381 2382 2383 2384 2385 2386 2545 2548 2622 2644 2645 2646 2966 3151 3250 3315 3354 3355 3356 3435 3436 3944 3966 in 11-25/0627r13* [51 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Dmitry Akhmetov Second: Laurent Cariou
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc slot Wednesday AM2, May 14, 2025. *SP results: 81Y, 27N, 58A

## Slide 234: Motion 411 (PDT)
Move to remove the “TBD” in the “spatial reuse” subfield in UHR-SIG of UHR MU PPDU, U-SIG of UHR TB PPDU, Common Info and Special User Info Field of the trigger frame in the next revision of 11bn draft.
Note: Remove the “TBD” means SR subfield will be kept the same as that in EHT.
Move: Juan Fang Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[(DCN# 11-25/687r1):]. SP result: No objection.

## Slide 235: Motion 412 (PDT)
Move to add the following paragraph in OBSS PD-based Spatial reuse operation subclause of the next revision of 11bn draft
A UHR STA follows the rules defined in 35.10.2 (OBSS PD-based spatial reuse operation), except that the condition 5 defined in 26.10.2.2 (General operation with non-SRG OBSS PD level) is updated as follows:
  The received PPDU is one of the following:
    For non-EHT PPDU, the SPATIAL_REUSE subfield (if present) is not set to PSR_AND_NON_SRG_OBSS_PD_PROHIBITED.
    For other PPDUs, the SPATIAL_REUSE subfield is present and is not set to PSR_AND_NON_SRG_OBSS_PD_PROHIBITED.
NOTE— As a result, a UHR STA is not allowed to use OBSS PD-based spatial reuse when the received PPDU is a UHR ELR PPDU or a value of PHY Version Identifier field in U-SIG is one of Validate values..
Move: Juan Fang Second: Wook Bong Lee
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[(DCN# 11-25/687r1):]. SP result: No objection.

## Slide 236: Motion 413 (PDT)
Move to add the following paragraph in 3.1 Definitions subclause of the next revision of 11bn draft:
non-extremely-high-throughput (non-EHT) physical layer (PHY) protocol data unit (PPDU): [non-EHT PPDU] A PPDU that is transmitted using a PPDU format defined in Clause 15 (DSSS PHY specification for the 2.4 GHz band designated for ISM applications), Clause 16 (High rate direct sequence spread spectrum (HR/DSSS) PHY specification), Clause 17 (Orthogonal frequency division multiplexing (OFDM) PHY specification), Clause 18 (Extended Rate PHY (ERP) specification), Clause 19 (High Throughput (HT) PHY specification(#2297)), Clause 21 (Very high throughput (VHT) PHY specification) or Clause 27 (High Efficiency (HE) PHY specification)
Move: Juan Fang Second: Wook Bong Lee
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[(DCN# 11-25/687r1):]. SP result: No objection.

## Slide 237: Motion 414 (SFD)
Move to include the following text to the 11bn SFD:
UHR STA shall set the Spatial Reuse subfield to ‘PSR_AND_NON_SRG_OBSS_PD_PROHIBITED’ in the Co-SR and Co-BF transmission.
Move: Juan Fang Second: Wook Bong Lee
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[(11-25/389r2, 11-25/687r1 and 11-25/842r0):]. SP result: No objection.

## Slide 238: Motion 415 (PDT)
Move to add the following table at the end of the subclause 38.3.23.4.3: Transmitter constellation error of next revision of 11bn draft
Move: Juan Fang Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs [#721/r3, #726/r0]. SP result: No objection.

## Slide 239: Motion 416 (SFD)
Move to include the following to the 11bn SFD
The PSDU length for receiver minimum input sensitivity and adjacent channel rejection measurement shall be 512 octets for UHR ELR PPDU.
Move: Juan Fang Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference docs [#721/r3]. SP result: No objection.

## Slide 240: Motion 417 (SFD)
Move to include the following to the 11bn SFD
Receiver Minimum Input sensitivity for new MCSs are as follows:
Move: Juan Fang
Second: Alice Chen
Discussion: None
Result: Approved with unanimous consent.
Reference docs [DCN #721/r3, #726/r0]. SP result: No objection.

## Slide 241: Motion 418 (SFD)
Move to include the following to the 11bn SFD
Minimum required adjacent and nonadjacent channel rejection levels for four new MCSs are as follows:
Move: Juan Fang
Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs DCN #721/r3, #726/r0]. SP result: No objection.

## Slide 242: Motion 419 (SFD)
Move to include the following to the 11bn SFD
The definition for the transmit constellation error in an UHR TB PPDU using RRU:
Transmit Constellation Error requirement of UHR TB PPDU using RRU for MCS0-15 follows the same definition as in EHT.
Transmit Constellation Error requirement of UHR TB PPDU using RRU for the new MCSs (QPSK 2/3, 16QAM 2/3, 16QAM 5/6 and 256QAM 2/3) is:
Move: Ying Liu
Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs [11-25/843r0]. SP result: No objection.

## Slide 243: Motion 420 (SFD)
Move to include the following to the 11bn SFD
The unused tone EVM definition and requirement of UHR TB PPDU when all users are scheduled with RRU is the same as in EHT TB PPDU:
Move: Ying Liu Second: Genadiy Tsodik
Discussion: None.
Result: Approved with unanimous consent.
Reference docs [11-25/843r0]. SP result: No objection.

## Slide 244: Motion 421 (SFD)
Move to include the following to the 11bn SFD
APs exchange the following 2-bit capability fields with values 1, 2, 3, or 4 at the time of group formation between the members of a COBF pair. The capabilities are defined for the AP declared BW and assume Nc=2 (# of columns in the feedback)
  Field 1 – Total number of OBSS sounding reports that the AP can store for this COBF pair at a given time
  Field 2 – Total number of OBSS joint sounding reports that the AP can store for this COBF pair at a given time (can’t be higher than number in field 1)
Move: Ron Porat Second: Wook Bong Lee
Discussion: None.
Result: Approved with unanimous consent.
Reference docs [25/0734r1]. SP result: No objection.

## Slide 245: Motion 422 (SFD)
Move to include the following to the 11bn SFD
In the TB PPDU carrying OBSS AP sounding feedback do you support limiting Nss to 1
In TB PPDU carrying cross BSS (including joint) sounding feedback for COBF the T_PE is fixed as 20uS (nominal_packet_padding=20uS and aFactor=4) and LDPC extra symbol set as 1
  AP will set the UL length field and other parameters in the BFRP trigger frame according to this rule
Move: Ron Porat Second: Wook Bong Lee
Discussion: None.
Result: Approved with unanimous consent.
Reference docs [25/0734r1]. SP result: No objection.

## Slide 246: Motion 423 (SFD)
Move to include the following to the 11bn SFD
In COBF, cross-BSS/joint sounding feedback max Nc is limited to 2
Move: Ron Porat Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs [25/0734r1]. SP result: No objection.

## Slide 247: Motion 424 (EC)
Move to revise the following erroneous DCNs in the approved motions.
Motion 376: revise 11-24/0414r0 to 11-25/0414r0.
Motion 380: revise 11-5/0505r0 to 11-25/0505r0.
Move: Yusuke Asai
Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.

## Slide 248: Motion 425 (MAC)
Move to approve resolutions to the CIDs (33C):
2697 in 11-25/0757r8 & 1378 in 11-25/0479r10 [2 CIDs]
  Instructions to be executed based on 11-25/479r10 (not r2)
94, 217, 624, 684, 687, 688, 691, 991, 1048, 1049, 1430, 1526, 1541, 1544, 1700, 1702, 1710, 2458, 2815, 2817, 3170, 3256, 3322, 3327, 3336, 3444, 3604, 3790, 3873, 3874, 3877 in 11-25/0755r11 [31 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Sanket Kalamkar Second: Salvatore Talarico
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC meeting slot of Thursday AM1, and Joint meeting slot of Thursday AM2, May 15, 2025.

## Slide 249: Motion 426 (PHY-PDT)
Move to incorporate into the latest TGbn draft the proposed text changes from the following documents:
11-25/857r1,
Move: Qisheng Huang Second: Bo Sun
Discussion: None.
Result: Approved with unanimous consent.
Note: These are proposed draft text documents that obtained ≥ 75% support during the straw poll phase of a PHY ad-hoc slot.

## Slide 250: Motion 427 (Joint)
Move to approve resolutions to the CIDs(169C):
9, 10, 61, 84, 193, 404, 405, 1065, 1203, 1567, 1568, 1985, 2084, 2340, 2523, 2875, 2876, 2877, 2878, 2879, 2880, 3161, 3270, 3271, 3474, 3631, 3722 in 11-25/442r5 [27 CIDs]
16, 113, 283, 557, 558, 1609, 2091, 2344, 2345, 2470, 2905, 2906, 3273, 3643, 3644, 3725 in 11-25/634r3 [16 CIDs]
73 74 75 76 77 78 79 133 134 135 146 167 168 196 197 198 215 216 285 286 287 412 413 414 773 774 862 863 906 917 918 919 920 921 922 923 961 966 967 968 970 971 972 973 974 975 978 979 980 981 1031 1205 1382 1403 1404 1495 1525 1572 1573 1574 1575 1576 1577 1752 1920 1921 1935 1936 1944 1951 1952 1953 1957 2112 2113 2114 2219 2220 2221 2222 2223 2224 2225 2467 2546 2803 2804 2809 2980 2981 2982 2983 2984 2985 2986 2987 2988 2989 2990 2991 2992 3166 3167 3168 3280 3281 3282 3283 3284 3288 3289 3290 3527 3528 3549 3550 3576 3608 3674 3675 3676 3677 3727 3901 3969 3970 in 11-25/681r10 [126 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Alice Chen Second: You-Wei Chen
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the Joint meeting slot of Thursday AM2, May 15,2025.

## Slide 251: Motion 428 (SFD)
Move to add to the TGbn SFD the following:
TGbn defines a procedure based on pre-association security negotiation (PASN) or uses PASN with necessary extensions to derive the key(s) needed for the protected version of individually addressed MAPC Negotiation Request frame and MAPC Negotiation Response frame exchanged between two APs as part of MAPC operation
Move: Jay Yang Second: Bo Sun
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[24/1693r3, 23/1836r3, 24/1220r2]. SP result: No objection.

## Slide 252: Motion 429 (SFD)
Move to add to the TGbn SFD the following:
In Coordinated Spatial Reuse, the following information shall be carried in the Trigger frame that initiates concurrent CSR transmissions:
The transmit power limit of the shared AP
The shared AP Tx power limitation indicated by the sharing AP should not be lower than the minimum TX power indicated by the shared AP in its request.
The transmit power of the sharing AP
Move: Jason Guo Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[23/1868r2; 24/2060r1; 25/254r0]. SP result: No objection.

## Slide 253: Motion 430 (Joint)
Move to approve resolutions to the CIDs(107C):
17, 18, 19, 20, 21, 115, 128, 129, 131, 370, 406, 408, 409, 468, 469, 470, 559, 560, 816, 817, 964, 1037, 1269, 1460, 1461, 1462, 1463, 1464, 1523, 1570, 1571, 1610, 1968, 2346, 2347, 2348, 2665, 2799, 2801, 2907, 2908, 2909, 2912, 2913, 2914, 2915, 2916, 2919, 2920, 2921, 2922, 2924, 2925, 2927, 2928, 2929, 2930, 2931, 3223, 3224, 3225, 3276, 3478, 3479, 3481, 3673, 3837, 3838, 3839, 3840 in 11-25/0635r2 [70 CIDs]
1783 in 11-25/0537r3 [1 CID]
23, 24, 25, 471, 1270, 1271, 1465, 2579, 2668, 2935, 2936, 2937, 3726, 3756 in 11-25/0637r4 [14 CIDs]
279, 460, 909, 1026, 1785, 2654, 2657, 2841, 3814 in 11-25/646r5 [9 CIDs]
400, 1458, 1680, 3222, 3957, 2396 in 11-25/0717r5 [6 CIDs]
122, 916, 1945, 1946, 1947, 1667, 3630 in 11-25/0773r1 [7 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Xiaofei Wang Second: Alice Chen
Discussion: None
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the Joint meeting slot of Thursday PM2, May 15,2025.

## Slide 254: Motion 431 (SFD)
Move to add to the TGbn SFD the following:
Define in 11bn an optional mechanism for L4S support on the AP as below?
• Define an MLME primitive that provides congestion notification from the MAC layer to the higher layer at the AP, to enable the upper layer to mark ECN bits on subsequent DL packets for L4S congestion signaling.
• Enhance the MA-UNITDATA.request primitive to provide an indication whether the MSDU carries the packet of L4S flow
NOTE - The conditions and criteria based on which the MAC layer determines to signal L4S congestion experienced notification to the upper layer is implementation specific and is outside the scope of this specification
Move: Binita Gupta Second: Lili Hervieu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[880r2]. SP result: No objection.

## Slide 255: Motion 432 (MAC)
Move to approve resolutions to the CIDs:
3942, 3943, 2212, 2213, 3575 in 11-25/503r13 [5 CIDs]
Move: Binita Gupta Second: Gaurang Naik
Discussion: None.
Result: Approved with unanimous consent.
SP result: No objection.

## Slide 256: Motion 433 (SFD)
Move to add the following to 11bn SFD
– Use fixed values for the following fields in the CoBF transmission
  UHR-SIG MCS is fixed to MCS0
  Spatial Reuse is fixed to ‘PSR_AND_NON_SRG_OBSS_PD_PROHIBITED’
  LDPC Extra Symbol Segment is fixed to 1
  PE Disambiguity is fixed to 1
Move: Alice Chen Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Supporting doc: 11-25/842r1, 11-25/389r2, 11-25/399r1, 11-25/401r0; SP result: No objection.

## Slide 257: Motion 434 (SFD)
Move to add to the TGbn SFD the following:
During the COBF sounding phase, cross-BSS NDPA recipient always pre-corrects the frequency of the NDP it transmits in response (pre-correction done based on the NDPA’s frequency estimate), regardless of reference/follower designation
During the COBF sounding phase, when transmitting the NDPA
  Reference AP does not perform pre-correction
  The follower AP should use a recent frequency pre-correction value for the CFO estimated to the reference AP
Move: Sameer Vermani Second: Eugene Baik
Discussion: None
Result: Approved with unanimous consent.
Supporting docs: 11-25/0836r1, 11-25/0283r1 : SP result: First one was no objection, and second was 45Y, 14N, some Abstains.

## Slide 258: Motions on May 15th, 2025 PM2 PART 2

## Slide 259: Motion (CAD)
Approve the P802.11bn Coexistence Assessment document in 11-25/0847r1, for inclusion in the TGbn Working Group Technical Letter Ballot
Move: Abhishek Patil Second: Rakesh Taori
Discussion: Some discussion.
Preliminary Result: 162Y, 58N, 44A (fails)
Result: 158Y, 56N, 41A (fails)

## Slide 260: WG LB Motion
Instruct the editor to prepare TGbn Draft D1.0
Approve a 45 day Working Group Technical Letter Ballot asking the question “Should TGbn Draft 1.0 be forwarded to SA Ballot?”
[Moved by <name> on behalf of <group>
<group> vote:
Moved: Abhishek Patil, Seconded: Bin Tian
Recorded motion.
Preliminary Result: 125Y, 170N, 18A (fails)
Result: 122Y, 160N, 18A (fails)
Click below for recorded
preliminary results

## Slide 261: Motions on July 10th, 2025

## Slide 262: Motion 435 (Joint)
Move to approve resolutions to the CIDs (18C):
870, 1453, 1454, 1456, 1457, 1492, 1744, 2655, 2658, 2659, 2812, 2813, 2830, 2839, 2840, 3157, 3613, 3817 in 11-25/657r6 [18 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Xiaofei Wang Second: Jay Yang
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the Joint teleconference call of May 29, 2025.

## Slide 263: Motion 436 (PHY)
Move to add to the TGbn SFD the following:
During the COBF sounding phase, cross-BSS NDPA recipient always pre-corrects the frequency of the NDP it transmits in response (pre-correction done based on the NDPA’s frequency estimate), regardless of reference/follower designation
Move: Sameer Vermani Second:
Discussion:
Result:
Reference docs:[11-25/0836r1]. SP result: No objection.

## Slide 264: Motion 437 (PHY)
Move to add to the TGbn SFD the following:
During the COBF sounding phase, when transmitting the NDPA
  Reference AP does not perform pre-correction
  The follower AP should use a recent frequency pre-correction value for the CFO estimated to the reference AP
Move: Sameer Vermani Second:
Discussion:
Result:
Reference docs:[11-25/0836r1]. SP result: 45Y/14N/??A

## Slide 265: Motion 436 (PHY)
Move to add to the TGbn SFD the following:
The Number of UHR-SIG Symbols in CoBF transmission is equal to the minimum number of UHR-SIG symbols needed to accommodate the UHR-SIG information
  No extra UHR-SIG symbols will be allowed
Move: Alice Chen Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0842r1]. SP result: No objection.

## Slide 266: Motion 437 (PHY)
Move to add to the TGbn SFD the following:
Use fixed value for the following field in the CoBF transmission
  Interference Mitigation is fixed to ‘Disable’
Move: Alice Chen Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0842r1, 11-25/389r2, 11-25/399r1, 11-25/401r0]. SP result: No objection.

## Slide 267: Motion 438 (PHY)
Move to add to the TGbn SFD the following:
The Bandwidth and Punctured Channel Information indication in the CoBF Invite and Sync frames are the same with the following rules:
  When the static puncturing patterns of the two APs are the same, the puncturing information in the invite and sync frames corresponds to that
  If the static puncturing patterns of the two APs are not the same, the sharing AP will need to reduce to a smaller BW in which the two APs have the same puncturing pattern, and the information in the invite and sync frames will correspond to that reduced BW configuration
  Note: Indication format is TBD
Move: Alice Chen Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0842r1]. SP result: No objection.

## Slide 268: Motion 439 (PHY)
Move to add to the TGbn SFD the following:
The indicated GI+LTF Size (for the COBF transmission) in the CoBF Invite and Sync frames is the same
  GI+LTF size indication format is TBD
Move: Alice Chen Second: Juan Fang
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0842r1]. SP result: 190Y/26N/82A.

## Slide 269: Motion 440 (Miscellaneous)
Move to approve resolutions to the CIDs:
2697 in 11-25/0757r8 [1 CID]1
  Instructions to be executed based on 11-25/0757r8 (not r0)
34 in 11-25/0679r3 [1 CID]2
919 in 11-25/0681r11 [1 CID]3
and incorporate the text changes into the latest TGbn draft.
Move: Kiseon Ryu Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Note 1: Motioned earlier but the instructions to editor incorrectly pointed to r0 as opposed to r8.
Note 2: Motioned earlier but the CID has a typo (was 324 instead of the actual 34).
Note 3: Motioned earlier but the resolution was deleted by accident in r6. Resolution is “accepted”, there is no additional text change from r10.

## Slide 270: Motion 441 (MAC)
Move to approve resolutions to the CIDs:
1550 in 11-25/571r6 [1 CID]
and incorporate the text changes into the latest TGbn draft.
Move: Yajun Cheng Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of June 2, 2025.

## Slide 271: Motion 442 (Joint)
Move to approve resolutions to the CIDs (117C):
11, 12, 13, 14, 15, 59, 60, 112, 281, 282, 365, 366, 367, 407, 552, 553, 554, 555, 556, 614, 815, 1196, 1197, 1198, 1199, 1268, 1317, 1569, 1606, 1607, 1608, 1729, 1986, 2085, 2086, 2087, 2088, 2089, 2090, 2341, 2343, 2663, 2664, 2808, 2881, 2882, 2883, 2884, 2885, 2886, 2887, 2888, 2889, 2890, 2891, 2892, 2893, 2895, 2896, 2897, 2898, 2899, 2900, 2901, 2902, 2903, 3162, 3163, 3206, 3272, 3285, 3286, 3287, 3475, 3476, 3477, 3632, 3634, 3636, 3637, 3638, 3639, 3640, 3641, 3642, 3724, 3836 in 11-25/633r2 [87 CIDs]
1383, 2854, 2855, 2856, 2857, 2858, 2847, 2849, 2851 in 11-25/0707r7 [9 CIDs]
362, 363, 396, 3011, 3012, 3013, 3014, 3015, 3016, 3017, 3018, 3019 in 11-25/0852r2 [12 CIDs]
184, 399, 1329, 2860, 2923, 3544 in 11-25/0781r1 [6 CIDs]
2169, 2170, 2171 in 11-25/0905r3 [3 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Stephen McCann Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the Joint teleconference of June 12, 2025.

## Slide 272: Motion 443 (Withdrawal)
Move to approve “Rejected” resolutions to the CIDs (2C):
1451 and 1452 [2 CIDs]
With the following rejection reason: “The commenter has withdrawn the comment”.
Move: Ross. J. Yu Second: Bin Tian
Discussion: None.
Result: Approved with unanimous consent.

## Slide 273: Motion 444 (MAC)
Move to approve resolutions to the CIDs (17C):
743, 744, 745, 1696, 1989, 1425, 1990, 1991, 2570, 2656, 2842, 2843, 3815, 3900, 2653, 3194, 758 in 11-25/0638r7 [17 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Chun Huang Second: Stephen McCann
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of June 16, 2025.

## Slide 274: Motion 445 (Joint)
Move to add to the TGbn SFD the following:
If an eMLSR non-AP MLD that receives an ICF addressed to one of its affiliated STAs during CoBF sequences and if the affiliated STA responds with an ICR, then the eMLSR non-AP MLD shall follow the eMLSR procedure defined in 35.3.17, except that the STA shall use an extended time-out period prior to switching back upon inactivity:
  The duration of the extended time-out period shall be sufficient to cover any inactivity period within the COBF sequence, e.g. (but not limited to), from the end of the ICR to the beginning of the data PPDU, or from the DL PPDU until the beginning of the MU-BAR frame from the shared AP for STAs associated with the shared AP
  The duration of the extended timeout period is explicitly indicated to the STA in the ICF frame sent by its associated AP.
  Once the eMLSR STA(s) switch back to listen mode, they start using the default time-out period (aSIFSTime + aSlotTime + aRxPHYStartDelay) in future TXOPs unless otherwise indicated in the ICF.
  This is applicable to CoBF transmission sequence
Move: Sherief Helwa Second: George Cherian
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0412, 11-25/0879]. SP result: No objection.

## Slide 275: Motion 446 (Joint)
Move to add to the TGbn SFD the following:
For DPS non-AP STA(s) scheduled with CoBF in high capability mode, the same switch-back behavior as for eMLSR with extended time-out period is used
  The RTS frame shall not be used as an ICF for DPS in the CoBF Transmission sequence even when the DPS STA does not have any DPS padding required
NOTE: The RTS frame cannot be modified to include the extended timeout period usage and the extended timeout period duration indications.
Move: Sherief Helwa Second: Maolin Zhang
Discussion: Minor discussion.
Result: Approved with unanimous consent.
Reference docs:[11-25/0412, 11-25/0879, 11-24/1512, 11-24/2080]. SP result: No objection.

## Slide 276: Motion 447 (Joint)
Move to add to the TGbn SFD the following:
An AP shall use the BSRP NTB Trigger frame variant for the Sounding Invite frame
  The Sounding Response frame shall be M-BA
  TBD whether there’s another frame variant allowed for the Sounding Invite/Response frame
Move: Sherief Helwa Second: Yusuke Asai
Discussion: Minor discussion.
Result: Approved with unanimous consent.
Reference docs:[11-25/0412, 11-25/0879]. SP result: No objection.

## Slide 277: Motion 448 (Joint)
Move to add to the TGbn SFD the following:
An AP shall use the BSRP NTB Trigger frame variant for the CoBF Invite frame
  The CoBF Response frame shall be M-BA
  TBD whether there’s another frame variant allowed for the CoBF Invite/Response frame
Move: Sherief Helwa Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0412, 11-25/0879]. SP result: No objection.

## Slide 278: Motion 449 (Joint)
Move to add to the TGbn SFD the following:
An AP MLD that receives an ICR from a STA affiliated with an EMLSR non-AP MLD during CBF data frame exchange does not attempt to transmit to the eMLSR non-AP MLD on another link during the extended time-out periods, per baseline behavior.
Move: Sherief Helwa Second: Dibakar Das
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0412, 11-25/0879]. SP result: No objection.

## Slide 279: Motion 450 (Joint)
Move to add to the TGbn SFD the following:
Any CoBF sounding sequence that includes Cross-BSS CSI collection shall be initiated by a two-way handshake between the two APs participating in the sequence
  The two-way handshake exchange consists of a Sounding Invite frame and a Sounding Response frame.
  The Sounding Invite/Response frame exchange is used to:
    Confirm the availability of both APs for CSI collection.
    TBD for indication whether each AP will include ICF/ICR exchanges with its client or not.
    Further information to be exchanged is TBD.
Move: Sherief Helwa Second: Dibakar Das
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0412, 11-25/0879, 11-25/492, 11-25/0553]. SP result: No objection.

## Slide 280: Motion 451 (Joint)
Move to add to the TGbn SFD the following:
In CBF transmission phase, the Feedback User Info field in the BSRP/MU-RTS Trigger addressed to EMLSR/DPS STA carries the extended timeout period duration?
  A new feedback type value is defined for CoBF.
  An “Extended Timeout Duration” field with a TBD length is included in the Feedback user Info field
    The duration value is reported with granularity of 4 us.
    A value 0 of the “Extended Timeout Duration” field is an indication to the STA to follow the default eMLSR/DPS switch back behavior, i.e., do not use an extended timeout period.
    Whether the field indicates maximum value or actual value is TBD
Move: Sherief Helwa Second: George Cherian
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0412, 11-25/0879]. SP result: No objection.

## Slide 281: Motion 452 (Joint)
Move to add to the TGbn SFD the following:
A non-AP STA is allowed to enable/disable CoBF/CoSR operation for the non-AP STA by using 11bn’s feature enabling/disabling procedure (by using Link Reconfiguration Request/Notify frame)
  There are restrictions on how often CoBF/CoSR enablement/disablement requests by the non-AP STA can be sent, those restrictions are TBD
Move: Dibakar Das Second: Sherief Helwa
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0413]. SP result: No objection.

## Slide 282: Motion 453 (MAC)
Move to approve resolutions to the CIDs [68C]:
148, 152, 153, 160, 161, 181, 669, 775, 876, 1318, 1319, 1320, 1324, 1395, 1398, 1399, 1428, 1491, 1494, 1739, 1788, 1789, 2466, 3254, 3438, 3606, 3779, 3780, 3781 in 11-25/0599r16 [29 CIDs]
480, 611, 612, 613, 772, 859, 861, 1681, 1682, 1683, 2106, 2107, 2669, 2670, 2968, 2969, 2970, 2971, 2972, 3164, 3867 in 11-25/0909r1 [21 CIDs]
91, 92, 1969, 2108, 2671, 2973, 2974 in 11-25/0910r1 [7 CIDs]
1925, 2105, 2376, 2377, 2963, 2964 in 11-25/0838r9 [6 CIDs]
3824, 3861, 3862, 3863 in 11-25/0937r2 and 2165 in 11-25/946r2 [5 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Xiaofei Wang Second: Kiseon Ryu
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of June 30, 2025.

## Slide 283: Motion 454 (PHY)
Move to approve resolutions to the CIDs [26C]:
415, 3573, 3574 in 11-25/0735r6 & 2557 in 11-25/0950r1 & 372, 374 in 11-25/0823r4 [6 CIDs]
37, 38, 39, 40, 1092, 1168, 1353, 1354, 2292, 2293, 2294, 2786, 3507, 3508 in 11-25/0964r1 [14 CIDs]
207, 1117, 1745, 1754, 573 in 11-25/0965r2 [5 CIDs]
3570 as “Revised - TGbn editor: D0.3 already incorporated the changes to resolve this comment based on motion 1 to motion 4 in 11-25/687r1. No further changes are needed.”
and incorporate the text changes into the latest TGbn draft.
Move: Yurong Qian Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of June 30, 2025.

## Slide 284: Motion 455 (PHY)
Move to add to the TGbn SFD the following:
During Co-SR invite and Co-SR response exchange, sharing AP indicates single intended PHY version for its own PPDU in the upcoming Co-SR transmission. Shared AP responds with single intended PHY version for its own PPDU in the upcoming Co-SR transmission, if it accepts the invitation.
Move: Ross J. Yu Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0851r0]. SP result: No objection.

## Slide 285: Motion 456 (PHY)
Move to add to the TGbn SFD the following:
In Co-SR Trigger frame, the PHY version of PPDU 1 and the PHY version of PPDU 2 are indicated.
  How to signal is TBD
Move: Ross J. Yu Second: Alice Chen
Discussion: None.
Result: Approved with unanimous consent.
Reference docs:[11-25/0851r0]. SP result: No objection.

## Slide 286: Motions on July 28th, 2025

## Slide 287: Motion 457 (MAC)
Move to approve resolutions to the CIDs [142C]:
2037, 3069, 3268, 3219, 3213, 3211, 3954, 3776, 3777, 2200, 1067, 2156, 2405, 2408, 2588, 2426, 2589, 2590, 3190, 3690, 2489, 3692, 2229, 3066, 3067, 3215, 2597, 504, 1884, 1885, 2454, 3951, 3693, 3694, 887, 3068, 3659, 3695, 3696, 3195, 1835, 3072, 3073, 3426, 425, 722, 1840, 1903, 1927, 1971, 2157, 2427, 2493, 2598, 3145, 3393, 3427, 3697, 3074, 3717, 1912, 3076, 3075, 723, 3077, 1839, 1886, 2599, 1913, 738, 3428, 3698, 3078, 724, 1285, 2494, 2496, 2600, 3079, 3080, 3699, 3214, 103, 739, 799, 1286, 1887, 2495, 2601, 3082, 3700, 3765, 1844, 3081, 509, 102, 2198, 2602, 3083, 1287, 2497, 2603, 3661, 3701, 800, 3084, 508, 725, 2195, 2199, 2604, 3218, 2605, 1914, 1915, 2230, 3217, 2606, 3766, 1563, 3205, 3070 in 11-25/0437r18* [140 CIDs]
3338, 3843 in 11-25/0552r8 [2 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of July 3, 2025.
*r18 expected to handle some inconsistencies in the proposed resolution column of tables.

## Slide 288: Motion 458 (PHY)
Move to approve resolutions to the CIDs [42C]:
602, 607, 1098, 1651, 1747, 603, 604 , 605 , 606 , 1591, 2332, 2333, 608 , 1186, 1187, 1188, 1189, 1190, 1646, 1647, 1648, 1649, 1650, 1652, 1746, 1185, 2331, 233 in 11-25/1081r0 [28 CIDs]
341, 342, 597, 2310, 598, 2311, 1176, 1177, 1749, 1750, 3556, 2185, 3245, 3534 in 11-25/0963r1 [14 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc teleconference of July 7, 2025.

## Slide 289: Motion 459 (PHY)
Move to incorporate the proposed text changes in 11-25/1085r1 to the latest TGbn draft
Move: Ron Porat Second:
Discussion:
Result:
Reference docs:[11-25/1085r1]. SP result: No objection.

## Slide 290: Motion 460 (PHY)
Move to add to the TGbn SFD the following:
COBF/COSR use a common frame exchange design.
  There will be a COSR Invite/ Response/ Sync before the COSR data transmission.
  Note: ICF/ICR (between Response and Sync), if present, will be discussed in MAC
Move: You-Wei Chen Second:
Discussion:
Result:
Reference docs:[11-25/0869r2]. SP result: No objection.

## Slide 291: Motion 461 (PHY)
Move to add to the TGbn SFD the following:
In the COSR data transmission, the same power level is applied to the whole PPDU.
Move: You-Wei Chen Second:
Discussion:
Result:
Reference docs:[11-25/0869r2]. SP result: No objections.

## Slide 292: Motion 462 (PHY)
Move to add to the end of Clause 3.8.3 (Synchronization) of the TGbn SFD the following:
When a CoBF AP receives a cross-BSS or joint CSI feedback in a TB PPDU, the carrier frequency of the TB PPDU may not be synchronized with its own.
Move: Shuling Feng Second:
Discussion:
Result:
Reference docs:[11-25/0872r0]. SP result: No objection.

## Slide 293: Motion 463 (PHY)
Move to add to the TGbn SFD the following:
11bn defines the three “Number of Data OFDM Symbols” subfields in CoBF Invite and Response frames to be 9-bits, and
  Value n indicate “Number of OFDM Symbols – 1”
  Value 511 (‘111111111’) indicates “No suggestion” in “Suggested Number of Data OFDM Symbols” subfield in CoBF Response frame
  Note:
    Minimum Number of Data OFDM Symbols
    Maximum Number of Data OFDM Symbols
    Suggested Number of Data OFDM Symbols
Move: Rui Cao Second:
Discussion:
Result:
Reference docs:[11-25/0845r0]. SP result: No objection.

## Slide 294: Motion 464 (Joint)
Move to approve resolutions to the CIDs (2C):
142, 143 in 11-25/1105r1 [2 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the Joint teleconference of July 10th, 2025.

## Slide 295: Motion 465 (MAC)
Move to approve resolutions to the CIDs [44C]:
22, 1038, 1421, 1564, 1730, 2092, 2510, 2578, 2666, 2667, 2932, 2933, 2934, 3755, 3840 in 11-25/0636r7 [15 CIDs]
2946 762 2949 2950 2424 1736 2097 1536 2388 2394 3617 3377 2414 3616 476 3378 1503 1504 2415 1924 3379 2098 3380 719 2413 2952 1524 3402 2425 in 11-25/908r4 [29 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc Day 1, on July 23, 2025.

## Slide 296: Motion 466 (PHY)
Move to approve resolutions to the CIDs [47C]:
322 in 11-25/0892r2 & 1627, 1633 in 11-25/1120r0 [3 CIDs]
82, 208, 380, 381, 382, 383, 384, 385, 386, 387, 388, 389, 390, 391, 392, 393, 394, 395, 458, 550, 1101, 1592, 2558, 3314 in 11-25/0775r2 [24 CIDs]
360, 1204, 2339, 1497 in 11-25/1166r2 [4 CIDs]
941, 35, 440, 1955, 330, 1207, 47, 334, 335, 2349, 2351, 2035 in 11-25/1136r1 [12 CIDs]
1330, 2553, 2255, 2256 in 11-25/1194r1 [4 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc Day 1, on July 23, 2025.

## Slide 297: Motion 467 (PHY PDT)
Move to insert the following in page 319 line 54 of the latest TGbn draft:
A Co-BF AP shall be capable of being a sync-reference or a sync-follower. Co-BF APs’ sync-reference and sync-follower roles are determined when a Co-BF MAPC agreement is established using procedures described in Clause 37.13.1.3.2 (MAPC agreement establishment). The sync-reference and sync-follower roles can be changed when a Co-BF MAPC agreement is updated using procedure described in Clause 37.13.1.3.3 (MAPC agreement update).
Move: Julia Feng Second:
Discussion:
Result:
Reference docs:[25/1129r1]. SP result: No objection.

## Slide 298: Motion 468 (PHY PDT)
Move to insert the following in page 128 line 4 (in 37.12.3 (Rules for UHR Co-BF sounding protocol sequences) of the latest TGbn draft:
In a UHR Co-BF sounding sequence, the Starting Spatial Streams field in the UHR NDP Announcement shall be set to 0 in a UHR Co-BF sequential NDP sounding sequence and set to 1 in a UHR Co-BF joint NDP sounding sequence.
Move: You-Wei Chen Second:
Discussion:
Result:
Reference docs:[25-1191r1]. SP result: No objection.

## Slide 299: Motion 469 (PHY)
Move to add to the TGbn SFD the following:
The user information in the Sync frame and in the UHR-SIG of CoBF DL PPDU corresponds to all the users that were listed, in the Invite as well as the Response frames
  Nss for each user in the Invite/Response frame and the corresponding number of spatial streams for the same user interpreted from the spatial configuration in the Sync frame is consistent, i.e., the spatial stream allocation does not change.
  The MCS and 2xLDPC bits for each user in the Sync frame should be consistent with those in the Response frame
Move: Junghoon Su Second:
Discussion:
Result:
Reference docs:[25/1186r2, 25/1191r1]. SP result: No objection.

## Slide 300: Motion 470 (MAC)
Move to approve resolutions to the CIDs (102C):
1288, 1596, 2218, 3394, 3089, 3430, 426, 726, 754, 801, 1068, 1289, 1290, 1555, 2406, 2607, 3702, 660, 727, 802, 2158, 3395, 2159, 3088, 427, 428, 728, 729, 755, 1556, 1557, 2160, 2161, 2407, 2608, 3429, 3087, 1558, 1291, 2498, 2609, 3662, 3768, 1292, 3090, 1559, 2610, 3767, 3092, 512, 3093, 1294, 2611, 2682, 2455, 2499, 2612, 3396, 3397, 1295, 1296, 1297, 1298, 1299, 1300, 1301, 1302, 1560, 3191, 730, 877, 2613, 3398, 3663, 3095, 3094, 1303, 1304, 1305, 1306, 269, 2500, 3666 in 11-25/0508r5 [88 CIDs]
899, 2409, 3612, 2643, 2939, 1040, 771, 2647, 2675, 3614 in 11-25/1090r3 [10 CIDs]
2848, 3026, 3071 in 25/0888r2 [3 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc Day 2, on July 24, 2025.

## Slide 301: Motion 471 (PHY)
Move to approve resolutions to the CIDs (3C):
3520, 3521, 3522 in 11-25/1283r0 [3 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc Day 2, on July 24, 2025.

## Slide 302: Motion 472 (PHY SFD)
Move to add to the TGbn SFD the following:
When Co-SR Invite frame indicates 2x LTF type and indicates the intended number of LTF symbols in Co-SR Invite frame, then in the Co-SR Response frame, AP2 could reject the invitation due to the number of LTF limitation.
  The existence of a rejection reason in the CO-SR Response frame is TBD and if a rejection reason field is adopted in TGbn, the presence of a specific rejection reason for LTF limitation is also TBD
Move: Ross J. Yu Second:
Discussion:
Result:
Reference docs:[11-25/1182r1]. SP result: No objection.

## Slide 303: Motion 473 (PHY SFD)
Move to add to the TGbn SFD the following:
The number of LTF is limited to the set {2,4,8} for any MU PPDU carrying MU-MIMO in at least one RU or MRU
Move: Ron Porat Second:
Discussion:
Result:
Reference docs:[11-25/1190r1]. SP result: No objection.

## Slide 304: Motion 474 (PHY SFD)
Move to add to the TGbn SFD the following:
“LDPC Extra Symbol Segment is fixed to 1” for all CoSR modes transmissions that use LDPC
Move: Ron Porat Second:
Discussion:
Result:
Reference docs:[11-25/1190r1]. SP result: No objection.

## Slide 305: Motion 475 (PHY)
Move to modify the spec text in D0.3 (page 312, line14) as follows (changes highlighted in yellow):
For a UHR MU PPDU with the a Co-BF or any mode of Co-SR transmission, the nominal packet padding value shall be equal to 20 μs, and the pre-FEC padding factor α shall be equal to 4. This leads to a fixed TPE value equal to 20 μs.
Move: Ron Porat Second:
Discussion:
Result:
Reference docs:[11-25/1190r1]. SP result: No objection.

## Slide 306: Motion 476 (PHY SFD)
Move to add to the TGbn SFD the following:
The CoSR transmissions from the two APs will use an aligned OFDM symbol boundary during the entire PPDUs (both LTF field and data field) and the same number of EHT-SIG or UHR-SIG field symbols
  No changes to the existing extra-LTF rules shall be made
Move: Sameer Vermani Second:
Discussion:
Result:
Reference docs:[11-25/1178r0]. SP result: No objection.

## Slide 307: Motion 477 (PHY SFD)
Move to add to the TGbn SFD the following:
The invite frame for CoSR will carry the following
  GI+LTF combination
  Number of LTF symbols
Move: Sameer Vermani Second:
Discussion:
Result:
Reference docs:[11-25/1178r0, 11-25/1192r0]. SP result: No objection.

## Slide 308: Motion 478 (PHY SFD)
Move to add to the TGbn SFD the following:
The CoSR length indication will be done as follows:
  Invite frame signals
    Min and Max number of data OFDM symbols
Response frame signals
  Suggested number of data OFDM symbols
Sync frame signals
  L-SIG length
The same 9 bit encoding as COBF shall be used for the following 3 fields
  Min and Max number of data OFDM symbols in invite
  Suggested number of data OFDM symbols in response
    Value 511 (‘111111111’) indicates “No suggestion”
Move: Sameer Vermani Second:
Discussion:
Result:
Reference docs:[11-25/1178r0, 11-25/1192r0]. SP result: No objection.

## Slide 309: Motion 479 (PHY SFD)
Move to add to the TGbn SFD the following:
For CoSR transmissions the UHR or EHT SIG MCS shall be fixed to MCS0 and the number of UHR or EHT SIG symbols shall be fixed to 2
Move: Sameer Vermani Second:
Discussion:
Result:
Reference docs:[11-25/1178r0]. SP result: No objection.

## Slide 310: Motion 480 (PHY SFD)
Move to add to the TGbn SFD the following:
A Shared (Responding) AP may reject a Co-BF/Co-SR transmission or Co-BF sounding invitation received from a Sharing (Initiating) AP.
  In case of rejection, the Shared (Responding) AP can include the reason for rejection in the Co-BF/Co-SR Response or Co-BF Sounding Response frame.
  Reasons for rejecting a Co-BF/Co-SR transmission or Co-BF sounding invitation are TBD.
Move: Mahmoud Hasabel Naby Second:
Discussion:
Result:
Reference docs:[11-25/0865r0]. SP result: No objection.

## Slide 311: Motion 481 (PHY)
Move to approve resolutions to the CIDs (9C):
1201, 1770, 2571 in 11-25/1298r3 & 2700, 2708, 2709 in 11-25/1294r2 [6 CIDs]
952, 1349 in 11-25/1311r0 & 1663 in 11-25/1299r1 [3 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the PHY ad-hoc Day 3, on July 25, 2025.

## Slide 312: Motion 482 (PHY PDT)
Move to incorporate the proposed text changes in 11-25/1316r0 to the latest TGbn draft
Move: Ross J. Yu Second:
Discussion:
Result:
Reference docs:[11-25/1316]. SP result: No objection.

## Slide 313: Motion 483 (MAC)
Move to approve resolutions to the CIDs (43C):
1252 , 3645 , 1127, 1202 in 11-25/915r7 [4 CIDs]
855, 3847, 1498, 2941, 473, 1466, 1230, 911, 1534, 2942, 132, 910, 3615, 2944, 794, 2620, 3375, 2411, 3400, 3376, 2945, 2451, 1041, 2395, 2947, 1042, 1501, 1500, 2948, 1535, 3857, 3858, 3860, 3140 in 11-25/907r4 [35 CIDs]
101, 3252, 3645, 3868, 3869 in 11-25/1071r7 [5 CIDs]
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc Day 3, on July 25, 2025.

## Slide 314: Motion 484 (MAC)
Move to incorporate the proposed text changes in 11-25/1087r2 to the latest TGbn draft
Move: Jeongki Kim Second:
Discussion:
Result:
Reference docs:[11-25/1087r2]. SP result: No objection.

## Slide 315: Motion 485 (PHY SFD)
Move to add to the TGbn SFD the following:
In COBF, cross-BSS/joint sounding feedback shall use resolution of (9,7) and Ng=4
Move: Ron Porat Second:
Discussion:
Result:
Reference docs:[11-25/0734r2 ]. SP result: No objection.

## Slide 316: backup

## Slide 317: Motion X (CR Template)
Move to approve resolutions to the CIDs:
…
and incorporate the text changes into the latest TGbn draft.
Move: Second:
Discussion:
Result:
Note: These are comment resolution documents that obtained ≥ 75% support during the straw poll phase of the MAC ad-hoc teleconference of March ??, 2025.

## Slide 318: Motion Y (SFD Template)
Move to add to the TGbn SFD the following:
Move: Second:
Discussion:
Result:
Reference docs:[]. SP result:

## Slide 319: Motion Z (Draft Template)
Move to incorporate the proposed text changes in 11-24/xxxxry to the latest TGbn draft
Move: Second:
Discussion:
Result:
Reference docs:[]. SP result: