## Slide 1: DPS Operation for Sounding Procedure
Date: 2025-07-25
Authors:

## Slide 2: Introduction
Dynamic power saving (DPS) is one of the features being considered for 802.11bn.
We consider a DPS assisting AP that intends perform sounding procedure with a DPS non-AP STA while the DPS non-AP STA initially operates in the LC mode. The DPS non-AP STA transitions from the LC mode to the HC mode to complete the sounding procedure.

## Slide 3: Background
In Draft IEEE802.11bn D0.3, subclause 37.15.1 DPS Operation:
  An AP may enable its DPS mode only under TBD conditions. A DPS AP shall have value 1 in its transmitted DPS Enabled field to announce that it has enabled DPS and 0 otherwise. The mechanism for enablement/disablement of DPS by an AP is TBD.
  A DPS STA is either a DPS non-AP STA or a DPS mobile AP. It is TBD whether an AP that is not a Mobile AP may be a DPS AP or not.
  The DPS operation allows a DPS STA to operate in lower capability (LC) mode and to transition to higher capability (HC) mode upon reception of an ICF [TBD] transmitted by its associated DPS assisting STA. The DPS STA in higher capability (HC) mode transitions back to the LC mode under TBD conditions.
  A DPS STA that is in LC mode shall be capable of receiving TBD PPDUs (e.g., with non-HT (duplicate) format using a rate of 6 Mb/s, 12 Mb/s, 24Mb/s[TBD]). A DPS STA that is in HC mode (e.g., operating BW, NSS and MCSs) shall be capable of receiving all supported PPDU formats corresponding to the HC mode.

## Slide 4: Sounding Procedure with DPS STA
A DPS assisting AP (AP1, beamformer) intends to perform a sounding procedure with a DPS non-AP STA (STA1, beamformee) to transmit traffic using transmitter beamforming .
The AP1 may transmit an ICF to the STA1, so that the STA1 transitions from the LC mode to a HC mode.
While the STA1 operates in the HC mode, the AP1 then transmits an NDP Announcement (NDPA) followed by a NDP to initiate a sounding sequence (e.g., an EHT non-TB sounding sequence).
Problem
  STA1 that receives NDPA during the HC mode may spend full receive power. As such, power efficiency of DPS non-AP STA operating in PS mode is reduced.
  Since the ICF already start the TXOP for sounding procedure, it is redundant to send a separate NDPA frame to initiate the sounding procedure.

## Slide 5: DPS Operation for Sounding Procedure (Solution 1)
The DPS assisting AP (AP1) sends an NDPA with MAC padding to the DSP non-AP STA (STA1) followed by an NDP.
  The NDPA request STA1 transition from LC mode to the HC mode.
  The NDPA announce the NDP to be transmitted after STA1 transitions to the HC mode.
  The padding allows STA1 transition from the LC mode to the HC mode before receiving the NDP.
STA1 receives the NDPA and transitions from the LC mode to the HC mode.
While operating in the HC mode, STA1 receives the NDP and sends BF/CQI report.

## Slide 6: DPS Operation for Sounding Procedure (Solution 2)
A DPS assisting AP (AP1) sends an ICF to a DPS non-AP STA (STA1) to initiate the sounding sequence.
  The ICF announces an NDP to be transmitted, after the STA1 transitions to the HC mode.
  The NDP is to be transmitted a SIFS after the AP1 receives an ICR from the STA1.
  The ICF includes parameters as used in NDPA for STA1.
After ICF/ICR exchange, AP sends NDP and receives BF/CQI report from STA1.
Example - ICF format
  Sounding Dialog Token Number field may be included in the Trigger Dependent Common Info of the Common Info field.
  STA Info field may be included in the User Info field.

## Slide 7: Summary
In this contribution, we shared some thoughts of DPS operation for sounding procedure.

## Slide 8: Straw Polls
SP1. Do you support defining a DPS operation that includes the following?
  NDPA may be transmitted by a DPS assisting AP for use as an ICF to initiate a sounding procedure with the DPS non-AP STA.
  Yes
  No
  Abstain

## Slide 9: Straw Polls
SP2. Do you support defining a DPS operation that includes the following?
  A DPS assisting AP may send an ICF to initiate a sounding procedure and announce a sounding NDP to be transmitted after it receives an ICR.
  Note: signaling in the ICF for the sounding procedure is TBD.
  Yes
  No
  Abstain

## Slide 10: References
Draft P802.11bn D0.3
Draft P802.11be D7.0
24/0209r9: Specification Framework for TGbn, Ross Jian Yu (Huawei)
24/2016r3: PDT MAC Power Save, Liwen Chu (NXP)
24/1987r2: Detailed text proposal for dynamic power save and eMLSR, Liwen Chu (NXP)
23/1875r1: Power save proposal for non-AP/mobile-AP, Shubhodeep Adhikari (Broadcom)
23/1965r2: Dynamic power save follow-up, Alfred Asterjadhi (Qualcomm)
23/2003r1: Client power save, Laurent Cariou (Intel)