## Slide 1: Thoughts on Context Transfer in Seamless Roaming
Date: 2025-02-05
Authors:

## Slide 2: Introduction
11bn has agreed to support context transfer and context renegotiation for seamless roaming
  [Motion #26] TGbn defines that when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD, the context related to the non-AP MLD is transferred to the target AP MLD such that it preserves the data exchange context for the non-AP MLD or the context can be renegotiated with the target AP MLD.
    Details on what context can be transferred and what context can be renegotiated are TBD.
    How to transfer the context is TBD.
  [Motion #162] As part of the seamless roaming procedure, before the request/response exchange requesting the roaming transition from a current AP MLD to a target AP MLD, a roaming preparation procedure can be performed that includes:
    Transfer or renegotiation of the context to a target AP MLD, and
    Setting up the link(s) with a target AP MLD.
    Details on what context can be transferred or renegotiated is TBD

## Slide 3: Introduction
Context can be transferred to target AP MLD to reduce overhead
  Static context: BA agreement, SCS/MSCS, TWT, …
  Dynamic context: SN
  Context can also be renegotiated with target AP MLD
Context transfer/renegotiation can happen in different roaming phases
  Static context can be transferred/renegotiated in both preparation phase and transition phase
  Dynamic context can be transferred in transition phase
In this contribution, we discuss several aspects of context transfer and renegotiation
*Naming of the request/response above is TBD

## Slide 4: Ping-pong roaming problem
In some scenarios, non-AP MLD may roam between two AP MLDs back and forth
  e.g., AP MLD’s signal fluctuates around roaming threshold
It is difficult to completely avoid ping-pong roaming from happening
  Non-AP MLD may realize it only after roaming between two AP MLDs a few times
Context needs to be transferred or negotiated every time
  Results in additional overhead
  If ping-pong roaming happens, how to reduce this overhead?

## Slide 5: Context preserve by current AP MLD
To minimize context to be transferred or renegotiated in ping-pong roaming scenario, we propose:
  Current AP MLD preserves context of non-AP MLD within a timeout after roaming is completed or retrieval of buffered DL data is finished
    Including BA, SCS/MSCS, TWT, ...
  PTKSA and the setup links between current AP MLD and non-AP MLD can also be preserved
  Context preserve timeout can be
    BSS max idle period, or
    Reassociation deadline (as used in FT), or
    Defined as a new parameter and carried in Timeout Interval Element
  Overhead of preparation phase is reduced if non-AP MLD decides to roam back to current AP MLD within the timeout

## Slide 6: Context transfer indication
By default, non-AP MLD may assume context transfer from current AP MLD to target AP MLD is successful
However, target AP MLD may reject some transferred context due to limited capability
  e.g., SCS, TWT, etc.
Non-AP MLD can indicate whether/what context needs to be transferred
Context transfer result needs to be indicated to non-AP MLD in roaming response
  In this way, non-AP MLD knows which context is maintained and which needs renegotiation
Target AP MLD can provide context suggestion for rejected context
  e.g., SCS parameters recommended by target AP MLD
  Non-AP MLD can use it for efficient renegotiation

## Slide 7: Roaming timeout update
After roaming preparation is completed, non-AP MLD needs to initiate roaming transition within a roaming timeout
  the timeout is between roaming prep response and exec request
  to avoid target AP MLD reserving resources for non-AP MLD for a long time
However, non-AP MLD might not be able to initiate roaming within the timeout
  e.g., due to DUO, OBSS interference, fluctuating signal strength, etc.
  Non-AP MLD may want to extend the timeout, to avoid overhead of repeating roaming preparation
  Or early terminate roaming, to release reserved resources at target AP MLD
A mechanism can be defined for non-AP MLD to request updating roaming timeout
  Allows non-AP MLD to flexibly adjust roaming timeout based on its needs

## Slide 8: Conclusion
In this contribution, we have discussed several aspects of context transfer and renegotiation in seamless roaming
To reduce overhead in some roaming scenarios, we propose
  Current AP MLD preserves context about non-AP MLD within a timeout after roaming is completed or retrieval of buffered DL data is finished
  Context transfer result is indicated to non-AP MLD, optionally with suggestions by target AP MLD
  Non-AP MLD can request to update timeout for initiate roaming

## Slide 9: References
11-24-0052-00-00bn-seamless-roaming-details
11-24-0349-03-00bn-enhanced-fast-bss-transition
11-24-0396-02-00bn-seamless-roaming-within-a-mobility-domain-follow-up
11-24-0480-00-00bn-details-on-context-transfer-and-data-forwarding-under-ft-protocol
11-24-0679-01-00bn-thoughts-on-functionality-and-security-architecture-for-uhr-seamless-roaming
11-24-0830-00-00bn-improve-roaming-between-mlds-follow-up
11-24-0881-00-00bn-improving-stability-during-roaming-process
11-24-1425-00-00bn-considerations-for-context-transfer-in-11bn
11-24-1746-01-00bn-comparision-between-enhanced-fast-bss-transition-and-smd
11-24-1824-00-00bn-discussion-on-context-transfer-in-seamless-roaming
11-24-1883-00-00bn-seamless-roaming

## Slide 10: SP 1
Do you agree to include a Status Code field in the Link Reconfiguration Response frame to indicate whether the context has been successfully transferred from current AP MLD to target AP MLD or not?

## Slide 11: SP 2
Do you support to enable the SCS context transfer from current AP MLD to target AP MLD?

## Slide 12: SP 3
Do you agree that if the SCS context transfer is rejected, the target AP MLD may suggest alternative parameters for this SCS context in the Link Reconfiguration Response frame?

## Slide 13: SP 4
Do you agree that a non-AP MLD may send a TBD frame to request updating the timeout for sending roaming execution request, after roaming preparation has been performed with target AP MLD?
  Note 1: updating the timeout includes extending the timeout, or canceling roaming preparation that has been performed.
  Note 2: the TBD frame can be sent to current AP MLD or target AP MLD.