## Slide 1: Follow up on AMP identification
Date: 2025-01-15
Authors:

## Slide 2: Motivation
During the study group stage, we discussed different AMP device types, AMP-only devices and AMP- assisted devices. Correspondingly, four transmission methods have been proposed,
Backscatter-close range
Backscatter-long range
Active TX
Legacy enhanced
Based on this, many contributions[3]-[7] are discussing the different PHY/MAC/energizing capabilities supported by AMP functional entities.
For AMP functional entities with different capabilities, different transmission methods and channel access methods[8]-[13] are required. Based on the ‘identification’ of AMP STA, AMP APs or readers obtaining the capability or existence information of AMP STAs can help implement more effective scheduling and management.
To enable coexistence, flexible scheduling and management, AMP identification can include
Identify AMP devices (distinguished from legacy STAs)
Identify different types of AMP devices
Notes: AMP-assisted devices tend to achieve compatibility and coexistence with legacy STAs, and further reduce power consumption through environmental energy harvesting, while AMP-only devices may have active transmitters or just transmit through backscatter

## Slide 3: AMP STA identification
For AMP STAs which are unable to initiate transmission through EDCA, the AMP STA capability collection should be initiated by the AMP AP or reader. AMP STAs which can obtain transmission opportunities on their own can follow the existing association way.
The capability reporting can be used for AMP STA identification, which allows the reader to learn about the AMP STA’s existence and capabilities
  For devices that cannot/do not require capability reporting, it is only necessary to declare their existence to achieve identification – just a simple response
The capability information is TBD, and may include data rate, WPT capability, support for TWT, etc,

## Slide 4: Identification vs. Association
For the .11 association, in general
  AP and STAs exchange capabilities
  AP assigns AID to STA
  Association is always initiated by the non-AP STA, not the AP
For the AMP STA capability report,
  AMP Non-AP STAs perform capability or existence reporting, and AP capability exchange is not necessary
  The allocation of identifiers is optional
  Capability collection is initiated by the AMP AP / reader
    AP sends a control frame or a management frame to indicate the protection window for capability reporting to AMP STA
Within an identification protection window, multiple capability collections of AMP STA can be conducted.
  AP or reader can decide the number of times to trigger capability reporting within the protection window, and can also terminate the protection window in advance when no response is received from AMP STA after multiple triggers
Periodic identification can be scheduled based on broadcast TWT or r-TWT, etc
January 2025
*Taking trigger frames as an example here

## Slide 5: ID allocation for AMP STA
Conditions for ID allocation to AMP STA
  AMP STA can store assigned ID(s), i.e. with memory capability
  AMP STA has a unique identifier (device code\MAC address)…→Map with the ID assigned by AP
  One to many
  Long term communication scenarios that require maintenance or detection of link status
  other conditions could be further discussed
The assigned ID can be used for device grouping and access restrictions, which is beneficial for
  Improving the reliability of AMP IoT
    More precise scheduling, control and management
    Maintenance and updating of device information and link status
  Improving transmission efficiency
The assigned ID is featured by
  Shorter length than AMP STA’s own identifier (device code\MAC address)…
  usage within the scope of AP
January 2025

## Slide 6: Summary
In [1], we have a preliminary discussion on the necessity and methods of capability reporting and ID allocation for AMP STAs.
In [2], we further discussed
  Details of the capability reporting for AMP STA
  Details of the ID allocation for AMP STA
  ID conflict avoidance and ID update
In this contribution, we have clarified and summarized the motivation, methods, and benefits of AMP identification, and proposed relevant SPs.
January 2025

## Slide 7: SP1
Do you agree to add the following text to TGbp SFD?
11bp supports a MAC mechanism to enable AMP STAs to report their existence or capabilities if needed.
  The detailed capability information is TBD.
Y/N/A
January 2025

## Slide 8: SP2
Do you agree to add the following text to TGbp SFD?
11bp supports a MAC mechanism to enable an ID to be assigned to an AMP STA based on its reported existence.
  Conditions for ID allocation are TBD.
Y/N/A
January 2025

## Slide 9: References
[1] 11-24-1194-00-00bp-capability-report-for-AMP-STA
[2] 11-24-1560-00-00bp-Follow-up-on-capability-report-and-ID-allocation-for-AMP-STA
[3] 11-24-0867-00-00bp-thoughts-and-questions-on-amp-phy
[4] 11-24-0853-00-00bp-design-target-and-device-capabilities-for-amp-iot
[5] 11-24-1794-00-00bp-Robust Method for AMP Active Uplink Multiple Data Rate Support
[6] 11-25-33-01-00bp-UL Data Rates for AMP
[7] 11-24-1767-00-00bp-AMP Energizer
[8] 11-24-1805-00-00bp-AMP Time-based channel access discussions
[9] 11-24-1806-00-00bp-AMP Time-based channel access for active tags
[10] 11-25-45-00-00bp-Channel access for Backscatter non-AP AMP STAs
[11] 11-25-46-00-00bp-Channel access for Active Tx non-AP AMP STAs
[12] 11-24-1775-01-00bp-Duty-cycle AMP operation
[13] 11-24-1774-01-00bp-Details of AMP trigger procedure
...
January 2025

## Slide 10: Appendix(1/3): AP as reader-ID allocation method a & b
When AMP AP acts as a reader, there are two options for further ID allocation based on the identification of AMP STAs
AMP AP or reader can immediately assign an ID to AMP non-AP STA upon receiving its response (method a),
or it can assign IDs upon receiving multiple responses (method b).
AMP STAs that receive ACK or ID should not respond to subsequent Trigger frames.
Energy-sensitive devices can switch to PS mode within the remaining protection window
Reduce the collision probability of subsequent response frames sent by other AMP STAs
If there are multiple readers, there are two options for the assigned ID
Independent ID: To avoid ID conflicts, AMP STA stores the ID and its source information( such as the reader‘s MAC address or BSS ID). When the reader changes, it can obtain a new ID from a new reader
Global ID: when the reader changes, AMP STA will indicate the existing ID through a response frame, while AMP AP and AMP STA can negotiate whether existing IDs need to be modified
January 2025
Method a
Method b
Notes: 11ah AID：page、block、sub-block。。。。。

## Slide 11: Appendix(2/3): non-AP STA as reader-ID allocation method c
January 2025
A non-AP STA acts as a reader, similar to a relay node.
Capability collection can be initiated by the reader or AP.
After receiving multiple responses, the reader can forward the information of AMP STA to AP for ID allocation.
Due to the unified allocation of IDs by AMP AP, even if multiple readers exist, there will be no ID conflicts.
Referring to .11 association procedure, there is also a limit to the number of IDs allocated by readers or AMP APs.
AMP AP should be able to update and reassign IDs
AMP STA should be able to determine whether the assigned ID is still valid
Notes: Considering the implementation of relay, both AP and non-AP STA can serve as readers

## Slide 12: Appendix(3/3): ID update
January 2025
Due to some AMP STAs being unable to actively send association requests, we have designed a trigger based identification method in our contribution. Similarly, referring to the disassociation procedure, AMP STA may not be able to actively send disassociation request frame and may directly leave the transmission area of the current reader.
For AMP AP or reader:
The ID assigned to AMP STA can be lifetime or short-term valid
The identification and polling of AMP STA should be periodic
If the AMP AP unicast control frames to a AMP STA multiple times based on the assigned ID but does not receive a response, the AMP AP will reclaim and reassign this ID
For AMP non-AP STA:
When the ID becomes invalid or be reassigned, the AMP STA should respond to the identification initiated by the AMP AP again to reacquire the ID
Notes: Considering the implementation of relay, both AP and non-AP STA can serve as readers