## Slide 1: NPCA NAV Operation
Date: 2025-01-07
Authors:
Jeongsoo Lee KSTL
504-225, 9 Gangnam-ro,Giheung-gu
Yongin-si Gyeonggi-do 16977
South Korea
+82 010 2327 0210
Kstlkorea@gmail.com

## Slide 2: Abstract
This presentation discusses the NPCA NAV operation

## Slide 3: Introduction
A STA supporting NPCA can access the wireless medium (WM) on the NPCA primary channel while the primary channel is occupied by inter-BSS traffic. [1]
When the STA accesses the WM on the NPCA primary channel, it needs to maintain another NAV counter, which is independent of the NAV counter used for channel access on the primary channel.
This presentation discusses how to update the NAV counters for the primary channel and the NPCA primary channel.

## Slide 4: NPCA NAV Operation: Case 1
Accessing the primary channel,
  A STA can decode the PPDU that occupies at least the primary channel.
  Therefore, the STA receiving the PPDU should update the NAV counter for the primary channel.
  However, if the received PPDU also occupies the NPCA primary channel, it should update the NAV counter for the NPCA primary channel based on the received PPDU.

## Slide 5: NPCA NAV Operation: Case 1
For example,
  A STA accessing the primary channel receives an inter-BSS PPDU occupying both the primary channel and the NPCA primary channel.
  In this case, the STA should update the NAV counters for both the primary channel and the NPCA primary channel.
Inter-BSS PPDU
(OBSS1)
Inter-BSS PPDU (OBSS1)
Inter-BSS PPDU
(OBSS1)
Inter-BSS PPDU
(OBSS1)
Primary Channel
NPCA Primary Channel
……
Basic NAV for NPCA Primary Channel (OBSS1)
Basic NAV for Primary Channel (OBSS1)
OBSS1 TXOP

## Slide 6: NPCA NAV Operation: Case 1
Observation:
  When the STA receives another inter-BSS PPDU that does not occupy the NPCA primary channel, the STA may not switch to the NPCA primary channel and does not use the NPCA because the virtual CS of the NPCA primary channel is busy.
  This behavior can help address the issue of blindness on the NPCA.
Inter-BSS PPDU
(OBSS2)
Inter-BSS PPDU
(OBSS2)
NPCA Primary Channel
……
Basic NAV for NPCA Primary Channel (OBSS1)
Basic NAV for Primary Channel (OBSS1)
Basic NAV for Primary Channel (OBSS2)
Not swtiching to the NPCA primary channel
OBSS2 TXOP
Inter-BSS PPDU
(OBSS2)
Primary Channel

## Slide 7: NPCA NAV Operation: Case 1
Observation:
  Alternatively, to simplify the implementation, while the NAV (either the intra-BSS NAV or the basic NAV) is set, the STA, upon receiving an inter-BSS PPDU, does not use the NPCA.
  In this case, the previous solution may not be necessary.

## Slide 8: NPCA NAV Operation: Case 2
After switching to the NPCA primary channel,
  The STA can decode the PPDU that occupies at least the NPCA primary channel.
  Therefore, the STA receiving the PPDU should update the NAV counter for the NPCA primary channel.
  However, if the received PPDU also occupies the primary channel, it shall update the NAV counter for the primary channel based on the received PPDU.

## Slide 9: NPCA NAV Operation: Case 2
For example,
  A STA accessing the NPCA primary channel receives an intra-BSS PPDU occupying the NPCA primary channel but not the primary channel.
  In this case, the STA should update the NAV counter for the NPCA primary channel.
Intra-BSS PPDU
Inter-BSS PPDU
(OBSS1)
Basic NAV for Primary Channel (OBSS1)
Intra-BSS PPDU
Inter-BSS PPDU
(OBSS1)
Primary Channel
……
Switching to the NPCA primary channel
Intra-BSS NAV for NPCA Primary Channel
Intra-BSS PPDU
(sent by AP)
NPCA Primary Channel
Intra-BSS TXOP

## Slide 10: NPCA NAV Operation: Case 2
Intra-BSS PPDU
For example,
  A STA accessing the NPCA primary channel receives an intra-BSS PPDU occupying both the primary channel and the NPCA primary channel that is sent from its associated AP.
    NOTE- If the intra-BSS PPDU is addressed to the AP and there is no response PPDU from the AP, the NAV can be discarded.
  In this case, the STA should update the NAV counter for the primary channel and it switches back to the primary channel.
Intra-BSS PPDU
Inter-BSS PPDU
(OBSS1)
Basic NAV for Primary Channel (OBSS1)
Inter-BSS PPDU
(OBSS1)
Primary Channel
……
Switching back to the primary channel
Intra-BSS NAV for Primary Channel
Intra-BSS PPDU
(sent by AP)
NPCA Primary Channel
Switching to the NPCA primary channel
Intra-BSS TXOP

## Slide 11: NPCA NAV Operation: Case 2
For example,
  A STA accessing the NPCA primary channel receives an inter-BSS PPDU occupying the NPCA primary channel but not the primary channel.
  In this case, the STA should update the NAV counter for the NPCA primary channel and it switches back to the primary channel if the remaining time after the NAV of the NPCA primary channel is less than the duration of the OBSS activity on the Primary Channel.
    The STA does not switch back to the primary channel if the remaining time after the NAV of the NPCA primary channel is greater than the duration of the OBSS activity on the Primary Channel.
Inter-BSS PPDU
(OBSS2)
Inter-BSS PPDU
(OBSS1)
Basic NAV for Primary Channel (OBSS1)
Inter-BSS PPDU
(OBSS2)
Inter-BSS PPDU
(OBSS1)
Primary Channel
……
Intra-BSS NAV for NPCA Primary Channel
Inter-BSS PPDU
(OBSS2)
NPCA Primary Channel
Basic NAV for NPCA Primary Channel (OBSS2)
Switching back to the primary channel
Switching to the NPCA primary channel
OBSS2 TXOP

## Slide 12: NPCA NAV Operation: Case 2
For example,
  A STA accessing the NPCA primary channel receives an inter-BSS PPDU occupying both the primary channel and the NPCA primary channel.
  In this case, the STA should update the NAV counters for the primary channel and NPCA primary channel and it switches back to the primary channel if the remaining time after the NAV of the NPCA primary channel is less than the duration of the OBSS activity on the Primary Channel.
Inter-BSS PPDU
(OBSS2)
Inter-BSS PPDU
(OBSS1)
Basic NAV for Primary Channel (OBSS1)
Inter-BSS PPDU
(OBSS2)
Inter-BSS PPDU
(OBSS1)
Primary Channel
……
Inter-BSS PPDU
(OBSS2)
NPCA Primary Channel
Switching to the NPCA primary channel
OBSS2 TXOP
Basic NAV for NPCA Primary Channel (OBSS2)
Basic NAV for Primary Channel (OBSS2)
Switching back to the primary channel

## Slide 13: NPCA NAV Operation: Case 2
Observation:
  After switching back to the primary channel, the STA cannot access the primary channel because the virtual CS of the primary channel is busy. This behavior helps address the issue of blindness on the NPCA.

## Slide 14: Conclusion
In this presentation, the NPCA NAV operation is discussed, and NAV updating rules for the primary channel and the NPCA primary channel are proposed.

## Slide 15: References
[1] https://mentor.ieee.org/802.11/dcn/24/11-24-1762-13-00bn-pdt-mac-npca.docx