## Slide 1: BSRP NTB TF and M-BA
Date: 2025-05-12
Authors:

## Slide 2: Introduction
TGbn has agreed to use the BSRP NTB Trigger Frame (TF) as the initial control frame (ICF) and the Multi-STA BlockAck (BA) frame as the initial response frame for various features [1]
Ensuring that a STA using the BSRP NTB TF as an ICF does not have a lower chance of successfully obtaining a TXOP compared to when using legacy ICFs (e.g., RTS or MU-RTS) is crucial for the features
In this contribution, we discuss channel access rules for the BSRP NTB transmission and the response rules for the received BSRP NTB TF

## Slide 3: BSRP NTB TF transmission
Recap: (26.5.2.2.5) An AP sending a PPDU that contains only Trigger Frames can use any AC
  A PPDU carrying a BSRP NTB TF thus seems to be permitted to use any AC under this rule
When an AP initiates a TXOP by transmitting a BSRP NTB TF to a single non-AP STA, the TXOP is not for either UL or MU frame exchange sequence
  Therefore, if there is no justification for allowing an AP performing unicast communication to have higher priority than the non-AP STAs and the legacy STAs, it might be necessary to restrict the transmission of a BSRP NTB TF to the AC corresponding to the TID of the QoS Data the AP intends to transmit
    A BSRP NTB TF for MAPC operation may be subject to a different rule, which requires further discussion
A non-AP STA may also transmit a BSRP NTB TF to indicate its unavailability info[3]
  It seems evident that when a non-AP STA intends to transmit QoS Data frames after sending a BSRP NTB TF, the BSRP NTB TF should be transmitted using an AC corresponding to the QoS Data frames
  On the other hand, in the case of a stand-alone BSRP NTB TF transmission (i.e., without any QoS Data transmission), it may be necessary to allow the non-AP STA to use any AC

## Slide 4: Recap: Responding rules in the baseline
  1. Response rule for a received RTS frame
    A STA that has received an RTS frame responds with a CTS frame through the idle subchannels, according to the configuration of the RTS frame
      If DYN_BANDWIDTH_IN_NON_HT is set to Static:
        The STA may respond with a CTS frame using the same bandwidth as the received RTS frame
      DYN_BANDWIDTH_IN_NON_HT is set to Dynamic
        The STA may respond with a CTS frame using the same or a narrower bandwidth than that of the received RTS frame
    * The STA determines state(idle/busy) of the 20 MHz subchannels based on the CCA result of PIFS prior to the start of the RTS frame
The baseline provides two types of response frame transmission rules:
RTS
RTS
RTS
RTS
CTS
CTS
IDLE
IDLE
IDLE
BUSY
CTS
CTS
P20
DYN_BANDWIDTH_IN_NON_HT = Dynamic
RTS
RTS
RTS
RTS
CTS
CTS
IDLE
IDLE
IDLE
BUSY
P20
DYN_BANDWIDTH_IN_NON_HT
= Static

## Slide 5: Recap: Responding rules in the baseline (cont’d)
    *The STA that has received the Trigger frame determines state(idle/busy) of the 20 MHz subchannels based on the CCA result of SIFS after the end of the Trigger frame
P20
MU-RTS/CTS
P20
P20
MU-RTS
MU-RTS
MU-RTS
MU-RTS
IDLE
IDLE
IDLE
BUSY
CTS
CTS
CTS
CTS
CTS
CTS
CTS
P40
P80
Basic TF
Basic TF
Basic TF
Basic TF
IDLE
IDLE
IDLE
BUSY
TB PPDU
TB PPDU
TB PPDU
S20
S40
P20
Basic TF/TB PPDU
  2. Response rule for a received TF
    A STA that receives an MU-RTS Trigger frame responds with a CTS frame in non-HT (duplicate) PPDU format, provided that all 20 MHz subchannels within the bandwidth indicated by the MU-RTS Trigger frame are idle
    A STA that has received a TF other than an MU-RTS Trigger frame responds with a TB PPDU, if all the 20 MHz subchannels containing the RUs allocated by the TF are idle
The baseline provides two types of response frame transmission rules:

## Slide 6: Proposal: Multi-STA BA responding rules
Enabling dynamic BW response
  Increasing the probability of receiving a response to the ICF is important, as the originator of the ICF can only obtain a TXOP upon reception of a response frame
    Note that when an AP transmits a BSRP NTB TF, it has a lower probability of receiving a response frame compared to a TF addressed to multiple non-AP STAs
  Therefore, the recipient STA of a BSRP NTB TF should be allowed to respond with a Multi-STA BA frame, provided that the CCA result for the Primary 20 MHz subchannel is idle
    The baseline rule for dynamic bandwidth CTS frame responses could be reused for this purpose
Using CCA result of SIFS after the Trigger frame
  Using the CCA result during the SIFS between the Trigger frame and the PPDU sent in response is preferred
    This ensure that the recipient STA can utilize the same CCA period, regardless of whether the response is sent using a TB PPDU or non-HT (duplicate) PPDU format

## Slide 7: Considerations
Indication for the dynamic BW Multi-STA BA response
  An AP may choose to allow or disallow dynamic BW Multi-STA BA responses
    Similar to the RTS frame, an AP can indicate whether dynamic BW responses are permitted when transmitting a BSRP NTB Trigger frame
    This can be achieved by using a 1-bit indication in the BSRP NTB TF
BW information of the PPDU carrying the Multi-STA BA frame
  A STA responding with a Multi-STA BA frame should indicate the bandwidth of the PPDU that it transmits
    Without such indication, the AP receiving the Multi-STA BA frame cannot determine the actual bandwidth of the received PPDU, as the Multi-STA BA frame does not utilize bandwidth signaling TA

## Slide 8: Illustration of the dynamic BW M-BA response
BSRP NTB TF
BSRP NTB TF
M-BA
busy
M-BA
Dynamic BW indication
== Dynamic
BSRP NTB TF
BSRP NTB TF
BSRP NTB TF
BSRP NTB TF
BSRP NTB TF
BSRP NTB TF
busy
idle
idle
SIFS
M-BA
M-BA
BW info == 40 MHz
Unavailable
Reported IDC-related info.
Frame exchanges
(up to 40 MHz)
Frame exchanges
(up to 40 MHz)
AP
Non-AP STA
TXOP of AP
BW of the PPDUs are limited up to 40 MHz
P20
S20
S40
P20
S20
S40

## Slide 9: Frame format (Dynamic BW Resp indication & Responded BW info)
BSRP NTB TF
(Common Info field)
Multi-STA BA frame (responded to the BSRP)
Trigger Type | UL Length | More TF | CS Required | UL BW | GI And HE/EHT/UHR-LTF Type/ Triggered TXOP Sharing Mode | Dynamic BW Response | Reserved
Frame Control | Duration | RA | TA | BA Control | BA Information | FCS
2 | 2 | 6 | 6 | 2 | variable | 4
Octets:
Reserved | BA Type (value= 11) | Reserved | No Memory Kept | Memory Config. Tag | Management Ack | Bandwidth (TID_INFO)
Bits:
1 | 4 | 4 | 1 | 1 | 1 | 4
4 | 12 | 1 | 1 | 2 | 2 | 1 | 41
Bits:
*TID_INFO subfield of the Multi-STA BA frame is reserved. (BA Type=11)

## Slide 10: Summary
Channel access rule for the BSRP NTB TF transmission has been discussed
Rules for responding a Multi-STA BA frame to the received BSRP NTB TF have been discussed
  We proposed to inherit the rules for the dynamic BW CTS frame to the Multi-STA BA frame
    Allowance of the dynamic BW response can be indicated by an AP transmitting the BSRP TF
    Multi-STA BA frame includes BW information of the PPDU carrying the frame

## Slide 11: Straw poll 1
Do you agree to add the following text to the TGbn SFD?
  A STA that transmits a BSRP NTB Trigger frame as the initial control frame shall use the access category corresponding to the QoS Data frame, QoS Null frame or Management frame it intends to transmit during the TXOP initiated with the BSRP NTB Trigger frame.
    A STA that has no QoS Data frames to transmit can use any AC.
    QoS Data frame(s) corresponding to the secondary AC may also be transmitted during the TXOP, in accordance with the rule defined in 10.23.2.7 (Sharing an EDCA TXOP).

## Slide 12: Straw poll 2
Do you agree to add the following text to the TGbn SFD?
  A STA that has received a BSRP NTB Trigger frame responds with a Multi-STA BlockAck frame using the non-HT (duplicate) PPDU with the same or narrower than the bandwidth of the BSRP NTB Trigger frame.

## Slide 13: Straw poll 3
Do you agree to add the following text to the TGbn SFD?
  A BSRP NTB Trigger frame indicates whether the dynamic BW Multi-STA BlockAck frame response is allowed or not.

## Slide 14: Straw poll 4
Do you agree to add the following text to the TGbn SFD?
  A Multi-STA BlockAck frame sent in response to the BSRP NTB Trigger frame indicates bandwidth information of the responding PPDU.

## Slide 15: References
[1] 11-24/0209 Specification Framework for TGbn
[2] 11-24/2040 PDT MAC Coexistence
[3] 11-25/0437 CC D0.1 subclause 37.11