## Slide 1: Thoughts on IM pilots and other PHY parameters
Date: 2025-07-25
Authors:
Name | Affiliations | Address | Phone | Email
Shengquan Hu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | Shengquan.hu@mediatek.com
Jianhan Liu |  |  |  | Jianhan.liu@mediatek.com
Thomas Pare |  |  |  | 

## Slide 2: Introduction
A motion was passed to add additional pilots for interference mitigation (IM) for 11bn in 2024 Sept. IEEE meeting
However, detailed IM designs are still TBD and need be resolved
In this contribution, we will share our thoughts on IM pilot design and other related topics with the following focuses:
  Scope of IM operation
  IM pilot design method
  Number of IM pilots and performance evaluation
  IM pilot values
  Pre-FEC padding parameter Nsd,short for IM

## Slide 3: General Considerations for IM Operation Scope
Shengquan Hu, Mediatek Inc.
Slide 3
IM for SU only
  Each STA may experience different interference pattern, IM for MU makes scheduling challenge, and may also suffer overall efficiency
  AP has the flexibility to schedule the resources to avoid interference with proper RU/MRUs assignments for each STA (e.g. with OFDMA)
IM for non-punctured/full BW PPDU only
  MRU itself has the certain capability to mitigate interference by puncturing subchannels
  IM on MRU results in extra complexity in implementation such as:
    Different size RU in MRU has the different # of IM pilot tone & separations/patterns
    Support of IM on MRU may result in IM pilot tone wrapped-around issue in order to avoid modifications of leftover bits for PRR segment parser
Limited Nss for IM
  Make implementation & testing simple
  Focus on more reasonable & practical IM application scenarios
  IM need one degree of freedom for receiver antennas to mitigate the interference
  Propose Nss is limited to 1 for IM in DL
  Open for more discussions for Nss in UL IM
No MCS15 for IM
  MCS15 is operated in lower SNR region which is noise dominated, our simulations show that IM doesn’t provide notable performance gain in low SNR region
  IM with MCS 15 requires additional spec efforts
July 2025

## Slide 4: Consideration of IM Pilot Design
Some IM pilot design methods are proposed & discussed in [1~3].
Proposal [1] uses LDPC tone mapper based method to spread IM pilot tones
IM pilots would be better distributed as evenly as possible
For a given BW & number of IM pilots, Dtm value determines IM pilot distribution pattern and pilot tone separation distance
For ~10% IM pilots (simulations show ~10% IM pilots achieves near-optimal performance), some of existing Dtm values need be modified to achieve better IM pilot distribution
LDPC tone mapper
IM pilots
IM data
Nsd
For BW20/RU242 with Nsp_im=26 (~11%), existing Dtm=9 works fine, achieve near evenly IM pilot distribution with separation distance = 9
(NOTE: tone amplitude scaling is for illustration purpose only)
Dtm

## Slide 5: IM Pilots for BW40 with Existing Dtm
Shengquan Hu, Mediatek Inc.
Slide 5
Nsp_im=52, Dtm=12
  IM pilot tone separation 12 (will cause some performance degradation vs separation by 9)
  IM pilot tones wrap-around (2 IM pilots adjacent together)
  Two IM pilots are near DC
Zoom in
(NOTE: tone amplitude scaling is for illustration purpose only)
July 2025

## Slide 6: IM Pilots for BW40 with New Proposed Dtm
Shengquan Hu, Mediatek Inc.
Slide 6
Nsp_im=52, Dtm=9
  IM pilot tone separation 9, same as BW20
  NO wrap-around, near evenly distributed
  IM pilots away from DC
(NOTE: tone amplitude scaling is for illustration purpose only)
Zoom in
July 2025

## Slide 7: IM Pilots for BW80 with Existing Dtm
Shengquan Hu, Mediatek Inc.
Slide 7
Nsp_im=98, Dtm=20
  IM pilot tone separation 20 (will cause some performance degradation vs separation by 10)
  IM pilot tones wrap-around (2 IM pilots adjacent together)
  Two IM pilots are near DC
Zoom in
(NOTE: tone amplitude scaling is for illustration purpose only)
July 2025

## Slide 8: IM Pilots for BW80 with New Proposed Dtm
Shengquan Hu, Mediatek Inc.
Slide 8
Nsp_im=98, Dtm=10
  IM pilot tone separation 10
  NO wrap-around, near evenly distributed
  IM pilots away from DC
(NOTE: tone amplitude scaling is for illustration purpose only)
Zoom in
July 2025

## Slide 9: PER Performance NOT Degrade with New Dtm
BW40: Dtm=12 vs Dtm=9
BW80: Dtm=20 vs Dtm=10
Simulation Settings
  1x2x1 (1T,2R,1ss), MCS=[4, 7, 9, 11] (for 16QAM, 64QAM, 256QAM, 1024QAM)
  D-NLOS, practical channel estimation with smoothing
  4kB for BW40, 8kB for BW80
Observations:
  The performance difference is negligible (around +/- 0.1dB) for Dtm=12 vs 9 of BW40 and Dtm=20 vs 10 of BW80/160/320

## Slide 10: IM Simulation/Modeling For IM Performance Evaluation
Encoding/mod
mod
CH
CHintf
+
Desired signal
Interference
signal
+
Nsp_im
ZE or NZE
D-NLOS
noise
Receiver
Demod_method:
MRC (IM off)
MVDR (IM on)
Cov Estimate/Average/Interpolation:
Est. CE/Cov
IM pilots based Cov estimate
Cov average over symbols
interpolation
PER
Goodput
IM pilots
option
PHY rate
unsync
16QAM
Full BW
SIR=5/10dB
Data only/or LTF&data
D-NLOS
To evaluate IM performance with different number of IM pilots
  ~5% (Nsp_im = 13 for BW20, 26 for BW40, 49 for BW80)
  ~10% (Nsp_im = 26 for BW20, 52 for BW40, 98 for BW80)
  ~20% (Nsp_im = 52 for BW20, 104 for BW40, 196 for BW80)

## Slide 11: Simulation Scenarios & Settings
General:
  20MHz/80MHz, i.e. RU242/996
  1T2R, 1T4R, 1ss
  D-NLOS (for both desired and interference signals, but uncorrelated)
  Packet sizes with 1024B for RU242, 2048/4096bytes for RU996)
  MCS1~8 (some cases are limited to lower MCS due to error floor)
  No RF impairments
Interference:
  Random data & 16QAM modulated OFDM signals
  Unsynchronized with desired signals
  SIR=5/10dB
  Full BW
  On data symbol only or on both LTF & data
  Static
Receiver:
  Practical estimated channel with smoothing
  MRC when IM off
  Advanced Receiver for interference suppression (e.g. MVDR, etc) when IM on
  Covariance estimation using IM pilots for interference estimation
  Covariance average over OFDM symbols & interpolation in FD
Measurements:
  PER
  Goodput (taking account IM pilots overhead)

## Slide 12: Performance Comparison of IM Pilots: RU996, 1x4x1, SIR=5dB
Simulations:
  RU996, 1x4x1,D-NLOS
  SIR=5dB, interference on LTF & data
  ZE
  Cov average over symbols
  No intf no IM: MCS1~9
  Intf,no IM: MCS1~3
  IM: MCS1~8
Observations:
  10% IM pilots achieve near-optimal goodput performance
  5% & 20% IM pilots are suboptimal
  No IM with interference, error floor for MCS3
  IM achieves Gput up to ~3x of no-IM
>3x

## Slide 13: Performance Comparison of IM Pilots: RU242, 1x2x1, SIR=10dB
Simulations:
  RU242, 1x2x1,D-NLOS
  SIR=10dB, interference on data only
  ZE
  Cov average over symbols
  No intf no IM: MCS1~9
  Intf,no IM: MCS1~4
  IM: MCS1~8
Observations:
  10% IM pilots achieve near-optimal goodput performance
  5% & 20% IM pilots are suboptimal
  No IM with interference, error floor for MCS4
  IM achieves Gput up to ~3x of no-IM
~3x

## Slide 14: IM Pilot Values: ZE vs NZE
Shengquan Hu, Mediatek Inc.
Slide 14
IM pilot values can be two options:
  Zero-Energy (ZE)
  None-Zero Energy (NZE)
Zero-Energy (ZE) pilots have several advantages, such as:
  ~ 0.5dB power boost gains
  Decouple frequency offset estimation and interference estimation
  Less complexity
  No need pilot values/sequence design to reduce PAPR
We prefer and propose to use Zero Energy IM pilots
July 2025

## Slide 15: PAPR of ZE IM Pilots
Shengquan Hu, Mediatek Inc.
Slide 15
July 2025

## Slide 16: PHY Parameter of Nsd_short for IM
For IM, some of data tones (e.g. ~10%) will be used as IM pilots for interference covariance estimation
Number of data tones in IM operation will be reduced, thus, the pre-FEC padding parameter Nsd_short need be updated accordingly
Following the same design methodology as 11ax/be, a set of new PHY parameters of Nsd_short for IM is proposed as below
RU Size | Nsd_IM & Nsp_IM |  | Nsd_short for IM
RU/MRU | Nsd_IM | Nsp_IM | MCS=[0:13,17,19,20,23]
242 | 208 | 26 | 48
484 | 416 | 52 | 108
996 | 882 | 98 | 216
2x996 | 1764 | 196 | 444
4x996 | 3528 | 392 | 888

## Slide 17: Summary
IM can greatly improve system performance when interference occurs
IM operation scopes are discussed in this contribution, suggest to focus on main IM application scenarios such as full BW/non-punctured SU cases
~10% of Nsd used for IM pilots seems a good choice to achieve near-optimal goodput, which correspond to 26 IM pilots for BW20, 52 for BW40, 98 for BW80
LDPC tone mapper based IM pilot design was studied, new Dtm values are proposed to achieve better IM pilot distribution pattern and avoid pilot wrap around issues
ZE & NZE IM pilots are studied, we propose to use ZE IM pilots with less complexity in interference covariance estimation and achieve slightly better performance than NZE
A set of new Nsd,short parameters for pre-FEC padding is proposed when IM is used

## Slide 18: Reference
[1]. 11-24-1264-00-00bn-supporting-rx-interference-mitigation-in-tgbn
[2]. 11-25-0808-00-00bn-discussion-on-design-of-interference-mitigation-pilots-follow-up
[3]. 11-25-0739-01-00bn-on-interference-mitigation-pilots

## Slide 19: SP#1
Do you agree to include the following into 11bn SFD?
IM pilots are only applied for non-punctured/full bandwidth SU PPDU

## Slide 20: SP#2
Do you agree to include the following into 11bn SFD?
when IM pilots are applied, the value of D_TM for LDPC tone mapper is as below:
  9 for 242-tone RU for non-DCM
  9 for 484-tone RU for non-DCM
  10 for 996-tone RU for non-DCM (same value is used for each 80MHz frequency subblock when PPDU bandwidth is 160MHz and 320MHz)

## Slide 21: SP#3
Do you agree to include the following into 11bn SFD?
IM pilots have values of 0’s (i.e. Zero-Energy)

## Slide 22: SP#4
Do you agree to include the following into 11bn SFD?
Nsd_short values are defined as below when IM pilots are applied
RU/MRU | Nsd_IM & Nsp_IM |  | Nsd_short_IM
RU/MRU | Nsd_IM | Nsp_IM | MCS=[0:13,17,19,20,23]
242 | 208 | 26 | 48
484 | 416 | 52 | 108
996 | 882 | 98 | 216
2x996 | 1764 | 196 | 444
4x996 | 3528 | 392 | 888

## Slide 23: SP#5
Do you agree to include the following into 11bn SFD?
the number of spatial streams is defined as below if IM pilots are applied?
  1 spatial stream for DL

## Slide 24: SP#6
Do you agree to include the following into 11bn SFD?
IM pilots are not applicable when MCS 15 is used

## Slide 25: SP#7
Do you agree to include the following into 11bn SFD?
number of IM pilots is defined as below
  26 for BW20
  52 for BW40
  98 for BW80
  2*98 (=196) for BW160
  4*98 (=392) for BW320