## Slide 1: Further Considerations on Client Power Save
Date: 2025-05-06
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Chaoming Luo |  |  |  | 
Ning Gao |  |  |  | 
Liangxiao Xin |  |  |  | 

## Slide 2: Introduction
Power save is very important especially for client devices such as mobile phones. Currently 802.11bn task group has agreed to define cross link power save signaling mechanism and DPS mode .
Cross link power save signaling mechanism
  Allowing a non-AP MLD to indicate to its associated AP MLD that supports the mechanism, in a frame sent on one enabled link, the power management mode for one or more of its affiliated non-AP STAs
  Whether support for the mechanism is mandatory or optional is TBD
  Dynamic Power Save（DPS） mode
  the STA that uses DPS mode may transition from a lower capability (LC) mode to a higher capability (HC) mode upon reception of an initial control frame
This contribution analyzes the issues needed to be resolved for cross link power save signaling mechanism and gives some proposals.

## Slide 3: Recap
ML power-save operation in 11be
Each non-AP STA affiliated with a non-AP MLD that is operating on an enabled link shall maintain its own power management mode and power states.
Frame exchanges on an enabled link are possible when the non-AP STA affiliated with the non-AP MLD operating on that link is in the awake state
Figure. Each non-AP STA affiliated with a non-AP MLD maintains its own power state

## Slide 4: Issues for cross link power save signaling
DPS mode as a power management mode needs to be considered for cross link power save signaling
the time that the STA enters into target power management mode indicated by cross link power save signaling is impacted by the following factors:
the STA corresponding to the indicated link needs to enter into target power management mode as soon as possible.
Enough time needs to be reserved for AP corresponding to indicated link to make it get ready for serving the STA of the indicated link for its target power management mode as there exists potential cross-link signaling delay

## Slide 5: Proposal : Cross link signaling for power save should support the indications for DPS and PS mode
Cross link signaling for DPS mode
A STA affiliated with a MLD can indicate that the other STA that is affiliated with the same MLD will enter into DPS mode. In this case, DPS parameters can also be included by the cross link signaling.
  Enabling/disabling DPS mode
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  Higher capability mode (e.g., operating BW, NSS and MCSs, with at least one higher capability than that in the lower power capability mode)
  The Transition timeout for the indicated DPS/PS mode is introduced by considering cross-link signaling delay to make the associated AP get ready for serving the STA

## Slide 6: Summary
There exist issues needed to be solved for cross link power save signaling.
This contribution analyzes the issues and proposes that:
the cross link power save signaling mechanism to be specified should support the signaling for DPS mode in UHR.
The transition timeout for indicated DPS/PS mode is introduced by considering cross-link signaling delay to make the associated AP get ready for serving the STA.

## Slide 7: References
[1] tgbn-motions-list-part-2, https://mentor.ieee.org/802.11/dcn/25/11-25-0014-16-00bn-tgbn-motions-list-part-2.pptx
[2] tgbn-motions-list-part-1, https://mentor.ieee.org/802.11/dcn/24/11-24-0171-26-00bn-tgbn-motions-list-part-1.pptx
[3] Power Save Protocols for UHR - follow up, https://mentor.ieee.org/802.11/dcn/24/11-24-0544-01-00bn-power-save-protocols-for-uhr-follow-up.pptx
[4] Client power save, https://mentor.ieee.org/802.11/dcn/23/11-23-2003-00-00bn-client-power-save.pptx
[5] Multi link Power Management for MLO, https://mentor.ieee.org/802.11/dcn/24/11-24-0602-00-00bn-multi-link-power-management-for-mlo.pptx
Liuming Lu (OPPO)

## Slide 8: SP1
SP 1: Do you agree that the cross link power save signaling mechanism to be specified should support the signaling for DPS mode in UHR?
The mechanism is TBD.
Liuming Lu (OPPO)

## Slide 9: SP2
SP 2: Do you agree that the transition timeout for indicated DPS/PS mode is defined by considering cross-link signaling delay to make the associated AP get ready for serving the STA for its indicated PS mode by cross link power save signaling mechanism?