## Slide 1: Further Considerations on Client Power Save
Date: 2025-06-30
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Chaoming Luo |  |  |  | 
Ning Gao |  |  |  | 
Liangxiao Xin |  |  |  | 

## Slide 2: Introduction
Power save is very important especially for client devices such as mobile phones. Currently 802.11bn task group has agreed to define cross link PM mode signaling mechanism and DPS mode .
cross link PM mode signaling mechanism
  Allowing a non-AP MLD to indicate to its associated AP MLD that supports the mechanism, in a frame sent on one enabled link, the power management mode for one or more of its affiliated non-AP STAs
  Whether support for the mechanism is mandatory or optional is TBD
  Dynamic Power Save（DPS） mode
  the STA that uses DPS mode may transition from a lower capability (LC) mode to a higher capability (HC) mode upon reception of an initial control frame
This contribution analyzes the issues needed to be resolved for cross link PM mode signaling mechanism and gives some proposals.

## Slide 3: Recap
Power management - baseline
Non-AP STA can be in one of two power management modes:
1. Active mode: The STA receives and transmits frames at any time if the STA is in awake state. A non-HE STA remains in the awake state. An HE STA remains in the awake state, unless the STA is unavailable.
2. Power save (PS) mode: The STA enters the awake state to receive or transmit frames. The STA remains in the doze state otherwise. STA in PS mode can be in one of two power states:
Awake: STA is fully powered.
Doze: STA is not able to transmit or receive non-WUR PPDUs and consumes very low power.
ML power-save operation in EHT
Each non-AP STA affiliated with a non-AP MLD that is operating on an enabled link shall maintain its own power management mode and power states.
Frame exchanges on an enabled link are possible when the non-AP STA affiliated with the non-AP MLD operating on that link is in the awake state

## Slide 4: Extended PM modes in UHR
Power management - UHR
Non-AP STA can be in one of three power management modes:
1. Active mode: The STA receives and transmits frames at any time if the STA is in awake state. A non-HE STA remains in the awake state. An HE STA remains in the awake state, unless the STA is unavailable.
Awake: STA is fully powered
2. Power save (PS) mode: The STA enters the awake state to receive or transmit frames. The STA remains in the doze state otherwise. A STA in PS mode can be in one of two power states:
Awake: STA is fully powered.
Doze: STA is not able to transmit or receive non-WUR PPDUs and consumes very low power.
3. DPS mode: The STA receives and transmits frames at any time if the STA is in awake state. An UHR STA remains in the awake state, unless the STA is unavailable.
Awake: STA operates in lower capability (LC) mode and to transition to higher capability (HC) mode upon reception of an ICF transmitted by its associated DPS assisting STA

## Slide 5: Issues for cross link PM mode signaling
1. Three power management modes including active mode, PS mode, DPS mode need to be considered for cross link PM mode signaling
2. The following factors should be taken into account when considering the expected effective time that the STA enters into target power management mode indicated by cross link PM mode signaling :
the STA corresponding to the indicated link needs to enter into target power management mode as soon as possible.
Enough time needs to be reserved for AP corresponding to indicated link to make it get ready for serving the STA of the indicated link for its target power management mode as there exists potential cross-link signaling delay
3. The actual effective time for the indicated STA to enter into target PM mode may be different from the expected effective time.
For example, the indicated STA to enter into PS mode may still do frame exchanges when the expected effective time arrive.
To resolve this inconsistent issue, special rules need to be specified.

## Slide 6: Proposal 1: Cross link signaling for power save should support the indications for three PM modes
Cross link signaling for three PM modes
A STA affiliated with a MLD can indicate that the other STA that is affiliated with the same MLD will enter into the target PM mode that may be active mode, PS mode, DPS mode.
1. The indicated STA will transition from one PM mode to another PM mode within the three PM modes
2. The indicated STA will also transition from one DPS mode to the other DPS mode as there may exist DPS modes with different Rx/Tx parameters for their LC modes and/or HC modes
Active mode
PS mode
DPS mode
Active mode
PS mode
DPS mode
Current PM mode
Target PM mode
DPS mode 1
DPS mode 2
Current PM mode
Target PM mode
LC mode (20 MHz BW, 1 SS）
HC mode (80 MHz BW, 1 SS)
LC mode (40 MHz BW, 1 SS）
HC mode (80 MHz BW, 2 SS)

## Slide 7: Proposal 2: the transition timeout is introduced for cross link PM mode signaling
  The Transition timeout for the indicated PM mode is introduced by considering cross-link signaling delay to make the associated AP get ready for serving the STA
the indicated STA may enter into target PM mode, either:
a) At the end of the transition timeout interval, or
b) Before the end of the transition timeout interval, immediately after transmitting an acknowledgment as a response to the received ML PM mode indication notification frame from one of the APs affiliated with the AP MLD.
whichever comes first.

## Slide 8: Proposal 3: special rules are specified to resolve the inconsistency issue for cross link PM mode signaling
  The AP with which the indicated STA is associated may still keep sending DL traffic to the STA after the ML PM mode indication that the STA will enter into PS mode has been sent. In such case, a special rule can be considered to be specified, e.g. :
  If the indicated STA to enter into target PM mode still do frame exchanges that include no ML PM mode indication when the expected effective time arrives (e.g. the transition timeout expires) the STA will enter into the target PM mode after the end of the frame exchanges.

## Slide 9: Summary
There exist issues needed to be solved for cross link PM mode signaling.
This contribution analyzes the issues and proposes that:
Cross link signaling for power save should support the indications for three PM modes
the transition timeout is introduced for cross link PM mode signaling
special rules are specified to resolve the inconsistency issue for cross link PM mode signaling

## Slide 10: References
[1] tgbn-motions-list-part-2, https://mentor.ieee.org/802.11/dcn/25/11-25-0014-16-00bn-tgbn-motions-list-part-2.pptx
[2] tgbn-motions-list-part-1, https://mentor.ieee.org/802.11/dcn/24/11-24-0171-26-00bn-tgbn-motions-list-part-1.pptx
[3] Power Save Protocols for UHR - follow up, https://mentor.ieee.org/802.11/dcn/24/11-24-0544-01-00bn-power-save-protocols-for-uhr-follow-up.pptx
[4] Client power save, https://mentor.ieee.org/802.11/dcn/23/11-23-2003-00-00bn-client-power-save.pptx
[5] Multi link Power Management for MLO, https://mentor.ieee.org/802.11/dcn/24/11-24-0602-00-00bn-multi-link-power-management-for-mlo.pptx
Liuming Lu (OPPO)

## Slide 11: SP1
SP 1: Do you agree that the cross link PM mode signaling mechanism to be specified should support the signaling for power management modes including active mode, PS mode, DPS mode in UHR?
The mechanism is TBD.
Liuming Lu (OPPO)

## Slide 12: SP2
SP 2: Do you agree that the transition timeout for the indicated STA to enter into the target PM mode is defined by considering cross-link signaling delay to make the associated AP get ready for serving the STA for its target PM mode by cross link PM mode signaling mechanism?

## Slide 13: SP3
SP 3: Do you agree that the following rule is specified to resolve the inconsistency issue
If the indicated STA to enter into target PM mode still do frame exchanges that include no ML PM mode indication when the expected effective time arrives (e.g. the transition timeout expires) the STA will enter into the target PM mode after the end of the frame exchanges.