## Slide 1: Further Considerations on Seamless Roaming
Date: 2025-04-10
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Chaoming Luo |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 

## Slide 2: Introduction
TGbn has agreed to specify a seamless roaming procedure that a non-AP MLD can use to transition from its current AP MLD to a target AP MLD without requiring reassociation within the same Seamless Mobility Domain (SMD)
During the transition the non-AP MLD preserves the context for data transmission to maintain data continuity for a seamless experience and minimizes the time during which connectivity between the non-AP MLD and the DS is lost.
The PMKSA and PTKSA created as part of RSNA security association established between the non-AP MLD and the SMD-ME is a key feature for seamless roaming
PTK sharing: The non-AP MLD roams by using a single encryption key (in the single PTKSA) when remaining in state 4 with the SMD-ME
per-AP MLD TK : The non-AP MLD roams using different (per-AP MLD) TKs for encryption.
This contribution analyses how to guarantee the data continuity for seamless experience while reducing the risk of data breaching due to PTK sharing, and proposes a mechanism for RSNA rekeying to improve seamless roaming.

## Slide 3: Recap
Seamless Roaming
PMK/PTK sharing:
when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD within the SMD, the same PMKSA/ PTKSA, established with the SMD-ME, shall be used to protect communications with the current AP MLD and the target AP MLD.[Motion 285/286]
PTK renegotiation:
Non-AP MLD and the target AP MLD derive the PTK based on the shared PMK and DHss in TBD request and TBD response frames .[Motion 356]
RSNA rekeying
Rekeying is the process by which an existing security association is renewed or a new instance of an existing type of security association (e.g., PTKSA, GTKSA) is created.
When both ends of the link support extended key IDs for individually addressed frames, it is possible to install the new PTKSA without data loss, provided the new PTKSA uses a different key ID from the old PTKSA.

## Slide 4: Proposal: RSNA rekeying before/after roaming execution
Proposal: RSNA rekeying before/after roaming execution
The non-AP MLD establishes the PMKSA and PTKSA as part of RSNA security association with the SMD and use it to protect the data communications with the current AP MLD, and for future possible roaming it creates another instance of security association with the SMD-ME for seamless roaming and catches the PTKSA before the initiation of the roaming
After the initiation of the roaming, the non-AP MLD installs the PTKSA for seamless roaming before the roaming execution.
The PTKSA(i.e. the PTKSA for seamless roaming ) remains the same when it transitions from its current AP MLD to a target AP MLD within the same SMD.
After the roaming execution the non-AP MLD renews the PTKSA.
Benefits:
Avoiding the renegotiation of PTKSA during the transition to decrease the signaling overhead and reduce the impact on the data continuity for seamless experience
reducing the risk of data breaching due to PTK sharing during transition
Making the security sensible to clients to relieve their worries

## Slide 5: Summary
The signaling overhead needs to be minimized during the process of roaming from the current AP MLD to a target AP MLD for a seamless experience.
Since the PMKSA and PTKSA created as part of RSNA security association are established between the non-AP MLD and the SMD-ME, RSNA rekeying before/after roaming execution can be considered.

## Slide 6: References
[1] Draft P802.11bn_D0.2
[2] TGbn Motions List - Part 2, https://mentor.ieee.org/802.11/dcn/25/11-25-0014-14-00bn-tgbn-motions-list-part-2.pptx
[3] Thoughts on Functionality and Security Architecture for UHR Seamless Roaming, https://mentor.ieee.org/802.11/dcn/24/11-24-0679-04-00bn-thoughts-on-functionality-and-security-architecture-for-uhr-seamless-roaming.pptx
[4] Link Setup for Seamless Roaming, https://mentor.ieee.org/802.11/dcn/24/11-24-1882-02-00bn-link-setup-for-seamless-roaming.pptx
[5] PDT MAC on Seamless Roaming Part 1, https://mentor.ieee.org/802.11/dcn/25/11-25-0566-00-00bn-pdt-mac-on-seamless-roaming-part-1.docx
Liuming Lu (OPPO)

## Slide 7: SP1
SP1 : Do you support to specify a mechanism for RSNA rekeying before/after roaming execution by using PTK sharing for seamless roaming?