## Slide 1: Discussion on In-device Coexistence
Date: 2025-06-01
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com

## Slide 2: Introduction
A non-AP STA in Dynamic Unavailability Operation (DUO) mode can indicate unavailability in certain Control frames, where the unavailability might overlap with the ongoing TXOP. Two types of unavailability indications are considered:
Solicited unavailability indications
  A non-AP STA in the DUO mode that receives a BSRP Trigger frame from its associated DUO Supporting AP indicates unavailability in a response Multi-STA BlockAck frame
  Unsolicited unavailability indications
  A DUO non-AP STA that is operating in the DUO mode and that is a TXOP holder may indicate unavailability in a BSRP Trigger frame
This contribution analyzes the issues for unsolicited unavailability indications and gives some proposals for the conditions for the unsolicited unavailability indications to be further considered.

## Slide 3: Issues for unsolicited unavailability indications
The following motion has passed, but the detailed conditions for the unsolicited unavailability indications need further consideration.
The following conditions for transmitting unsolicited unavailability indications that can be sent by a non-AP as a TXOP holder in a BSRP GI3 trigger frame:
  No restriction when sent with QoS data transmitted in the TXOP
  When sent without QoS data transmitted in the TXOP, not more than MaxStandaloneDuoBSRP number of times every beacon interval where MaxStandaloneDuoBSRP is a non-zero value and part of the DUO parameter set indicated by the AP
  Note: BSRP GI3 Trigger frame is a BSRP Trigger frame that solicits an M-BA response that is carried in non-HT (dup) PPDU format
The excessive unsolicited unavailability indications would increase communication overhead and decrease the network performance. Unnecessary unsolicited unavailability indications especially carried in BSRP GI3 trigger frames should be disallowed.

## Slide 4: Proposals for unsolicited unavailability indications
The following conditions for transmitting unsolicited unavailability indications that can be sent by a non-AP as a TXOP holder in a BSRP GI3 trigger frame:
AP can enable or disable the non-AP STA to transmit unsolicited unavailability indications in a BSRP GI3 trigger frame during a time period if allowed.
The non-AP STA in DUO mode can transmit unsolicited unavailability indications in a BSRP GI3 trigger frame if it has received the indications that AP has buffered data for the non-AP STA.

## Slide 5: Summary
This contribution analyzes the issues for the unsolicited unavailability indications and proposes that the following conditions for transmitting unsolicited unavailability indications need to be considered :
AP can enable or disable the non-AP STA to transmit unsolicited unavailability indications in a BSRP GI3 trigger frame during a time period if allowed.
The non-AP STA in DUO mode can transmit unsolicited unavailability indications in a BSRP GI3 trigger frame if it has received the indications that AP has buffered data for the non-AP STA.

## Slide 6: References
[1] IEEE P802.11bn/D0.3
[2] tgbn-motions-list-part-2, https://mentor.ieee.org/802.11/dcn/25/11-25-0014-24-00bn-tgbn-motions-list-part-2.pptx
[3] tgbn-motions-list-part-1, https://mentor.ieee.org/802.11/dcn/24/11-24-0171-26-00bn-tgbn-motions-list-part-1.pptx
[4] Improving acknowledgment mechanisms, https://mentor.ieee.org/802.11/dcn/24/11-24-0414-01-00bn-improving-acknowledgment-mechanisms.pptx
Liuming Lu (OPPO)

## Slide 7: SP1
SP 1: Do you agree that the following conditions for transmitting unsolicited unavailability indications in a BSRP GI3 trigger frame for the non-AP STA in DUO mode need to be considered :
AP can enable or disable the non-AP STA in DUO mode to transmit unsolicited unavailability indications in a BSRP GI3 trigger frame during a time period if allowed.
The non-AP STA in DUO mode can transmit unsolicited unavailability indications in a BSRP GI3 trigger frame if it has received the indications that AP has buffered data for the non-AP STA.
Liuming Lu (OPPO)