## Slide 1: Discussion on In-device Coexistence
Date: 2025-06-01
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Chaoming Luo |  |  |  | 
Ning Gao |  |  |  | 
Liangxiao Xin |  |  |  | 

## Slide 2: Introduction
A non-AP STA in Dynamic Unavailability Operation (DUO) mode can indicate unavailability in certain Control frames, where the unavailability might overlap with the ongoing TXOP.
  Unsolicited unavailability indications:
  A DUO non-AP STA that is operating in the DUO mode and that is a TXOP holder may indicate unavailability in a BSRP Trigger frame
  Internal Interference Indication:
  The STA may indicate to the AP whether the errors of receiving MPDUs are due to internal interference.
This contribution analyzes the issues for unsolicited unavailability indications and internal interference indication, and gives some proposals to resolve the two issues to be further considered.

## Slide 3: Issues for unsolicited unavailability indications
The following motion has passed, but the detailed conditions for the unsolicited unavailability indications need further consideration.
The following conditions for transmitting unsolicited unavailability indications that can be sent by a non-AP as a TXOP holder in a BSRP GI3 trigger frame:
  No restriction when sent with QoS data transmitted in the TXOP
  When sent without QoS data transmitted in the TXOP, not more than MaxStandaloneDuoBSRP number of times every beacon interval where MaxStandaloneDuoBSRP is a non-zero value and part of the DUO parameter set indicated by the AP
  Note: BSRP GI3 Trigger frame is a BSRP Trigger frame that solicits an M-BA response that is carried in non-HT (dup) PPDU format
The excessive unsolicited unavailability indications would increase communication overhead and decrease the network performance. Unnecessary unsolicited unavailability indications especially carried in BSRP GI3 trigger frames should be disallowed.

## Slide 4: Proposals for unsolicited unavailability indications
The following conditions for transmitting unsolicited unavailability indications that can be sent by a non-AP as a TXOP holder in a BSRP GI3 trigger frame:
AP can enable or disable the non-AP STA to transmit unsolicited unavailability indications in a BSRP GI3 trigger frame during a time period if allowed.
The non-AP STA in DUO mode can transmit unsolicited unavailability indications in a BSRP GI3 trigger frame if it has received the indications that AP has buffered data for the non-AP STA.

## Slide 5: Issues for Internal Interference Indication
The following SP has been run but fails:
Do you support to add internal errors reporting in M-BA frame
Internal (in device) Error Occurred bit is 1 if internal (in-device) error(s) occurred during the reception of the PPDU that solicited the M-BA response
  I.e., unsuccessful RX reports in BlockAck Bitmaps in the M-BA are due to internal errors
Internal (in device) Error Occurred bit is 0 if no internal (in-device) error(s) occurred or if the source of error is unknown
  I.e., unsuccessful RX reports (if any) in BlockAck Bitmaps in M-BA are not due to internal (in-device) errors or if the source of error is unknown
Location of the Internal Error Occurred bit in the M-BA frame is TBD
Note: Internal errors might be due to internal in-device coexistence or other internal limitations
During the discussion some members mentioned that more information needs to be added to the M-BA frame to help the originator distinguish between IDC issues and channel issues

## Slide 6: Proposals for Internal Interference Indication
Proposal: to add more info. (i.e. channel measurement info., past and/or future unavailability info) help the originator distinguish between IDC issues and channel issues
Suggest to add internal errors reporting in M-BA frame with additional information
 Internal (in device) Error Occurred bit is 1 if internal (in-device) error(s) occurred during the reception of the PPDU that solicited the M-BA response
o I.e., unsuccessful RX reports in BlockAck Bitmaps in the M-BA are due to internal errors
 Internal (in device) Error Occurred bit is 0 if no internal (in-device) error(s) occurred or if the source of error is unknown
o I.e., unsuccessful RX reports (if any) in BlockAck Bitmaps in M-BA are not due to internal (in-device) errors or if the source of error is unknown
o  SNR degradation bit is 1 if SNR degradation occurred, 0 otherwise.
o  RSSI degradation bit is 1 if RSSI degradation occurred, 0 otherwise.
o  Past unavailability info if have not been reported.
 future unavailability info if known
 Location of the Internal Error Occurred bit in the M-BA frame is TBD
Note: Internal errors might be due to internal in-device coexistence or other internal limitations

## Slide 7: Summary
This contribution analyzes the issues for the unsolicited unavailability indications and proposes that :
The following conditions for transmitting unsolicited unavailability indications need to be considered :
AP can enable or disable the non-AP STA to transmit unsolicited unavailability indications in a BSRP GI3 trigger frame during a time period if allowed.
The non-AP STA in DUO mode can transmit unsolicited unavailability indications in a BSRP GI3 trigger frame if it has received the indications that AP has buffered data for the non-AP STA.
More info. (i.e. channel measurement info., past and/or future unavailability info) for internal interference indication needs to be added in in M-BA frame to help the originator distinguish between IDC issues and channel issues

## Slide 8: References
[1] IEEE P802.11bn/D0.3
[2] tgbn-motions-list-part-2, https://mentor.ieee.org/802.11/dcn/25/11-25-0014-24-00bn-tgbn-motions-list-part-2.pptx
[3] tgbn-motions-list-part-1, https://mentor.ieee.org/802.11/dcn/24/11-24-0171-26-00bn-tgbn-motions-list-part-1.pptx
[4] Improving acknowledgment mechanisms, https://mentor.ieee.org/802.11/dcn/24/11-24-0414-01-00bn-improving-acknowledgment-mechanisms.pptx
[5] Improving acknowledgment mechanisms, https://mentor.ieee.org/802.11/dcn/24/11-24-0414-01-00bn-improving-acknowledgment-mechanisms.pptx
[6] D0.1 CID1751 CR, https://mentor.ieee.org/802.11/dcn/25/11-25-1009-01-00bn-d0-1-cid1751-cr.docx
[7] may-july-tgbn-teleconference-agenda, https://mentor.ieee.org/802.11/dcn/25/11-25-0986-20-00bn-may-july-tgbn-teleconference-agenda.docx
Liuming Lu (OPPO)

## Slide 9: SP1
SP 1: Do you agree that the following conditions for transmitting unsolicited unavailability indications in a BSRP GI3 trigger frame for the non-AP STA in DUO mode need to be considered :
AP can enable or disable the non-AP STA in DUO mode to transmit unsolicited unavailability indications in a BSRP GI3 trigger frame during a time period if allowed.
The non-AP STA in DUO mode can transmit unsolicited unavailability indications in a BSRP GI3 trigger frame if it has received the indications that AP has buffered data for the non-AP STA.
Liuming Lu (OPPO)

## Slide 10: SP2
Do you support to add internal errors reporting in M-BA frame with the following information:
Internal (in device) Error Occurred bit is 1 if internal (in-device) error(s) occurred during the reception of the PPDU that solicited the M-BA response
  I.e., unsuccessful RX reports in BlockAck Bitmaps in the M-BA are due to internal errors
Internal (in device) Error Occurred bit is 0 if no internal (in-device) error(s) occurred or if the source of error is unknown
  I.e., unsuccessful RX reports (if any) in BlockAck Bitmaps in M-BA are not due to internal (in-device) errors or if the source of error is unknown
  SNR degradation bit is 1 if SNR degradation occurred, 0 otherwise.
  RSSI degradation bit is 1 if RSSI degradation occurred, 0 otherwise.
  Past unavailability info if have not been reported.
  future unavailability info if known
Location of the Internal Error Occurred bit in the M-BA frame is TBD
Note: Internal errors might be due to internal in-device coexistence or other internal limitations