## Slide 1: EDP AID-list handling on long power-save scenarios
Date: 2025-01-16
Authors:

## Slide 2: Abstract
Proposed method to handle idle EDP stations, for durations longer than the AID Storage Size, ensuring a smooth transition to active phase, without having to do a full new authentication and parameter negotiation process.

## Slide 3: Problem statement
BSS max idle period allows battery operated devices to avoid waking up often and send null frames, just to signal their continuous presence in the BSS.
The max idle time can reach more than 16 minutes (1000x1024 µSec).
With 802.11bi EDP, when setting a large Max Idle Timeout, the non-AP MLD may sleep beyond the AID Storage Size, resulting in a scenario where the STA wakes up with no usable AID.

## Slide 4: Proposed solution
Define the following:
AID-list handling policy during the EDP non-AP MLD sleep time
  Enforced by the AP MLD
Method to refresh the AID-list when the EDP non-AP MLD wakes up
  Freezing the current AID list is not possible as the AP MLD may reassign AIDs to other non-AP MLDs outside the assigned epochs
  Use when no usable AID is available (either expired or flushed)

## Slide 5: AID list sleep management policy
How long the AP should preserve the AID list for an EDP non-AP MLD that goes to sleep, depends on the usage scenario.
Some examples:
Residential use case
  No constraint on AID availability, prioritize quick recovery of the STA when waking up
  The AP shall keep the full AID list while the STA sleeps
Enterprise/Public Venue use case
  The AP may want to reuse the AIDs as much as possible, given the scarce number of available AIDs
  The AP may flush the AIDs soon after the STA goes to sleep to reassign them to other STAs

## Slide 6: AID list sleep management policy (cont.)
EDP AP MLD to advertise the policy as a new EDP Epoch Settings field element.
Use a counter to define the maximum number of epochs the AP will preserve the current AID list.

## Slide 7: Refresh the expired AID list
The non-AP MLD may not have any usable AID when it wakes up:
The list has expired due to long sleep
The AP MLD flushed the AID list based on the AID list sleep policy
In this scenario, the non-AP MLD shall request a new AID list at wake-up time:
Use AID Assignment Response frame with Status Code set to NO_ASSIGNED_AID to request AP to provide a new AID value assignment (as per 1714r6)
If the non-AP MLD doesn’t request the refreshed list as the first action on wake-up, the AP MLD shall disassociate the non-AP MLD, with Status Code NO_ASSIGNED_AID

## Slide 8: Conclusions
Long sleep time requires a method to handle the AID assignment
Proposal to introduce an AID list management on sleep policy
Proposal to extend use of AID assignment response frame to be used when non-AP MLD wakes up without a valid AID

## Slide 9: Straw poll #1
Do you support a mechanism where the EDP AP MLD can advertise its policy for AID-List management on power-save?
Yes
No
Abstain

## Slide 10: Straw poll #2
Do you support a mechanism for the EDP non-AP MLD to request an AID-List refresh on wake-up without a valid AID via protected action frame?
Yes
No
Abstain

## Slide 11: References
IEEE 802.11-24/1714r5 Proposed spec text for AID anonymization
IEEE 802.11-24/1105r1 AID anonymization