## Slide 1: Channel Measurement Announcement
Date: 2025-1-15
Authors:

## Slide 2: Introduction
Off Channel Scan is widely used on AP devices to measure channel quality to optimize channel
Still many APs or non-AP STAs have difficulty obtaining accurate channel measurements without dedicated scan period.
We found issues with packet losses in mesh networks when the Controller sends small packets to the Wireless Extender, while the latter is busy doing an off-channel scan.
In this contribution, we propose a Channel Measurement Announcement (CMA) to signal an off-channel scan to peer STAs. The CMA will include information about the channel to be scanned.

## Slide 3: Packet lost issue during off channel scan
Topology: Mesh network (root – wireless backhaul - extender)
Continuous Ping(Small size packet, no RTS/CTS) from root to extender (no dedicated scan chain)
Extender perform off channel every 1min, dwell time is 100ms
Packet Loss is seen on root during extender perform off channel sometimes
We also monitor packet loss issue especially Hi-Q video service played on backhaul during peer off channel scan
Root AP
Extender STA-AP
AP txop
STA txop
AP Send packet to STA on channel 1
STA response packet to STA on channel 1
AP txop
STA switch to channel 11 to scan.
AP send new packet on channel 1 to STA, after maximum retires reach, packet drop or send successfully but with many retires
Time

## Slide 4: Recap) In-Device Coexistence
In [1] introduced,
In general, for predictable and non-urgent co-ex events, the STA (/AP) can notify the other AP(/STA) ahead of time about the upcoming unavailability for operation
  Existing technologies defined in 802.11, such as peer-to-peer TWT, can be used or enhanced to support these co-ex events For urgent co-ex events, a TXOP-level intervention is needed
  The STA(/AP) can indicate within a TXOP the reduced capability of operation due to the co-ex events
  Control frames can be used to make such indications—
    Truncated TXOP
    Reduced BW
    Reduced RX NSS etc.
  Measurement as off channel scan is similar with co-existence event which is absence event with availability info on new channel or reduced RX NSS on current operating channel, and unavailability info as start time and duration on current operating channel.

## Slide 5: Measurement Benefits
  Recap )[2], list problems of existing Measurement,
  Measurement usual takes long time due to Beacon interval or active scans.
  Long term measurement create several problems as power consumption.
  Coordinated Observation Type and Transmission Type proposed.
  Also, we found some user cases as band steering, we want to observe unassociated
  link metric(RSSI) but some stations don’t send probes on that link.
  But if we can announce measurement type to that station, the station could send a probe
  packet on measurement link. It can reduce measurement time and help observer get accurate
  unassociated link metric.
  Measurement Announcement should be benefit to various measurement types.

## Slide 6: CMA signaling
Root AP
Extender STA-AP
AP txop
STA txop
AP Send packet to STA on channel 1
STA repsonse packet to AP on channel 1
AP txop
STA switch to channel 11 to scan.
AP defers transmitting to STA on channel 1
Time
CMA
We proposal to send Channel Measurement Announcement to Peer before do measurement on off channel
Signal Info Field:
Measurement Type 2) Measurement Mode( Any restriction on receive packet on scan channel)
3) Target Channel 4) Target Bandwidth 5) Start time 6) Duration 7) Available NSS

## Slide 7: CMA VS Unavailability reporting
CMA | DUO/PUO/LOM
No negotiation requires | negotiation requires
AP/Non-AP STA support | AP DUO unsupported APPUO requires all associated stations support PUO AP LOM requesting mode unsupported
One frame contains all signal info | Need multiple frames (assumption: No dedicate unavailability reason and its info in Unavailability feedback)

## Slide 8: Option 1
A new Channel Announcement Frame including:
Measurement info
Unavailability info
LOM info (Option)

## Slide 9: Option 2
Add Channel Measurement Info into unavailability feedback of :
1) DUO
2) PUO
3) LOM (Option)
Channel Measurement Info can be limited to Channel index(20Mhz),
Measurement Type to simplify, Measurement time is the same as
unavailability time info.

## Slide 10: Summary
We proposal a new signaling method (Define a new Channel Measurement Announcement frame) in 11bn to support signal channel and radio measurement information as measurement type, mode, channel, bandwidth, start time, duration, available NSS etc. to fix packet loss, latency, long measurement time and other measurement issues.
Also, we add option proposal to extend unavailability feedback info to include dedicated channel measurement info.

## Slide 11: Straw Poll 1
Do you agree that TGbn defines a new action frame(Channel Measurement Announcement) to signal channel and radio measurement info, detail signal info is TBD?
YES
No
Abstain

## Slide 12: Straw Poll 2
Do you agree that TGbn add channel measurement info(channel index, measurement type) into unavailability feedback on DUO/PUO mode if unavailability reason is channel or radio measurement?
Note. Measurement Bandwidth is 20Mhz, Measurement Start Time and Duration is the same as Unavailability Target Start Time and Unavailability Duration in the unavailability feedback.
YES
No
Abstain

## Slide 13: Straw Poll 3
Do you agree that TGbn add below info into Channel Measurement Info? Other signal info is TBD
Measurement Type
2) Measurement Mode( Any restriction on receive packet on scan channel)
Target Channel
Target Bandwidth
Start time
Duration
Available NSS
YES
No
Abstain

## Slide 14: References
[1] 24/0509r1, “Thoughts on in-device coexistence and P2P for 11bn”
[2] 24/1452r3, “Coordinated Measurement: Follow-up”
[3] 24/2040r9, “PDT MAC Coexistence”
[4] Draft P802.11bn_D1.0.pdf