## Slide 1: Elicitation of Response Transmissions in Coordinated Spatial Reuse
Date: 2025-01-17
Authors:

## Slide 2: Abstract
This contribution discusses an issue that may happen in coordinated spatial reuse (C-SR) when a response transmission is elicited by a shared AP and proposes a solution to deal with this issue.

## Slide 3: Backgrounds
Coordinated spatial reuse (C-SR) is a UHR feature that allows two APs to perform concurrent downlink (DL) single-user (SU) equal-duration transmissions, which are initiated using a trigger frame transmitted by a sharing AP and carrying a specified duration of the initiated C-SR transmissions (Motions 29, 206, 253, and 254)
In C-SR, a sharing AP controls the maximum transmit power of a shared AP but not that of any non-AP STA in the shared AP’s BSS [1] (Motion 29)
Hence, if a shared AP elicits a response transmission from a non-AP STA, the elicited response transmission may be sent with a (non-controlled) transmit power that results in a corruption of another response transmission elicited by the sharing AP, as described in the following

## Slide 4: Main Issue
Consider the following scenario:
  STA1 is associated with AP1 and STA2 is associated with AP2
  The path loss between AP1 and STA1 is equal to the path loss between AP1 and STA2
  By employing C-SR, the simultaneous DL transmissions from AP1 and AP2 are successful, if the sharing AP properly controls the maximum transmit power of the shared AP, and the shared AP properly selects an MCS value for its transmission to STA2, based on the interference from the sharing AP to STA2 (which is known to the shared AP via a measurement/report scheme) [2]
time
Co-trigger
Sharing AP
DL PPDU
SIFS
time
Shared AP
DL PPDU
Desired signal
Interference signal
STA1
STA2
AP1
(Sharing AP)
AP2
(Shared AP)
Room 3
Room 1
Room 2
Room 4
An interference that is controlled by the sharing AP
Successful DL transmissions by the sharing AP and shared AP
Illustration of DL PPDU transmissions by the sharing AP and shared AP

## Slide 5: Main Issue
Consider the following scenario:
  STA1 is associated with AP1 and STA2 is associated with AP2
  The path loss between AP1 and STA1 is equal to the path loss between AP1 and STA2
  However, the ACK frame transmission from STA1 to AP1 may not be successful (even with MCS 0), as a result of a high interference that is caused by the ACK frame transmission from STA2 to AP2 with an uncontrolled transmit power, resulting in an SINR of approximately 0 dB at the sharing AP
Desired signal
Interference signal
STA1
STA2
AP1
(Sharing AP)
AP2
(Shared AP)
Room 3
Room 1
Room 2
Room 4
Uncontrolled interference
time
Co-trigger
Sharing AP
DL PPDU
SIFS
ACK
SIFS
time
Shared AP
DL PPDU
ACK
SIFS
Illustration of ACK frame transmissions by STA1 and STA2
Unsuccessful ACK transmission from STA1 to the sharing AP

## Slide 6: Proposed Solution
Allow a sharing AP to optionally require a shared AP not to transmit any frame that elicits an SIFS-separated response transmission
In this case, the Ack policy for a DL frame sent by the shared AP can possibly be set to ‘No Ack’ or ‘Block Ack’
Hassan Omar et al., Huawei Technologies
time
Co-trigger
Sharing AP
DL PPDU
SIFS
ACK
SIFS
time
Shared AP
DL PPDU
BA
Successful ACK transmission from STA1 to the sharing AP
BAR
SIFS
Block Ack transmitted by STA2 after receiving a Block Ack Request (BAR) frame
The Ack policy of a carried frame is set to Block Ack

## Slide 7: Conclusions
In several C-SR scenarios, the elicitation of a response transmission by a shared AP may impact another response transmission elicited by a sharing AP
To deal with this issue, it is suggested that, a sharing AP can optionally require a shared AP not to transmit any frame that elicits an SIFS-separated response transmission

## Slide 8: References
[1] 11-24-0050-00bn-coordinated-spatial-reuse-types
[2] 11-23-1832-00bn-multi-ap-coordinated-spatial-reuse

## Slide 9: SP
In coordinated spatial reuse (C-SR), do you agree that:
  A sharing AP may require a shared AP not to transmit any frame that elicits an SIFS-separated response transmission.
  Note: this requirement applies only throughout the C-SR transmission duration specified in the trigger frame that initiates the C-SR transmissions
  Yes
  No
  Abstain