## Slide 1: Indication for co-exist event follow up
Date: 2025-01-24
Authors:
Name | Affiliation | Address | Mail
Xiangxin Gu | Spreadtrum | Spreadtrum Center, Lane 2288, Zu Chongzhi Road, Shanghai | Xiangxin.gu@unisoc.com
Yingqiao Quan | Spreadtrum |  | Yingqiao.quan@unisoc.com
Lei Zhou | H3C |  | zhou.leiH@h3c.com

## Slide 2: Recap
11bn has made good progress on mechanisms for coexistence and power save.
In Kobe session, we discussed and run the following SP.
SP6 – Laurent Cariou – Miscellaneous:
  Do you agree to add to the 11bn SFD:
  • For the following features, if an AP supports the feature, then it shall accept a request from an associated non-AP STA to enable or disable the feature for the non-AP STA
    • Dynamic unavailability operation
    • Dynamic power save
Result: 121Y, 50N, 54A
During the discussion, abuse issue was pointed out.

## Slide 3: Discussion
In document 24/1445, we discussed dynamic unavailability.
  For a STA’s dynamic unavailability:
    Unsolicited indication for the coming unavailability. It doesn’t always work because of stringent time. Taking Bluetooth 2.1 for instance, the TX event can be known only less than 1.25 milliseconds in advance.
    Always querying with ICF before transmission which leads to much overhead.
We also proposed the STA to inform its associated AP the statistic parameters of the dynamic unavailability when the STA request to enable dynamic unavailability, such as average periodicity, average duration, largest duration, etc.
  The AP may based on these parameters make the decision to accept or reject the request.
  If the AP accepts the request it can leverage these parameters and make better transmission:
    Transmitting to the STA with ICF or
    Transmitting at time of a lower possibility to encounter the STA’s unavailability period.
  If the AP rejects the request:
    The STA should indicate the AP the coming unavailability in advance with unsolicited indication.
    If it failed to indicate the unavailability, it may signal the AP the unavailability just happened for retransmission.

## Slide 4: Proposal 1
A STA requests to enable dynamic unavailability to its associated AP with the statistic parameters of the dynamic unavailability
  Such as average periodicity, average duration, largest duration, etc.
  The AP may based on these parameters make the decision to accept or reject the request.
  If the AP accept the request, it can leverage these parameters and make better transmission:
    Transmitting to the STA with ICF or
    Transmitting at time of a lower possibility to encounter the STA’s unavailability period.
AP
STA
OpenBT, …
Enable dynamic unavailability
(parameters)
…
Close BT, ….
Disable dynamic unavailability

## Slide 5: Proposal 2
The STA may signal the AP the unavailability just happened and not indicated ahead.
  With information such as the start time and the duration of the unavailability.
  To trigger a retransmission if a transmission failure happened during the unavailability.
  For the AP to decide MCS downgrading or not.
AP
STA
Co-ex Event happened
Co-ex Event happened
Data
Data (reTX)
BA

## Slide 6: SP 1
Do you agree to that a STA requests to enable dynamic unavailability to its associated AP with the statistic parameters of the dynamic unavailability?
  Such as average periodicity, average duration, largest duration, etc.
  For the AP to decide whether to accept or reject the request.

## Slide 7: SP 2
Do you agree to that a STA may signal its associated AP the unavailability just happened and not indicated ahead?
  With information such as the start time and the duration of the unavailability.
  To trigger a retransmission if a transmission failure happened during the unavailability.
  For the AP to decide MCS downgrading or not.

## Slide 8: References
[1] 11-23-1934-00-00bn-in-device-interference-mitigation-follow-up Liwen Chu
[2] 11-23-1964-01-00bn-coexistence-protocols-for-uhr Alfred Asterjadhi
[3] 11-23-2002-02-00bn-in-device-coexistence-and-interference-follow-up Laurent Cariou
[4] 11-23-2026-00-00bn-balanced-wireless-in-device Brian Hart
[5] 11-23-2078-05-00bn-coex-enhancement-for-xr-use-cases Guoqing Li
[6] 11-24-0094-00-00bn-probe-before-talk-and-unsolicited-unavailability-announcement-for-co-ex-management Qi Wang
[7] 11-24-0420-00-00bn-enabling-flexible-coexistence-operation Guogang Huang
[8] 11-24-0436-00-00bn-sp-based-in-device-coexistence Jason Guo
[9] 11-24-0494-02-00bn-in-device-coexistence-follow-up Liwen Chu
[10] 11-24-1445-01-00bn-indication-for-coex-event Xiangxin Gu
[11] meeting minutes