## Slide 1: SMD Roaming Context Transfer
Date: 2025-06-12
Authors:

## Slide 2: DL Context Transfer
As part of roaming context transfer, the next SN (per TD) to be assigned by the target AP MLD in DL is transferred to the target AP MLD.
  The next SN would account for some buffer SN values for more MSDUs that can trickle down from DS
Per PDT, the current AP MLD should send the information for termination of DL data transmissions to the non-AP MLD during DLDrainTime.
When non-AP MLD learns that DL data transmission is completed with current AP (per TID or AC), then it needs to advance its Receive BA window and not wait for MPDUs with SN smaller than the next SN
  MPDUs with SNs in the SN Gap will not be received
Hence, next SN value (per TID) should be provided to non-AP MLD in the roaming response, and the non-AP MLD needs to advance its Rx BA window if it receives an indication of termination of DL data from current AP MLD (overall or for that TID or corresponding AC)
1 | 2 | 3 | 4 | … | y1 |  |  |  | n1 | … |  | 
DL Rx Reorder
Buffer at Client
MPDUs from Serving AP
SN Gap = set of SNs that will not be received
MPDUs from Target AP
Next SN
Last MPDU

## Slide 3: UL Context Transfer (1)
For UL, the current AP MLD would transfer MPDUs up to the first in-order received MPDUs to the DS to preserve in-order delivery. Per PDT, latest SN (per TID) delivered to the DS is transferred to the target AP MLD as part of context transfer during roaming.
When SN continuity maintained, the non-AP MLD should send UL MPDUs with SNs following the ’latest SN’ to the target AP MLD, after it receives the roaming execution response.
Even when an UL MPDU is ack’d by the current AP and forwarded to the DS, the Ack may get lost and non-AP MLD may believe that the MPDU was not successfully received by the current AP.
  Then, STA would send that MPDU to the target AP again, which will get discarded by the target AP (since SN will be smaller than latest SN sent to target AP). This wastes network bandwidth.
Hence, useful to send the latest SN (per TID) that has been passed up to the DS to the non-AP MLD in roaming execution response. Non-AP MLD shall only transmit UL MPDUs to the target AP MLD with SNs higher than the latest SN (even if it didn’t receive Ack for some MPDU(s)).
Even when UL SN is reset for target AP, knowing latest SN (per TID) delivered to DS by current AP is needed, such that non-AP MLD does not transmit an MPDU to the target AP that was already delivered to the DS by the current AP. This is important to avoid duplicate delivery to upper layer.

## Slide 4: UL Context Transfer (2)

## Slide 5: DL/UL SN Context Transfer
Roaming PDT covers that SN context is transferred to the target AP (unless requested not to be transferred by STA), but it does not specify in what roaming phase SN context is transferred.
For SN continuity to work, the SN context needs to be transferred as part of the roaming execution phase, to provide latest SN context to the target AP. Need to add this clarification in the roaming PDT.

## Slide 6: SP: DL Context Transfer
SP1: Do you agree that for seamless roaming, the next SN (per TID) that is transferred to the target AP MLD to be assigned for DL individually addressed data frames, shall be provided to the non-AP MLD by the current AP MLD in the roaming execution response?
SP2: Do you agree that for seamless roaming if the next SN (per TID) is transferred to the target AP MLD, the non-AP MLD upon receiving an indication of termination of DL data transmission for a TID from the serving AP MLD or expiry of DLDrainTime, shall advance its WinStartB to either next SN (for that TID) or upto the SN that has been successfully received?

## Slide 7: SP: UL Context Transfer
SP3: Do you agree that for seamless roaming, the latest SN (per TID) that is delivered to the DS for UL by the current AP MLD is provided to the non-AP MLD in the roaming execution response?
  If UL SN is not reset at the target AP MLD, the non-AP MLD shall only transmit UL MPDUs to the target AP MLD with SNs higher than the latest SN received.
  If UL SN is reset at the target AP MLD, the non-AP MLD shall not transmit any MSDUs to the target AP that was already delivered to the DS as per latest SN received.

## Slide 8: SP: SN Context Transfer
SP4: Do you agree that for seamless roaming, when a non-AP MLD does not request that SN context for DL and UL is not to be transferred to the target AP MLD, the current AP MLD shall transfer the following SN context to the target AP MLD after it receives a roaming execution request from the non-AP MLD?
  The next SN to be assigned for DL individually addressed Data frame of each TID.
  The latest duplicate receiver cache for each TID without block ack agreement.
  The latest SN that has been passed up to the DS for each TID with UL block ack agreement.