## Slide 1: Buffered DL Data Handling for Seamless Roaming
Date: 2024-06-10
Authors:

## Slide 2: Introduction
TGbn SFD has following motion that cover the aspects of buffered DL data handling for seamless roaming:
  As part of the seamless roaming procedure, during roaming,
    after the request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD,
      The current AP MLD may deliver buffered DL data frames for a TBD period of time.
      The non-AP MLD may retrieve buffered DL data frames from the current AP MLD
      The non-AP MLD may send UL data to target AP MLD.
      It is assumed that the target AP MLD is able to deliver data frames to non-AP MLD after the DS mapping change
    The current AP MLD may forward DL data to the target AP MLD.
      When and how to initiate the forwarding of DL data is TBD
  [Motion #27, [1] and [3, 7, 8, 42-48]]
In this presentation we propose considerations and next level of details for buffered DL data handling during seamless roaming

## Slide 3: Buffered DL Data Handling
During seamless roaming procedure to a target AP MLD, we need to define ways to handle buffered DL data of the client
Default mode: should be that the buffered DL data is drained/delivered to the client, within a time period (per SFD motion)
  Both client and the serving AP MLD must support this mode of operation to avoid/minimize data loss
  A ‘DL Data Delivery Time’ is returned in roaming execution response.
It is desirable to drain data as fast as possible, to minimize data loss
  If client is active (PM=0) on multiple links and it is an STR client, then AP should try to deliver data over multiple links
  In roaming response, AP can request client to come out of PS on one or more other links for fast delivery of DL data
When serving AP is done with delivery of buffered DL data, it explicitly signals this to the client
When client decides to completely move to target AP before DL Drain Time expires:
  It is important that it signals this to serving AP, so that AP does not keep trying to deliver buffered data to the client
  Client should signal early termination for DL data drain to the serving AP

## Slide 4: Draining of Buffered DL Data
During the DL Data Delivery Time, a client may first drain all the data from the serving AP MLD before it switches to the target AP MLD
Alternatively, a multi-radio client can be connected with both serving and target AP MLDs over different links
A single-radio client implementation may switch back-and-forth between serving and target AP MLD
  Whenever client moves to target AP, it needs to signal PM=1 for its links to the serving AP MLD, and then signal PM=0 when it comes back to retrieve remaining DL data
When client fully moves to the target AP MLD, it should signal that to the serving AP e.g. by deleting links with serving AP or other signalling means

## Slide 5: Forwarding of Buffered DL Data
SFD defines a ‘may’ requirement for current AP MLD to forward DL data to the target AP MLD
We think that data forwarding should be an optional capability provided by AP MLDs in an SMD
AP MLDs can indicate:
  Data Forwarding Supported
  Data forwarding policy (e.g. all traffic, certain ACs/TIDs/SCS stream level, MUSDUs/A-MSDUs only, limit on data size or duration for data forwarding etc.)
If serving and target AP MLDs support data forwarding, then the serving AP can perform some data forwarding, along with draining data directly to the client
  Decision on what data to drain vs forward can be made by the serving AP based on multiple factors e.g. types of active flows (VO, VI, BE), amount of buffered data, RSSI/MCS of the client, backhaul link conditions etc.

## Slide 6: Summary
This presentation covers considerations for buffered DL data handling during seamless roaming
We propose draining of buffered DL data be the default mode, and supported by both AP & STA
  Serving AP can request client to come out of PS on other links to deliver buffered DL data fast (e.g. in roaming response)
  When serving AP is done with delivery of buffered DL data, it can signal this to the client
  When client completely moves to the target AP, client notifies serving AP of early termination of DL data drain
Data forwarding can be an optional capability, announced by AP MLDs in an SMD
  AP MLD can also announce their data forwarding policy (e.g. all data, certain ACs/TIDs/SCS stream level, MSDUs/A-MSDUs only, limit on data size or duration for data forwarding etc.)
  If supported, serving AP can perform some data forwarding along with data draining.
  Decision on what to drain vs forward can be AP implementation based on e.g. active flows (VO, VI, BE), amount of buffered data, RSSI/MCS of the client, backhaul conditions etc.

## Slide 7: SP 1
Do you agree to support following for buffered DL data handling during the seamless roaming transition?
By default, the buffered DL data is drained to the non-AP MLD by the serving AP MLD
Serving AP MLD indicates whether it supports data forwarding and its TBD policy for data forwarding
If data forwarding is supported, the serving AP MLD can drain, forward or perform a combination of the two for buffered DL data

## Slide 8: SP 2
Do you agree that during the TBD time for retrieving DL data from the current AP MLD, if the non-AP MLD terminates DL data retrieval before the TBD time ends, then the non-AP MLD shall provide an indication to the current AP MLD that the DL data retrieval is early-terminated?
So that the current AP MLD can stop trying to deliver any buffered DL data to the non-AP MLD
TBD signaling of the indication