## Slide 1
Name | Affiliation | Address | Phone | Email
Ian Bajaj | Huawei | Singapore |  | ian.bajaj@huawei.com
Lei Huang |  |  |  | 
Rojan Chitrakar |  |  |  | 
SP Timing Synchronization with AMP Beacon
Date: 4 Mar 2025
Notes: Jul 12, 2010
Page 1

## Slide 2
Background
AMP Beacon was first discussed in [1]-[3] as a lighter variant of the Beacon frame used in IEEE 802.11, primarily to provide timing information to the AMP non-AP STAs.
AMP Open Service Period (OSP) was highlighted in [2] to discuss how unassociated AMP non-AP STAs can cycle between idle and operational states based on an SP Interval (namely, duty cycle period) to save significant power from random channel sensing. [4] proposed to use AMP Trigger Frame to target specific AMP non-AP STAs for duty cycle operation.
Motion MM-4 was passed in Jan F2F: “If an AMP device is able to support TSF, it can monitor AMP DL Frame in a duty-cycle manner.”
In this contribution, we wish to discuss:
  The timing synchronization issue to maintain duty cycle operation in AMP Open Service Period
  The AMP Beacon signaling method and content
  The means for AMP non-AP STAs that do not support TSF to still maintain timing synchronization to operate in a duty cycle manner.

## Slide 3
AMP Open Service Period [2] – Recap
In [2], AMP Open Service Period (OSP) was defined as a window that the AMP AP will gain a TXOP for any AMP non-AP STAs in its BSS, regardless of association.
At the start of the OSP, within the SP minimum wake duration, the AMP AP will send an AMP Poll to enable channel access for the AMP non-AP STAs. If the AMP non-AP STAs do not receive any AMP DL PPDU from the AP, the AMP non-AP STA will return to idle mode for the SP interval duration (wake up at the start of the following OSP).
The OSP parameters, namely, SP start time, SP interval and SP minimum wake duration maybe carried in an AMP Beacon frame sent periodically by the AMP AP. The SP start time maybe expressed as an absolute TSF time or a relative time from the end of frame carrying this field.

## Slide 4
Issue using AMP Trigger for Timing Synchronization
In [4], duty cycle operation was discussed for AMP, with a target trigger for each AMP non-AP STA. Each AMP non-AP STA scans for the first AMP trigger that configures the duty cycle operation, pointing the AMP non-AP STA to its target trigger or service period.
To enable this, the proposed AMP Trigger Frame may carry:
  Duty-cycle configuration (duty-cycle period/service period interval)
  Information for AMP non-AP STA to determine its target trigger, e.g. Short timestamp (local TSF spanning one or more duty cycle periods)
The target trigger reception window is shown to span 2 TUs (time units), which should be equivalent to the minimum wake duration proposed in [2]. There are two important implications here:
  The AMP Trigger frequency has to be smaller than this minimum wake duration
  The minimum wake duration is directly correlated with the maximum power consumed for reception (the period the AMP non-AP STA stays in channel sensing state)
Therefore a smaller minimum wake duration is preferred, implying a higher frequency of AMP Trigger frame transmission.
Moreover, from our analysis, carrying the SP related parameters in the AMP Trigger frame may make the frame very large, implying more power is consumed by the AMP non-AP STA in decoding the frame.

## Slide 5
AMP Beacon frame for Timing Synchronization
Our proposal is to utilize the AMP Beacon to carry SP parameters and timing related information
  This minimizes the AMP Poll/Trigger frame size which is primarily meant to enable channel access for UL transmission, and restricts the power consumed during reception.
  AMP Beacon does not require a response, therefore decoding of the entire frame is optional.
Also from our analysis, the timestamp needed to support AMP OSP operation using TSF is not short.
  12 bits is not sufficient, as previously recommended for 802.11ba, and in [1]. If following 802.11ba, we can drop the first 5 LSB of TSF, as AMP may also not require the timing granularity in the order of 32us. So TSF [5:17], covers 0.13s, i.e. 13s SP interval (or duty cycle period) for a clock drift of 1%.
  For 802.11bp, we may need to operate on lower duty cycles, say half a day. e.g. An Active Tx non-AP AMP STA that sends sensor readings twice a day (12hr) to the AMP AP. This implies 24 bits of TSF need to be carried to support 1% clock drift for this range of operation: bits. TSF [5:29] can be used to correct the clock drift over this duty cycle period.
To maintain timing, and wake up at the start of the OSP, the AMP non-AP STA may:
  Wait till the LSB of its local TSF matches the absolute SP Start Time TSF
  Count down the relative SP Start Time with a free running counter implemented in hardware (ultra-low power RTC [5][6])
If the AMP non-AP STA wakes up to perform channel sensing at a time other than the SP Start Time, the AMP Beacon frame can correct the absolute TSF or reset the local counter to synchronize the AMP non-AP STA timer to the actual start of the OSP.

## Slide 6
Timing Synchronization without TSF
For timing synchronization without the use of TSF, the AMP AP can transmit the AMP Beacon frame that contains a counter that counts down with each AMP Beacon frame to the start of the SP. We call this counter the SP Advert count, as it advertises the start of an SP. An OSP ID can be used to identify the OSP that the SP Advert count is pointing to.
  The AMP Beacon Interval must be less than the SP minimum wake duration.
  The SP Advert count needs to be indicated only closer to the start of the OSP (only to cover clock drift).
The AMP non-AP STA can reset its counter based on the remaining time to the start of the SP, given by Beacon_interval * SP_Advert_count

## Slide 7
The Beacon Timestamp (24bits) – LSB of AP TSF [5:29] to cover a clock drift over a maximum duty cycle of 15 hours (at clock accuracy).
AP Capability (8 bits) – PHY/MAC/Security related capability [3]
Beacon Interval (8 bits) – To indicate the interval of the AMP Beacon (in ms)
SP Parameter Set (0 or N*16 bits) – Each set carries OSP ID (4 bits), SP Interval (8 bits), and SP Minimum Wake Duration (4 bits, expressed as a multiple of TUs) [2]
AMP Beacon Frame Body Details
The AMP Beacon Frame Body can have a Type Dependent Control (sub-type field, presence bitmap) And Type Dependent Payload.
The Type Dependent Payload may contain:
N - no. of OSPs
SP Timing Info Set (0 or N*16 bits) – Each set carries OSP ID (4 bits), SP Start Time (12 bits)
SP Timing Sync Set (0 or N*16 bits) – Each set carries OSP ID (4 bits), SP Advert Count (10 bits), and Reserved field (2 bits)

## Slide 8
Summary
The considerations needed for timing synchronization to support duty-cycle AMP operation were discussed.
The use of the AMP Beacon frame to carry SP Parameters, and SP timing related information was proposed, to support AMP non-AP STAs operating in an AMP Open Service Period.
The means to achieve timing synchronization using TSF was discussed.
SP Advert count was introduced as a means for timing synchronization for AMP non-AP STAs that do not support TSF.
The details of the AMP Beacon Frame Body were discussed, including the number of bits necessary to cover clock drift for 802.11bp use cases.

## Slide 9: SP1
Do you agree to add the following text to TGbp SFD?
IEEE 802.11bp defines an AMP Open Service Period, that allows an AMP non-AP STA to enter doze state after a minimum wake up time since the start of the AMP Open Service Period, if the AMP non-AP STA does not receive any AMP DL PPDU from the AMP AP. An AMP Open Service Period can be uniquely identified by an OSP ID.
[Reference: 11-25/0039r0, 11-25/0285r0]

## Slide 10: SP2
Do you agree to add the following text to TGbp SFD?
IEEE 802.11bp defines an AMP Beacon frame to carry in its frame body at least one of Beacon Interval, SP Start Time, SP Minimum Wake Duration, SP Interval, and OSP ID.
[Reference: 11-25/0285r0]

## Slide 11: SP3
Do you agree to add the following text to TGbp SFD?
IEEE 802.11bp allows the SP Advert Count (name TBD) to be carried in the AMP Beacon frame, as a decremental counter that is updated with every AMP Beacon frame preceding the start of the AMP OSP, to cover the worst clock drift for the AMP non-AP STAs.
[Reference: 11-25/0285r0]

## Slide 12: References
[1] 11-24/1202r0, Scanning and discovery for AMP IoT
[2] 11-25/0039r0, AMP Open Service Period
[3] 11-25/0094r0, AMP Device Management
[4] 11-25/0032r1, Duty-cycle AMP Operation
[5] Y. Lin et al., "A 150pW Program-and-Hold Timer for Ultra-Low-Power Sensor Platforms", ISSCC Dig. Tech. Papers, pp. 326-327, Feb. 2009
[6] Y. Lee et al., "A 660pW multi-stage temperature-compensated timer for ultra-low-power wireless sensor node synchronization," 2011 IEEE International Solid-State Circuits Conference, 2011, pp. 46-48.