## Slide 1: R-TWT Sharing Follow-Up
Date: 2025-3-3
Authors:

## Slide 2: Introduction
11be defined Restricted Target Wake Time (R-TWT) to support latency sensitive traffic (e.g., by providing start time protection within the BSS)
In the TGbn SFD [1], Co-RTWT builds on R-TWT by providing mechanisms for multiple APs to coordinate and/or protect their R-TWT schedules
In addition, we proposed in 11-24/1457r0 [2] to negotiate and enable the sharing of the TXOP obtained during an R-TWT SP to support latency sensitive traffic of a neighbour (OBSS) AP
In this contribution, we provide more information on the proposed procedure

## Slide 3: Some R-TWT scheduling options
When an AP determines to schedule an R-TWT SP, it can…
Ignore OBSS R-TWT schedules
  Simplest approach
  May result in issues due to scheduling conflicts
Consider OBSS R-TWT schedules – e.g., shift to avoid conflicts
  Avoids conflicts but may result in non-optimal schedule (e.g., too early or late)
  The AP may further request protection from OBSS based on Co-RTWT
(Proposed) Leverage OBSS R-TWT schedules
  By establishing an agreement with the OBSS AP to share the TXOPs obtained for an R-TWT schedule
  The OBSS AP may accept or reject the request
  This option can allow the AP to achieve a more optimal schedule

## Slide 4: Proposed R-TWT sharing protocol
R-TWT sharing setup request – AP
  AP requests to join an OBSS AP’s R-TWT
  E.g., in an MAPC Negotiation Request (Motion#360[3])
  Includes Broadcast TWT ID to identify the desired OBSS AP’s R-TWT
  May contain information regarding the needs of the requesting AP (e.g., a preferred allocation duration)

## Slide 5: Proposed R-TWT sharing protocol
R-TWT sharing setup response – OBSS AP
  OBSS AP responds to accept or reject the request
  E.g., in an MAPC Negotiation Response (Motion#361[3])
  Includes the Broadcast TWT ID to identify the identified R-TWT
  If accepted, the AP becomes a member AP of the R-TWT (similar to baseline R-TWT operation)
  If rejected, the OBSS AP provides a reason (e.g., not able to satisfy a preferred allocation duration)

## Slide 6: Proposed R-TWT sharing protocol
R-TWT sharing teardown request – AP or OBSS AP
  An AP terminates its R-TWT sharing agreement (similar to baseline R-TWT operation)
  E.g., in an MAPC Negotiation Request
  Includes Broadcast TWT ID to identify the identified R-TWT
  May provide reason (e.g., from OBSS AP)
  No response is required

## Slide 7: Proposed R-TWT sharing protocol
Additional considerations
  The AP can obtain the OBSS AP’s R-TWT schedule from the Beacon frame
    May indicate if an AP can request sharing for this R-TWT schedule
  The OBSS AP is expected to share the TXOP obtained for the R-TWT SP with member AP(s)
    Similar to baseline R-TWT operation for member STAs in the BSS
    Sharing mechanism based on MU-RTS TXS (similar to triggered TXOP sharing)
  The AP may announce an overlapping R-TWT schedule for STAs in its BSS

## Slide 8: Summary
When considering to schedule an R-TWT SP, an AP may prefer to leverage an existing R-TWT schedule of a neighbour (OBSS) AP by requesting the neighbour AP to share the TXOP obtained during the R-TWT SP (R-TWT sharing)
A protocol for enabling R-TWT sharing is proposed

## Slide 9: Straw Poll 1
Do you agree to add the following text to the SFD “11bn shall define a mechanism that enables an AP to request an OBSS AP to share the TXOPs obtained during the R-TWT SPs of a desired R-TWT schedule of the OBSS AP.”
  Y
  N
  A

## Slide 10: Straw Poll 2
Do you agree to add the following text to the SFD “Upon acceptance of a request to share its R-TWT with an OBSS AP, an AP shall share a portion of the TXOP obtained for the corresponding R-TWT SPs, with the OBSS AP.”
  Y
  N
  A

## Slide 11: References
[1] Ross Jian Yu (Huawei), 'Specification Framework for TGbn', 24/209r9, Feb, 2025
[2] Gaius Wee (Panasonic), 'R-TWT Sharing', 24/1457r0, Sep, 2024
[3] Alfred Asterjadhi (Qualcomm Technologies Inc.), 'tgbn-motions-list-part-2', 25/14r13, Mar, 2025