## Slide 1: Feasibility Study of Phase-Synchronization for Wireless Federated Learning on WLAN
Date: 2025-03-07
Authors:

## Slide 2: Abstract
In this contribution, we discuss the feasibility of coherent over-the-air computation (OAC) to support federated learning on WLAN
  We discuss an approach to compensate the phase mismatches between the STAs and AP to achieve phase synchronization in the network
  We show proof-of-concept demonstrations on the phase synchronization

## Slide 3: Federated Learning over WLAN
Federated learning (FL) is one of the approaches to train or refine a neural network based on data distributed across a network
  Since the data does not leave where it is generated, it promotes the data privacy [1]
With FL, a large number of neural network parameters (e.g., ) is transmitted in the uplink (UL) and downlink (DL) many times and there can be many devices
  Problem: Congestion in spectrum that is worsened with the number of STAs and the neural network size

## Slide 4: Recap - How Does FL Work over a Wireless Network? [2]
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
An example procedure:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model
(and go back Step 1)
Model update rule:

## Slide 5: Recap - How Does FL Work over a Wireless Network? [2]
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
An example procedure:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model
(and go back Step 1)
Model update rule:

## Slide 6: Recap - How Does FL Work over a Wireless Network? [2]
STA
STA 2
STA
AP
…
…
Calculate gradients
An example procedure:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model
(and go back Step 1)
Model update rule:

## Slide 7: Recap - How Does FL Work over a Wireless Network? [2]
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
An example procedure:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model
(and go back Step 1)
Model update rule:

## Slide 8: Recap - How Does FL Work over a Wireless Network? [2]
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
Averaging & model update
An example procedure:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model
(and go back Step 1)
Model update rule:

## Slide 9: Communication Bottleneck
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
  The occupied time (or bandwidth) increase linearly with the number of STAs and the neural network size
…
Bandwidth
Time
Frequency
Occupied time
e.g., with TDMA:

## Slide 10: Over-the-Air Computation (OAC)
OAC aims to aggregate the gradients via superposition in the channel
  Benefit: A major saving in resource consumption as the resource utilization does not grow with the number of STAs
Bandwidth
Time
Frequency
Occupied time
All STAs transmit simultaneously & gradient aggregation occurs in the wireless channel through signal superposition
…
Is this really feasible given multi-path channel & hardware impairments?

## Slide 11: Over-the-Air Computation (OAC)
OAC aims to aggregate the gradients via superposition in the channel
  Benefit: A major saving in resource consumption as the resource utilization does not grow with the number of STAs
Bandwidth
Time
Frequency
Occupied time
All STAs transmit simultaneously & gradient aggregation occurs in the wireless channel through signal superposition
…
Is this really feasible given multi-path channel & hardware impairments?

## Slide 12: A Primary Challenge for OAC: Phase Synchronization
The transmitted symbols (e.g., gradients) from all STAs should add up coherently at the AP side
  However, the channel coefficients cause incoherent superposition
    They depend on multipath, impairments (e.g., CFO, phase offset (PO)), and RX’ed power
  The AP side processing (e.g., equalization) is not helpful to recover from
    This is because the superposition occurs after the impact of channels on the transmitted signals
Multi-path channel & CFO, noise?
Incoherent superposition
…

## Slide 13: A Closer Look at Phase Errors in UL and DL (1/2)
Assuming that the same oscillator is used at the TX and RX chains at each radio, the channel between the AP and a STA for an OFDM subcarrier:
DL channel
CFO and PO
UL channel
CFO and PO
AP
STA
STA
STA
…
…
Downlink (DL) channel
Uplink (UL) channel
(: a pilot symbol)

## Slide 14: A Closer Look at Phase Errors in UL and DL (2/2)
Observation: The phase errors in UL and DL evolve rapidly due to the CFO
  A CFO pre-compensation, e.g. [3], may be used to mitigate the phase evolutions
DL phase error
UL phase error
AP
STA
STA
STA
…
…
Downlink (DL) channel
Uplink (UL) channel
(: a pilot symbol)

## Slide 15: Phase-Coded Pilots (1/4)
An example procedure to correct the UL phase error for OAC is as follows:
AP:
STA :
Phase est.
Step 1a
: Transmit a pilot from AP
: Transmit a phase-coded pilot from STA
: Transmit a phase-coded pilot from AP
(Aggregation) : Transmit a phase-coded parameter (e.g., is a gradient) from STA
STA estimates the phase in DL:
Note: We assume

## Slide 16: Phase-Coded Pilots (2/4)
An example procedure to correct the UL phase error for OAC is as follows:
AP:
STA :
Phase est.
Step 1b
Step 1a
Phase est.
: Transmit a pilot from AP
: Transmit a phase-coded pilot from STA
: Transmit a phase-coded pilot from AP
(Aggregation) : Transmit a phase-coded parameter (e.g., is a gradient) from STA
AP estimates the phase in UL:

## Slide 17: Phase-Coded Pilots (3/4)
An example procedure to correct the UL phase error for OAC is as follows:
AP:
STA :
Phase est.
Step 1c
Step 1b
Step 1a
Phase est.
Phase est.
: Transmit a pilot from AP
: Transmit a phase-coded pilot from STA
: Transmit a phase-coded pilot from AP
(Aggregation) : Transmit a phase-coded parameter (e.g., is a gradient) from STA`
STA estimates the phase in DL:

## Slide 18: Phase-Coded Pilots (4/4)
An example procedure to correct the UL phase error for OAC is as follows:
AP:
STA :
Phase est.
Step 2
Step 1c
Step 1b
Step 1a
Phase est.
Phase est.
: Transmit a pilot from AP
: Transmit a phase-coded pilot from STA
: Transmit a phase-coded pilot from AP
(Aggregation) : Transmit a phase-coded parameter (e.g., is a gradient) from STA`
The remaining phase error at the AP:

## Slide 19: An Example for Phase Error
Suppose that the residual CFO after a pre-compensation is [4, pg. 904]
Timings
  NDP + SIFS ~
Velocity ,

## Slide 20: Extending Phased-Coded Pilots to Multiple STAs
More STAs cause more overhead in this example procedure
  Room for optimization by exploiting the coherence bandwidth of the channel
  Notice that the duration of the aggregation phase will be much larger than the one for phase synchronization as the aggregation phase carries phase-coded symbols (e.g., local gradients)
:Phase-coded pilots
:Phase-coded OAC symbols
:Pilots (without phase coding)
AP:
STA 1:
STA 2:
STA 3:
Request
NDP
FB
NDP
FB
NDP
FB
Aggregation phase
Local gradients
Local gradients
Local gradients
Phase synchronization phase

## Slide 21: Proof-of-Concept Demonstration – SDR Specifications
In the demonstrations, we use low-cost & off-the-shelf SDRs (Analog Device Adalm Pluto) (see [5] and [6] for specifications)
  For plausibility of the demos, we do not use cable- or GPS-based clock synchronization
  The clock rate is set to 20 Msps for all SDRs
The SDR has a very small FPGA; not possible to implement 802.11 PHY
  Instead, we implement a minimum set of TX and RX blocks to demonstrate the ideas
  SDRs transmit phase-coded sequences to obtain the phase correction values
  The gap between the sequences does not follow IEEE 802.11 rules
We use a basic CFO pre-compensation before phase-coded pilots:
  The AP transmits a sequence and the STAs adjust their local oscillators
  Measured residual CFO is about 25 Hz – 50 Hz in our experiments

## Slide 22: Proof-of-Concept Demonstration 1 – Single STA
The STA transmits as IQ data ( is the correction, )
  The goal is to observe whether the phase is aligned at 0 radians (i.e., in-phase) after UL channel
  We capture the signals at the AP while AP and STA are transmitting
AP TX:
STA TX:
AP RX:
: Phase-coded pilots
: Phase-coded waveform
: Pilots (without phase coding)
  \
Goal: Recover
After the channel
  Without phase correction:

## Slide 23: Proof-of-Concept Demonstration 1 – Single STA
STA
AP

## Slide 24: Proof-of-Concept Demonstration 2 – Two STAs
STA 1 and STA 2 transmit and , respectively, where and
  We do not superpose the signals to observe whether their phases are aligned at 0 radians (i.e., in-phase) at the AP side
AP TX:
STA 1 TX:
AP RX:
STA 2 TX:
: Phase-coded pilots
: Phase-coded waveform
: Pilots (without phase coding)
Goal: Observe phase synchronization (recovering and )
After the channels

## Slide 25: Proof-of-Concept Demonstration 2 – Two STAs
STA 2
STA 1
AP

## Slide 26: Proof-of-Concept Demonstration 3 – Superposition
STA 1 and STA 2 transmit a ramp function and a sine function as test waveforms at the same time to demonstrate the coherent superposition
AP TX:
STA 1 TX:
AP RX:
STA 2 TX:
Goal: Observe coherent superposition:
: Phase-coded pilots
: Phase-coded waveform
: Pilots (without phase coding)

## Slide 27: Proof-of-Concept Demonstration 3 – Superposition
STA 2
STA 1
AP

## Slide 28: Conclusions
We study phase synchronization in the network for wireless federated learning with over-the-air computation
  We demonstrate on how we can maintain phase synchronization with phase-coded pilots
Note that our demos are not based on 802.11 sounding procedures
  Our goal is to study the feasibility of phase synchronization
  The existing procedures may be reused or enhanced for phase synchronization
Areas to explore:
  Phase and amplitude synchronization
  A model to study the existing 802.11 protocols
  A better residual CFO performance

## Slide 29: References
[1] H. B. McMahan, E. Moore, D. Ramage, S. Hampson, and B. A. y Arcas, “Communication-efficient learning of deep networks from decentralized data,” 2017
[2] 09/22 - IEEE 802.11-22/1483r1 Wireless for ML - Over-the-Air Computation
[3] 11/24 - IEEE 802.11-24/1542r5 Sounding Schemes for Coordinated Beamforming
[4] IEEE 802.11be/D7.0, August 2024
[5] Rev. C. https://wiki.analog.com/university/tools/pluto/devs/specs
[6] AD9363, https://www.analog.com/media/en/technical-documentation/data-sheets/AD9363.pdf