## Slide 1: PPDU Format for IMMW
Date: 2025-03-12
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St 550, San Diego CA 92131 |  | sanggook.kim@lge.com

## Slide 2: Introduction
Many contributions discussed high level design ways and technical scope for IMMW during the SG phase [1-6]
  Although some details are slightly different, all of them have almost identical views
    Leverage the sub-7 GHz PHY design and 11be MLO architecture
In this contribution, we discuss PPDU formats for IMMW
  We consider two options for a basic PPDU format
  We also introduce two additional PPDU formats which can be considered in IMMW

## Slide 3: Basic PPDU Format (1/4)
We propose the following two PPDU formats
  Option 1: 11a like PPDU
  Option 2: 11ac/ax like PPDU
STF and STF1 need to have a structure which can perform packet detection, CFO measure as well as AGC
  E.g, 10 times repetition of a 0.8/N us signal (N times upclocking applied)
LTF and LTF1 need to have a structure which can perform CFO measure as well as channel estimation
  E.g., GI2 + LTS + LTS
SIG can consist of a couple of different types
Other fields can be added such as PE and TRN
STF | LTF | SIG | Data
STF1 | LTF1 | SIG | STF2 | LTF2 | Data

## Slide 4: Basic PPDU Format (2/4)
Option 1: 11a like PPDU
  11bq is the first version leveraging the sub-7 GHz PHY design in a mmWave band, and thus, we may not have to consider a legacy preamble part
    This option has an advantage in terms of the overhead
    While we can consider forward compatibility and the SIG part can include PHY version ID
  If IMMW supports multi-bandwidth and multi-stream, these information may need to be exchanged in sub-7 GHz prior to a mmWave PPDU transmission
    In order to decode the Data part, bandwidth and the number of streams / LTF symbols may need to be known before receiving the PPDU for the AGC and channel estimation performed in the STF and LTF, respectively
  Each field design depends on a tone plan and we can consider two approaches
    For implementation simplicity, the tone plan can be defined for the smallest bandwidth and it can be duplicated in a wide bandwidth, i.e., all of the fields have a duplicated structure
    For throughput enhancement, the tone plan can be independently defined in each bandwidth and STF, LTF and SIG design can also follow the tone plan, i.e., the structure of these fields is not duplicated in each channel
  We can also further consider data duplication similar to non-HT duplicate PPDU assuming the first approach on the tone plan design

## Slide 5: Basic PPDU Format (3/4)
Option 2: 11ac/ax like PPDU
  We can simply use an 11ac/ax PPDU with a slight modification for consistent implementation between sub-7 GHz and mmWave bands
  If MIMO is supported in IMMW, this structure may be more efficient for MIMO AGC and MIMO channel estimation
    For future extension, this structure, especially 11ax like PPDU which can also support OFDMA, may have benefits
  Information regarding bandwidth and the number of streams / LTF symbols can be included in SIG which enables a flexible use of bandwidth and spatial stream
  Similar to option 1, we can consider two approaches for a tone plan design
    For implementation simplicity, the tone plan can be defined for the smallest bandwidth and it can be duplicated in a wide bandwidth, i.e., all of the fields have a duplicated structure
    For throughput enhancement, the tone plan can be independently defined in each bandwidth and STF2 and LTF2 can follow them while STF1, LTF1 and SIG can still have a duplicated structure similar to the pre-VHT/HEW modulated part in a sub-7 GHz PPDU. In this case, estimated channel state obtained from LTF1 and LTF2 can be used to decode SIG and Data part, respectively.

## Slide 6: Basic PPDU Format (4/4)
If most of the mmWave PPDU transmissions use one spatial stream in the smallest bandwidth to reduce implementation complexity and beamforming training overhead, option 1 may be reasonable
  When using option 2 in this case, STF2 and LTF2 can be just overhead
Considering supporting a variety of use cases including high throughput and low latency in IMMW, it would be good to define multiple bandwidths and/or support MIMO
  In this case, option 2 may be more reasonable
We are open for both PPDU formats for now and need further discussion
  We can adopt both PPDU formats to support different use cases
Meanwhile, when it comes to the tone plan design, we propose to duplicate a tone plan of the smallest bandwidth
  The allowed bandwidths may be already enough for high data rate and we don’t think we need to further optimize the tone plan according to the bandwidth
  This approach allows separate PHYs to process each frequency subblock

## Slide 7: Consideration on Additional PPDU formats
In 11bn, there are some additional PPDUs for specific purposes
  EHT sounding NDP for sounding and beamforming
  Enhanced long range PPDU to overcome coverage difference between DL and UL
In IMMW, we can also consider several additional PPDUs
  NDP like PPDU
    It can be formed based on the basic PPDU format by excluding the Data part and used for (fast / simplified) beam training
    Required information for beam training can be exchanged in the sub-7 GHz band and/or included in the SIG field of the PPDU
  Enhanced long range PPDU
    It can be used to overcome coverage limit caused by a beamforming gain difference between STAs, roughly trained beamforming or an omnidirectional transmission/reception
    As a result, it can help to prevent a frequent transition to a sub-7 GHz band caused by beamforming issues
    To this end, several approaches such as power boosting, lower MCS and signal repetition can be applied to the basic PPDU format

## Slide 8: Summary
We have discussed two basic PPDU formats
  There are pros and cons in each option and we are open for now
  We can consider adopting both formats for different use cases
We have also proposed how to design a tone plan for a wide bandwidth
  We can have benefits from duplicating a tone plan of the smallest bandwidth
Finally, we have introduced two additional PPDU formats
  The purpose of them can be beamforming training and coverage extension

## Slide 9: Straw Poll #1
Do you support to define the following PPDU format in 11bq?
  11a like PPDU
    Details for each field are TBD
STF | LTF | SIG | Data

## Slide 10: Straw Poll #2
Do you support to define the following PPDU format in 11bq?
  11ac/ax like PPDU
    Details for each field are TBD
STF1 | LTF1 | SIG | STF2 | LTF2 | Data

## Slide 11: Straw Poll #3
Do you support a duplicated tone plan for a Data field of a wider bandwidth PPDU based on a tone plan of the smallest bandwidth?

## Slide 12: Straw Poll #4
Do you support to define NDP like PPDU in 11bq?
  Details for each field are TBD
  Note that this PPDU can be used for beamforming training but need further discussion

## Slide 13: Straw Poll #5
Do you support to define enhanced long range PPDU in 11bq?
  Details for each field are TBD
  Note that this PPDU can be used to overcome coverage limit but need further discussion

## Slide 14: References
[1] 11-23-1819-01-immw-integrated-mmwave-design-considerations
[2] 11-23-1878-01-immw-high-level-design-considerations-of-immw
[3] 11-23-1905-00-immw-high-level-thoughts-on-immw
[4] 11-23-1968-00-immw-discussion-on-general-direction-of-integrated-mmwave
[5] 11-23-2004-00-immw-technical-scope-proposal
[6] 11-24-0066-00-immw-discussion-on-target-objectives-for-immw