## Slide 1: Co-BF CSI Feedback Discussions
Date: YYYY-MM-DD
Authors:

## Slide 2: Introduction
Two sounding sequences are defined for Co-BF in 11bn [1].
  Joint Sounding
  Sequential Sounding
Unlike non-Co-BF AP sounding, Co-BF sounding requires CSI reception at two APs.
STA’s sounded CSI needs to be delivered to an OBSS AP. It has been a challenging issue.
Overhearing has been implied as the default option to enable OBSS CSI feedback and discussed in multiple contributions [2][3][5].
We aim to complete Co-BF CSI delivery scheme dealing with the cases when in-BSS or cross-BSS CSI delivery fails.

## Slide 3: Joint Sounding
STA1’s sounded CSI needs to be sent to AP1(the initiating AP) and AP2 (the responding AP)

## Slide 4: Sequential Sounding
STA1’s sounded CSI needs to be sent to AP2 (the responding AP) in cross-BSS sounding stage

## Slide 5: Default CSI Delivery Mechanism
CSI from STA1 is sent using over the air link to AP1. AP2 overhears the CSI feedback PPDU
Pros:
  Save time ( if AP2 can overhear successfully)
Cons:
  Link quality from STA1 to AP2 is unknown to AP1. AP1 relies on AP2 to provide recommended MCS(s) in previous NDPA frame [4].
  Channel condition may change significantly between previous OBSS AP NDPA frame and current sounding time. Recommended MCS from AP2 may be outdated.
  Next step is undefined yet. Unlike non-Co-BF AP sounding, both AP1 and AP2 may fail in CSI reception.

## Slide 6: The Next Step
If AP1 fails to receive CSI
Option: Similar to EHT, AP1 may repeat the entire sounding sequence.
If AP1 succeeds in receiving CSI
  AP1 needs to get the status (a Boolean value) of AP2’s OBSS CSI reception status
  If AP2 indicates OBSS CSI reception failure, AP1 may decide either
    To send CSI to AP2 (via over-the-air link or wired backhaul) or
    To restart the entire sounding sequence or
    To terminate the Co-BF sounding and cancels the subsequent Co-BF transmission.

## Slide 7: OBSS CSI Reception Status Check
OBSS CSI reception at the responding AP status check is needed for the initiating AP to make decision on the next move.
Either the initiating AP or the responding AP may start the process to complete OBSS CSI reception status check
  AP1 inquires AP2 (preferred)
  Or AP2 reports to AP1
The details of each option is TBD.

## Slide 8: If AP2 fails in OBSS CSI reception: Option A
AP1 sends the OBSS CSI to AP2 via over the air link if AP2 overhearing fails.
Pros:
  Link between APs are secure and usually higher quality. AP1 can measure the link quality before sounding phase to set MCS and NSS properly.
  Prior efforts for Co-BF preparation are not wasted.
Cons:
  Additional procedure to exchange information between two APs is to be defined.
Note: the option that AP1 sends CSI to AP2 via wired backhaul (if exists) is possible
but is beyond the scope of 802.11 standards.

## Slide 9: If AP2 fails in OBSS CSI reception: Option B
Option B: AP1 restarts the entire sounding sequence
Pros:
  No new sequence to be defined.
  Behaves similarly as in EHT
  Prior efforts for Co-BF preparation are not wasted.
Cons:
  More time than option A.
  Prone to fail again if channel condition does not change meaningfully between these two sounding phases.

## Slide 10: If AP2 fails in OBSS CSI reception: Option C
AP1 terminates the sounding sequence and subsequent Co-BF transmission.
Pros:
  No new sequence to be defined.
Cons:
  Prior efforts in Co-BF preparation are wasted.

## Slide 11: Summary of Our Proposal
In UHR Co-BF sounding phase, if the initiating AP (AP1) fails to receive CSI over the air, the initiating AP may repeat the entire sounding sequence.
If the initiating AP receives CSI, it needs to get CSI reception status from the responding AP.
In case OBSS CSI overhearing fails, the initiating AP may
  Send CSI to the responding AP (AP2) (preferred) or
  Repeat the sounding sequence or
  Terminate the sounding sequence and subsequent Co-BF transmission

## Slide 12: References
[1] IEEE P802.11bn/D0.1
[2] 11-24-1823r0, CSI in Sounding in CBF
[3] 11-24-1843r0, OBSS Sounding for C-BF
[4] 11-25-0078r0, Special STA Info Field in UHR NDPA
[5] 11-25-0014r8, TGbn Motions List –Part 2, Motion 250.