## Slide 1: Multiple Shared AP Allocation in Co-TDMA
Date: 2025-03-07
Authors:

## Slide 2: Introduction
According to Motion #46 [1], TGbn shall define a Coordinated TDMA (Co-TDMA) procedure for an AP to share its time resources of an obtained TXOP with a set of APs.
  Set of APs is TBD, where the set can consist of one AP.
Accordingly, Co-TDMA sharing AP may share portions of its obtained TXOP with one or more polled APs.
Before sharing a portion/portions of the obtained TXOP with one or more polled APs, Co-TDMA sharing AP may not be transmitting an announcement frame to inform polled APs of upcoming TXOP allocations according to the PDT MAC Co-TDMA [2].
In this contribution, we consider several solutions to inform polled APs of upcoming TXOP allocations in the absence of an announcement frame.

## Slide 3: Announcement Frame during Co-TDMA
In some proposals for Co-TDMA, sharing AP transmitted an announcement frame to inform shared APs of upcoming TXOP allocation schedules in the current TXOP [3-5].
Accordingly, after receiving response(s) to the ICF, AP1 announced the upcoming TXOP allocation schedule for APs with a separate frame. Hence, polled APs could plan their upcoming transmission schedules.
However, one disadvantage of the announcement frame may be to increase the overhead.
ICF
Resp. to AP1
Frame exchanges within BSS1
MU-RTS TXS TF
AP1
AP2
AP3
Resp. to AP1
CTS to AP1
Frame exchanges within BSS2
(Co-TDMA sharing AP)
AP4
TXOP return
Resp. to AP1
Announ. frame
Allocation info for AP2
AP3 learns it will not be assigned TXOP
AP4 learns it will not be assigned TXOP
AP2 learns it will be assigned TXOP

## Slide 4: Problem due to not knowing TXOP Allocation Schedule
According to the current PDT MAC Co-TDMA [2], after AP1 transmits an ICF to poll the AP(s) and receives responses to the ICF, it does not announce the TXOP allocation schedule to the polled AP(s).
In case AP1 wants to allocate portions of its TXOP to multiple APs, the polled APs do not know whether and/or when they will be allocated TXOP.
Not knowing this information, polled APs may not plan their upcoming transmissions effectively.
  For example, AP3 may have requested TXOP allocation for transmission of buffered traffic. If AP3 waits for a second MU-RTS TXS TF for TXOP allocation, it may have to discard buffered traffic if not allocated a portion of TXOP. However, if AP3 knows it will not be allocated TXOP, it may try to transmit buffered traffic (e.g., via NPCA) instead of waiting for a TXOP allocation.
ICF
Resp. to AP1
Frame exchanges within BSS1
MU-RTS TXS TF
AP1
AP2
AP3
Resp. to AP1
CTS to AP1
Frame exchanges within BSS2
TXOP
(Co-TDMA sharing AP)
AP4
Polling phase
TXOP allocation phase
TXOP return
TXOP return phase
Resp. to AP1
CTS to AP1
Frame exchanges within BSS4
AP3 and AP4 do not know whether and/or when they will be allocated TXOP
MU-RTS TXS TF

## Slide 5: Option-1: Announcement during TXOP Allocation
Instead of transmitting an additional frame to announce the schedule for TXOP allocation at the end of polling phase, AP1 may transmit an MU-RTS TXF trigger frame with user info fields indicating the allocation order and the allocation (e.g., 1st user info field is for AP2 and the 2nd user info field is for AP4) at the beginning of TXOP allocation phase.
Multiple user info fields are not used to allocate TXOP to APs in the 2nd and later (3rd, 4th, etc.) user info fields but to inform the APs of upcoming allocations. As such, after the first allocation, AP2 returns the TXOP to AP1 and AP1 re-allocates TXOP.
Receiving MU-RTS TXS trigger frame and finding its own AID12 in a user info field, AP4 may prepare for an upcoming TXOP allocation. Not finding its own AID12 in a user info field, AP3 may plan transmission of its buffered data accordingly.
Multiple user info fields
(1st:AP2; 2nd:AP4)
AP3 learns it will not be assigned TXOP
AP4 learns it will be assigned TXOP
ICF
Resp. to AP1
Frame exchanges within BSS1
MU-RTS TXS TF
AP1
AP2
AP3
Resp. to AP1
CTS to AP1
Frame exchanges within BSS2
TXOP
(Co-TDMA sharing AP)
AP4
Polling phase
TXOP allocation phase
TXOP return
TXOP return phase
Resp. to AP1
CTS to AP1
Frame exchanges within BSS4
MU-RTS TXS TF

## Slide 6: Option-2: Indicating whether single/multiple AP allocation
AP1 may inform polled APs whether a portion/portions of TXOP will be shared with a single AP or multiple APs.
AP1 may transmit this indication either in the ICF or the MU-RTS TXS trigger frame.
If the indication is in the ICF, all polled APs may wait to receive the first TXOP allocation.
  If the indication is for multiple AP allocation, AP3 and AP4 may prepare for an upcoming TXOP allocation after the first MU-RTS TXS TF.
If the indication is in the MU-RTS TXS trigger frame (and the indication is for multiple AP allocation), AP3 and AP4 may prepare for an upcoming TXOP allocation. As in the example, the second TXOP allocation may be for AP4.
Indication of TXOP allocation to single/multiple AP(s)
AP3 learns it may be assigned TXOP
AP4 learns it may be assigned TXOP
ICF
Resp. to AP1
Frame exchanges within BSS1
MU-RTS TXS TF
AP1
AP2
AP3
Resp. to AP1
CTS to AP1
Frame exchanges within BSS2
TXOP
(Co-TDMA sharing AP)
AP4
Polling phase
TXOP allocation phase
TXOP return
TXOP return phase
Resp. to AP1
CTS to AP1
Frame exchanges within BSS4
MU-RTS TXS TF
Indication of TXOP allocation to single/multiple AP(s)
OR

## Slide 7: Conclusion
In this contribution, we considered several solutions to inform polled APs of upcoming TXOP allocations in the absence of an announcement frame in a Co-TDMA procedure.
As one solution, Co-TDMA sharing AP can use user information fields of the MU-RTS TXS trigger frame to inform polled APs of upcoming TXOP allocations.
  Polled APs are informed about accurate TXOP allocation(s). This can be achieved by using 2nd, 3rd, etc. user info fields for schedule announcement purposes.
As another solution, Co-TDMA sharing AP may inform polled APs regarding whether there will be a portion/portions of TXOP allocated to a single AP or multiple APs.
  Polled APs are informed about whether there is/are single/multiple AP allocations. This may help polled APs make more informed decisions during the Co-TDMA procedure. This can be achieved by having an indication in the ICF or in the MU-RTS TXS trigger frame.

## Slide 8: References
[1] 24/0171r26, TGbn Motions List – Part 1
[2] 25/0521r2, PDT-MAC-Co-TDMA-CR-CC50-Part-1
[3] 23/1895r2, C-TDMA Follow-up
[4] 24/0423r0, NAV Rules in C-TDMA
[5] 24/2126r1, Intention Announcement and Feedback in Multi-AP Coordination

## Slide 9: Straw Poll – 1
Do you agree to add the following text to the TGbn SFD?
As part of Co-TDMA operation, TGbn defines a mechanism for a Co-TDMA sharing AP to inform polled APs, during the TXOP allocation phase via the MU-RTS TXS Trigger frame, of any further allocations of the TXOP.
  Yes
  No
  Abstain
  Y/N/A:

## Slide 10: Straw Poll – 2
Do you agree to add the following text to the TGbn SFD?
As part of Co-TDMA operation, TGbn defines a mechanism for a Co-TDMA sharing AP to indicate whether the TXOP will be shared with a single AP or more than one APs.
  Yes
  No
  Abstain
  Y/N/A: