## Slide 1: Roaming through Target AP - Follow Up
Date: 2025-06-10
Authors:

## Slide 2: Seamless Roaming Sequences
For 11bn SR, roaming preparation and execution phases have been defined in D0.1
Following sequences are possible for SR:
  Sequence A1: Roaming preparation and roaming execution through current AP MLD.
  Sequence A2: Given roaming preparation is optional, a non-AP MLD directly performs roaming execution through current AP MLD, that also includes link setup and context transfer.
  Sequence B1: Roaming preparation through current AP MLD and PMF protected roaming execution directly through a target AP MLD (for panic/last-minute roam, shared PTK or per-AP PTK mode).
  Sequence B2: PMF protected roaming execution directly through a target AP MLD (that was prepared with STA context using a pre-roaming prep), no roaming prep was done through current AP. Direct roaming execution through target performs both link setup and context transfer (for panic/last-minute roaming, shared PTK mode)
A1, A2 sequences are for SR through current AP MLD
B1, B2, sequences are for SR through a target AP MLD

## Slide 3: Sequence B1: Roaming Through Target AP
SMD level PMK, PTK, Roaming MAC Address provided to target AP during roaming prep
STA sends a PMF protected Roaming execution request to the target AP, with TA set to Roaming MAC Address
Target AP MLD identifies the STA based on TA and maps to shared PTK
  PN based replay detection will pass
  Fetches latest PN from serving AP MLD

## Slide 4: Sequence B2: Roaming Through Target AP
SMD level PMK, PTK and the Roaming MAC Address transferred to target APs during pre-roaming prep
STA is notified of pre-roaming prep completion (e.g. using BTM Request)
STA sends a PMF protected Roaming execution request to the target AP, with TA set to Roaming MAC Address
Target AP MLD identifies the STA based on TA and maps to shared PTK
  Replay check based on a Timestamp/TSF field from the encrypted frame body (see next slide)
  STA context fetched from old AP after replay check passes (then can perform PN replay check)

## Slide 5: SP
Do you agree that a non-AP MLD that has performed initial SMD association using the shared PTK mode, can send a PMF protected roaming execution request directly to a target AP MLD in following conditions?
The non-AP MLD has performed a roaming preparation for that target AP MLD through the current AP MLD, or it has received a BTM Request from its current AP MLD indicating that the target AP MLD has been prepared by the network for direct roaming through target AP.
TA field in the PMF protected roaming execution request is set to a Roaming MAC address
Target AP MLD uses the Roaming MAC address received (in TA field) to identify the non-AP MLD

## Slide 6: References
[1] 11-24-1812 “Seamless Roaming through a Target AP - Follow Up”