## Slide 1: Enhancement of DPS Operation - in the Presence of Legacy STA
Date: 2025-05-07
Authors:

## Slide 2: Introduction
Dynamic power saving (DPS) is one of the features being considered for 802.11bn.
In this work, we consider a DPS (mobile) AP operating in the presence of a legacy STA that is lack of DPS capability and discuss some methods to improve the power-efficiency of DPS (mobile) AP.

## Slide 3: Background
In Draft IEEE802.11bn D0.2, subclause 37.10.1 DPS Operation:
  An AP may enable its DPS mode only under TBD conditions. A DPS AP shall have value 1 in its transmitted DPS Enabled field to announce that it has enabled DPS and 0 otherwise. The mechanism for enablement/disablement of DPS by an AP is TBD.
  A DPS STA is either a DPS non-AP STA or a DPS mobile AP. It is TBD whether an AP that is not a Mobile AP may be a DPS AP or not.
  The DPS operation allows a DPS STA to operate in lower capability (LC) mode and to transition to higher capability (HC) mode upon reception of an ICF [TBD] transmitted by its associated DPS assisting STA. The DPS STA in higher capability (HC) mode transitions back to the LC mode under TBD conditions.
  A DPS STA that is in LC mode shall be capable of receiving TBD PPDUs (e.g., with non-HT (duplicate) format using a rate of 6 Mb/s, 12 Mb/s, 24Mb/s[TBD]). A DPS STA that is in HC mode (e.g., operating BW, NSS and MCSs) shall be capable of receiving all supported PPDU formats corresponding to the HC mode.

## Slide 4: UHR AP in the Presence of Legacy STA (Motivation)
Before an UHR (mobile) AP (AP1) enables DPS mode, or after it enables DPS mode, aka. DPS (mobile) AP, while operating in HC mode, it may receive an association procedure from an STA (STA1) with AP1.
STA1 may be a legacy STA that does not have the capability of DPS mode.
  STA1 doesn’t support to solicit AP1 to transition from the LC mode to the HC mode. In other words, STA1 doesn’t support to send an ICF ahead of transmitting a PPDU other than non-HT format.
Based on STA1 associating with AP1, AP1 may decide not to transition to the LC mode. So that AP1 can continue serve STA1.
  e.g., AP1 may send a management frame (beacon/association response) to announce the transition in advance; but STA1 doesn’t recognize the announcement.
As such, AP1 may remain in the HC mode (i.e. being precluded from operating in the LC mode), and may not leverage its support of the DPS mode to reduce its power consumption.

## Slide 5: DPS (mobile) AP in the Presence of Legacy STA
During period 1, DPS (mobile) AP (AP1) sends a management frame (e.g., beacon) indicating that AP1 enables the DPS operation during period 2. AP1 transitions from HC mode to LC mode at T1.
During period 2, A legacy STA (STA1) associated with AP1 has data arrival and transmit PPDU1 (other than non-HT format) to AP1.
Without a non-HT PPDU soliciting AP1 transition from LC to HC mode, AP1 remains in LC mode and fails to receive PPDU1 and retransmissions (e.g., PPDU2, PPDU3, …) from STA1.

## Slide 6: Inter-AP Notification for DPS (mobile) AP (Solution)
Assumption: The DPS (mobile) AP (AP1) and a DPS assisting AP (AP2) are in a same multi-AP coordination group.
DPS (mobile ) AP (AP1) sends a request frame to AP2, requesting for AP2 to:
  monitor PPDUs addressed to AP1 (e.g., detecting PPDUs other than non-HT PPDU format) and
  send an ICF notifying AP1 of reception of the PPDUs (other than non-HT PPDU), when AP1 operates in the LC mode.
AP2 sends to AP1 the ICF notifying the receiving PPDU1 transmitted by a legacy STA (STA1) associated with AP1.
After receiving the ICF (notification), AP1 transitions from the LC mode to the HC mode.
STA1 retransmits to AP1 PPDU 1 as PPDU 2.
  e.g., AP1 may sends a trigger frame (TF) soliciting PPDU 2 from STA1.

## Slide 7: Summary
We propose a method of inter-AP notification to solicit a DPS (mobile) AP transition from LC to HC to receiving PPDU from a legacy STA.

## Slide 8: Straw Poll
SP1. Do you support defining a DPS mode of operation that includes the following?
  A DPS (mobile) AP may request another STA that is an OBSS AP or a non-AP STA associated with the DPS (mobile) AP to detect PPDUs other than non-HT PPDU format addressed to the DPS (mobile) AP.
  The other STA should send to the DPS (mobile) AP an ICF to notify the DPS (mobile) AP of reception of the PPDUs other than non-HT PPDU format, when the DPS (mobile) AP operates in the LC mode.
  The PPDUs other than non-HT PPDU format may be transmitted by a non-AP STA that doesn’t support DPS mode of operation and is associated with the DPS (mobile) AP.
  Yes
  No
  Abstain

## Slide 9: References
P802.11bn Spec Draft 2.0
23/0010, UHR-SG, Considerations for enabling AP power save, Alfred Asterjadhi (Qualcomm)
23/2040, TGbn, Enabling AP power save - follow up, Alfred Asterjadhi (Qualcomm)
23/1965, TGbn, Dynamic power save – follow up, George Cherian (Qualcomm)
23/1875, TGbn, Power save proposal for non-AP/mobile-AP, Shubhodeep Adhikari (Broadcom)