## Slide 1: mmWave Link MAC: Beaconing, TXOP Protection, Medium Access, Power Save
Date: 2025-05-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Justification of mmWave Beaconing
It is difficult to figure out whether a non-AP MLD can reach an AP MLD in mmWave link through the measurement of non-mmWave link.
An unassociated non-AP MLD figures out the Beacon Tx time and mmWave link channel of the mmWave AP affiliated with the same AP MLD as the non-mmWave AP(s) through the non-mmWave AP(s).
The unassociated non-AP MLD may listen to the mmWave Beacon at the Beacon Tx time in the mmWave link to figure out whether it can reach the AP MLD in mmWave link.

## Slide 3: On-demand vs Periodic Beacon/NDP
A mmWave Beacon can be a NDP PPDU with BSS color, Beam sector used to transmit the Beacon, remaining Beacons being transmitted in this Beacon burst.
On-demand Beacon (or NDP on mmWave Link):
  When a non-AP MLD needs to decide whether it can reach an AP MLD in mmWave link, the non-AP MLD and the AP MLD can negotiate the mmWave Beacon Tx SP (start time, duration).
    The AP of the AP MLD in mWave link schedules the transmission of the Beacons (NDP frames) at the mmWave Beacon Tx SP for the non-AP MLD’s link quality measurement.
Periodic Beacon:
  When an IMMW AP schedules the transmission of its Beacons, e.g. at TBTT, a group of Beacons are transmitted through the different sectors sequentially in a TXOP.
    Such Beacons belong to a Beacon burst.

## Slide 4: TSF Related Operation
A non-AP MLD can’t do the TSF synchronization with the AP MLD when on-demand Beacon is used.
One method for TSF related operation is that the TSF time and number of TBTT are defined based on another active link (reference link) of the AP MLD.
  The operation per the TBTT, e.g. BSS color change of mmWave link will use the TBTT of the reference link.
  The operation per the TBTT, e.g. BSS color change of mmWave link will use the reference link’s TBTT.
Another method is that the TSF time and TBTT of the mmWave link are defined without the Beacon transmission
  TBTT is virtual since no Beacon is scheduled for the transmission at the TBTT on mmWave link.
  The operation per the TBTT, e.g. BSS color change of mmWave link will use the virtual TBTT.

## Slide 5: TXOP Protection
The duplicate PPDU is defined with each PPDU covers the narrowest BW of mmWave link, e.g. 160MHz.
  The duplicate PPDU can be one PPDU in BW of 160MHz, two PPDUs in BW of 320MHz, 4 PPDUs in BW of 640MHz…
The TXOP can be protected by the RTS/CTS exchange at the beginning of the TXOP in duplicate PPDU.
  MU-RTS/CTS is not allowed.
Static and dynamic BW negotiation are allowed.
The TXOP field in PHY SIG indicates the remaining of the TXOP if the BSS color collision doesn’t happen. Otherwise the TXOP field in PHY SIG indicates UNSPECIFIED.
  An variant is that the TXOP field in PHY SIG indicates the remaining time of the TXOP even if the BSS color collision happens.

## Slide 6: Responding PPDU
The responding frame is carried in duplicate PPDU so that the third-party STA can detect the Duration field in MAC header of the responding frame.
  Justification of such operation: the Duration field provide more accurate remaining time of a TXOP then the TXOP field in PHY header.

## Slide 7: EDCA Backoff in mmWave Link
NAV timer at non-AP STA or AP
  Option 1:
    Each STA has one basic NAV timer and one intra-BSS NAV timer.
      This is useful when multiple STAs are scheduled in one TXOP by the associated AP and CCA sensing is required for STA’s UL long PPDU transmission.
  Option 2:
    Each STA has one NAV timer.
A mmWave AP performs backoff before initiating a TXOP.
A mmWave AP announces the EDCA parameters through non-mmWave link.
A non-AP mmWave STA performes backoff if allowed by the peer mmWave AP (e.g. when the AP is near the STA enough, or when single non-AP STA exists in a TWT SP) or peer non-AP mmWave STA.

## Slide 8: Frame Exchanges in mmWave Link
After the mmWave link is established (i.e. beam sector is selected after beam training), the responding frames to acknowledge the QoS Data frame(s) or Management frames in mmWave link are transmitted in mmWave link.
After the mmWave link is established, the control frame exchange to protect the TXOP of mmWave link is done in mmWave link.
STA’s frame transmission under the condition that the STA is not allowed to do the backoff
  Option 1: Trigger-based PPDU transmission.
    Non-TB PPDU solicited by the Trigger frame.
  Option 2: transmission per TXOP sharing.

## Slide 9: Frame Exchange with and without ITWT
TWT for frame exchanges
  A non-AP MLD with MMW link negotiates the TWT agreement of MMW link with its associated AP MLD through <=7GHz band link.
  At the start time of the negotiated MMW TWT SP, a MMW STA does the frame exchanges by using its the receive/transmit beam decided through sounding procedure with its peer STA until the end of MMW ITWT SP.

## Slide 10: Frame Exchange with and without ITWT
Frame Exchanges outside TWT SP.
  A MMW STA notifies its intention of frame exchange with the peer MMW STA through <=7GHz band link.
  The ICF, ICR in <=7GHz band link can be designed for such negotiation.
  At the agreed start time, the associated MMW STA does the frame exchanges by using its the receive/transmit beam decided through sounding procedure with the peer MMW STA until the end of the TXOP.
    One variant is that if the used BW is not same as the reference BW of the negotiation, the SP duration will be updated accordingly.
      The AP can decide whether the SP extension is allowed or not.

## Slide 11: Power Save
AP power save
  Outside the negotiated MMW ITWT SP, the MMW AP is in power save mode and doze state.
    At the start of the negotiated TWT SP with an MMW STA, the AP is in awake state until the end of the TWT SP or there are no DL frames, UL frames for the transmission.
  Without the negotiated MMW ITWT agreement with any MMW STA, the MMW AP is in power save mode and doze state.
    If the MMW AP and MMW STA negotiate the active duration to do the frame exchanges, at the negotiated start time, the AP is in awake state until the end of the negotiated active duration or there are no DL frames, UL frames that need to be transmitted.
Non-AP STA power save
  Outside the negotiated MMW ITWT SP, the MMW non-AP STA is in power save mode and doze state.
    At the start of the negotiated ITWT SP with an MMW non-AP STA, the STA is in awake state until the end of the TWT SP or there are no DL frames, UL frames that need to be transmitted.
  Without the negotiated MMW ITWT agreement with the MMW AP, the MMW non-AP STA is in power save mode and doze state.
    If the MMW AP and MMW non-AP STA negotiate the active duration to do the frame exchanges, at the negotiated start time, the non-AP STA is in awake state until the end of the negotiated active duration or there are no DL frames, UL frames that need to be transmitted.