## Slide 1: NAV Setting in NPCA
Date: 2024-12-01
Authors:

## Slide 2: Introduction
To meet throughput and latency requirements mentioned in UHR PAR [1], non-primary channel access (NPCA) was proposed [2,3] as a potential method
NPCA enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions
It is a default assumption that if the secondary channel (i.e., NPCA primary channel) is occupied by the OBSS traffic or other TBD condition, the STA does not switch from the primary channel to NPCA primary channel
Inappropriate switching may occur if OBSS bandwidth occupation is determined upon the triggering even only
 NAV setting should be enhanced to note if the secondary channel is occupied by OBSS

## Slide 3: Problem Statement: An Example
STA 1 enabling NPCA is in the coverage of both OBSS STA 1 and OBSS STA 2, while OBSS STA 1 and 2 can not hear each other
  t1: STA 1 receives OBSS 1 PPDU and TXOP ends at t3
  t2: STA 1 receives OBSS 2 PPDU and TXOP ends at t4
Based on current rule, STA 1 will switch at t2
  NPCA primary channel is not covered by OBSS 2 transmission
But if STA 1 gains channel access after switching but before t3, it interferes with OBSS 1 TXOP
  STA 1 should not switch at t2, or
  STA 1 can switch at t2, but do not perform channel access until t3
OBSS 1 duration
OBSS 2 duration
STA 1
OBSS STA 1
OBSS STA 2
OBSS 1
OBSS 2
STA 1
NPCA primary channel
t1
t3
t2
t4
OBSS peer STA 1
OBSS peer STA 2
p80
s80
Peer STA 1

## Slide 4: Primary NAV + Secondary NAV
An NPCA STA maintains not only NAV for the primary channel but also opportunistically NAV for the NPCA primary channel when parking on primary channel
  If a received PPDU indicates bandwidth covering the NPCA primary channel, the NAV for the primary channel can be updated
Optionally, the NPCA STA maintains not only NAV for the NPCA primary channel but also opportunistically NAV for the primary channel when parking on NPCA primary channel
  If a received PPDU indicates bandwidth covering the primary channel, the NAV for the primary channel can be update
Denote the proposed NAV setting in the form of (NAV_p, NAV_s)
  t1: (~t3, ~t3)  t2: (~t4, ~t3)
OBSS 1 duration
OBSS 2 duration
OBSS 1
OBSS 2
t1
t3
t2
t4
p80
s80
STA 1
NPCA primary channel
Bandwidth for NAV_p
Bandwidth for NAV_s

## Slide 5: Summary
NAV should be enhanced to keep track of the occupancy time of NPCA primary channel

## Slide 6: SP 1
Do you support to include the following in the spec?
  An NPCA STA shall not access the NPCA primary channel when there is an ongoing OBSS TXOP which indicates to cover the NPCA primary channel.

## Slide 7: SP 2
Do you support to include the following in the spec?
  When NPCA is enabled, primary channel and NPCA primary channel has independent basic NAV timers.

## Slide 8: References
[1] 11-24/0209r6, “Specification Framework for TGbn,” Ross Jian Yu
[2] 11-23/1935r1, “secondary channel usage follow up,” Liwen Chu
[3] 11-24/0070r2, “Some details about non-primary channel access,” Yunbo Li