## Slide 1: DS MAC Collision Warning
Date: 2025-03-10
Authors:

## Slide 2: Abstract
Why an OTA MAC can collide with more than same-link STAs

## Slide 3: Background
OTA MAC is used by the non-AP MLD on the radio link
  The STA/non-AP MLD may also express a DS MAC, for the AP to represent the STA/non-AP MLD over the DS
Question asked during D1.0 comment collection:
Can OTA collision occur with a MAC beyond the local link?

## Slide 4: IEEE 802.11 is under IEEE 802 Rules
802-2014 recommends uniqueness of MAC addresses in a LAN, i.e. a network consisting of one or more interconnected networks each using a medium access control (MAC) protocol specified in an IEEE 802 standard.
In short: you should not have the same MAC for 2 devices that can talk to each other using the MAC as SA/DA
Failure to do so is particularly problematic for devices performing forwarding functions – the AP is one of them (4.3.5.1), forwarding between WMs and DSM
  In some cases, the AP/DS forwarding function implements 802.1Q, which also forbids duplication of MACs

## Slide 5: How MACs Are Learned
The forwarding device (call it bridge for simplicity) learns MAC from hearing SA values on an interface
The bridge updates its forwarding table accordingly
SA/TA: a.b.c
radio0
radio1
radio2
Eth0
Radio0 | Radio1 | Radio2 | Eth0
a.b.c |  |  | 

## Slide 6: How MACs Are Learned
The forwarding table is used to forward (or not) incoming frames
DA: a.b.c
radio0
radio1
radio2
Eth0
Radio0 | Radio1 | Radio2 | Eth0
a.b.c |  |  | 

## Slide 7: How Fwd Tables are Updated
The forwarding table is usually CAM, and can be updated
SA/TA: a.b.c
radio0
radio1
radio2
Eth0
Radio0 | Radio1 | Radio2 | Eth0
a.b.c | a.b.c |  | 

## Slide 8: What Happens When a MAC is on 2 Interfaces
The forwarding table is updated as the MAC moves
1. SA/TA: a.b.c
radio0
radio1
radio2
Eth0
Radio0 | Radio1 | Radio2 | Eth0
 | a.b.c |  | a.b.c
2. SA: a.b.c

## Slide 9: What Happens When a MAC is on 2 Interfaces
The forwarding table is updated as the MAC moves
a.b.c
radio0
radio1
radio2
Eth0
Radio0 | Radio1 | Radio2 | Eth0
 | a.b.c |  | 
a.b.c
Need to go to yahoo: DA: a.b.c

## Slide 10: What Happens When a MAC is on 2 Interfaces
The forwarding table is updated as the MAC moves
radio0
radio1
radio2
Eth0
Radio0 | Radio1 | Radio2 | Eth0
 |  |  | a.b.c
a.b.c
Need to go to watch: DA: a.b.c

## Slide 11: How Many Times Can a MAC Move?
Implementation-dependent, but usually “not too often”
Beyond some hysteresis, the MAC, or the entire interface, may get blocked
radio0
radio1
radio2
Eth0
I am a.b.c
I am a.b.c

## Slide 12: Conclusion
A MAC cannot exist for multiple devices on an 802 Forwarding device
A STA OTA MAC should not collide with the MAC of any other device in the collision domain, wireless or wired